## Slide 1: CS 61C: Great Ideas in Computer Architecture RISC-V Instruction Formats
Instructors:
Krste Asanović and Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa17
9/14/17
Fall 2017 - Lecture #7

## Slide 2: Levels of Representation/Interpretation
lw x10, 0(x12)
lw x11, 4(x12)
sw x11, 0(x12)
sw x10, 4(x12)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., RISC-V)
Machine Language Program (RISC-V)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
Logic Circuit Description (Circuit Schematic Diagrams)
9/14/17

## Slide 3: ENIAC (U.Penn., 1946) First Electronic General-Purpose Computer
Blazingly fast (multiply in 2.8ms!)
  10 decimal digits x 10 decimal digits
But needed 2-3 days to setup new program, as programmed with patch cords and switches
9/14/17
3
Notes: -Electronic Numerical Integrator and Computer
-Digital (electronic), capable of being reprogrammed to solve a variety of mathematical problems
-Dev began at the end of WWII, was designed and primarily used to calculate artillery firing tables for the US Army’s
-Very slow to program
-Story about 2 architects who designed it and Von Neumann, how it led to EDSAC
-Slow program entry, I/O

## Slide 4: Big Idea: Stored-Program Computer
  Instructions are represented as bit patterns - can think of these as numbers
  Therefore, entire programs can be stored in memory to be read or written just like data
  Can reprogram quickly (seconds), don’t have to rewire computer (days)
  Known as the “von Neumann” computers after widely distributed tech report on EDVAC project
    Wrote-up discussions of Eckert and Mauchly
    Anticipated earlier by Turing and Zuse
First Draft of a Report on the EDVAC
by
John von Neumann
Contract No. W–670–ORD–4926
Between the
United States Army Ordnance Department and the
University of Pennsylvania
Moore School of Electrical Engineering
University of Pennsylvania
June 30, 1945
9/14/17

## Slide 5: EDSAC (Cambridge, 1949) First General Stored-Program Computer
Programs held as numbers in memory
35-bit binary 2’s complement words
9/14/17
Notes: Programming EDSAC

## Slide 6: Consequence #1: Everything Has a Memory Address
Since all instructions and data are stored in memory, everything has a memory address: instructions, data words
  Both branches and jumps use these
C pointers are just memory addresses: they can point to anything in memory
  Unconstrained use of addresses can lead to nasty bugs; avoiding errors up to you in C; limited in Java by language design
One register keeps address of instruction being executed: “Program Counter” (PC)
  Basically a pointer to memory
  Intel calls it Instruction Pointer (a better name)
9/14/17

## Slide 7: Consequence #2: Binary Compatibility
Programs are distributed in binary form
  Programs bound to specific instruction set
  Different version for phones and PCs
New machines want to run old programs (“binaries”) as well as programs compiled to new instructions
Leads to “backward-compatible” instruction set evolving over time
Selection of Intel 8088 in 1981 for 1st IBM PC is major reason latest PCs still use 80x86 instruction set; could still run program from 1981 PC today
9/14/17

## Slide 8: Instructions as Numbers (1/2)
Most data we work with is in words (32-bit chunks):
  Each register is a word
  lw and sw both access memory one word at a time
So how do we represent instructions?
  Remember: Computer only understands 1s and 0s, so assembler string “add x10,x11,x0” is meaningless to hardware
  RISC-V seeks simplicity: since data is in words, make instructions be fixed-size 32-bit words also
    Same 32-bit instructions used for RV32, RV64, RV128
9/14/17

## Slide 9: Instructions as Numbers (2/2)
One word is 32 bits, so divide instruction word into “fields”
Each field tells processor something about instruction
We could define different fields for each instruction, but RISC-V seeks simplicity, so define six basic types of instruction formats:
  R-format for register-register arithmetic operations
  I-format for register-immediate arithmetic operations and loads
  S-format for stores
  B-format for branches (minor variant of S-format, called SB before)
  U-format for 20-bit upper immediate instructions
  J-format for jumps (minor variant of U-format, called UJ before)
9/14/17

## Slide 10: Summary of RISC-V Instruction Formats

## Slide 11: R-Format Instruction Layout
32-bit instruction word divided into six fields of varying numbers of bits each: 7+5+5+3+5+7 = 32
Examples
  opcode is a 7-bit field that lives in bits 6-0 of the instruction
  rs2 is a 5-bit field that lives in bits 24-20 of the instruction
9/14/17
Field’s bit positions
Number of bits in field
Name of field

## Slide 12: R-Format Instructions opcode/funct fields
  opcode: partially specifies what instruction it is
    Note: This field is equal to 0110011two for all R-Format register-register arithmetic instructions
  funct7+funct3: combined with opcode, these two fields describe what operation to perform
Question: Why aren’t opcode and funct7 and funct3 a single 17-bit field?
  We’ll answer this later
9/14/17

## Slide 13: R-Format Instructions register specifiers
  rs1 (Source Register #1): specifies register containing first operand
  rs2 : specifies second register operand
  rd (Destination Register): specifies register which will receive result of computation
  Each register field holds a 5-bit unsigned integer (0-31) corresponding to a register number (x0-x31)
9/14/17

## Slide 14: R-Format Example
RISC-V Assembly Instruction:
  add x18,x19,x10
9/14/17
0000000
01010
10011
000
10010
0110011
Reg-Reg OP
rd=18
ADD
ADD
rs2=10
rs1=19

## Slide 15: All RV32 R-format instructions
Different encoding in funct7 + funct3 selects different operations

## Slide 16: I-Format Instructions
What about instructions with immediates?
  5-bit field only represents numbers up to the value 31: immediates may be much larger than this
  Ideally, RISC-V would have only one instruction format (for simplicity): unfortunately, we need to compromise
Define new instruction format that is mostly consistent with R-format
  Notice if instruction has immediate, then uses at most 2 registers (one source, one destination)
9/14/17

## Slide 17: I-Format Instruction Layout
9/14/17
  Only one field is different from R-format, rs2 and funct7 replaced by 12-bit signed immediate, imm[11:0]
  Remaining fields (rs1, funct3, rd, opcode) same as before
  imm[11:0] can hold values in range [-2048ten , +2047ten ]
  Immediate is always sign-extended to 32-bits before use in an arithmetic operation
  We’ll later see how to handle immediates > 12 bits

## Slide 18: I-Format Example
RISC-V Assembly Instruction:
  addi x15,x1,-50
9/14/17
111111001110
00001
000
01111
0010011
OP-Imm
rd=15
ADD
imm=-50
rs1=1

## Slide 19: All RV32 I-format Arithmetic Instructions
“Shift-by-immediate” instructions only use lower 5 bits of the immediate value for shift amount (can only shift by 0-31 bit positions)
One of the higher-order immediate bits is used to distinguish “shift right logical” (SRLI) from “shift right arithmetic” (SRAI)

## Slide 20: Administrivia
HW0 Grades were released
  If you have an issue with them, please fill out this form by tonight: https://goo.gl/forms/QH44Iw746pcCxOyH2
HW1 Part 1 Due next Monday, Part 2 Due Friday Sept 22
  Homework-oriented office hours next Monday (check the website)
  Homework Party on next Wednesday (6:30-10pm in 293 Cory)
  Autograded results to be released every noon starting this Friday
Midterm #1 in 1.5 weeks: September 26!
  Two sided 8.5” x 11” cheat sheet + RISC-V Green Card that we give you
  DSP students: please make sure we know about your special accommodations (contact Steven Ho the head TA if you haven’t yet)
9/14/17

## Slide 21: Break!
9/14/17

## Slide 22: Load Instructions are also I-Type
The 12-bit signed immediate is added to the base address in register rs1 to form the memory address
  This is very similar to the add-immediate operation but used to create address not to create final result
The value loaded from memory is stored in register rd

## Slide 23: I-Format Load Example
RISC-V Assembly Instruction:
  lw x14, 8(x2)
9/14/17
000000001000
00010
010
01110
0000011
LOAD
rd=14
LW
imm=+8
rs1=2

## Slide 24: All RV32 Load Instructions
LBU is “load unsigned byte”
LH is “load halfword”, which loads 16 bits (2 bytes) and sign-extends to fill destination 32-bit register
LHU is “load unsigned halfword”, which zero-extends 16 bits to fill destination 32-bit register
There is no LWU in RV32, because there is no sign/zero extension needed when copying 32 bits from a memory location into a 32-bit register
funct3 field encodes size and signedness of load data

## Slide 25: S-Format Used for Stores
9/14/17
  Store needs to read two registers, rs1 for base memory address, and rs2 for data to be stored, as well as need immediate offset!
  Can’t have both rs2 and immediate in same place as other instructions!
  Note that stores don’t write a value to the register file, no rd!
  RISC-V design decision is move low 5 bits of immediate to where rd field was in other instructions – keep rs1/rs2 fields in same place
    register names more critical than immediate bits in hardware design

## Slide 26: S-Format Example
RISC-V Assembly Instruction:
  sw x14, 8(x2)
9/14/17
0000000
01110
00010
010
01000
0100011
STORE
offset[4:0]
=8
SW
offset[11:5]
=0
rs2=14
rs1=2
combined 12-bit offset = 8
0000000
01000

## Slide 27: All RV32 Store Instructions

## Slide 28: RISC-V Conditional Branches
E.g., BEQ x1, x2, Label
Branches read two registers but don’t write a register (similar to stores)
How to encode label, i.e., where to branch to?

## Slide 29: Branching Instruction Usage
Branches typically used for loops (if-else, while, for)
  Loops are generally small (< 50 instructions)
  Function calls and unconditional jumps handled with jump instructions (J-Format)
Recall: Instructions stored in a localized area of memory (Code/Text)
  Largest branch distance limited by size of code
  Address of current instruction stored in the program counter (PC)
9/14/17

## Slide 30: PC-Relative Addressing
PC-Relative Addressing: Use the immediate field as a two’s-complement offset to PC
  Branches generally change the PC by a small amount
  Can specify ± 211 addresses from the PC
Why not use byte address offset from PC?
9/14/17

## Slide 31: Scaling Branch Offset
One idea: To improve the reach of a single branch instruction, multiply the offset by four bytes before adding to PC
This would allow one branch instruction to reach ± 211 × 32-bit instructions either side of PC
  Four times greater reach than using byte offset

## Slide 32: Branch Calculation
If we don’t take the branch:
  PC = PC + 4 (i.e., next instruction)
If we do take the branch:
  PC = PC + immediate*4
Observations:
  immediate is number of instructions to jump (remember, specifies words) either forward (+) or backwards (–)
9/14/17

## Slide 33: RISC-V Feature, n×16-bit instructions
Extensions to RISC-V base ISA support 16-bit compressed instructions and also variable-length instructions that are multiples of 16-bits in length
To enable this, RISC-V scales the branch offset by 2 bytes even when there are no 16-bit instructions
Reduces branch reach by half and means that ½ of possible targets will be errors on RISC-V processors that only support 32-bit instructions (as used in this class)
RISC-V conditional branches can only reach ± 210 × 32-bit instructions either side of PC

## Slide 34: RISC-V B-Format for Branches
B-format is mostly same as S-Format, with two register sources (rs1/rs2) and a 12-bit immediate
But now immediate represents values -4096 to +4094 in 2-byte increments
The 12 immediate bits encode even 13-bit signed byte offsets (lowest bit of offset is always zero, so no need to store it)

## Slide 35: Branch Example, determine offset
RISC-V Code:
  Loop: beq x19,x10,End add x18,x18,x10 addi x19,x19,-1 j Loop End: # target instruction
Branch offset =
(Branch with offset of 0, branches to itself)
4×32-bit instructions = 16 bytes
9/14/17
1
2
3
4
Count instructions from branch

## Slide 36: Branch Example, encode offset
RISC-V Code:
  Loop: beq x19,x10,End add x18,x18,x10 addi x19,x19,-1 j Loop End: # target instruction
9/14/17
???????
01010
10011
000
?????
1100011
BRANCH
imm
BEQ
imm
rs2=10
rs1=19
offset = 16 bytes = 8x2

## Slide 37: RISC-V Immediate Encoding
Instruction Encodings, inst[31:0]
32-bit immediates produced, imm[31:0]
Only bit 7 of instruction changes role in immediate between S and B
Upper bits sign-extended from inst[31] always

## Slide 38: Branch Example, complete encoding
9/14/17
0
01010
10011
000
1000
1100011
0
000000
BRANCH
BEQ
rs2=10
rs1=19
beq x19,x10, offset = 16 bytes
13-bit immediate, imm[12:0], with value 16
0000000010000
imm[4:1]
imm[0] discarded, always zero
imm[10:5]
imm[11]
imm[12]

## Slide 39: All RISC-V Branch Instructions

## Slide 40: Questions on PC-addressing
Does the value in branch immediate field change if we move the code?
  If moving individual lines of code, then yes
  If moving all of code, then no
What do we do if destination is > 210 instructions away from branch?
  Other instructions save us
9/14/17
Notes: As we will see, jumping instructions can reach farther than branching

## Slide 41: Questions on PC-addressing
Does the value in branch immediate field change if we move the code?
  If moving individual lines of code, then yes
  If moving all of code, then no (because PC-relative offsets)
What do we do if destination is > 210 instructions away from branch?
  Other instructions save us
  beq x10,x0,far bne x10,x0,next # next instr  j far next: # next instr
9/14/17
Notes: As we will see, jumping instructions can reach farther than branching

## Slide 42: Break!
9/14/17

## Slide 43: U-Format for “Upper Immediate” instructions
Has 20-bit immediate in upper 20 bits of 32-bit instruction word
One destination register, rd
Used for two instructions
  LUI – Load Upper Immediate
  AUIPC – Add Upper Immediate to PC

## Slide 44: LUI to create long immediates
LUI writes the upper 20 bits of the destination with the immediate value, and clears the lower 12 bits.
Together with an ADDI to set low 12 bits, can create any 32-bit value in a register using two instructions (LUI/ADDI).
LUI x10, 0x87654 # x10 = 0x87654000
ADDI x10, x10, 0x321 # x10 = 0x87654321

## Slide 45: One Corner Case
How to set 0xDEADBEEF?
LUI x10, 0xDEADB # x10 = 0xDEADB000
ADDI x10, x10, 0xEEF # x10 = 0xDEADAEEF
ADDI 12-bit immediate is always sign-extended, if top bit is set, will subtract -1 from upper 20 bits

## Slide 46: Solution
How to set 0xDEADBEEF?
LUI x10, 0xDEADC # x10 = 0xDEADC000
ADDI x10, x10, 0xEEF # x10 = 0xDEADBEEF
Pre-increment value placed in upper 20 bits, if sign bit will be set on immediate in lower 12 bits.
Assembler pseudo-op handles all of this:
li x10, 0xDEADBEEF # Creates two instructions

## Slide 47: AUIPC
Adds upper immediate value to PC and places result in destination register
Used for PC-relative addressing
Label: AUIPC x10, 0 # Puts address of label in x10

## Slide 48: J-Format for Jump Instructions
JAL saves PC+4 in register rd (the return address)
  Assembler “j” jump is pseudo-instruction, uses JAL but sets rd=x0 to discard return address
Set PC = PC + offset (PC-relative jump)
Target somewhere within ±219 locations, 2 bytes apart
  ±218 32-bit instructions
Immediate encoding optimized similarly to branch instruction to reduce hardware cost

## Slide 49: Uses of JAL
# j pseudo-instruction
j Label = jal x0, Label # Discard return address
# Call function within 218 instructions of PC
jal ra, FuncName

## Slide 50: JALR Instruction (I-Format)
JALR rd, rs, immediate
  Writes PC+4 to rd (return address)
  Sets PC = rs + immediate
  Uses same immediates as arithmetic and loads
    no multiplication by 2 bytes

## Slide 51: Uses of JALR
# ret and jr psuedo-instructions
ret = jr ra = jalr x0, ra, 0
# Call function at any 32-bit absolute address
lui x1, <hi20bits>
jalr ra, x1, <lo12bits>
# Jump PC-relative with 32-bit offset
auipc x1, <hi20bits>
jalr x0, x1, <lo12bits>

## Slide 52: Summary of RISC-V Instruction Formats

## Slide 53: Complete RV32I ISA
Not in CS61C