## Slide 1: CS 61C: Great Ideas in Computer Architecture Lecture 12: Control & Operating Speed
Krste Asanović & Randy Katz
http://inst.eecs.berkeley.edu/~cs61c/fa17

## Slide 2: Agenda
Finish Single-Cycle RISC-V Datapath
Controller
Instruction Timing
Performance Measures
Introduction to Pipelining
Pipelined RISC-V Datapath
And in Conclusion, ...

## Slide 3: Recap: Adding branches to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 4: Implementing JALR Instruction (I-Format)
JALR rd, rs, immediate
  Writes PC+4 to Reg[rd] (return address)
  Sets PC = Reg[rs1] + immediate
  Uses same immediates as arithmetic and loads
    no multiplication by 2 bytes

## Slide 5: Adding jalr to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 6: Adding jalr to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=I
RegWEn=1
BrUn=*
BrEq=*
BrLT=*
Asel=0
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=2
PCSel
wb

## Slide 7: Implementing jal Instruction
JAL saves PC+4 in Reg[rd] (the return address)
Set PC = PC + offset (PC-relative jump)
Target somewhere within ±219 locations, 2 bytes apart
  ±218 32-bit instructions
Immediate encoding optimized similarly to branch instruction to reduce hardware cost

## Slide 8: Adding jal to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 9: Adding jal to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=J
RegWEn=1
BrUn=*
BrEq=*
BrLT=*
Asel=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=2
PCSel
wb

## Slide 10: “Upper Immediate” instructions
Has 20-bit immediate in upper 20 bits of 32-bit instruction word
One destination register, rd
Used for two instructions
  LUI – Load Upper Immediate (add to zero)
  AUIPC – Add Upper Immediate to PC

## Slide 11: Implementing lui
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=U
RegWEn=1
BrUn=*
BrE=*
BrLT=*
Asel=*
Bsel=1
ALUSel=B
MemRW=Read
WBSel=1
PCSel=pc+4
wb
pc

## Slide 12: Implementing auipc
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=U
RegWEn=1
BrUn=*
BrE=*
BrLT=*
Asel=1
Bsel=1
ALUSel=Add
MemRW=0
WBSel=1
PCSel=pc+4
wb
pc

## Slide 13: Recap: Complete RV32I ISA
Not in CS61C
RV32I has 47 instructions total
37 instructions covered in CS61C

## Slide 14: Single-Cycle RISC-V RV32I Datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 15: Agenda
Finish Single-Cycle RISC-V Datapath
Controller
Instruction Timing
Performance Measures
Introduction to Pipelining
Pipelined RISC-V Datapath
And in Conclusion, ...

## Slide 16: Processor
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Bytes
Enable?
Read/Write
Address
Write Data
Read Data
Processor-Memory Interface
Program
Data

## Slide 17: Single-Cycle RISC-V RV32I Datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
Control Logic
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 18: Control Logic Truth Table (incomplete)
Inst[31:0] | BrEq | BrLT | PCSel | ImmSel | BrUn | ASel | BSel | ALUSel | MemRW | RegWEn | WBSel
add | * | * | +4 | * | * | Reg | Reg | Add | Read | 1 | ALU
sub | * | * | +4 | * | * | Reg | Reg | Sub | Read | 1 | ALU
(R-R Op) | * | * | +4 | * | * | Reg | Reg | (Op) | Read | 1 | ALU
addi | * | * | +4 | I | * | Reg | Imm | Add | Read | 1 | ALU
lw | * | * | +4 | I | * | Reg | Imm | Add | Read | 1 | Mem
sw | * | * | +4 | S | * | Reg | Imm | Add | Write | 0 | *
beq | 0 | * | +4 | B | * | PC | Imm | Add | Read | 0 | *
beq | 1 | * | ALU | B | * | PC | Imm | Add | Read | 0 | *
bne | 0 | * | ALU | B | * | PC | Imm | Add | Read | 0 | *
bne | 1 | * | +4 | B | * | PC | Imm | Add | Read | 0 | *
blt | * | 1 | ALU | B | 0 | PC | Imm | Add | Read | 0 | *
bltu | * | 1 | ALU | B | 1 | PC | Imm | Add | Read | 0 | *
jalr | * | * | ALU | I | * | Reg | Imm | Add | Read | 1 | PC+4
jal | * | * | ALU | J | * | PC | Imm | Add | Read | 1 | PC+4
auipc | * | * | +4 | U | * | PC | Imm | Add | Read | 1 | ALU

## Slide 19: Control Realization Options
ROM
  “Read-Only Memory”
  Regular structure
  Can be easily reprogrammed
    fix errors
    add instructions
  Popular when designing control logic manually
Combinatorial Logic
  Today, chip designers use logic synthesis tools to convert truth tables to networks of gates

## Slide 20: RV32I, a nine-bit ISA!
Not in CS61C
Instruction type encoded using only 9 bits inst[30],inst[14:12], inst[6:2]
inst[30]
inst[14:12]
inst[6:2]

## Slide 21: ROM-based Control
ROM
Inst[30,14:12,6:2]
BrEq
9
PCSel
ALUSel[3:0]
4
11-bit address (inputs)
15 data bits (outputs)
BrLT
ImmSel[2:0]
3
BrUn
ASel
BSel
MemRW
RegWEn
WBSel[1:0]
2

## Slide 22: ROM Controller Implementation
Control Word for add
Control Word for sub
Control Word for or
.
.
.
Address
Decoder
.
.
.
Inst[]
BrEQ
BrLT
Controller output (PCSel, ImmSel, …)
add
sub
or
jal
11

## Slide 23: Administrivia
Homework 2 Due tomorrow 11:59 pm
Project 1 Part 1 Due Monday Oct. 9
  Part 2 due Monday Oct. 16
Midterm 1 Regrades due next Tuesday
  Talk to a TA if you don’t understand a midterm question or are unsure of a regrade

## Slide 24: Break!

## Slide 25: Agenda
Finish Single-Cycle RISC-V Datapath
Controller
Instruction Timing
Performance Measures
Introduction to Pipelining
Pipelined RISC-V Datapath
And in Conclusion, ...

## Slide 26: Instruction Timing
IF | ID | EX | MEM | WB | Total
I-MEM | Reg Read | ALU | D-MEM | Reg W | 
200 ps | 100 ps | 200 ps | 200 ps | 100 ps | 800 ps

## Slide 27: Instruction Timing
Maximum clock frequency
  fmax = 1/800ps = 1.25 GHz
Most blocks idle most of the time
  E.g. fmax,ALU = 1/200ps = 5 GHz!
  How can we keep ALU busy all the time?
  5 billion adds/sec, rather than just 1.25 billion?
  Idea: Factories use three employee shifts - equipment is always busy!
Instr | IF = 200ps | ID = 100ps | ALU = 200ps | MEM=200ps | WB = 100ps | Total
add | X | X | X |  | X | 600ps
beq | X | X | X |  |  | 500ps
jal | X | X | X |  |  | 500ps
lw | X | X | X | X | X | 800ps
sw | X | X | X | X |  | 700ps

## Slide 28: Agenda
Finish Single-Cycle RISC-V Datapath
Controller
Instruction Timing
Performance Measures
Introduction to Pipelining
Pipelined RISC-V Datapath
And in Conclusion, ...

## Slide 29: Performance Measures
“Our” RISC-V executes instructions at 1.25 GHz
  1 instruction every 800 ps
Can we improve its performance?
  What do we mean with this statement?
  Not so obvious:
    Quicker response time, so one job finishes faster?
    More jobs per unit time (e.g. web server returning pages)?
    Longer battery life?

## Slide 30: Transportation Analogy
 | Sports Car | Bus
Passenger Capacity | 2 | 50
Travel Speed | 200 mph | 50 mph
Gas Mileage | 5 mpg | 2 mpg
 | Sports Car | Bus
Travel Time | 15 min | 60 min
Time for 100 passengers | 750 min | 120 min
Gallons per passenger | 5 gallons | 0.5 gallons
50 Mile trip:
Notes: “Winner” depends on objectives

## Slide 31: Computer Analogy
Transportation | Computer
Trip Time | Program execution time: e.g. time to update display
Time for 100 passengers | Throughput: e.g. number of server requests handled per hour
Gallons per passenger | Energy per task*: e.g. how many movies you can watch per battery charge or energy bill for datacenter
* Note: power is not a good measure, since low-power CPU might run for a long time to complete one task consuming more energy than faster computer running at higher power for a shorter time

## Slide 32: “Iron Law” of Processor Performance
Time = Instructions Cycles Time
Program Program * Instruction * Cycle

## Slide 33: Instructions per Program
Determined by
Task
Algorithm, e.g. O(N2) vs O(N)
Programming language
Compiler
Instruction Set Architecture (ISA)

## Slide 34: (Average) Clock cycles per Instruction
Determined by
ISA
Processor implementation (or microarchitecture)
E.g. for “our” single-cycle RISC-V design, CPI = 1
Complex instructions (e.g. strcpy), CPI >> 1
Superscalar processors, CPI < 1 (next lecture)

## Slide 35: Time per Cycle (1/Frequency)
Determined by
Processor microarchitecture (determines critical path through logic gates)
Technology (e.g. 14nm versus 28nm)
Power budget (lower voltages reduce transistor speed)

## Slide 36: Speed Tradeoff Example
For some task (e.g. image compression) …
 | Processor A | Processor B
# Instructions | 1 Million | 1.5 Million
Average CPI | 2.5 | 1
Clock rate f | 2.5 GHz | 2 GHz
Execution time | 1 ms | 0.75 ms
Processor B is faster for this task, despite executing more instructions and having a lower clock rate!

## Slide 37: Energy per Task
Energy = Instructions Energy
Program Program * Instruction
Energy α Instructions * C V2
Program Program
“Capacitance” depends on
technology,
processor features
e.g. # of cores
Supply voltage,
e.g. 1V
Want to reduce capacitance and voltage to reduce energy/task

## Slide 38: Energy Tradeoff Example
“Next-generation” processor
  C (Moore’s Law): -15 %
  Supply voltage, Vsup: -15 %
  Energy consumption: 1 - (1-0.85)3 = -39 %
Significantly improved energy efficiency thanks to
  Moore’s Law AND
  Reduced supply voltage

## Slide 39: Energy “Iron Law”
Performance = Power * Energy Efficiency
(Tasks/Second) (Joules/Second) (Tasks/Joule)
Energy efficiency (e.g., instructions/Joule) is key metric in all computing devices
For power-constrained systems (e.g., 20MW datacenter), need better energy efficiency to get more performance at same power
For energy-constrained systems (e.g., 1W phone), need better energy efficiency to prolong battery life

## Slide 40: End of Scaling
In recent years, industry has not been able to reduce supply voltage much, as reducing it further would mean increasing “leakage power” where transistor switches don’t fully turn off (more like dimmer switch than on-off switch)
Also, size of transistors and hence capacitance, not shrinking as much as before between transistor generations
Power becomes a growing concern – the “power wall”
Cost-effective air-cooled chip limit around ~150W

## Slide 41: Processor Trends
Chart: 
Frequency (MHz) | 0.7 | 0.5 | 2 | 5 | 6 | 16 | 16 | 40 | 25 | 33 | 66 | 100 | 60 | 200 | 40 | 66 | 300 | 150 | 300 | 90 | 200 | 200 | 200 | 200 | 90 | 500 | 250 | 533 | 233 | 300 | 500 | 400 | 300 | 450 | 500 | 750 | 1000 | 1000 | 900 | 2000 | 800 | 1400 | 2200 | 1800 | 1000 | 1150 | 2160 | 1800
Power (W) | 0.45 | 0.42 | 0.92 | 1.7 | 3 | 1.5 | 3 | 4 | 2.75 | 3.5 | 5.8 | 15 | 14.2 | 35 | 3 | 13 | 28 | 3 | 50 | 16 | 32.6 | 30 | 10 | 30 | 11 | 43 | 25 | 36 | 17 | 32 | 91 | 14 | 30 | 17 | 21 | 35 | 49 | 20 | 70 | 72 | 98 | 56 | 48 | 62 | 98 | 155 | 74 | 89
Cores | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 1800 | 2600 | 1900 | 3600 | 3200 | 2800 | 1200 | 2200 | 2600 | 3600 | 2800 | 2660 | 2800 | 2330 | 2930 | 4700 | 4000 | 2000 | 1400 | 2000 | 2300 | 3000 | 2500 | 3200 | 2660 | 3200 | 2300 | 3500 | 2266 | 1660 | 2400 | 3330 | 3000 | 3600
 | 89 | 89 | 100 | 115 | 130 | 85 | 72 | 25 | 65 | 130 | 125 | 65 | 75 | 31 | 130 | 100 | 100 | 31 | 84 | 75 | 95 | 65 | 95 | 130 | 130 | 130 | 250 | 200 | 130 | 139 | 130 | 130 | 139 | 125
 | 1 | 1 | 2 | 1 | 2 | 1 | 8 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 4 | 2 | 9 | 2 | 8 | 4 | 4 | 2 | 3 | 4 | 6 | 8 | 16 | 8 | 8 | 16 | 10 | 6 | 8 | 8
[Olukotun, Hammond,Sutter,Smith,Batten]

## Slide 42: Break!

## Slide 43: Agenda
Finish Single-Cycle RISC-V Datapath
Controller
Instruction Timing
Performance Measures
Introduction to Pipelining
Pipelined RISC-V Datapath
And in Conclusion, ...

## Slide 44: Pipelining
A familiar example:
  Getting a university degree
Shortage of Computer scientists (your startup is growing):
  How long does it take to educate 16,000?
Year 1
Year 2
Year 3
Year 4

## Slide 45: Computer Scientist Education
Option 1: serial
Option 2: pipelining
7 years
16,000 in 16 years, average throughput is 1000/year
16,000 in 7 years
Steady state throughput is 4000/year
Resources used efficiently
4-fold improvement over serial education
4000 graduate
4 years
4000 graduate
4 years
4000 graduate
4 years
4000
4 years
4000 graduate
4000 graduate
4000 graduate
4000 graduate
4000 enter
1 year

## Slide 46: Latency versus Throughput
Latency
  Time from entering college to graduation
  Serial 4 years
  Pipelining 4 years
Throughput
  Average number of students graduating each year
  Serial 1000
  Pipelining 4000
Pipelining
  Increases throughput (4x in this example)
  But does nothing to latency
    sometimes worse (additional overhead e.g. for shift transition)

## Slide 47: Simultaneous versus Sequential
What happens sequentially?
What happens simultaneously?
4 years
4000 graduate
4000 graduate
4000 graduate
4000 graduate
4000 graduate
4000 graduate
4000 graduate
4000 graduate
4000 graduate
4000 graduate

## Slide 48: Agenda
Finish Single-Cycle RISC-V Datapath
Controller
Instruction Timing
Performance Measures
Introduction to Pipelining
Pipelined RISC-V Datapath
And in Conclusion, ...

## Slide 49: Pipelining with RISC-V
Phase | Pictogram | tstep Serial
Instruction Fetch |  | 200 ps
Reg Read |  | 100 ps
ALU |  | 200 ps
Memory |  | 200 ps
Register Write |  | 100 ps
tinstruction |  | 800 ps
add t0, t1, t2
or t3, t4, t5
sll t6, t0, t3
tcycle
instruction sequence
tinstruction
tcycle Pipelined
200 ps
200 ps
200 ps
200 ps
200 ps
1000 ps
Notes: Tc = “Time between completion of instructions”

## Slide 50: Pipelining with RISC-V
add t0, t1, t2
or t3, t4, t5
sll t6, t0, t3
tcycle
instruction sequence
tinstruction
 | Single Cycle | Pipelining
Timing | tstep = 100 … 200 ps | tcycle = 200 ps
 | Register access only 100 ps | All cycles same length
Instruction time, tinstruction | = tcycle = 800 ps | 1000 ps
Clock rate, fs | 1/800 ps = 1.25 GHz | 1/200 ps = 5 GHz
Relative speed | 1 x | 4 x
Notes: Tc = “Time between completion of instructions”

## Slide 51: Sequential vs Simultaneous
add t0, t1, t2
or t3, t4, t5
sll t6, t0, t3
tcycle
= 200 ps
instruction sequence
tinstruction = 1000 ps
sw t0, 4(t3)
lw t0, 8(t3)
addi t2, t2, 1
What happens sequentially, what happens simultaneously?
Notes: Tc = “Time between completion of instructions”

## Slide 52: Agenda
Finish Single-Cycle RISC-V Datapath
Controller
Instruction Timing
Performance Measures
Introduction to Pipelining
Pipelined RISC-V Datapath
And in Conclusion, ...

## Slide 53: And in Conclusion, …
Controller
  Tells universal datapath how to execute each instruction
Instruction timing
  Set by instruction complexity, architecture, technology
  Pipelining increases clock frequency, “instructions per second”
    But does not reduce time to complete instruction
Performance measures
  Different measures depending on objective
    Response time
    Jobs / second
    Energy per task