## Slide 1: CS 61C: Great Ideas in Computer Architecture (Machine Structures) Caches Part 2
Instructors:
Krste Asanović & Randy H. Katz
http://inst.eecs.berkeley.edu/~cs61c/
10/16/17
Fall 2017 - Lecture #15

## Slide 2: Outline
Cache Organization and Principles
Write Back vs. Write Through
Cache Performance
Cache Design Tradeoffs
And in Conclusion …
10/16/17
Fall 2017 – Lecture #15

## Slide 3: Outline
Cache Organization and Principles
Write Back vs. Write Through
Cache Performance
Cache Design Tradeoffs
And in Conclusion …
10/16/17
Fall 2017 – Lecture #15

## Slide 4: Typical Memory Hierarchy
Second-Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk
Or Flash)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Speed (cycles): ½’s 1’s 10’s 100’s-1000 1,000,000’s
Size (bytes): 100’s 10K’s M’s G’s T’s
Principle of locality + memory hierarchy presents programmer with ≈ as much memory as is available in the cheapest technology at the ≈ speed offered by the fastest technology
Cost/bit: highest lowest
Third-Level
Cache
(SRAM)
10/16/17
Fall 2017 - Lecture #15
Notes: Instead, the memory system of a modern computer consists of a series of black boxes ranging from the fastest to the slowest.
Besides variation in speed, these boxes also varies in size (smallest to biggest) and cost.
What makes this kind of arrangement work is one of the most important principle in computer design. The principle of locality. The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in detail in the next lectures on caches).

## Slide 5: Adding Cache to Computer
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data
Cache
10/16/17
Fall 2017 - Lecture #15
Processor organized around words and bytes
Memory (including
cache) organized around blocks, which are typically multiple words

## Slide 6: Key Cache Concepts
Principle of Locality
  Temporal Locality and Spatial Locality
Hierarchy of Memories (speed/size/cost per bit) to exploit locality
Cache – copy of data in lower level of memory hierarchy
Direct Mapped to find block in cache using Tag field and Valid bit for Hit
Cache Design Organization Choices:
  Fully Associative, Set-Associative, Direct-Mapped
10/16/17
Fall 2017 - Lecture #15

## Slide 7: Cache Organizations
“Fully Associative”: Block placed anywhere in cache
  First design last lecture
  Note: No Index field, but one comparator/block
“Direct Mapped”: Block goes only one place in cache
  Note: Only one comparator
  Number of sets = number blocks
“N-way Set Associative”: N places for block in cache
  Number of sets = Number of Blocks / N
  N comparators
  Fully Associative: N = number of blocks
  Direct Mapped: N = 1
10/16/17
Fall 2017 - Lecture #15

## Slide 8: Memory Block vs. Word Addressing
10/16/17
Fall 2017 - Lecture #15

## Slide 9: Memory Block Number Aliasing
Block #
Block # mod 8
Block # mod 2
12-bit memory addresses, 16 Byte blocks
10/16/17
Fall 2017 - Lecture #15

## Slide 10: Processor Address Fields Used by Cache Controller
Block Offset: Byte address within block
Set Index: Selects which set
Tag: Remaining portion of processor address
Size of Index = log2(number of sets)
Size of Tag = Address size – Size of Index – log2(number of bytes/block)
Block offset
Set Index
Tag
Processor Address (32-bits total)
10/16/17
Fall 2017 - Lecture #15
Notes: For class handout

## Slide 11: What Limits Number of Sets?
For a given total number of blocks, we save comparators if have more than two sets
Limit: As Many Sets as Cache Blocks => only one block per set – only needs one comparator!
Called “Direct-Mapped” Design
Block offset
Index
Tag
10/16/17
Fall 2017 - Lecture #15

## Slide 12: Direct Mapped Cache Example: Mapping a 6-bit Memory Address
In example, block size is 4 bytes/1 word
Memory and cache blocks always the same size, unit of transfer between memory and cache
# Memory blocks >> # Cache blocks
  16 Memory blocks = 16 words = 64 bytes => 6 bits to address all bytes
  4 Cache blocks, 4 bytes (1 word) per block
  4 Memory blocks map to each cache block
Memory block to cache block, aka index: middle two bits
Which memory block is in a given cache block, aka tag: top two bits
0
5
1
Byte Within Block
Byte Offset
2
3
Block Within $
4
Mem Block Within $ Block
Tag
Index
10/16/17
Fall 2017 - Lecture #15

## Slide 13: One More Detail: Valid Bit
When start a new program, cache does not have valid information for this program
Need an indicator whether this tag entry is valid for this program
Add a “valid bit” to the cache tag entry
  0 => cache miss, even if by chance, address = tag
  1 => cache hit, if processor address = tag
10/16/17
Fall 2017 - Lecture #15

## Slide 14: Cache Organization: Simple First Example
00
01
10
11
Cache
Main Memory
Q: Where in the cache is the mem block?
Use next 2 low-order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
Tag
Data
Q: Is the memory block in cache?
Compare the cache tag to the high-order 2 memory address bits to tell if the memory block is in the cache (provided valid bit is set)
Valid
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
One word blocks
Two low order bits (xx) define the byte in the block (32b words)
Index
10/16/17
Fall 2017 - Lecture #15
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block

## Slide 15: Example: Alternatives in an 8 Block Cache
Direct Mapped: 8 blocks, 1 way, 1 tag comparator, 8 sets
Fully Associative: 8 blocks, 8 ways, 8 tag comparators, 1 set
2 Way Set Associative: 8 blocks, 2 ways, 2 tag comparators, 4 sets
4 Way Set Associative: 8 blocks, 4 ways, 4 tag comparators, 2 sets
10/16/17
Fall 2017 - Lecture #15
15
0
1
2
3
DM: 8 sets
1 way
4
5
6
7
0
1
2
3
FA: 1 set
8 ways
4
5
6
7
0
1
2
3
2 Way SA: 4 sets
Set 0
Set 1
Set 2
Set 3
4
5
6
7
0
1
2
3
4 Way SA: 2 sets
Set 0
Set 1
4
5
6
7

## Slide 16: Direct-Mapped Cache
One word blocks, cache size = 1K words (or 4KB)
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
20
Data
32
Hit
Valid bit ensures something useful in cache for this index
Compare Tag with upper part of Address to see if a Hit
Read data from cache instead of memory if a Hit
Comparator
10/16/17
Fall 2017 - Lecture #15
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
Temporal!

## Slide 17: Peer Instruction
For a cache with constant total capacity, if we increase the number of ways by a factor of two, which statement is false:
A : The number of sets could be doubled
B : The tag width could decrease
C : The block size could stay the same
D : The block size could be halved
10/16/17
Fall 2017 - Lecture #15

## Slide 18: Break!
10/16/17
Fall 2017 - Lecture #15

## Slide 19: Outline
Cache Organization and Principles
Write Back vs. Write Through
Cache Performance
Cache Design Tradeoffs
And in Conclusion …
10/16/17
Fall 2017 – Lecture #15

## Slide 20: Handling Stores with Write-Through
Store instructions write to memory, changing values
Need to make sure cache and memory have same values on writes: two policies
1) Write-Through Policy: write cache and write through the cache to memory
  Every write eventually gets to memory
  Too slow, so include Write Buffer to allow processor to continue once data in Buffer
  Buffer updates memory in parallel to processor
10/16/17
Fall 2017 - Lecture #15

## Slide 21: Write-Through Cache
Write both values in cache and in memory
Write buffer stops CPU from stalling if memory cannot keep up
Write buffer may have multiple entries to absorb bursts of writes
What if store misses in cache?
Processor
32-bit
Address
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
1022
99
252
7
20
12
131
2041
Addr
Data
Write Buffer
10/16/17
Fall 2017 - Lecture #15

## Slide 22: Handling Stores with Write-Back
2) Write-Back Policy: write only to cache and then write cache block back to memory when evict block from cache
  Writes collected in cache, only single write to memory per block
  Include bit to see if wrote to block or not, and then only write back if bit is set
    Called “Dirty” bit (writing makes it “dirty”)
10/16/17
Fall 2017 - Lecture #15

## Slide 23: Write-Back Cache
Store/cache hit, write data in cache only and set dirty bit
  Memory has stale value
Store/cache miss, read data from memory, then update and set dirty bit
  “Write-allocate” policy
Load/cache hit, use value from cache
On any miss, write back evicted block, only if dirty. Update cache with new block and clear dirty bit
Processor
32-bit
Address
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
1022
99
252
7
20
12
131
2041
D
D
D
D
Dirty Bits
10/16/17
Fall 2017 - Lecture #15

## Slide 24: Write-Through vs. Write-Back
Write-Through:
  Simpler control logic
  More predictable timing simplifies processor control logic
  Easier to make reliable, since memory always has copy of data (big idea: Redundancy!)
Write-Back
  More complex control logic
  More variable timing (0,1,2 memory accesses per cache access)
  Usually reduces write traffic
  Harder to make reliable, sometimes cache has only copy of data
10/16/17
Fall 2017 - Lecture #15

## Slide 25: Administrivia
Midterm #2 2 weeks away! October 31!
  In class! 8-9:30 AM
  Synchronous digital design and Project 2 (processor design) included
  Pipelines and Caches
  ONE Double sided Crib sheet
  Review Session: Saturday, Oct 28 (Location TBA)
5-10 open drop-in seats for these tutoring sessions:
    M 1-2 Soda 611
    Th 3-4 Soda 380
    F 5-6 Soda 651
Guerrilla Session tonight 7-9 pm in Cory 293
Project 2-1 Party tomorrow 7-9 pm Cory 293
If you would like to change your partnership for Project 2, email your lab TA
  We will send out a Google form to track all Project 2 partnerships
10/16/17
Fall 2017 - Lecture #15

## Slide 26: Outline
Cache Organization and Principles
Write Back vs. Write Through
Cache Performance
Cache Design Tradeoffs
And in Conclusion …
10/16/17
Fall 2017 – Lecture #15

## Slide 27: Cache (Performance) Terms
Hit rate: fraction of accesses that hit in the cache
Miss rate: 1 – Hit rate
Miss penalty: time to replace a block from lower level in memory hierarchy to cache
Hit time: time to access cache memory (including tag comparison)
Abbreviation: “$” = cache (a Berkeley innovation!)
10/16/17
Fall 2017 - Lecture #15

## Slide 28: Average Memory Access Time (AMAT)
Average Memory Access Time (AMAT) is the average time to access memory considering both hits and misses in the cache
  AMAT = Time for a hit + Miss rate × Miss penalty
10/16/17
Fall 2017 - Lecture #15
Important Equation!
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 29: Peer Instruction
  AMAT = Time for a hit + Miss rate x Miss penalty
Given a 200 psec clock, a miss penalty of 50 clock cycles, a miss rate of 0.02 misses per instruction and a cache hit time of 1 clock cycle, what is AMAT?
A : ≤200 psec
B : 400 psec
C : 600 psec
D : ≥ 800 psec
10/16/17
Fall 2017 - Lecture #15

## Slide 30: Ping Pong Cache Example: Direct-Mapped Cache w/4 Single-Word Blocks, Worst-Case Reference String
0
4
0
4
0
4
0
4
Consider the main memory address reference string of word numbers: 0 4 0 4 0 4 0 4
Start with an empty cache - all blocks initially marked as not valid
10/16/17
Fall 2017 - Lecture #15
Notes: For class handout

## Slide 31: Ping Pong Cache Example: Direct-Mapped Cache w/4 Single-Word Blocks, Worst-Case Reference String
0
4
0
4
0
4
0
4
miss
miss
miss
miss
miss
miss
miss
miss
00 Mem(0)
00 Mem(0)
01
4
01 Mem(4)
0
00
00 Mem(0)
01
4
00 Mem(0)
01
4
00 Mem(0)
01
4
01 Mem(4)
0
00
01 Mem(4)
0
00
Start with an empty cache - all blocks initially marked as not valid
Ping-pong effect due to conflict misses - two memory locations that map into the same cache block
  8 requests, 8 misses
Consider the main memory address reference string of word numbers: 0 4 0 4 0 4 0 4
10/16/17
Fall 2017 - Lecture #15
Notes: For class handout

## Slide 32: Outline
Cache Organization and Principles
Write Back vs. Write Through
Cache Performance
Cache Design Tradeoffs
And in Conclusion …
10/16/17
Fall 2017 – Lecture #15

## Slide 33: Example: 2-Way Set Associative $ (4 words = 2 sets x 2 ways per set)
0
Cache
Main Memory
Q: How do we find it?
Use next 1 low order memory address bit to determine which cache set (i.e., modulo the number of sets in the cache)
Tag
Data
Q: Is it there?
Compare all the cache tags in the set to the high order 3 memory address bits to tell if the memory block is in the cache
V
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Set
1
0
1
Way
0
1
One word blocks
Two low order bits define the byte in the word (32b words)
10/16/17
Fall 2017 - Lecture #15
Notes: For lecture
This picture is as opposed to
Way 0
both red Set 0
Way 1
------------------------------------
Way 0
both green Set 1
Way 1

## Slide 34: Ping Pong Cache Example: 4 Word 2-Way SA $, Same Reference String
0
4
0
4
Consider the main memory word reference string
  0 4 0 4 0 4 0 4
Start with an empty cache - all blocks initially marked as not valid
10/16/17
Fall 2017 - Lecture #15
Notes: For class handout

## Slide 35: Ping Pong Cache Example: 4-Word 2-Way SA $, Same Reference String
0
4
0
4
Consider the main memory address reference string
  0 4 0 4 0 4 0 4
miss
miss
hit
hit
000 Mem(0)
000 Mem(0)
Start with an empty cache - all blocks initially marked as not valid
010 Mem(4)
010 Mem(4)
000 Mem(0)
000 Mem(0)
010 Mem(4)
Solves the ping-pong effect in a direct-mapped cache due to conflict misses since now two memory locations that map into the same cache set can co-exist!
  8 requests, 2 misses
10/16/17
Fall 2017 - Lecture #15
Notes: For lecture
Another sample string to try 0 1 2 3 0 8 11 0 3

## Slide 36: Four-Way Set-Associative Cache
28 = 256 sets each with four ways (each with one block)
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select
Way 0
Way 1
Way 2
Way 3
10/16/17
Fall 2017 - Lecture #15
Notes: This is called a 4-way set associative cache because there are four cache entries for each cache index. Essentially, you have four direct mapped cache working in parallel.
This is how it works: the cache index selects a set from the cache. The four tags in the set are compared in parallel with the upper bits of the memory address.
If no tags match the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data from the way where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 37: Break!
10/16/17
Fall 2017 - Lecture #15

## Slide 38: Range of Set-Associative Caches
For a fixed-size cache and fixed block size, each increase by a factor of two in associativity doubles the number of blocks per set (i.e., the number or ways) and halves the number of sets – decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Word offset
Byte offset
Index
Tag
10/16/17
Fall 2017 - Lecture #15
Notes: For class handout

## Slide 39: Range of Set-Associative Caches
For a fixed-size cache and fixed block size, each increase by a factor of two in associativity doubles the number of blocks per set (i.e., the number or ways) and halves the number of sets – decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Word offset
Byte offset
Index
Tag
Decreasing associativity, lower way, more sets
Fully associative
(only one set)
Tag is all the bits except
block and byte offset
Direct mapped
(only one way)
Smaller tags, only a single comparator
Increasing associativity, higher way, less sets
Selects the set
Used for tag compare
Selects the word in the block
10/16/17
Fall 2017 - Lecture #15
Notes: For lecture
In 2008, the greater size and power consumption of CAMs generally leads to 2-way and 4-way set associativity being built from standard SRAMs with comparators with 8-way and above being built using CAMs

## Slide 40: Total Cache Capacity =
Associativity × # of sets × block_size
Bytes = blocks/set × sets × Bytes/block
Byte Offset
Tag
Index
C = N × S × B
address_size = tag_size + index_size + offset_size
= tag_size + log2(S) + log2(B)
10/16/17
Fall 2017 - Lecture #15

## Slide 41: Total Cache Capacity =
Associativity * # of sets * block_size
Bytes = blocks/set * sets * Bytes/block
Byte Offset
Tag
Index
C = N * S * B
address_size = tag_size + index_size + offset_size
= tag_size + log2(S) + log2(B)
Double the Associativity: Number of sets?
tag_size? index_size? # comparators?
Double the Sets: Associativity?
tag_size? index_size? # comparators?
10/16/17
Fall 2017 - Lecture #15

## Slide 42: Your Turn
For a cache of 64 blocks, each block four bytes in size:
The capacity of the cache is: ____ bytes.
Given a 2-way Set Associative organization, there are ___ sets, each of __ blocks, and __ places a block from memory could be placed.
Given a 4-way Set Associative organization, there are ____ sets each of __ blocks and __ places a block from memory could be placed.
Given an 8-way Set Associative organization, there are ____ sets each of __ blocks and ___ places a block from memory could be placed.
10/16/17
Fall 2017 - Lecture #15

## Slide 43: Peer Instruction
For S sets, N ways, B blocks, which statements hold?
(i) The cache has B tags
(ii) The cache needs N comparators
(iii) B = N x S
(iv) Size of Index = Log2(S)
A : (i) only
B : (i) and (ii) only
C : (i), (ii), (iii) only
D : All four statements are true
10/16/17
Fall 2017 - Lecture #15

## Slide 44: Peer Instruction
For S sets, N ways, B blocks, which statements hold?
(i) The cache has B tags
(ii) The cache needs N comparators
(iii) B = N x S
(iv) Size of Index = Log2(S)
A : (i) only
B : (i) and (ii) only
C : (i), (ii), (iii) only
D : All four statements are true
10/16/17
Fall 2017 - Lecture #15

## Slide 45: Costs of Set-Associative Caches
N-way set-associative cache costs
  N comparators (delay and area)
  MUX delay (set selection) before data is available
  Data available after set selection (and Hit/Miss decision). DM $: block is available before the Hit/Miss decision
    In Set-Associative, not possible to just assume a hit and continue and recover later if it was a miss
When miss occurs, which way’s block selected for replacement?
  Least Recently Used (LRU): one that has been unused the longest (principle of temporal locality)
    Must track when each way’s block was used relative to other blocks in the set
    For 2-way SA $, one bit per set → set to 1 when a block is referenced; reset the other way’s bit (i.e., “last used”)
10/16/17
Fall 2017 - Lecture #15
Notes: First of all, a N-way set associative cache will need N comparators instead of just one comparator (use the right side of the diagram for direct mapped cache).
A N-way set associative cache will also be slower than a direct mapped cache because of this extra multiplexer delay.
Finally, for a N-way set associative cache, the data will be available AFTER the hit/miss signal becomes valid because the hit/mis is needed to control the data MUX.
For a direct mapped cache, that is everything before the MUX on the right or left side, the cache block will be available BEFORE the hit/miss signal (AND gate output) because the data does not have to go through the comparator.
This can be an important consideration because the processor can now go ahead and use the data without knowing if it is a Hit or Miss. Just assume it is a hit.
Since cache hit rate is in the upper 90% range, you will be ahead of the game 90% of the time and for those 10% of the time that you are wrong, just make sure you can recover.
You cannot play this speculation game with a N-way set-associative cache because as I said earlier, the data will not be available to you until the hit/miss signal is valid.
+2 = 38 min. (Y:18)

## Slide 46: Cache Replacement Policies
Random Replacement
  Hardware randomly selects a cache evict
Least-Recently Used
  Hardware keeps track of access history
  Replace the entry that has not been used for the longest time
  For 2-way set-associative cache, need one bit for LRU replacement
Example of a Simple “Pseudo” LRU Implementation
  Assume 64 Fully Associative entries
  Hardware replacement pointer points to one cache entry
  Whenever access is made to the entry the pointer points to:
    Move the pointer to the next entry
  Otherwise: do not move the pointer
  (example of “not-most-recently used” replacement policy)
:
Entry 0
Entry 1
Entry 63
Replacement
Pointer
10/16/17
Fall 2017 - Lecture #15

## Slide 47: Benefits of Set-Associative Caches
Choice of DM $ versus SA $ depends on the cost of a miss versus the cost of implementation
Largest gains are in going from direct mapped to 2-way (20%+ reduction in miss rate)
10/16/17
Fall 2017 - Lecture #15
Notes: As cache sizes grow, the relative improvement from associativity increases only slightly; since the overall miss rate of a larger cache is lower, the opportunity for improving the miss rate decreases and the absolute improvement in miss rate from associativity shrinks significantly.

## Slide 48: Outline
Cache Organization and Principles
Write Back vs. Write Through
Cache Performance
Cache Design Tradeoffs
And in Conclusion …
10/16/17
Fall 2017 – Lecture #15

## Slide 49: Chip Photos
10/16/17
Fall 2017 - Lecture #15

## Slide 50: And in Conclusion …
Name of the Game: Reduce AMAT
  Reduce Hit Time
  Reduce Miss Rate
  Reduce Miss Penalty
Balance cache parameters (Capacity, associativity, block size)
10/16/17
Fall 2017 - Lecture #15