## Slide 1: CS 61C: Great Ideas in Computer Architecture (Machine Structures) Caches Part 3
Instructors:
Krste Asanović & Randy H. Katz
http://inst.eecs.berkeley.edu/~cs61c/
10/19/17
Fall 2017 - Lecture #16

## Slide 2: You Are Here!
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s
Lecture
10/19/17
Fall 2017 - Lecture #16

## Slide 3: Typical Memory Hierarchy
Second-Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk
Or Flash)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Speed (cycles): ½’s 1’s 10’s 100’s-1000 1,000,000’s
Size (bytes): 100’s 10K’s M’s G’s T’s
Principle of locality + memory hierarchy presents programmer with ≈ as much memory as is available in the cheapest technology at the ≈ speed offered by the fastest technology
Cost/bit: highest lowest
Third-Level
Cache
(SRAM)
10/19/17
Fall 2017 - Lecture #16
Notes: Instead, the memory system of a modern computer consists of a series of black boxes ranging from the fastest to the slowest.
Besides variation in speed, these boxes also varies in size (smallest to biggest) and cost.
What makes this kind of arrangement work is one of the most important principle in computer design. The principle of locality. The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in detail in the next lectures on caches).

## Slide 4: Review: Direct-Mapped Cache
One word blocks, cache size = 1K words (or 4KB)
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Byte within block offset
20
Data
32
Hit
Valid bit ensures something useful in cache for this index
Compare Tag with upper part of Address to see if a Hit
Read data from cache instead of memory if a Hit
Comparator
10/19/17
Fall 2017 - Lecture #16
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
Temporal!

## Slide 5: Review: Four-Way Set-Associative Cache
28 = 256 sets each with four ways (each with one word block)
31 30 . . . 11 10 9 . . . 2 1 0
Byte within block offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select
Way 0
Way 1
Way 2
Way 3
10/19/17
Fall 2017 - Lecture #16
# Sets x # Ways = # Blocks
# Blocks x Bytes/Block = Cache Capacity
Notes: This is called a 4-way set associative cache because there are four cache entries for each cache index. Essentially, you have four direct mapped cache working in parallel.
This is how it works: the cache index selects a set from the cache. The four tags in the set are compared in parallel with the upper bits of the memory address.
If no tags match the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data from the way where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 6: Review: Range of Set-Associative Caches
For a fixed-size cache and fixed block size, each increase by a factor of two in associativity doubles the number of blocks per set (i.e., the number or ways) and halves the number of sets – decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Word offset
Byte offset
Index
Tag
Decreasing associativity, less ways, more sets
Fully associative
(only one set)
Tag is all the bits except
word and byte offset
Direct mapped
(only one way)
Smaller tags, only a single comparator
Increasing associativity, more ways, less sets
Selects the set
Used for tag compare
Selects the word in the block
10/19/17
Fall 2017 - Lecture #15
# Sets x # Ways = # Blocks
# Blocks x Bytes/Block = Cache Capacity
Notes: For lecture
In 2008, the greater size and power consumption of CAMs generally leads to 2-way and 4-way set associativity being built from standard SRAMs with comparators with 8-way and above being built using CAMs

## Slide 7: Review: Costs of Set-Associative Caches
N-way set-associative cache costs
  N comparators (delay and area)
  MUX delay (set selection) before data is available
  Data available after set selection (and Hit/Miss decision). DM $: block is available before the Hit/Miss decision
    In Set-Associative, not possible to just assume a hit and continue and recover later if it was a miss
When miss occurs, which way’s block selected for replacement?
  Least Recently Used (LRU): one that has been unused the longest (principle of temporal locality)
    Must track when each way’s block was used relative to other blocks in the set
    For 2-way SA $, one bit per set → set to 1 when a block is referenced; reset the other way’s bit (i.e., “last used”)
10/19/17
Fall 2017 - Lecture #16
Notes: First of all, a N-way set associative cache will need N comparators instead of just one comparator (use the right side of the diagram for direct mapped cache).
A N-way set associative cache will also be slower than a direct mapped cache because of this extra multiplexer delay.
Finally, for a N-way set associative cache, the data will be available AFTER the hit/miss signal becomes valid because the hit/mis is needed to control the data MUX.
For a direct mapped cache, that is everything before the MUX on the right or left side, the cache block will be available BEFORE the hit/miss signal (AND gate output) because the data does not have to go through the comparator.
This can be an important consideration because the processor can now go ahead and use the data without knowing if it is a Hit or Miss. Just assume it is a hit.
Since cache hit rate is in the upper 90% range, you will be ahead of the game 90% of the time and for those 10% of the time that you are wrong, just make sure you can recover.
You cannot play this speculation game with a N-way set-associative cache because as I said earlier, the data will not be available to you until the hit/miss signal is valid.
+2 = 38 min. (Y:18)

## Slide 8: Review: Cache Replacement Policies
Random Replacement
  Hardware randomly selects a cache block for eviction
Least-Recently Used
  Hardware keeps track of access history
  Replace the entry that has not been used for the longest time
  For 2-way set-associative cache, need one bit for LRU replacement
Example of a Simple “Pseudo” LRU Implementation
  Assume 64 Fully Associative entries
  Hardware replacement pointer points to one cache entry
  Whenever access is made to the entry the pointer points to:
    Move the pointer to the next entry
  Otherwise: do not move the pointer
  (example of “not-most-recently used” replacement policy)
:
Entry 0
Entry 1
Entry 63
Replacement
Pointer
10/19/17
Fall 2017 - Lecture #16

## Slide 9: Review: Write Policy Choices
Cache Hit:
  Write through: writes both cache & memory on every access
    Generally higher memory traffic but simpler pipeline & cache design
  Write back: writes cache only, memory written only when dirty entry evicted
    A dirty bit per line reduces write-back traffic
    Must handle 0, 1, or 2 accesses to memory for each load/store
Cache Miss:
  No write allocate: only write to main memory
  Write allocate (aka fetch on write): fetch into cache
Common combinations:
  Write through and no write allocate
  Write back with write allocate
10/19/17
Fall 2017 - Lecture #16

## Slide 10: Review: Benefits of Set-Associative Caches
Choice of DM $ vs. SA $ depends on cost of a miss vs. cost of implementation
Largest gains are in going from direct mapped to 2-way (20%+ reduction in miss rate)
10/19/17
Fall 2017 - Lecture #16
Notes: As cache sizes grow, the relative improvement from associativity increases only slightly; since the overall miss rate of a larger cache is lower, the opportunity for improving the miss rate decreases and the absolute improvement in miss rate from associativity shrinks significantly.

## Slide 11: Review: Average Memory Access Time (AMAT)
Average Memory Access Time (AMAT) is the average time to access memory considering both hits and misses in the cache
  AMAT = Time for a hit + Miss rate × Miss penalty
10/19/17
Fall 2017 - Lecture #16
Important Equation!
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 12: Outline
Understanding Cache Misses
Increasing Cache Performance
Performance of multi-level Caches (L1,L2, …)
Real world example caches
And in Conclusion …
10/19/17
Fall 2017 – Lecture #16

## Slide 13: Outline
Understanding Cache Misses
Increasing Cache Performance
Performance of multi-level Caches (L1,L2, …)
Real world example caches
And in Conclusion …
10/19/17
Fall 2017 – Lecture #16

## Slide 14: Miss Rate vs. Cache Size on the Integer Portion of SPECCPU2000

## Slide 15: Sources of Cache Misses (3 C’s)
Compulsory (cold start, first reference):
  1st access to a block, not a lot you can do about it
    If running billions of instructions, compulsory misses are insignificant
Capacity:
  Cache cannot contain all blocks accessed by the program
    Misses that would not occur with infinite cache
Conflict (collision):
  Multiple memory locations mapped to same cache set
    Misses that would not occur with ideal fully associative cache
10/19/17
Fall 2017 - Lecture #16
Notes: (Capacity miss) That is the cache misses are due to the fact that the cache is simply not large enough to contain all the blocks that are accessed by the program.
The solution to reduce the Capacity miss rate is simple: increase the cache size.
Here is a summary of other types of cache miss we talked about.
First is the Compulsory misses. These are the misses that we cannot avoid. They are caused when we first start the program.
Then we talked about the conflict misses. They are the misses that caused by multiple memory locations being mapped to the same cache location.
There are two solutions to reduce conflict misses. The first one is, once again, increase the cache size. The second one is to increase the associativity.
For example, say using a 2-way set associative cache instead of directed mapped cache.
But keep in mind that cache miss rate is only one part of the equation. You also have to worry about cache access time and miss penalty. Do NOT optimize miss rate alone.
Finally, there is another source of cache miss we will not cover today. Those are referred to as invalidation misses caused by another process, such as IO , update the main memory so you have to flush the cache to avoid inconsistency between memory and cache.
+2 = 43 min. (Y:23)

## Slide 16: How to Calculate 3C’s Using Cache Simulator
Compulsory: set cache size to infinity and fully associative, and count number of misses
Capacity: Change cache size from infinity, usually in powers of 2, and count misses for each reduction in size
  16 MB, 8 MB, 4 MB, … 128 KB, 64 KB, 16 KB
Conflict: Change from fully associative to n-way set associative while counting misses
  Fully associative, 16-way, 8-way, 4-way, 2-way, 1-way
10/19/17
Fall 2017 - Lecture #16

## Slide 17: 3Cs Analysis
Three sources of misses (SPEC2000 integer and floating-point benchmarks)
  Compulsory misses 0.006%; not visible
  Capacity misses, function of cache size
  Conflict portion depends on associativity and cache size
10/19/17
Fall 2017 - Lecture #16

## Slide 18: Outline
Understanding Cache Misses
Increasing Cache Performance
Performance of multi-level Caches (L1,L2, …)
Real world example caches
And in Conclusion …
10/19/17
Fall 2017 – Lecture #16

## Slide 19: Pipelined RISC-V RV32I Datapath (with I,D$)
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
Recalculate PC+4 in M stage to avoid sending both PC and PC+4 down pipeline
instM
instW
Must pipeline instruction along with data, so control operates correctly in each stage
10/19/17
Fall 2017 - Lecture #16
Primary I$
Hit?
Addr Instr
pcF
instD
“Bubble”
PCen
To Memory Controller
Refill $ Data from Lower Levels of Memory Hierarchy
Primary D$
Hit?
Addr DataR
DataW
Refill D$ data from Lower Levels of Memory Hierarchy
Memory Controller & Stall entire CPU on D$ miss
Write Back/Thru to Memory

## Slide 20: Improving Cache Performance
Reduce the time to hit in the cache
  E.g., Smaller cache
Reduce the miss rate
  E.g., Bigger cache
Reduce the miss penalty
  E.g., Use multiple cache levels
  AMAT = Time for a hit + Miss rate x Miss penalty
10/19/17
Fall 2017 - Lecture #16

## Slide 21: Cache Design Space
Several interacting dimensions
  Cache size
  Block size
  Associativity
  Replacement policy
  Write-through vs. write-back
  Write allocation
Optimal choice is a compromise
  Depends on access characteristics
    Workload
    Use (I-cache, D-cache)
  Depends on technology / cost
Simplicity often wins
Associativity
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B
Computer architects expend considerable effort optimizing organization of cache hierarchy – big impact on performance and power!
10/19/17
Fall 2017 - Lecture #16
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.

## Slide 22: Break!
10/19/17
Fall 2017 - Lecture #16

## Slide 23: Peer Instruction
For a cache with constant total capacity, if we increase the number of ways by a factor of two, which statement is false:
A : The number of sets is halved
B : The tag width decreases
C : The block size stays the same
D : The set index decreases
10/19/17
Fall 2017 - Lecture #16

## Slide 24: Peer Instruction
For a cache with constant total capacity, if we increase the number of ways by a factor of two, which statement is false:
A : The number of sets is halved
B : The tag width decreases
C : The block size stays the same
D : The set index decreases
10/19/17
Fall 2017 - Lecture #16

## Slide 25: Peer Instruction
For S sets, N ways, B blocks, which statements hold?
(i) The cache has B tags
(ii) The cache needs N comparators
(iii) B = N x S
(iv) Size of Set Index = Log2(S)
A : (i) only
B : (i) and (ii) only
C : (i), (ii), (iii) only
D : All four statements are true
10/19/17
Fall 2017 - Lecture #16

## Slide 26: Peer Instruction
For S sets, N ways, B blocks, which statements hold?
(i) The cache has B tags
(ii) The cache needs N comparators
(iii) B = N x S
(iv) Size of Set Index = Log2(S)
A : (i) only
B : (i) and (ii) only
C : (i), (ii), (iii) only
D : All four statements are true
10/19/17
Fall 2017 - Lecture #16

## Slide 27: Primary Cache Parameters
Block size
  How many bytes of data in each cache entry?
Associativity
  How many ways in each set?
  Direct-mapped => Associativity = 1
  Set-associative => 1 < Associativity < #Entries
  Fully associative => Associativity = #Entries
Capacity (bytes) = Total #Entries * Block size
#Entries = #Sets * Associativity
10/19/17
Fall 2017 - Lecture #16

## Slide 28: Impact of Larger Cache on AMAT?
1) Reduces misses (what kind(s)?)
2) Longer Access time (Hit time): smaller is faster
  Increase in hit time will likely add another stage to the pipeline
At some point, increase in hit time for a larger cache may overcome improvement in hit rate, yielding a decrease in performance
Computer architects expend considerable effort optimizing organization of cache hierarchy – big impact on performance and power!
10/19/17
Fall 2017 - Lecture #16
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 29: Increasing Associativity?
Hit time as associativity increases?
  Increases, with large step from direct-mapped to >=2 ways, as now need to mux correct way to processor
  Smaller increases in hit time for further increases in associativity
Miss rate as associativity increases?
  Goes down due to reduced conflict misses, but most gain is from 1->2->4-way with limited benefit from higher associativities
Miss penalty as associativity increases?
  Unchanged, replacement policy runs in parallel with fetching missing line from memory
10/19/17
Fall 2017 - Lecture #16

## Slide 30: Increasing #Entries?
Hit time as #entries increases?
  Increases, since reading tags and data from larger memory structures
Miss rate as #entries increases?
  Goes down due to reduced capacity and conflict misses
  Architects rule of thumb: miss rate drops ~2x for every ~4x increase in capacity (only a gross approximation)
Miss penalty as #entries increases?
  Unchanged
At some point, increase in hit time for a larger cache may overcome the improvement in hit rate, yielding a decrease in performance
10/19/17
Fall 2017 - Lecture #16

## Slide 31: Increasing Block Size?
Hit time as block size increases?
  Hit time unchanged, but might be slight hit-time reduction as number of tags is reduced, so faster to access memory holding tags
Miss rate as block size increases?
  Goes down at first due to spatial locality, then increases due to increased conflict misses due to fewer blocks in cache
Miss penalty as block size increases?
  Rises with longer block size, but with fixed constant initial latency that is amortized over whole block
10/19/17
Fall 2017 - Lecture #16

## Slide 32: Administrivia
Midterm #2 1.5 weeks away! October 31!
Review Session: 10am-12pm on Saturday, Oct 28. Location: Hearst Annex A1
Project 2-1 due Monday, Oct 23 at 11:59pm
  We will release a project edX assignment in lab
  Worth a small portion of project 2 points
  Due on edX along with Project 2-1 (Monday night)
Homework 3 due this Friday
Reminder: notify your lab TA about a change in Project 2 partners
10/19/17
Fall 2017 - Lecture #16

## Slide 33: Peer Instruction
For a cache of fixed capacity and blocksize, what is the impact of increasing associativity on AMAT:
A : Increases hit time, decreases miss rate
B : Decreases hit time, decreases miss rate
C : Increases hit time, increases miss rate
D : Decreases hit time, increases miss rate
10/19/17
Fall 2017 - Lecture #16

## Slide 34: Peer Instruction
For a cache of fixed capacity and blocksize, what is the impact of increasing associativity on AMAT:
A : Increases hit time, decreases miss rate
B : Decreases hit time, decreases miss rate
C : Increases hit time, increases miss rate
D : Decreases hit time, increases miss rate
10/19/17
Fall 2017 - Lecture #16

## Slide 35: Peer Instruction
Impact of Larger Blocks on AMAT:
For fixed total cache capacity and associativity, what is effect of larger blocks on each component of AMAT:
A : Decrease
B : Unchanged
C : Increase
Hit Time?
Miss Rate?
Miss Penalty?
10/19/17
Fall 2017 - Lecture #16

## Slide 36: Peer Instruction
Impact of Larger Blocks on AMAT:
For fixed total cache capacity and associativity, what is effect of larger blocks on each component of AMAT:
A : Decrease
B : Unchanged
C : Increase
Hit Time? C: Unchanged (but slight increase possible)
Miss Rate? A: Decrease (spatial locality; conflict???)
Miss Penalty? C: Increase (longer time to load block)
10/19/17
Fall 2017 - Lecture #16
Write Allocation? It depends!
Shorter tags +, mux at edge -

## Slide 37: Peer Instruction
Impact of Larger Blocks on Misses:
For fixed total cache capacity and associativity, what is effect of larger blocks on each component of miss:
A : Decrease
B : Unchanged
C : Increase
Compulsory?
Capacity?
Conflict?
10/19/17
Fall 2017 - Lecture #16

## Slide 38: Peer Instruction
Impact of Larger Blocks on Misses:
For fixed total cache capacity and associativity, what is effect of larger blocks on each component of miss:
A : Decrease
B : Unchanged
C : Increase
Compulsory? A: Decrease (if good Spatial Locality)
Capacity? B: Increase (smaller blocks fit better)
Conflict? A: Increase (more ways better!)
10/19/17
Fall 2017 - Lecture #16
Less effect for large caches

## Slide 39: How to Reduce Miss Penalty?
Could there be locality on misses from a cache?
  Use multiple cache levels!
  With Moore’s Law, more room on die for bigger L1$ and for second-level L2$
  And in some cases even an L3$!
Mainframes have ~1GB L4 cache off-chip
10/19/17
Fall 2017 - Lecture #16

## Slide 40: Break!
10/19/17
Fall 2017 - Lecture #16

## Slide 41: Outline
Understanding Cache Misses
Increasing Cache Performance
Performance of Multi-level Caches (L1,L2, …)
Real world example caches
And in Conclusion …
10/19/17
Fall 2017 – Lecture #16

## Slide 42: Memory Hierarchy
Processor
Size of memory at each level
Increasing distance from processor, decreasing speed
Level 1
Level 2
Level n
Level 3
. . .
Inner
Outer
Levels in memory hierarchy
As we move to outer levels the latency goes up and price per bit goes down.
10/19/17
Fall 2017 - Lecture #16

## Slide 43: Local vs. Global Miss Rates
Local miss rate: fraction of references to a given level of a cache that miss
  Local Miss rate L2$ = L2$ Misses / L1$ Misses = L2$ Misses / total_L2_accesses
Global miss rate: the fraction of references that miss in all levels of a multilevel cache and go all the way to memory
  L2$ local miss rate >> than the global miss rate
10/19/17
Fall 2017 - Lecture #16

## Slide 44: Local vs. Global Miss Rates
Local miss rate – the fraction of references to one level of a cache that miss
  Local Miss rate L2$ = $L2 Misses / L1$ Misses
Global miss rate – the fraction of references that miss in all levels of a multilevel cache
  L2$ local miss rate >> than the global miss rate
  Global Miss rate = L2$ Misses / Total Accesses
  = (L2$ Misses / L1$ Misses) × (L1$ Misses / Total Accesses)
  = Local Miss rate L2$ × Local Miss rate L1$
  AMAT = Time for a hit + Miss rate × Miss penalty
  AMAT = Time for a L1$ hit + (local) Miss rate L1$ × (Time for a L2$ hit + (local) Miss rate L2$ × L2$ Miss penalty)
10/19/17
Fall 2017 - Lecture #16

## Slide 45: Multilevel Cache Considerations
Different design considerations for L1$ and L2$
  L1$ focuses on fast access: minimize hit time to achieve shorter clock cycle, e.g., smaller $
  L2$, L3$ focus on low miss rate: reduce penalty of long main memory access times: e.g., Larger $ with larger block sizes/higher levels of associativity
Miss penalty of L1$ is significantly reduced by presence of L2$, so can be smaller/faster even with higher miss rate
For the L2$, fast hit time is less important than low miss rate
  L2$ hit time determines L1$’s miss penalty
  L2$ local miss rate >> than the global miss rate
Notes: Global miss rate – the fraction of references that miss in all levels of a multilevel cache. The global miss rate dictates how often we must access the main memory.
Local miss rate – the fraction of references to one level of a cache that miss

## Slide 46
L1 Cache: 32KB I$, 32KB D$
L2 Cache: 256 KB
L3 Cache: 4 MB
10/19/17
Fall 2017 - Lecture #16
Cache Buster

## Slide 47: Outline
Understanding Cache Misses
Increasing Cache Performance
Performance of Multi-level Caches (L1,L2, …)
Real world example caches
And in Conclusion …
10/19/17
Fall 2017 – Lecture #16

## Slide 48
10/19/17
Fall 2017 - Lecture #16

## Slide 49: CPI/Miss Rates/DRAM Access SpecInt2006
Instructions and Data
Data Only
Data Only
Fall 2017 - Lecture #16

## Slide 50: Skylark: Intel’s Recent Generation Laptop/Tablet Class CPUs

## Slide 51: Outline
Understanding Cache Misses
Increasing Cache Performance
Performance of Multi-level Caches (L1,L2, …)
Real world example caches
And in Conclusion …
10/19/17
Fall 2017 – Lecture #16

## Slide 52: Bottom Line: Cache Design Space
Several interacting dimensions
  Cache size
  Block size
  Associativity
  Replacement policy
  Write-through vs. write-back
  Write allocation
Optimal choice is a compromise
  Depends on access characteristics
    Workload
    Use (I-cache, D-cache)
  Depends on technology / cost
Simplicity often wins
Associativity
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B
10/19/17
Fall 2017 - Lecture #16
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.