## Slide 1: CS 61C: Great Ideas in Computer Architecture Lecture 18: Parallel Processing – SIMD
Krste Asanović & Randy Katz
http://inst.eecs.berkeley.edu/~cs61c

## Slide 2: 61C Survey
It would be nice to have a review lecture every once in a while, actually showing us how things fit in the bigger picture

## Slide 3: Agenda
61C – the big picture
Parallel processing
Single instruction, multiple data
SIMD matrix multiplication
Amdahl’s law
Loop unrolling
Memory access strategy - blocking
And in Conclusion, …

## Slide 4: 61C Topics so far …
What we learned:
  Binary numbers
  C
  Pointers
  Assembly language
  Datapath architecture
  Pipelining
  Caches
  Performance evaluation
  Floating point
What does this buy us?
  Promise: execution speed
  Let’s check!

## Slide 5: Reference Problem
Matrix multiplication
  Basic operation in many engineering, data, and imaging processing tasks
  Image filtering, noise reduction, …
  Many closely related operations
    E.g. stereo vision (project 4)
dgemm
  double-precision floating-point matrix multiplication

## Slide 6: Application Example: Deep Learning
Image classification (cats …)
Pick “best” vacation photos
Machine translation
Clean up accent
Fingerprint verification
Automatic game playing

## Slide 7: Matrices
N-1
N-1
0
0
Square matrix of dimension NxN

## Slide 8: Matrix Multiplication
C = A*B
Cij = Σk (Aik * Bkj)
A
B
C

## Slide 9: Reference: Python
Matrix multiplication in Python
N | Python [Mflops]
32 | 5.4
160 | 5.5
480 | 5.4
960 | 5.3
1 MFLOP = 1 Million floating-point operations per second (fadd, fmul)
dgemm(N …) takes 2*N3 flops

## Slide 10: C
c = a * b
a, b, c are N x N matrices

## Slide 11: Timing Program Execution

## Slide 12: C versus Python
N | C [GFLOPS] | Python [GFLOPS]
32 | 1.30 | 0.0054
160 | 1.30 | 0.0055
480 | 1.32 | 0.0054
960 | 0.91 | 0.0053
Which class gives you this kind of power?
We could stop here … but why? Let’s do better!
240x!

## Slide 13: Agenda
61C – the big picture
Parallel processing
Single instruction, multiple data
SIMD matrix multiplication
Amdahl’s law
Loop unrolling
Memory access strategy - blocking
And in Conclusion, …

## Slide 14: Why Parallel Processing?
CPU Clock Rates are no longer increasing
  Technical & economic challenges
    Advanced cooling technology too expensive or impractical for most applications
    Energy costs are prohibitive
Parallel processing is only path to higher speed
  Compare airlines:
    Maximum speed limited by speed of sound and economics
    Use more and larger airplanes to increase throughput
    And smaller seats …
Notes: Smaller seats … what kind of Moore’s law is this?

## Slide 15: Using Parallelism for Performance
Two basic ways:
  Multiprogramming
    run multiple independent programs in parallel
    “Easy”
  Parallel computing
    run one program faster
    “Hard”
We’ll focus on parallel computing in the next few lectures

## Slide 16: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s
Lecture

## Slide 17: Single-Instruction/Single-Data Stream (SISD)
Sequential computer that exploits no parallelism in either the instruction or data streams. Examples of SISD architecture are traditional uniprocessor machines
  E.g. our trusted RISC-V pipeline
Processing Unit
This is what we did up to now in 61C

## Slide 18: Single-Instruction/Multiple-Data Stream (SIMD or “sim-dee”)
SIMD computer exploits multiple data streams against a single instruction stream to operations that may be naturally parallelized, e.g., Intel SIMD instruction extensions or NVIDIA Graphics Processing Unit (GPU)
Today’s topic.

## Slide 19: Multiple-Instruction/Multiple-Data Streams (MIMD or “mim-dee”)
Multiple autonomous processors simultaneously executing different instructions on different data.
  MIMD architectures include multicore and Warehouse-Scale Computers
Instruction Pool
PU
PU
PU
PU
Data Pool
Topic of Lecture 19 and beyond.

## Slide 20: Multiple-Instruction/Single-Data Stream (MISD)
Multiple-Instruction, Single-Data stream computer that exploits multiple instruction streams against a single data stream.
  Historical significance
This has few applications. Not covered in 61C.

## Slide 21: Flynn* Taxonomy, 1966
SIMD and MIMD are currently the most common parallelism in architectures – usually both in same system!
Most common parallel processing programming style: Single Program Multiple Data (“SPMD”)
  Single program that runs on all processors of a MIMD
  Cross-processor execution coordination using synchronization primitives

## Slide 22: Agenda
61C – the big picture
Parallel processing
Single instruction, multiple data
SIMD matrix multiplication
Amdahl’s law
Loop unrolling
Memory access strategy - blocking
And in Conclusion, …

## Slide 23: SIMD – “Single Instruction Multiple Data”

## Slide 24: SIMD Applications & Implementations
Applications
  Scientific computing
    Matlab, NumPy
  Graphics and video processing
    Photoshop, …
  Big Data
    Deep learning
  Gaming
  …
Implementations
  x86
  ARM
  RISC-V vector extensions

## Slide 25: First SIMD Extensions: MIT Lincoln Labs TX-2, 1957

## Slide 26: x86 SIMD Evolution
http://svmoore.pbworks.com/w/file/fetch/70583970/VectorOps.pdf
New instructions
New, wider, more registers
More parallelism

## Slide 27: Laptop CPU Specs
$ sysctl -a | grep cpu
hw.physicalcpu: 2
hw.logicalcpu: 4
machdep.cpu.brand_string: Intel(R) Core(TM) i7-5557U CPU @ 3.10GHz
machdep.cpu.features: FPU VME DE PSE TSC MSR PAE MCE CX8 APIC SEP MTRR PGE MCA CMOV PAT PSE36 CLFSH DS ACPI MMX FXSR SSE SSE2 SS HTT TM PBE SSE3 PCLMULQDQ DTES64 MON DSCPL VMX EST TM2 SSSE3 FMA CX16 TPR PDCM SSE4.1 SSE4.2 x2APIC MOVBE POPCNT AES PCID XSAVE OSXSAVE SEGLIM64 TSCTMR AVX1.0 RDRAND F16C
machdep.cpu.leaf7_features: SMEP ERMS RDWRFSGS TSC_THREAD_OFFSET BMI1 AVX2 BMI2 INVPCID SMAP RDSEED ADX IPT FPU_CSDS

## Slide 28: SIMD Registers

## Slide 29: SIMD Data Types
(Now also AVX-512 available)

## Slide 30: SIMD Vector Mode

## Slide 31: Agenda
61C – the big picture
Parallel processing
Single instruction, multiple data
SIMD matrix multiplication
Amdahl’s law
Loop unrolling
Memory access strategy - blocking
And in Conclusion, …

## Slide 32: Problem
Today’s compilers (largely) do not generate SIMD code
Back to assembly …
x86 (not using RISC-V as no vector hardware yet)
  Over 1000 instructions to learn …
  Green Book
Can we use the compiler to generate all non-SIMD instructions?

## Slide 33: x86 Intrinsics AVX Data Types
Intrinsics: Direct access to registers & assembly from C
Register

## Slide 34: Intrinsics AVX Code Nomenclature

## Slide 35: x86 SIMD “Intrinsics”
https://software.intel.com/sites/landingpage/IntrinsicsGuide/
4 parallel multiplies
2 instructions per clock cycle (CPI = 0.5)
assembly instruction

## Slide 36: Raw Double-Precision Throughput
Characteristic | Value
CPU | i7-5557U
Clock rate (sustained) | 3.1 GHz
Instructions per clock (mul_pd) | 2
Parallel multiplies per instruction | 4
Peak double FLOPS | 24.8 GFLOPS
Actual performance is lower because of overhead
https://www.karlrupp.net/2013/06/cpu-gpu-and-mic-hardware-characteristics-over-time/

## Slide 37: Vectorized Matrix Multiplication
Inner Loop:
for i …; i+=4
for j ...
i += 4

## Slide 38: “Vectorized” dgemm

## Slide 39: Performance
N | Gflops | 
 | scalar | avx
32 | 1.30 | 4.56
160 | 1.30 | 5.47
480 | 1.32 | 5.27
960 | 0.91 | 3.64
4x faster
But still << theoretical 25 GFLOPS!

## Slide 40: Agenda
61C – the big picture
Parallel processing
Single instruction, multiple data
SIMD matrix multiplication
Amdahl’s law
Loop unrolling
Memory access strategy - blocking
And in Conclusion, …

## Slide 41: A trip to LA
Get to SFO & check-in | SFO  LAX | Get to destination
3 hours | 1 hour | 3 hours
Commercial airline:
Supersonic aircraft:
Get to SFO & check-in | SFO  LAX | Get to destination
3 hours | 6 min | 3 hours
Total time: 7 hours
Total time: 6.1 hours
Speedup:
Flying time Sflight = 60 / 6 = 10x
Trip time Strip = 7 / 6.1 = 1.15x
Notes: Google sign-up bonus: supersonic plane for A in 61C
Trip to LA: brief relief from traffic jams
Speedup … it’s still worth it to get an A in 61C. Perhaps for a weekend in Paris?

## Slide 42: Amdahl’s Law
Get enhancement E for your new PC
  E.g. floating-point rocket booster
E
  Speeds up some task (e.g. arithmetic) by factor SE
  F is fraction of program that uses this ”task”
1-F | F
1-F | F / SE
Execution Time:
Speedup:
T0 (no E)
TE (with E)
no speedup
speedup section
Speedup = TO / TE = 1 / ((1-F) + F/SE)
Notes: Computer scientists call this Amdahl’s law
Don’t forget, you may need the jargon for the Google interview

## Slide 43: Big Idea: Amdahl’s Law
Part not sped up
Part sped up
Example: The execution time of half of a program can be accelerated by a factor of 2. What is the program speed-up overall?
Speedup = TO / TE = 1 / ((1-F) + F/SE)
TO / TE = 1 / ((1-F) + F/SE) = 1/((1- 0.5)+0.5/2) = 1.33 << 2

## Slide 44: Maximum “Achievable” Speed-Up
Question: What is a reasonable # of parallel processors to speed up an algorithm with F = 95%? (i.e. 19/20th can be sped up)
a) Maximum speedup: Smax = 1/(1-0.95) = 20
but needs SE=∞!
Reasonable “engineering” compromise:
Equal time in sequential and parallel code: (1-F) = F/SE
SE = F/(1-F) = 0.95/0.05 = 20
S = 1/(0.05+0.05) = 10
Speedup = 1 / ((1-F) + F/SE)
(SE->∞) = 1/(1-F)
Notes: infinity? A few more years of Moore’s law …

## Slide 45
If the portion of the program that can be parallelized is small, then the speedup is limited
In this region, the sequential portion limits the performance
500 processors
for 19x
20 processors
for 10x

## Slide 46: Strong and Weak Scaling
To get good speedup on a parallel processor while keeping the problem size fixed is harder than getting good speedup by increasing the size of the problem.
  Strong scaling: when speedup can be achieved on a parallel processor without increasing the size of the problem
  Weak scaling: when speedup is achieved on a parallel processor by increasing the size of the problem proportionally to the increase in the number of processors
Load balancing is another important factor: every processor doing same amount of work
  Just one unit with twice the load of others cuts speedup almost in half
Notes: Add load balancing example here – page 638

## Slide 47: Peer Instruction
Suppose a program spends 80% of its time in a square-root routine. How much must you speedup square root to make the program run 5 times faster?
Speedup = 1 / ((1-F) + F/SE)
RED: 5
GREEN: 20
ORANGE: 500
YELLOW: None of above

## Slide 48: Administrivia
Midterm 2 is Tuesday during class time!
  Review Session: Saturday 10-12pm @Hearst Annex A1
  One double-sided crib sheet; we’ll provide the RISCV card
  Bring your ID! We’ll check it
  Room assignments posted on Piazza
Project 2 pre-lab due Friday
HW4 due 11/3, but advisable to finish by the midterm
Project 2-2 due 11/6, but also good to finish before MT2

## Slide 49: Agenda
61C – the big picture
Parallel processing
Single instruction, multiple data
SIMD matrix multiplication
Amdahl’s law
Loop unrolling
Memory access strategy - blocking
And in Conclusion, …

## Slide 50: Amdahl’s Law applied to dgemm
Measured dgemm performance
  Peak 5.5 GFLOPS
  Large matrices 3.6 GFLOPS
  Processor 24.8 GFLOPS
Why are we not getting (close to) 25 GFLOPS?
  Something else (not floating-point ALU) is limiting performance!
  But what? Possible culprits:
    Cache
    Hazards
    Let’s look at both!

## Slide 51: Pipeline Hazards – dgemm

## Slide 52: Loop Unrolling
Compiler does the unrolling
How do you verify that the generated code is actually unrolled?
4 registers

## Slide 53: Performance
N | Gflops |  | 
 | scalar | avx | unroll
32 | 1.30 | 4.56 | 12.95
160 | 1.30 | 5.47 | 19.70
480 | 1.32 | 5.27 | 14.50
960 | 0.91 | 3.64 | 6.91
?
WOW!

## Slide 54: Agenda
61C – the big picture
Parallel processing
Single instruction, multiple data
SIMD matrix multiplication
Amdahl’s law
Loop unrolling
Memory access strategy - blocking
And in Conclusion, …

## Slide 55: FPU versus Memory Access
How many floating-point operations does matrix multiply take?
  F = 2 x N3 (N3 multiplies, N3 adds)
How many memory load/stores?
  M = 3 x N2 (for A, B, C)
Many more floating-point operations than memory accesses
  q = F/M = 2/3 * N
  Good, since arithmetic is faster than memory access
  Let’s check the code …

## Slide 56: But memory is accessed repeatedly
q = F/M = 1! (2 loads and 2 floating-point operations)
Inner loop:

## Slide 57
Second-Level
Cache
(SRAM)
Typical Memory Hierarchy
Control
Datapath
Secondary
Memory
(Disk
Or Flash)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Speed (cycles): ½’s 1’s 10’s 100’s-1000 1,000,000’s
Size (bytes): 100’s 10K’s M’s G’s T’s
Where are the operands (A, B, C) stored?
What happens as N increases?
Idea: arrange that most accesses are to fast cache!
Cost/bit: highest lowest
Third-Level
Cache
(SRAM)

## Slide 58: Sub-Matrix Multiplication or: Beating Amdahl’s Law

## Slide 59: Blocking
Idea:
  Rearrange code to use values loaded in cache many times
  Only “few” accesses to slow main memory (DRAM) per floating point operation
   throughput limited by FP hardware and cache, not slow DRAM
  P&H, RISC-V edition p. 465

## Slide 60: Memory Access Blocking

## Slide 61: Performance
N | Gflops |  |  | 
 | scalar | avx | unroll | blocking
32 | 1.30 | 4.56 | 12.95 | 13.80
160 | 1.30 | 5.47 | 19.70 | 21.79
480 | 1.32 | 5.27 | 14.50 | 20.17
960 | 0.91 | 3.64 | 6.91 | 15.82

## Slide 62: Agenda
61C – the big picture
Parallel processing
Single instruction, multiple data
SIMD matrix multiplication
Amdahl’s law
Loop unrolling
Memory access strategy - blocking
And in Conclusion, …

## Slide 63: And in Conclusion, …
Approaches to Parallelism
  SISD, SIMD, MIMD (next lecture)
SIMD
  One instruction operates on multiple operands simultaneously
Example: matrix multiplication
  Floating point heavy  exploit Moore’s law to make fast
Amdahl’s Law:
  Serial sections limit speedup
  Cache
    Blocking
  Hazards
    Loop unrolling