## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Introduction to Machine Language

## Slide 2: Review of Last Lecture
C Memory Layout
  Local variables disappear because Stack changes
  Global variables don’t disappear because they are in Static Data
  Dynamic memory available using malloc and free, but must be used VERY CAREFULLY
Memory Management
  K&R: first-fit, last-fit, best-fit for malloc()
Many Common Memory Problems

## Slide 3: Great Idea #1: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
Higher-Level Language Program (e.g. C)
Assembly Language Program (e.g. MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g. block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
We are here_

## Slide 4: Agenda
Machine Languages
Registers
Administrivia
Instructions and Immediates
Data Transfer Instructions
Decision Making Instructions
Bonus: C to MIPS Practice
Bonus: Additional Instructions

## Slide 5: Machine Language (1/2)
“Word” a computer understands: instruction
Vocabulary of all “words” a computer understands: instruction set architecture (ISA)
Why might you want the same ISA? Why might you want different ISAs?
  e.g. iPhone and iPad use the same
  e.g. iPhone and Macbook use different

## Slide 6: Machine Language (2/2)
Single ISA
  Leverage common compilers, operating systems, etc.
  BUT fairly easy to retarget these for different ISAs (e.g. Linux, gcc)
Multiple ISAs
  Specialized instructions for specialized applications
  Different tradeoffs in resources used (e.g. functionality, memory demands, complexity, power consumption, etc.)
  Competition and innovation is good, especially in emerging environments (e.g. mobile devices)

## Slide 7: Why Study Assembly?
Understand computers at a deeper level
  Learn to write more compact and efficient code
  Can sometimes hand optimize better than a compiler
More sensible for minimalistic applications
  e.g. distributed sensing and systems
  Eliminating OS, compilers, etc. reduce size and power consumption
  Embedded computers outnumber PCs!

## Slide 8: Reduced Instruction Set Computing
The early trend was to add more and more instructions to do elaborate operations – this became known as Complex Instruction Set Computing (CISC)
Opposite philosophy later began to dominate: Reduced Instruction Set Computing (RISC)
  Simpler (and smaller) instruction set makes it easier to build fast hardware
  Let software do the complicated operations by composing simpler ones

## Slide 9: Common RISC Simplifications
Fixed instruction length: Simplifies fetching instructions from memory
Simplified addressing modes: Simplifies fetching operands from memory
Few and simple instructions in the instruction set: Simplifies instruction execution
Minimize memory access instructions (load/store): Simplifies necessary hardware for memory access
Let compiler do heavy lifting: Breaks complex statements into multiple assembly instructions

## Slide 10: Mainstream ISAs
Intel 80x86
  Used in Macbooks and PCs
  Found in Core i3, Core i5, Core i7, etc.
Advanced RISC Machine (ARM)
  Smart phone-like devices: iPhone, iPad, iPod, etc.
  The most popular RISC (20x more common than 80x86)
MIPS
  Networking equipment, PS2, PSP
  Very similar to ARM
This is the ISA we will learn in CS61C
Notes: MIPS was originally an acronym for Microprocessor without Interlocked Pipeline Stages. Developed by MIPS Technologies (formerly MIPS Computer Systems, Inc.).

## Slide 11: Agenda
Machine Languages
Registers
Administrivia
Instructions and Immediates
Data Transfer Instructions
Decision Making Instructions
Bonus: C to MIPS Practice
Bonus: Additional Instructions

## Slide 12: Five Components of a Computer
We begin our study of how a computer works!
  Control
  Datapath
  Memory
  Input
  Output
Registers are part of the Datapath
Processor
Computer
Control
(“brain”)
Datapath
Registers
Memory
Devices
Input
Output
Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts:
1) The input devices bring the data from the outside world into the computer.
2) These data are kept in the computer’s memory until...
3) The datapath request and process them.
4) The operation of the datapath is controlled by the computer’s controller.
All the work done by the computer will NOT do us any good unless we can get the data back to the outside world, so…
5) Getting the data back to the outside world is the job of the output devices.
The most COMMON way to connect these 5 components together is to use a network of busses.

## Slide 13: Computer Hardware Operands
In high-level languages, number of variables limited only by available memory
ISAs have a fixed, small number of operands called registers
  Special locations built directly into hardware
  Benefit: Registers are EXTREMELY FAST (faster than 1 billionth of a second)
  Drawback: Operations can only be performed on these predetermined number of registers
Notes: Registers visible to compiler (or MIPS programmer).

## Slide 14: MIPS Registers
MIPS has 32 registers
  Each register is 32 bits wide and hold a word
Tradeoff between speed and availability
  Smaller number means faster hardware but insufficient to hold data for typical C programs
Registers have no type (C concept); the operation being performed determines how register contents are treated
Notes: word = group of 32 bits (like how byte = group of 8 bits)
For the sake of comparison, ARM uses 16 registers.

## Slide 15: MIPS Registers
Register denoted by ‘$’ can be referenced by number ($0-$31) or name:
  Registers that hold programmer variables:
$s0-$s7 $16-$23
  Registers that hold temporary variables:
$t0-$t7 $8-$15
$t8-$t9 $24-$25
  You’ll learn about the other 14 registers later
In general, using register names makes code more readable
Notes: Both the book and the a quick Google search do not provide a sufficient explanation for why $t8 and $t9 are separated from the other temporary registers.

## Slide 16: Agenda
Machine Languages
Registers
Administrivia
Instructions and Immediates
Data Transfer Instructions
Decision Making Instructions
Bonus: C to MIPS Practice
Bonus: Additional Instructions

## Slide 17: Administrivia
HW2 posted, due this Sunday (7/1)
Lab 3 posted, Lab 4 posted tomorrow
Project 1 posted mid-week, due next Sunday (7/8)
  MIPS Instruction Set Emulator

## Slide 18: Agenda
Machine Languages
Registers
Administrivia
Instructions and Immediates
Data Transfer Instructions
Decision Making Instructions
Bonus: C to MIPS Practice
Bonus: Additional Instructions

## Slide 19: MIPS Green Sheet
Contains MIPS instructions and lots of other useful information
  http://inst.eecs.berkeley.edu/~cs61c/resources/MIPS_Green_Sheet.pdf
  Hard copy in textbook (will be provided on exams)
Inspired by the IBM 360 “Green Card” from the late 1960’s and 1970’s
  http://en.wikipedia.org/wiki/Green_card_(IBM/360)

## Slide 20: MIPS Instructions
Instruction Syntax is rigid:
op dst, src1, src2
  1 operator, 3 operands
    op = operation name (“operator”)
    dst = register getting result (“destination”)
    src1 = first register for operation (“source 1”)
    src2 = second register for operation (“source 2”)
Keep hardware simple via regularity

## Slide 21: MIPS Instructions
One operation per instruction, at most one instruction per line
Assembly instructions are related to C operations (=, +, -, *, /, &, |, etc.)
  Must be, since C code decomposes into assembly!
A single line of C may break up into several lines of MIPS

## Slide 22: MIPS Instructions Example
Your very first instructions! (assume here that the variables a, b, and c are assigned to registers $s1, $s2, and $s3, respectively)
Integer Addition (add)
  C: a = b + c
  MIPS: add $s1, $s2, $s3
Integer Subtraction (sub)
  C: a = b - c
  MIPS: sub $s1, $s2, $s3

## Slide 23: MIPS Instructions Example
Suppose a$s0, b$s1, c$s2, d$s3, and e$s4. Convert the following C statement to MIPS:
a = (b + c) – (d + e);
add $t1, $s3, $s4
add $t2, $s1, $s2
sub $s0, $t2, $t1
Ordering of instructions matters (must follow order of operations)
Utilize temporary registers
Notes: add $so, $s1, $s2
add $t0, $s3, $s4
sub $s0, $s0, $t0

## Slide 24: Comments in MIPS
Comments in MIPS follow hash mark (#) until the end of line
  Improves readability and helps you keep track of variables/registers!
add $t1, $s3, $s4 # $t1=d+e
add $t2, $s1, $s2 # $t2=b+c
sub $s0, $t2, $t1 # a=(b+c)-(d+e)

## Slide 25: The Zero Register
Zero appears so often in code and is so useful that it has its own register!
Register zero ($0 or $zero) always has the value 0 and cannot be changed!
  i.e. any instruction with $0 as dst has no effect
Example Uses:
  add $s3, $0, $0 # c=0
  add $s1, $s2, $0 # a=b

## Slide 26: Immediates
Numerical constants are called immediates
Separate instruction syntax for immediates:
opi dst, src, imm
  Operation names end with ‘i’, replace 2nd source register with an immediate (check Green Sheet for un/signed)
Example Uses:
  addi $s1, $s2, 5 # a=b+5
  addi $s3, $s3, 1 # c++
Why no subi instruction?
Notes: Goal of RISC is to minimize instruction set. subi dst, src, imm = addi dst, src, -imm.

## Slide 27: Agenda
Machine Languages
Registers
Administrivia
Instructions and Immediates
Data Transfer Instructions
Decision Making Instructions
Bonus: C to MIPS Practice
Bonus: Additional Instructions

## Slide 28: Five Components of a Computer
Data Transfer instructions are between registers (Datapath) and Memory
  Allow us to fetch and store operands in memory
Processor
Computer
Control
(“brain”)
Datapath
Registers
Memory
Devices
Input
Output
Store (to)
Load (from)
Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts:
1) The input devices bring the data from the outside world into the computer.
2) These data are kept in the computer’s memory until...
3) The datapath request and process them.
4) The operation of the datapath is controlled by the computer’s controller.
All the work done by the computer will NOT do us any good unless we can get the data back to the outside world, so…
5) Getting the data back to the outside world is the job of the output devices.
The most COMMON way to connect these 5 components together is to use a network of busses.

## Slide 29: Data Transfer
C variables map onto registers; What about large data structures like arrays?
  Don’t forget memory, our one-dimensional array indexed by addresses starting at 0
MIPS instructions only operate on registers!
Specialized data transfer instructions move data between registers and memory
  Store: register TO memory
  Load: register FROM memory

## Slide 30: Data Transfer
Instruction syntax for data transfer:
op reg, off(bAddr)
  op = operation name (“operator”)
  reg = register for operation source or destination
  bAddr = register with pointer to memory (“base address”)
  off = address offset (immediate) in bytes (“offset”)
Accesses memory at address bAddr+off
Reminder: A register holds a word of raw data (no type) – make sure to use a register (and offset) that point to a valid memory address

## Slide 31: Memory is Byte-Addressed
What was the smallest data type we saw in C?
  A char, which was a byte (8 bits)
  Everything in multiples of 8 bits (e.g. 1 word = 4 bytes)
Memory addresses are indexed by bytes, not words
Word addresses are 4 bytes apart
  Word addr is same as left-most byte
  Offsets are multiples of 4 to be “word-aligned”
Pointer arithmetic not done for you in assembly
  Must take data size into account yourself
0
1
2
3
…
Addr of lowest byte in word is addr of word
0
4
8
12
…
1
5
9
13
…
2
6
10
14
…
3
7
11
15
…

## Slide 32: Data Transfer Instructions
Load Word (lw)
  Takes data at address bAddr+off FROM memory and places it into reg
Store Word (sw)
  Takes data in reg and stores it TO memory at address bAddr+off
Example Usage:
# addr of int A[] -> $s3, a -> $s0
lw $t0,12($s3) # $t0=A[3]
add $t0,$s2,$t0 # $t0=A[3]+a
sw $t0,40($s3) # A[10]=A[3]+a

## Slide 33: Registers vs. Memory
What if more variables than registers?
  Keep most frequently used in registers and move the rest to memory (called spilling to memory)
Why not all variables in memory?
  Smaller is faster: registers 100-500 times faster
  Registers more versatile
    In 1 arithmetic instruction: read 2 operands, perform 1 operation, and 1 write
    In 1 data transfer instruction: 1 read/write, no operation

## Slide 34: Great Idea #3: Principle of Locality/ Memory Hierarchy
Memory
Registers

## Slide 35
Can byte address 8GB with a MIPS word
off must be a multiple of 4 for
lw $t0,off($s0) to be valid
If MIPS halved the number of registers
available, it would be twice as fast
add $t0,$t1,4($t2) is valid MIPS
☐
☐
☐
☐
Question: Which of the following is TRUE?

## Slide 36: Chars and Strings
Recall: A string is just an array of characters and a char in C uses 8-bit ASCII
Method 1: Move words in and out of memory using bit-masking and shifting
lw $s0,0($s1)
andi $s0,$s0,0xFF # lowest byte
Method 2: Load/store byte instructions
lb $s0,0($s1)
sb $s0,1($s1)
Offsets no longer need to be multiples of 4
Notes: lb/sb have same syntax as lw/sw
Aside: also load/store halfword (lh/sh)

## Slide 37: Byte Instructions
lb/sb utilize the least significant byte of the register
  On sb, upper 24 bits are ignored
  On lb, upper 24 bits are filled by sign-extension
For example, let *($s0) = 0x00000180:
lb $s1,1($s0) # $s1=0x00000001
lb $s2,0($s0) # $s2=0xFFFFFF80
sb $s2,2($s0) # *($s0)=0x00800180
Normally you don’t want to sign-extend chars
  Use lbu (load byte unsigned)

## Slide 38: Endianness
Big Endian: Most-significant byte at least address of word
  word address = address of most significant byte
Little Endian: Least-significant byte at least address of word
  word address = address of least significant byte
MIPS is bi-endian (can go either way)
  Using MARS simulator in lab, which is little endian
Why is this confusing?
  Data stored in reverse order than you write it out!
  Data 0x01020304 stored as 04 03 02 01 in memory
msb
lsb
3 2 1 0
little endian
0 1 2 3
big endian
Increasing address

## Slide 39: Get to Know Your Staff
Category: Games

## Slide 40: Agenda
Machine Languages
Registers
Administrivia
Instructions and Immediates
Data Transfer Instructions
Decision Making Instructions
Bonus: C to MIPS Practice
Bonus: Additional Instructions

## Slide 41: Computer Decision Making
In C, we had control flow
  Outcomes of comparative/logical statements determined which blocks of code to execute
In MIPS, we can’t define blocks of code; all we have are labels
  Defined by text followed by a colon (e.g. main:) and refers to the instruction that follows
  Generate flow control by jumping labels
  C has these too, but they are considered bad style

## Slide 42: Decision Making Instructions
Branch If Equal (beq)
  beq reg1,reg2,label
  If value in reg1 = value in reg2, go to label
Branch If Not Equal (bne)
  bne reg1,reg2,label
  If value in reg1 ≠ value in reg2, go to label
Jump (j)
  j label
  Unconditional jump to label

## Slide 43: Breaking Down the If Else
C Code:
if(i==j) {
a = b /* then */
} else {
a = -b /* else */
}
In English:
If TRUE, execute the THEN block
If FALSE, execute the ELSE block
MIPS (beq):
# i$s0, j$s1
# a$s2, b$s3
beq $s0,$s1,then
else:
sub $s2, $0, $s3
j end
then:
add $s2, $s3, $0
end:
???
This label unnecessary
???

## Slide 44: Breaking Down the If Else
C Code:
if(i==j) {
a = b /* then */
} else {
a = -b /* else */
}
In English:
If TRUE, execute the THEN block
If FALSE, execute the ELSE block
MIPS (bne):
# i$s0, j$s1
# a$s2, b$s3
bne $s0,$s1,else
then:
add $s2, $s3, $0
j end
else:
sub $s2, $0, $s3
end:
???
???

## Slide 45: Loops in MIPS
There are three types of loops in C:
  while, do…while, and for
  Each can be rewritten as either of the other two, so the same concepts of decision-making apply
You will examine how to write these in MIPS in discussion
Key Concept: Though there are multiple ways to write a loop in MIPS, the key to decision-making is the conditional branch
Notes: When you reach the end of a loop, use a conditional branch instruction to decide whether to jump to the start of the loop or not.

## Slide 46
We can make an unconditional branch from a conditional branch instruction
☐
We can make a loop with just j (no beq or bne)
☐
We can make a for loop without using j
☐
Every control flow segment written with beq can be written in the same number of lines with bne
☐
Question: Which of the following is FALSE?
(and if TRUE, try writing it out)

## Slide 47: Summary
Computers understand the instructions of their ISA
RISC Design Principles
  Smaller is faster, keep it simple
MIPS Registers: $s0-$s7, $t0-$t9, $0
MIPS Instructions
  Arithmetic: add, sub, addi
  Data Transfer: lw, sw, lb, sb, lbu
  Branching: beq, bne, j
Memory is byte-addressed

## Slide 48
You are responsible for the material contained on the following slides, though we may not have enough time to get to them in lecture.
They have been prepared in a way that should be easily readable and the material will be touched upon in the following lecture.
BONUS SLIDES

## Slide 49: Agenda
Machine Languages
Registers
Administrivia
Instructions and Immediates
Data Transfer Instructions
Decision Making Instructions
Bonus: C to MIPS Practice
Bonus: Additional Instructions

## Slide 50: C to MIPS Practice
Let’s put our all of our new MIPS knowledge to use in an example: “Fast String Copy”
C code is as follows:
/* Copy string from p to q */
char *p, *q;
while((*q++ = *p++) != ‘\0’) ;
What do we know about its structure?
  Single while loop
  Exit condition is an equality test

## Slide 51: C to MIPS Practice
Start with code skeleton:
# copy String p to q
# p$s0, q$s1 (pointers)
Loop: lb $t0,0($s0) # $t0 = *p
sb $t0,0($s1) # *q = $t0
addi $s0,$s0,1 # p = p + 1
addi $s1,$s1,1 # q = q + 1
beq $t0,$0,Exit # if *p==0, go to Exit
j Loop # go to Loop
Exit: # N chars in p => N*6 instructions
# $t0 = *p
# *q = $t0
# p = p + 1
# q = q + 1
# if *p==0, go to Exit
# go to Loop

## Slide 52: C to MIPS Practice
Fill in lines:
# copy String p to q
# p$s0, q$s1 (pointers)
Loop: lb $t0,0($s0) # $t0 = *p
sb $t0,0($s1) # *q = $t0
addi $s0,$s0,1 # p = p + 1
addi $s1,$s1,1 # q = q + 1
beq $t0,$0,Exit # if *p==0, go to Exit
j Loop # go to Loop
Exit: # N chars in p => N*6 instructions
lb $t0,0($s0)
sb $t0,0($s1)
addi $s0,$s0,1
addi $s1,$s1,1
beq $t0,$0,Exit

## Slide 53: C to MIPS Practice
Finished code:
# copy String p to q
# p$s0, q$s1 (pointers)
Loop: lb $t0,0($s0) # $t0 = *p
sb $t0,0($s1) # *q = $t0
addi $s0,$s0,1 # p = p + 1
addi $s1,$s1,1 # q = q + 1
beq $t0,$0,Exit # if *p==0, go to Exit
j Loop # go to Loop
Exit: # N chars in p => N*6 instructions
Notes: Is this the only way to write out this function? Of course not.

## Slide 54: C to MIPS Practice
Alternate code using bne:
# copy String p to q
# p$s0, q$s1 (pointers)
Loop: lb $t0,0($s0) # $t0 = *p
sb $t0,0($s1) # *q = $t0
addi $s0,$s0,1 # p = p + 1
addi $s1,$s1,1 # q = q + 1
bne $t0,$0,Loop # if *p!=0, go to Loop
# N chars in p => N*5 instructions
Notes: Used fewer instructions!
Instead of “exit when equal to zero”, we are now using “loop when not equal to zero.”

## Slide 55: Agenda
Machine Languages
Registers
Administrivia
Instructions and Immediates
Data Transfer Instructions
Decision Making Instructions
Bonus: C to MIPS Practice
Bonus: Additional Instructions

## Slide 56: MIPS Arithmetic Instructions
The following commands place results in the special registers HI and LO
  Access these values with “move from HI” (mfhi dst) and “move from LO” (mflo dst)
Multiplication (mult)
  mult src1,src2
  src1*src2: lower 32-bits in LO, upper 32-bits in HI
Division (div)
  div src1,src2
  src1/src2: puts quotient in LO, remainder in HI

## Slide 57: MIPS Arithmetic Instructions
Example:
# mod using div: $s2 = $s0 mod $s1
mod:
div $s0,$s1 # LO = $s0/$s1
mfhi $s2 # HI = $s0 mod $s1

## Slide 58: Arithmetic Overflow
Recall: Overflow occurs when there is a mistake in arithmetic due to the limited precision in computers
  i.e. not enough bits to represent answer
MIPS detects overflow (throws error)
  Arithmetic “unsigned” instructions ignore overflow
Overflow Detection | No Overflow Detection
add dst,src1,src2 | addu dst,src1,src2
addi dst,src1,src2 | addiu dst,src1,src2
sub dst,src1,src2 | subu dst,src1,src2

## Slide 59: Arithmetic Overflow
Example:
# $s0=0x80000000, $s1=0x1
add $t0,$s0,$s0 # overflow (error)
addu $t1,$s0,$s0 # $t1=0
addi $t2,$s0,-1 # overflow (error)
addiu $t2,$s0,-1 # $t3=0x7FFFFFFF
sub $t4,$s0,$s1 # overflow (error)
subu $t5,$s0,$s1 # $t5=0x7FFFFFFF
Recall: this is the most negative number

## Slide 60: MIPS Bitwise Instructions
Note: a$s1, b$s2, c$s3
Instruction | C | MIPS
And | a = b & c; | and $s1,$s2,$s3
And Immediate | a = b & 0x1; | andi $s1,$s2,0x1
Or | a = b ¦ c; | or $s1,$s2,$s3
Or Immediate | a = b ¦ 0x5; | ori $s1,$s2,0x5
Not Or | a = ~(b ¦ c); | nor $s1,$s2,$s3
Exclusive Or | a = b ^ c; | xor $s1,$s2,$s3
Exclusive Or Immediate | a = b ^ 0xF; | xori $s1,$s2,0xF

## Slide 61: Shifting Instructions
In binary, shifting an unsigned number left is the same as multiplying by the corresponding power of 2
  Shifting operations are faster
  Does not work with shifting right/division
Logical shift: Add zeros as you shift
Arithmetic shift: Sign-extend as you shift
  Only applies when you shift right (preserves sign)
Can shift by immediate or value in a register

## Slide 62: Shifting Instructions
Instruction Name | MIPS
Shift Left Logical | sll $s1,$s2,1
Shift Left Logical Variable | sllv $s1,$s2,$s3
Shift Right Logical | srl $s1,$s2,2
Shift Right Logical Variable | srlv $s1,$s2,$s3
Shift Right Arithmetic | sra $s1,$s2,3
Shift Right Arithmetic Variable | srav $s1,$s2,$s3
When using immediate, only values 0-31 are accepted
When using variable, only lowest 5 bits are used (read as unsigned)

## Slide 63: Shifting Instructions
# sample calls to shift instructions
addi $t0,$0 ,-256 # $t0=0xFFFFFF00
sll $s0,$t0,3 # $s0=0xFFFFF800
srl $s1,$t0,8 # $s1=0x00FFFFFF
sra $s2,$t0,8 # $s2=0xFFFFFFFF
addi $t1,$0 ,-22 # $t1=0xFFFFFFEA
# low 5: 0b01010
sllv $s3,$t0,$t1 # $s3=0xFFFC0000
# same as sll $s3,$t0,10

## Slide 64: Shifting Instructions
Example 1:
# lb using lw: lb $s1,1($s0)
lw $s1,0($s0) # get word
andi $s1,$s1,0xFF00 # get 2nd byte
srl $s1,$s1,8 # shift into lowest

## Slide 65: Shifting Instructions
Example 2:
# sb using sw: sb $s1,3($s0)
lw $t0,0($s0) # get current word
andi $t0,$t0,0xFFFFFF # zero top byte
sll $t1,$s1,24 # shift into highest
or $t0,$t0,$t1 # combine
sw $t0,0($s0) # store back

## Slide 66: Shifting Instructions
Extra for Experts:
  Rewrite the two preceding examples to be more general
  Assume that the byte offset (e.g. 1 and 3 in the examples, respectively) is contained in $s2
Hint:
  The variable shift instructions will come in handy
  Remember, the offset can be negative