## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
More MIPS,
MIPS Functions

## Slide 2: Review of Last Lecture
RISC Design Principles
  Smaller is faster: 32 registers, fewer instructions
  Keep it simple: rigid syntax, fixed word length
MIPS Registers: $s0-$s7, $t0-$t9, $0
  Only operands used by instructions
  No variable types, just raw bits
Memory is byte-addressed
  Watch endianness when dealing with bytes

## Slide 3: Review of Last Lecture
MIPS Instructions
  Arithmetic: add, sub, addi,mult,div addu,subu,addiu
  Data Transfer: lw, sw, lb, sb, lbu
  Branching: beq, bne, j
  Bitwise: and,andi,or,ori, nor,xor,xori
  Shifting: sll,sllv,srl,srlv, sra,srav
Notes: Instructions shown in orange were presented in bonus slides from last lecture.

## Slide 4: Review of Last Lecture
Fast string copy code:
# copy String p to q
# p$s0, q$s1 (pointers)
Loop: lb $t0,0($s0) # $t0 = *p
sb $t0,0($s1) # *q = $t0
addi $s0,$s0,1 # p = p + 1
addi $s1,$s1,1 # q = q + 1
beq $t0,$0,Exit # if *p==0, go to Exit
j Loop # go to Loop
Exit: # N chars in p => N*6 instructions
Notes: Is this the only way to write out this function? Of course not.

## Slide 5: Great Idea #1: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
Higher-Level Language Program (e.g. C)
Assembly Language Program (e.g. MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g. block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
We are here_

## Slide 6: Agenda
Inequalities
Pseudo-Instructions
Administrivia
Implementing Functions in MIPS
Function Calling Conventions
Bonus: Remaining Registers
Bonus: Memory Address Convention
Bonus: Register Convention Analogy

## Slide 7: Inequalities in MIPS
Inequality tests: <, <=, >, and >=
  RISC: implement all with 1 additional instruction
Set on Less Than (slt)
  slt dst,src1,src2
  Stores 1 in dst if value in src1 < value in src2 and stores 0 in dst otherwise
Combine with bne, beq, and $0

## Slide 8: Inequalities in MIPS
C Code:
if (a < b) {
... /* then */
}
(let a$s0, b$s1)
MIPS Code:
slt $t0,$s0,$s1
# $t0=1 if a<b
# $t0=0 if a>=b
bne $t0, $0,then
# go to then
# if $t0≠0

## Slide 9: Inequalities in MIPS
C Code:
if (a >= b) {
... /* then */
}
(let a$s0, b$s1)
Try to work out the other two on your own:
  Swap src1 and src2
  Switch beq and bne
MIPS Code:
slt $t0,$s0,$s1
# $t0=1 if a<b
# $t0=0 if a>=b
beq $t0, $0,then
# go to then
# if $t0=0

## Slide 10: Immediates in Inequalities
Three variants of slt:
  sltu dst,src1,src2: unsigned comparison
  slti dst,src,imm: compare against constant
  sltiu dst,src,imm: unsigned comparison against constant
Example:
addi $s0,$0,-1 # $s0=0xFFFFFFFF
slti $t0,$s0,1 # $t0=1
sltiu $t1,$s0,1 # $t1=0
# $t0=1
# $t1=0

## Slide 11: Aside: MIPS Signed vs. Unsigned
MIPS terms “signed” and “unsigned” appear in 3 different contexts:
  Signed vs. unsigned bit extension
    lb
    lbu
  Detect vs. don’t detect overflow
    add, addi, sub, mult, div
    addu, addiu, subu, multu, divu
  Signed vs. unsigned comparison
    slt, slti
    sltu, sltiu

## Slide 12
do {i--;} while(_________);
Loop: # i$s0, j$s1
addi $s0,$s0,-1 # i = i - 1 slti $t0,$s1,2 # $t0 = (j < 2) beq $t0,$0 ,Loop # goto Loop if $t0==0
slt $t0,$s1,$s0 # $t0 = (j < i) bne $t0,$0 ,Loop # goto Loop if $t0!=0
j ≥ 2 || j < i
☐
j ≥ 2 && j < i
☐
j < 2 || j ≥ i
☐
j < 2 && j ≥ i
☐
Question: What C code properly fills in the
following blank?

## Slide 13: Agenda
Inequalities
Pseudo-Instructions
Administrivia
Implementing Functions in MIPS
Function Calling Conventions
Bonus: Remaining Registers
Bonus: Memory Address Convention
Bonus: Register Convention Analogy

## Slide 14: Assembler Pseudo-Instructions
Certain C statements are implemented unintuitively in MIPS
  e.g. assignment (a=b) via addition with 0
MIPS has a set of “pseudo-instructions” to make programming easier
  More intuitive to read, but get translated into actual instructions later
Example:
move dst,src translated into addi dst,src,0

## Slide 15: Assembler Pseudo-Instructions
List of pseudo-instructions: http://en.wikipedia.org/wiki/MIPS_architecture#Pseudo_instructions
  List also includes instruction translation
Load Address (la)
  la dst,label
  Loads address of specified label into dst
Load Immediate (li)
  li dst,imm
  Loads 32-bit immediate into dst
MARS has additional pseudo-instructions
  See Help (F1) for full list

## Slide 16: Assembler Register
Problem:
  When breaking up a pseudo-instruction, the assembler may need to use an extra register
  If it uses a regular register, it’ll overwrite whatever the program has put into it
Solution:
  Reserve a register ($1 or $at for “assembler temporary”) that assembler will use to break up pseudo-instructions
  Since the assembler may use this at any time, it’s not safe to code with it

## Slide 17: MAL vs. TAL
True Assembly Language (TAL)
  The instructions a computer understands and executes
MIPS Assembly Language (MAL)
  Instructions the assembly programmer can use (includes pseudo-instructions)
  Each MAL instruction becomes 1 or more TAL instruction
TAL ⊂ MAL

## Slide 18: Agenda
Inequalities
Pseudo-Instructions
Administrivia
Implementing Functions in MIPS
Function Calling Conventions
Bonus: Remaining Registers
Bonus: Register Convention Analogy

## Slide 19: Administrivia
HW2 due Sunday 7/1
Lab 4 posted today
Project 1 posted by Thursday, due 7/8
  No homework next week (still labs)

## Slide 20: Agenda
Inequalities
Pseudo-Instructions
Administrivia
Implementing Functions in MIPS
Function Calling Conventions
Bonus: Remaining Registers
Bonus: Memory Address Convention
Bonus: Register Convention Analogy

## Slide 21: Six Steps of Calling a Function
Put arguments in a place where the function can access them
Transfer control to the function
The function will acquire any (local) storage resources it needs
The function performs its desired task
The function puts return value in an accessible place and cleans up (restores any used registers)
Control is returned to you

## Slide 22: MIPS Registers for Function Calls
Registers way faster than memory, so use them whenever possible
$a0–$a3: four argument registers to pass parameters
$v0–$v1: two value registers to return values
$ra: return address register that saves where a function is called from

## Slide 23: MIPS Instructions for Function Calls
Jump and Link (jal)
  jal label
  Saves the location of following instruction in register $ra and then jumps to label (function address)
  Used to invoke a function
Jump Register (jr)
  jr src
  Unconditional jump to the address specified in src (almost always used with $ra)
  Used to return from a function

## Slide 24: Instruction Addresses
jal puts the address of an instruction in $ra
Instructions are stored as data in memory!
  Recall: Code section
  More on this next lecture
In MIPS, all instructions are 4 bytes long so each instruction differs in address by 4
  Recall: Memory is byte-addressed
Labels get converted to instruction addresses

## Slide 25: Program Counter
The program counter (PC) is a special register that holds the address of the current instruction being executed
  This register is inaccessible to the programmer, but accessible to jal
jal stores PC+4 into $ra
  What would happen if we stored PC instead?
All branches and jumps (beq, bne, j, jal, jr) work by storing an address into PC

## Slide 26: Function Call Example
... sum(a,b); ... /* a$s0,b$s1 */
int sum(int x, int y) { return x+y; }
1000 addi $a0,$s0,0 # x = a
1004 addi $a1,$s1,0 # y = b
1008 addi $ra,$zero,1016 # $ra=1016
1012 j sum # jump to sum
1016
...
2000 sum: add $v0,$a0,$a1
2004 jr $ra # return
C
MIPS
Would we know this before compiling?
address (decimal)
Otherwise we don’t know where we came from

## Slide 27: Function Call Example
... sum(a,b); ... /* a$s0,b$s1 */
int sum(int x, int y) { return x+y; }
1000 addi $a0,$s0,0 # x = a
1004 addi $a1,$s1,0 # y = b
1008 jal sum # $ra=1012, goto sum
1012
...
2000 sum: add $v0,$a0,$a1
2004 jr $ra # return
address (decimal)
C
MIPS

## Slide 28: Six Steps of Calling a Function
Put arguments in a place where the function can access them
Transfer control to the function
The function will acquire any (local) storage resources it needs
The function performs its desired task
The function puts return value in an accessible place and cleans up (restores any used registers)
Control is returned to you
$a0-$a3
jal
$v0-$v1
jr

## Slide 29: Saving and Restoring Registers
Why might we need to save registers?
  Limited number of registers for everyone to use
  What happens if a function calls another function?
  ($ra would get overwritten!)
Where should we save registers?
$sp (stack pointer) register contains pointer to current bottom (last used space) of stack
The Stack

## Slide 30: Recall: Memory Layout
Space for saved procedure information
Dynamically allocated space
Global variables, string literals
Program instructions
code
static data
heap
stack
∞
0
Address
$sp

## Slide 31: Example: sumSquare
int sumSquare(int x, int y) {
return mult(x,x)+ y; }
What do we need to save?
  Call to mult will overwrite $ra, so save it
  Reusing $a1 to pass 2nd argument to mult, but need current value (y) later, so save $a1
To save something to the Stack, move $sp down the required amount and fill the created space
Notes: In general, you would also want to save $a0 to the Stack, in case the function you call calls another function can overwrites $a0.

## Slide 32: Example: sumSquare
  int sumSquare(int x, int y) { return mult(x,x)+ y; }
sumSquare:
addi $sp,$sp,-8 # make space on stack
sw $ra, 4($sp) # save ret addr
sw $a1, 0($sp) # save y
add $a1,$a0,$zero # set 2nd mult arg
jal mult # call mult
lw $a1, 0($sp) # restore y
add $v0,$v0,$a1 # ret val = mult(x,x)+y
lw $ra, 4($sp) # get ret addr
addi $sp,$sp,8 # restore stack
jr $ra
mult: ...
“push”
“pop”
Notes: The 2nd add instruction is not really part of the “pop.”

## Slide 33: Basic Structure of a Function
func_label: addi $sp,$sp, -framesize sw $ra, [framesize-4]($sp) save other regs if need be
...
restore other regs if need be lw $ra, [framesize-4]($sp)
addi $sp,$sp, framesize jr $ra
Epilogue
Prologue
Body (call other functions…)
ra
stack
Notes: Substitute the proper immediate for [framesize-4].

## Slide 34: Local Variables and Arrays
Any local variables the compiler cannot assign to registers will be allocated as part of the stack frame (Recall: spilling to memory)
Locally declared arrays and structs are also allocated as part of the stack frame
Stack manipulation is same as before
  Move $sp down an extra amount and use the space it created as storage

## Slide 35: Stack Before, During, After Call
Notes: Exact ordering of saved registers is up to you (make sure you keep track, though!).

## Slide 36: Get to Know Your Staff
Category: Games

## Slide 37: Agenda
Inequalities
Pseudo-Instructions
Administrivia
Implementing Functions in MIPS
Function Calling Conventions
Bonus: Remaining Registers
Bonus: Memory Address Convention
Bonus: Register Convention Analogy

## Slide 38: Register Conventions
CalleR: the calling function
CalleE: the function being called
Register Conventions: A set of generally accepted rules as to which registers will be unchanged after a procedure call (jal) and which may have changed

## Slide 39: Saved Registers
These registers are expected to be the same before and after a function call
  If calleE uses them, must restore values before returning
  This means save the old values, use the registers, then reload the old values back into the registers
$s0-$s7 (saved registers)
$sp (stack pointer)
  If not in same place, the caller won’t be able to properly restore values from the stack
$ra (return address)

## Slide 40: Volatile Registers
These registers can be freely changed by the calleE
  If calleR needs them, must save values before making procedure call
$t0-$t9 (temporary registers)
$v0-$v1 (return values)
  These will contain the new returned values
$a0-$a3 (return address and arguments)
  These will change if calleE invokes another function (nested function means calleE is also a calleR)

## Slide 41: Register Conventions Summary
One more time for luck:
  CalleR must save any volatile registers it is using onto the stack before making a procedure call
  CalleE must save any saved registers it intends to use before garbling up their values
Notes:
  CalleR and calleE only need to save the appropriate registers they are using (not all!)
  Don’t forget to restore the values later

## Slide 42: Example: Using Saved Registers
myFunc: # Uses $s0 and $s1
addiu $sp,$sp,-12 # This is the Prologue
sw $ra,8($sp) # Save saved registers
sw $s0,4($sp)
sw $s1,0($sp)
... # Do stuff with $s0 and $s1
jal func1 # $s0 and $s1 unchanged by
... # function calls, so can keep
jal func2 # using them normally
... # Do stuff with $s0 and $s1
lw $s1,0($sp) # This is the Epilogue
lw $s0,4($sp) # Restore saved registers
lw $ra,8($sp)
addiu $sp,$sp,12
jr $ra # return
# This is the Prologue
# This is the Epilogue

## Slide 43: Example: Using Volatile Registers
myFunc: # Uses $t0
addiu $sp,$sp,-4
sw $ra,0($sp) # Save saved registers
... # Do stuff with $t0
addiu $sp,$sp,-4 # Save volatile registers
sw $t0,0($sp) # before calling a function
jal func1 # Function may change $t0
lw $t0,0($sp) # Restore volatile registers
addiu $sp,$sp,4 # before you use them again
... # Do stuff with $t0
lw $ra,0($sp)
addiu $sp,$sp,4 # Restore saved registers
jr $ra # return
# This is the Prologue
# This is the Epilogue

## Slide 44: Choosing Your Registers
Minimize register footprint
  Optimize to reduce number of registers you need to save by choosing which registers to use in a function
  Only save when you absolutely have to
Function does NOT call another function
  Use only $t0-$t9 and there is nothing to save!
Function calls other function(s)
  Values you need throughout go in $s0-$s7, others go in $t0-$t9
  At each function call, check number arguments and return values for whether you or not you need to save
Notes: Recall: memory is MUCH slower than registers.
The more you know about the internals of the other functions you call, the more you can get away with (e.g. using temporary registers that you know the other functions don’t use, so you don’t bother saving them across function calls).

## Slide 45
jal saves PC+1 in $ra
The callee can use temporary registers ($ti) without saving and restoring them
The caller can rely on save registers ($si) without fear of callee changing them
MIPS uses jal to invoke a function and jr to return from a function
☐
☐
☐
☐
Question: Which statement below is FALSE?

## Slide 46: Summary (1/2)
Inequalities done using slt and allow us to implement the rest of control flow
Pseudo-instructions make code more readable
  Count as MAL, later translated into TAL
MIPS function implementation:
  Jump and link (jal) invokes, jump register (jr $ra) returns
  Registers $a0-$a3 for arguments, $v0-$v1 for return values

## Slide 47: Summary (2/2)
Register conventions preserves values of registers between function calls
  Different responsibilities for calleR and calleE
  Registers classified as saved and volatile
Use the Stack for spilling registers, saving return address, and local variables

## Slide 48
You are responsible for the material contained on the following slides, though we may not have enough time to get to them in lecture.
They have been prepared in a way that should be easily readable and the material will be touched upon in the following lecture.
BONUS SLIDES

## Slide 49: Agenda
Inequalities
Pseudo-Instructions
Administrivia
Implementing Functions in MIPS
Function Calling Conventions
Bonus: Remaining Registers
Bonus: Memory Address Convention
Bonus: Register Convention Analogy

## Slide 50: MIPS Registers
The constant 0 $0 $zero
Reserved for Assembler $1 $at
Return Values $2-$3 $v0-$v1
Arguments $4-$7 $a0-$a3
Temporary $8-$15 $t0-$t7
Saved $16-$23 $s0-$s7
More Temporary $24-$25 $t8-$t9
Used by Kernel $26-27 $k0-$k1
Global Pointer $28 $gp
Stack Pointer $29 $sp
Frame Pointer $30 $fp
Return Address $31 $ra

## Slide 51: The Remaining Registers
$at (assembler)
  Used for intermediate calculations by the assembler (pseudo-code); unsafe to use
$k0-$k1 (kernal)
  May be used by the OS at any time; unsafe to use
$gp (global pointer)
  Points to global variables in Static Data; rarely used
$fp (frame pointer)
  Points to top of current frame in Stack; rarely used

## Slide 52: Agenda
Inequalities
Pseudo-Instructions
Administrivia
Implementing Functions in MIPS
Function Calling Conventions
Bonus: Remaining Registers
Bonus: Memory Address Convention
Bonus: Register Convention Analogy

## Slide 53: Memory Address Convention
(Code)
(Heap)
Notes: Recall: Stack grows downwards (decreasing addresses)
Static Data starts at 0x1000 0000 and is of a fixed size. The Heap starts immediately above that.

## Slide 54: Agenda
Inequalities
Pseudo-Instructions
Administrivia
Implementing Functions in MIPS
Function Calling Conventions
Bonus: Remaining Registers
Bonus: Memory Address Convention
Bonus: Register Convention Analogy

## Slide 55: Register Convention Analogy (1/5)
Parents (calleR) leave for the weekend and give the keys to the house to their kid (calleE)
Before leaving, they lay down a set of rules (calling conventions):
  You can trash the temporary rooms like the den and basement if you want; we don’t care about them (volatile registers)
  BUT you’d better leave the rooms for guests (living, dining, bed, etc.) untouched (saved registers): “These rooms better look the same when we return!”

## Slide 56: Register Convention Analogy (2/5)
Kid now “owns” all of the rooms (registers)
Kid is going to throw a wild, wild party (computation) and wants to use the guest rooms (saved registers)
So what does the kid (calleE) do?
  Takes stuff from guest rooms and moves it to the shed in the backyard (memory)
  Throws the party and everything in the house gets trashed (shed is outside, so it survives)
  Restores guest rooms by replacing the items from the backyard shed

## Slide 57: Register Convention Analogy (3/5)
Same scenario, except that during the party, the kid needs to run to the store for supplies
  Kid (calleE) has left valuable stuff (data) all over the house
  The party will continue, meaning the valuable stuff might get destroyed
Kid leaves friend (2nd calleE) in charge, instructing him/her on the rules of the house (conventions)
  Here the kid has become the “heavy” (calleR)

## Slide 58: Register Convention Analogy (4/5)
If kid has valuable stuff (data) in the temporary rooms (volatile registers) that are going to be trashed, there are three options:
  Move stuff to the backyard shed (memory)
  Move stuff to guest rooms (saved registers) whose contents have already been moved to the shed
  Optimize lifestyle (code) so that the amount you’ve got to schlep back and forth from shed is minimized.
    Mantra: “Minimize register footprint”
Otherwise: “Dude, where’s my data?!”

## Slide 59: Register Convention Analogy (5/5)
Friend now “owns” all of the rooms (registers)
Friend decides to allow the wild, wild party (computation) to use the guest rooms (saved registers)
What does the friend (2nd calleE) do?
  Takes stuff from guest rooms and moves it to the shed in the backyard (memory)
  Throws the party and everything in the house gets trashed (shed is outside, so it survives)
  Restores guest rooms by replacing the items from the backyard shed
Same as kid!