## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
MIPS Instruction
Formats

## Slide 2: Review of Last Lecture
New registers: $a0-$a3, $v0-$v1, $ra, $sp
  Also: $at, $k0-k1, $gp, $fp, PC
New instructions: slt, la, li, jal, jr
Saved registers: $s0-$s7, $sp, $ra Volatile registers: $t0-$t9, $v0-$v1, $a0-$a3
  CalleR saves volatile registers it is using before making a procedure call
  CalleE saves saved registers it intends to use
Notes: PC not accessible to the assembly programmer, but used/accessed in all jumping/branching instructions.

## Slide 3
int factorial(int n) {
if(n == 0) return 1;
else return(n*factorial(n-1));
}
This function MUST be implemented recursively
☐
We can write this function without using any saved or temporary registers
☐
We must save $ra on the stack since we need to know where to return to
☐
We could copy $a0 to $a1 to store n across recursive calls instead of saving it
☐
Question: Which statement below is TRUE about converting the following C code to MIPS?

## Slide 4: Great Idea #1: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
Higher-Level Language Program (e.g. C)
Assembly Language Program (e.g. MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g. block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
We__
are__
here._

## Slide 5: Agenda
Stored-Program Concept
R-Format
Administrivia
I-Format
  Branching and PC-Relative Addressing
J-Format
Bonus: Assembly Practice
Bonus: Disassembly Practice

## Slide 6: Big Idea: Stored-Program Concept
Encode your instructions as binary data
  Therefore, entire programs can be stored in memory to be read or written just like data
Simplifies SW/HW of computer systems
  Memory technology for data also used for programs
Stored in memory, so both instructions and data words have addresses
  Use with jumps, branches, and loads

## Slide 7: Binary Compatibility
Programs are distributed in binary form
  Programs bound to specific instruction set
  i.e. different versions for (old) Macs vs. PCs
New machines want to run old programs (“binaries”) as well as programs compiled to new instructions
Leads to “backward compatible” instruction sets that evolve over time
  The selection of Intel 80x86 in 1981 for 1st IBM PC is major reason latest PCs still use 80x86 instruction set (Pentium 4); you could still run program from 1981 PC today

## Slide 8: Instructions as Numbers (1/2)
Currently all data we work with is in words (32-bit blocks)
  Each register is a word in length
  lw and sw both access one word of memory
So how do we represent instructions?
  Remember: computer only understands 1s and 0s, so “add $t0,$0,$0” is meaningless.
  MIPS wants simplicity: since data is in words, let instructions be in words, too

## Slide 9: Instructions as Numbers (2/2)
Divide the 32 bits of an instruction into “fields”
  Each field tells the processor something about the instruction
  Could use different fields for every instruction, but regularity leads to simplicity
Define 3 types of instruction formats:
  R-Format
  I-Format
  J-Format

## Slide 10: Instruction Formats
I-Format: instructions with immediates, lw/sw (offset is immediate), and beq/bne
  But not the shift instructions
J-Format: j and jal
  But not jr
R-Format: all other instructions
It will soon become clear why the instructions have been partitioned in this way

## Slide 11: Agenda
Stored-Program Concept
R-Format
Administrivia
I-Format
  Branching and PC-Relative Addressing
J-Format
Bonus: Assembly Practice
Bonus: Disassembly Practice

## Slide 12: R-Format Instructions (1/4)
Define “fields” of the following number of bits each: 6 + 5 + 5 + 5 + 5 + 6 = 32
For simplicity, each field has a name:
Each field is viewed as its own unsigned int
  5-bit fields can represent any number 0-31, while 6-bit fields can represent any number 0-63
31
0
6
6
5
5
5
5
opcode
funct
rs
rt
rd
shamt
31
0

## Slide 13: R-Format Instructions (2/4)
opcode (6): partially specifies operation
  Set at 0b000000 for all R-Format instructions
funct (6): combined with opcode, this number exactly specifies the instruction
How many R-format instructions can we encode?
  opcode is fixed, so 64
Why aren’t these a single 12-bit field?
  We’ll answer this later

## Slide 14: R-Format Instructions (3/4)
rs (5): specifies register containing 1st operand (“source register”)
rt (5): specifies register containing 2nd operand (“target register” – name is misleading)
rd (5): specifies register that receives the result of the computation (“destination register”)
Recall: MIPS has 32 registers
  Fit perfectly in a 5-bit field (use register numbers)
These map intuitively to instructions
  e.g. add dst,src1,src2  add rd,rs,rt
  Depending on instruction, field may not be used

## Slide 15: R-Format Instructions (4/4)
shamt (5): The amount a shift instruction will shift by
  Shifting a 32-bit word by more than 31 is useless
  This field is set to 0 in all but the shift instructions
For a detailed description of field usage and instruction type for each instruction, see the MIPS Green Card

## Slide 16: R-Format Example (1/2)
MIPS Instruction:
  add $8,$9,$10
Pseudo-code (“OPERATION” column):
  add R[rd] = R[rs] + R[rt]
Fields:
  opcode = 0 (look up on Green Sheet)
  funct = 32 (look up on Green Sheet)
  rd = 8 (destination)
  rs = 9 (first operand)
  rt = 10 (second operand)
  shamt = 0 (not a shift)
Notes: $8 = $t0, $9 = $t1, $10 = $t2

## Slide 17: R-Format Example (2/2)
MIPS Instruction: add $8,$9,$10
  Field representation (decimal):
  Field representation (binary):
  hex representation: 0x 012A 4020
  decimal representation: 19,546,144
  Called a Machine Language Instruction
two
0
32
9
10
8
0
31
0
000000
100000
01001
01010
01000
00000
31
0
Notes: $8 = $t0, $9 = $t1, $10 = $t2

## Slide 18: NOP
What is the instruction 0x00000000?
  opcode is 0, so is an R-Format
Using Green Sheet, translates into: sll $0,$0,0
  What does this do?
This is a special instruction called nop for “No Operation Performed”
  We’ll see its uses later in the course
Nothing!

## Slide 19: Agenda
Stored-Program Concept
R-Format
Administrivia
I-Format
  Branching and PC-Relative Addressing
J-Format
Bonus: Converting to Machine Code Practice

## Slide 20: Administrivia
HW 2 due Sunday
Project 1 due 7/8
  No homework next week
  Will be released in the next two days

## Slide 21: Agenda
Stored-Program Concept
R-Format
Administrivia
I-Format
  Branching and PC-Relative Addressing
J-Format
Bonus: Assembly Practice
Bonus: Disassembly Practice

## Slide 22: I-Format Instructions (1/4)
What about instructions with immediates?
  5- and 6-bit fields too small for most immediates
Ideally, MIPS would have only one instruction format (for simplicity)
  Unfortunately here we need to compromise
Define new instruction format that is partially consistent with R-Format
  First notice that, if instruction has immediate, then it uses at most 2 registers

## Slide 23: I-Format Instructions (2/4)
Define “fields” of the following number of bits each: 6 + 5 + 5 + 16 = 32 bits
Field names:
Key Concept: Three fields are consistent with R-Format instructions
  Most importantly, opcode is still in same location
6
5
5
16
31
0
opcode
rs
rt
immediate
31
0

## Slide 24: I-Format Instructions (3/4)
opcode (6): uniquely specifies the instruction
  All I-Format instructions have non-zero opcode
  R-Format has two 6-bit fields to identify instruction for consistency across formats
rs (5): specifies a register operand
  Not always used
rt (5): specifies register that receives result of computation (“target register”)
  Name makes more sense for I-Format instructions

## Slide 25: I-Format Instructions (4/4)
immediate (16): two’s complement number
  All computations done in words, so 16-bit immediate must be extended to 32 bits
  Green Sheet specifies ZeroExtImm or SignExtImm based on instruction
Can represent 216 different immediates
  This is large enough to handle the offset in a typical lw/sw, plus the vast majority of values for slti
  We’ll see what to do when the number is too big later today…

## Slide 26: I-Format Example (1/2)
MIPS Instruction:
  addi $21,$22,-50
Pseudo-code (“OPERATION” column)
  addi R[rt] = R[rs] + SignExtImm
Fields:
  opcode = 8 (look up on Green Sheet)
  rs = 22 (register containing operand)
  rt = 21 (target register)
  immediate = -50 (decimal by default, can also be specified in hex)
Notes: $21 = $s5, $22 = $s6

## Slide 27: I-Format Example (2/2)
MIPS Instruction: addi $21,$22,-50
  Field representation (decimal):
  Field representation (binary):
  hex representation: 0x 22D5 FFCE
  decimal representation: 584,449,998
  Called a Machine Language Instruction
two
8
22
21
-50
31
0
001000
10110
10101
1111111111001110
31
0
Notes: $21 = $s5, $22 = $s6

## Slide 28
OPCODE/FUNCT: Register names and numbers:
subu 0/35 0: $0
lw 35/-- 8-15: $t0-$t7
addi 8/-- 16-23: $s0-$s7
subu $s0,$s0,$s0
☐
lw $0,0($0)
☐
addi $0,$0,35
☐
subu $0,$0,$0
☐
Question: Which instruction has the same representation as 35ten?
rd
funct
shamt
opcode
rs
rt
rd
funct
shamt
opcode
rs
rt
opcode
rs
rt
immediate
opcode
rs
rt
offset

## Slide 29: Dealing With Large Immediates
How do we deal with 32-bit immediates?
  Sometimes want to use immediates > ± 215 with addi, lw, sw and slti
  Bitwise logic operations with 32-bit immediates
Solution: Don’t mess with instruction formats, just add a new instruction
Load Upper Immediate (lui)
  lui reg,imm
  Moves 16-bit imm into upper half (bits 16-31) of reg and zeros the lower half (bits 0-15)

## Slide 30: lui Example
Want: addi $t0,$t0,0xABABCDCD
  This is a pseudo-instruction!
Translates into:
lui $at,0xABAB # upper 16 ori $at,$at,0xCDCD # lower 16 add $t0,$t0,$at # move
Now we can handle everything with a 16-bit immediate!
Only the assembler gets to use $at

## Slide 31: Branching Instructions
beq and bne
  Need to specify an address to go to
  Also take two registers to compare
Use I-Format:
  opcode specifies beq (4) vs. bne (5)
  rs and rt specify registers
  How to best use immediate to specify addresses?
opcode
rs
rt
immediate
31
0

## Slide 32: Branching Instruction Usage
Branches typically used for loops (if-else, while, for)
  Loops are generally small (< 50 instructions)
  Function calls and unconditional jumps handled with jump instructions (J-Format)
Recall: Instructions stored in a localized area of memory (Code/Text)
  Largest branch distance limited by size of code
  Address of current instruction stored in the program counter (PC)

## Slide 33: PC-Relative Addressing
PC-Relative Addressing: Use the immediate field as a two’s complement offset to PC
  Branches generally change the PC by a small amount
  Can specify ± 215 addresses from the PC
So just how much of memory can we reach?

## Slide 34: Branching Reach
Recall: MIPS uses 32-bit addresses
  Memory is byte-addressed
Instructions are word-aligned
  Address is always multiple of 4 (in bytes), meaning it ends with 0b00 in binary
  Number of bytes to add to the PC will always be a multiple of 4
Immediate specifies words instead of bytes
  Can now branch ± 215 words
  We can reach 216 instructions = 218 bytes around PC

## Slide 35: Branch Calculation
If we don’t take the branch:
  PC = PC + 4 = next instruction
If we do take the branch:
  PC = (PC+4) + (immediate*4)
Observations:
  immediate is number of instructions to jump (remember, specifies words) either forward (+) or backwards (–)
  Branch from PC+4 for hardware reasons; will be clear why later in the course

## Slide 36: Branch Example (1/2)
MIPS Code:
  Loop: beq $9,$0,End addu $8,$8,$10 addiu $9,$9,-1 j Loop End:
I-Format fields:
  opcode = 4 (look up on Green Sheet)
  rs = 9 (first operand)
  rt = 0 (second operand)
  immediate = ???
Start counting from instruction AFTER the branch
1
2
3
3

## Slide 37: Branch Example (2/2)
MIPS Code:
  Loop: beq $9,$0,End addu $8,$8,$10 addiu $9,$9,-1 j Loop End:
  Field representation (decimal):
  Field representation (binary):
4
9
0
3
31
0
000100
01001
00000
0000000000000011
31
0

## Slide 38: Questions on PC-addressing
Does the value in branch immediate field change if we move the code?
  If moving individual lines of code, then yes
  If moving all of code, then no
What do we do if destination is > 215 instructions away from branch?
  Other instructions save us
  beq $s0,$0,far bne $s0,$0,next # next instr --> j far next: # next instr
Notes: As we will see, jumping instructions can reach farther than branching

## Slide 39: Get to Know Your Staff
Category: Games

## Slide 40: Agenda
Stored-Program Concept
R-Format
Administrivia
I-Format
  Branching and PC-Relative Addressing
J-Format
Bonus: Assembly Practice
Bonus: Disassembly Practice

## Slide 41: J-Format Instructions (1/4)
For branches, we assumed that we won’t want to branch too far, so we can specify a change in the PC
For general jumps (j and jal), we may jump to anywhere in memory
  Ideally, we would specify a 32-bit memory address to jump to
  Unfortunately, we can’t fit both a 6-bit opcode and a 32-bit address into a single 32-bit word

## Slide 42: J-Format Instructions (2/4)
Define two “fields” of these bit widths:
As usual, each field has a name:
Key Concepts:
  Keep opcode field identical to R-Format and I-Format for consistency
  Collapse all other fields to make room for large target address
6
26
31
0
opcode
target address
31
0

## Slide 43: J-Format Instructions (3/4)
We can specify 226 addresses
  Still going to word-aligned instructions, so add 0b00 as last two bits (multiply by 4)
  This brings us to 28 bits of a 32-bit address
Take the 4 highest order bits from the PC
  Cannot reach everywhere, but adequate almost all of the time, since programs aren’t that long
  Only problematic if code straddles a 256MB boundary
If necessary, use 2 jumps or jr (R-Format) instead

## Slide 44: J-Format Instructions (4/4)
Jump instruction:
  New PC = { (PC+4)[31..28], target address, 00 }
Notes:
  { , , } means concatenation { 4 bits , 26 bits , 2 bits } = 32 bit address
    Book uses || instead
  Array indexing: [31..28] means highest 4 bits
  For hardware reasons, use PC+4 instead of PC

## Slide 45
Question: When combining two C files into one executable, we can compile them independently and then merge them together.
When merging two or more binaries:
Jump instructions don’t require any changes
Branch instructions don’t require any changes
F F
☐
F T
☐
T F
☐
T T
☐
1 2

## Slide 46: Summary
The Stored Program concept is very powerful
  Instructions can be treated and manipulated the same way as data in both hardware and software
MIPS Machine Language Instructions:
Branches use PC-relative addressing, Jumps use absolute addressing
opcode
funct
rs
rt
rd
shamt
R:
opcode
rs
rt
immediate
I:
opcode
target address
J:

## Slide 47
You are responsible for the material contained on the following slides, though we may not have enough time to get to them in lecture.
They have been prepared in a way that should be easily readable and the material will be touched upon in the following lecture.
BONUS SLIDES

## Slide 48: Agenda
Stored-Program Concept
R-Format
Administrivia
I-Format
  Branching and PC-Relative Addressing
J-Format
Bonus: Assembly Practice
Bonus: Disassembly Practice

## Slide 49: Assembly Practice
Assembly is the process of converting assembly instructions into machine code
On the following slides, there are 6-lines of assembly code, along with space for the machine code
For each instruction,
  Identify the instruction type (R/I/J)
  Break the space into the proper fields
  Write field values in decimal
  Convert fields to binary
  Write out the machine code in hex
Use your Green Sheet; answers follow

## Slide 50: Code Questions
Addr Instruction
800 Loop: sll $t1,$s3,2
804 addu $t1,$t1,$s6
808 lw $t0,0($t1)
812 beq $t0,$s5, Exit
816 addiu $s3,$s3,1
820 j Loop
Exit:
Material from past lectures:
What type of C variable is probably stored in $s6?
int * (or any pointer)
Write an equivalent C loop using a$s3, b$s5, c$s6. Define variable types (assume they are initialized somewhere) and feel free to introduce other variables as you like.
int a,b,*c;
/* values initialized */
while(c[a] != b) a++;
In English, what does this loop do?
Finds an entry in array c that matches b.
Material from past lectures:
What type of C variable is probably stored in $s6?
Write an equivalent C loop using a$s3, b$s5, c$s6. Define variable types (assume they are initialized somewhere) and feel free to introduce other variables as you like.
In English, what does this loop do?

## Slide 51: Assembly Practice Question
Addr Instruction
800 Loop: sll $t1,$s3,2
804 addu $t1,$t1,$s6
808 lw $t0,0($t1)
812 beq $t0,$s5, Exit
816 addiu $s3,$s3,1
820 j Loop
Exit:
__:
__:
__:
__:
__:
__:

## Slide 52: Assembly Practice Answer (1/4)
Addr Instruction
800 Loop: sll $t1,$s3,2
804 addu $t1,$t1,$s6
808 lw $t0,0($t1)
812 beq $t0,$s5, Exit
816 addiu $s3,$s3,1
820 j Loop
Exit:
opcode
target address
J:
R:
opcode
rs
rt
rd
shamt
funct
R:
opcode
rs
rt
rd
shamt
funct
I:
opcode
rs
rt
immediate
I:
opcode
rs
rt
immediate
I:
opcode
rs
rt
immediate

## Slide 53: Assembly Practice Answer (2/4)
Addr Instruction
800 Loop: sll $t1,$s3,2
804 addu $t1,$t1,$s6
808 lw $t0,0($t1)
812 beq $t0,$s5, Exit
816 addiu $s3,$s3,1
820 j Loop
Exit:
2
200
J:
R:
0
0
19
9
2
0
R:
0
9
22
9
0
33
I:
35
9
8
0
I:
4
8
21
2
I:
8
19
19
1

## Slide 54: Assembly Practice Answer (3/4)
Addr Instruction
800 Loop: sll $t1,$s3,2
804 addu $t1,$t1,$s6
808 lw $t0,0($t1)
812 beq $t0,$s5, Exit
816 addiu $s3,$s3,1
820 j Loop
Exit:
000010
00 0000 0000 0000 0000 1100 1000
J:
R:
000000
00000
10011
01001
00010
000000
R:
000000
01001
10110
01001
00000
100001
I:
100011
01001
01000
0000 0000 0000 0000
I:
000100
01000
10101
0000 0000 0000 0010
I:
001000
10011
10011
0000 0000 0000 0001

## Slide 55: Assembly Practice Answer (4/4)
Addr Instruction
800 Loop: sll $t1,$s3,2
0x 0013 4880
804 addu $t1,$t1,$s6
0x 0136 4821
808 lw $t0,0($t1)
0x 8D28 0000
812 beq $t0,$s5, Exit
0x 1115 0002
816 addiu $s3,$s3,1
0x 2273 0001
820 j Loop
0x 0800 00C8
Exit:
J:
R:
R:
I:
I:
I:

## Slide 56: Agenda
Stored-Program Concept
R-Format
Administrivia
I-Format
  Branching and PC-Relative Addressing
J-Format
Bonus: Assembly Practice
Bonus: Disassembly Practice

## Slide 57: Disassembly Practice
Disassembly is the opposite process of figuring out the instructions from the machine code
On the following slides, there are 6-lines of machine code (hex numbers)
Your task:
  Convert to binary
  Use opcode to determine format and fields
  Write field values in decimal
  Convert fields MIPS instructions (try adding labels)
  Translate into C (be creative!)
Use your Green Sheet; answers follow

## Slide 58: Disassembly Practice Question
Address Instruction
0x00400000 0x00001025
... 0x0005402A
0x11000003
0x00441020
0x20A5FFFF
0x08100001

## Slide 59: Disassembly Practice Answer (1/9)
Address Instruction
0x00400000 00000000000000000001000000100101
... 00000000000001010100000000101010
00010001000000000000000000000011
00000000010001000001000000100000
00100000101001011111111111111111
00001000000100000000000000000001
1) Converted to binary

## Slide 60: Disassembly Practice Answer (2/9)
Address Instruction
0x00400000 00000000000000000001000000100101
... 00000000000001010100000000101010
00010001000000000000000000000011
00000000010001000001000000100000
00100000101001011111111111111111
00001000000100000000000000000001
2) Check opcode for format and fields...
  0 (R-Format), 2 or 3 (J-Format), otherwise (I-Format)
R
R
I
R
I
J

## Slide 61: Disassembly Practice Answer (3/9)
Address Instruction
0x00400000
...
3) Convert to decimal
  Can leave target address in hex
0x0100001
R
R
I
R
I
J
0
0
4
0
8
2
0
0
0
2
37
0
5
0
8
42
2
4
0
2
32
8
0
+3
5
5
-1
Notes: Two ways to find the instruction:
Read field in hex and lookup in “OPCODE/FUNCT” column on the left side of the front of the MIPS Green Sheet (alphabetized by instruction).
Read field in decimal and lookup in table on left side of the back of the MIPS Green Sheet (ordered numerically).

## Slide 62: Disassembly Practice Answer (4/9)
Address Instruction
0x00400000 or $2,$0,$0
0x00400004 slt $8,$0,$5
0x00400008 beq $8,$0,3
0x0040000C add $2,$2,$4
0x00400010 addi $5,$5,-1
0x00400014 j 0x0100001
0x00400018
4) Translate to MIPS instructions (write in addrs)
Notes: Two ways to find the instruction:
Read field in hex and lookup in “OPCODE/FUNCT” column on the left side of the front of the MIPS Green Sheet (alphabetized by instruction).
Read field in decimal and lookup in table on left side of the back of the MIPS Green Sheet (ordered numerically).

## Slide 63: Disassembly Practice Answer (5/9)
Address Instruction
0x00400000 or $v0,$0,$0
0x00400004 slt $t0,$0,$a1
0x00400008 beq $t0,$0,3
0x0040000C add $v0,$v0,$a0
0x00400010 addi $a1,$a1,-1
0x00400014 j 0x0100001 # addr: 0x0400004
0x00400018
4) Translate to MIPS instructions (write in addrs)
  More readable with register names

## Slide 64: Disassembly Practice Answer (6/9)
Address Instruction
0x00400000 or $v0,$0,$0
0x00400004 Loop: slt $t0,$0,$a1
0x00400008 beq $t0,$0,Exit
0x0040000C add $v0,$v0,$a0
0x00400010 addi $a1,$a1,-1
0x00400014 j Loop
0x00400018 Exit:
4) Translate to MIPS instructions (write in addrs)
  Introduce labels

## Slide 65: Disassembly Practice Answer (7/9)
Address Instruction
or $v0,$0,$0 # initialize $v0 to 0
Loop: slt $t0,$0,$a1 # $t0 = 0 if 0 >= $a1
beq $t0,$0,Exit # exit if $a1 <= 0
add $v0,$v0,$a0 # $v0 += $a0
addi $a1,$a1,-1 # decrement $a1
j Loop
Exit:
4) Translate to MIPS instructions (write in addrs)
  What does it do?

## Slide 66: Disassembly Practice Answer (8/9)
/* a$v0, b$a0, c$a1 */
a = 0;
while(c > 0) {
a += b;
c--;
}
5) Translate into C code
  Initial direct translation

## Slide 67: Disassembly Practice Answer (9/9)
/* naïve multiplication: returns m*n */
int multiply(int m, int n) {
int p; /* product */
for(p = 0; n-- > 0; p += m) ;
return p;
}
5) Translate into C code
  One of many possible ways to write this