## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Virtual Memory

## Slide 2: Review of Last Lecture (1/2)
Multiple instruction issue increases max speedup, but higher penalty for a stall
  Superscalar because can achieve CPI < 1
  Requires a significant amount of extra hardware
Employ more aggressive scheduling techniques to increase performance
  Register renaming
  Speculation (guessing)
  Out-of-order execution

## Slide 3: Agenda
Virtual Memory
Page Tables
Administrivia
Translation Lookaside Buffer (TLB)
VM Performance

## Slide 4: Memory Hierarchy
Regs
L2 Cache
Memory
Disk
Tape
Instr Operands
Blocks
Pages
Files
Upper Level
Lower Level
Faster
Larger
L1 Cache
Blocks
Next Up:
Virtual Memory
Earlier: Caches

## Slide 5: Memory Hierarchy Requirements
Principle of Locality
  Allows caches to offer (close to) speed of cache memory with size of DRAM memory
  Can we use this at the next level to give speed of DRAM memory with size of Disk memory?
What other things do we need from our memory system?

## Slide 6: Memory Hierarchy Requirements
Allow multiple processes to simultaneously occupy memory and provide protection
  Don’t let programs read from or write to each other’s memories
Give each program the illusion that it has its own private address space (via translation)
  Suppose code starts at address 0x00400000, then different processes each think their code resides at the same address
  Each program must have a different view of memory

## Slide 7: Virtual Memory
Next level in the memory hierarchy
  Provides illusion of very large main memory
  Working set of “pages” residing in main memory (subset of all pages residing on disk)
Main goal: Avoid reaching all the way back to disk as much as possible
Additional goals:
  Let OS share memory among many programs and protect them from each other
  Each process thinks it has all the memory to itself

## Slide 8: Virtual to Physical Address Translation
Each program operates in its own virtual address space and thinks it’s the only program running
Each is protected from the other
OS can decide where each goes in memory
Hardware gives virtual  physical mapping
Program operates in its virtual address space
Virtual
Address (VA)
(inst. fetch
load, store)
HW mapping
Physical
Address (PA)
(inst. fetch
load, store)
Physical memory (including caches)

## Slide 9: VM Analogy (1/2)
Trying to find a book in the UCB system
Book title is like virtual address (VA)
  What you want/are requesting
Book call number is like physical address (PA)
  Where it is actually located
Card catalogue is like a page table (PT)
  Maps from book title to call number
  Does not contain the actual that data you want
  The catalogue itself takes up space in the library

## Slide 10: VM Analogy (2/2)
Indication of current location within the library system is like valid bit
  Valid if in current library (main memory) vs. invalid if in another branch (disk)
  Found on the card in the card catalogue
Availability/terms of use like access rights
  What you are allowed to do with the book (ability to check out, duration, etc.)
  Also found on the card in the card catalogue

## Slide 11: Agenda
Virtual Memory
Page Tables
Administrivia
Translation Lookaside Buffer (TLB)
VM Performance
VM Wrap-up

## Slide 12: First Attempt: Base and Bound Reg
0
¥
OS
User A
User B
User C
$base
$base+ $bound
Want:
  Discontinuous mapping
  Process size >> mem
Need to use indirection
Enough space for User D,
but discontinuous
(“fragmentation problem”)

## Slide 13: Mapping VM to PM
Divide into equal sized chunks (about 4 KiB - 8 KiB)
Any chunk of Virtual Memory can be assigned to any chunk of Physical Memory (“page”)
0
Physical Memory
¥
Virtual Memory
Code
Static
Heap
Stack
64 MB
0

## Slide 14: Paging Organization
Addr
Trans
MAP
page 0
4 Ki
4 Ki
4 Ki
0x00000
0x01000
0x1F000
Virtual Memory
Virtual
Address
page 1
page 31
4 Ki
0x02000
page 2
...
...
...
page 0
0x0000
0x1000
0x7000
Physical
Address
Physical
Memory
4 Ki
4 Ki
4 Ki
page 1
page 7
...
...
...
Here assume page size is 4 KiB
  Page is both unit of mapping and unit of transfer between disk and physical memory

## Slide 15: Virtual Memory Mapping Function
How large is main memory? Disk?
  Don’t know! Designed to be interchangeable components
  Need a system that works regardless of sizes
Use lookup table (page table) to deal with arbitrary mapping
  Index lookup table by # of pages in VM (not all entries will be used/valid)
  Size of PM will affect size of stored translation

## Slide 16: Address Mapping
Pages are aligned in memory
  Border address of each page has same lowest bits
  Page size is same in VM and PM, so denote lowest O = log2(page size/B) bits as page offset
Use remaining upper address bits in mapping
  Tells you which page you want (similar to Tag)
Page Offset
Virtual Page #
Page Offset
Physical Page #
Same Size
Not necessarily the same size

## Slide 17: Address Mapping: Page Table
Page Table functionality:
  Incoming request is Virtual Address (VA), want Physical Address (PA)
  Physical Offset = Virtual Offset (page-aligned)
  So just swap Virtual Page Number (VPN) for Physical Page Number (PPN)
Implementation?
  Use VPN as index into PT
  Store PPN and management bits (Valid, Access Rights)
  Does NOT store actual data (the data sits in PM)
Page Offset
Virtual Page #
Physical Page #
Page Offset

## Slide 18: Page Table Layout
V | AR | PPN
X | XX | 
. . . |  | 
Virtual Address:
VPN
offset
Page Table
1) Index into PT using VPN
2) Check Valid and Access Rights bits
+
3) Combine PPN and offset
Physical
Address
4) Use PA to access memory

## Slide 19: Page Table Entry Format
Contains either PPN or indication not in main memory
Valid = Valid page table entry
  1  virtual page is in physical memory
  0  OS needs to fetch page from disk
Access Rights checked on every access to see if allowed (provides protection)
  Read Only: Can read, but not write page
  Read/Write: Read or write data on page
  Executable: Can fetch instructions from page

## Slide 20: Page Tables (1/2)
A page table (PT) contains the mapping of virtual addresses to physical addresses
Page tables located in main memory – Why?
  Too large to fit in registers (220 entries for 4 KiB pages)
  Faster to access than disk and can be shared by multiple processors
The OS maintains the PTs
  Each process has its own page table
    “State” of a process is PC, all registers, and PT
  OS stores address of the PT of the current process in the Page Table Base Register

## Slide 21: Page Tables (2/2)
Solves fragmentation problem: all pages are the same size, so can utilize all available slots
OS must reserve “swap space” on disk for each process
  Running programs requires hard drive space!
To grow a process, ask Operating System
  If unused pages in PM, OS uses them first
  If not, OS swaps some old pages (LRU) to disk

## Slide 22: Paging/Virtual Memory Multiple Processes
User B: Virtual Memory
¥
Code
Static
Heap
Stack
0
Code
Static
Heap
Stack
Page
Table A
Page
Table B
User A: Virtual Memory
¥
0
0
Physical
Memory
64 MB

## Slide 23: Review: Paging Terminology
Programs use virtual addresses (VAs)
  Space of all virtual addresses called virtual memory (VM)
  Divided into pages indexed by virtual page number (VPN)
Main memory indexed by physical addresses (PAs)
  Space of all physical addresses called physical memory (PM)
  Divided into pages indexed by physical page number (PPN)

## Slide 24
Question: How many bits wide are the following fields?
16 KiB pages
40-bit virtual addresses
64 GiB physical memory
26 26
☐
24 20
☐
22 22
☐
26 22
☐
VPN PPN

## Slide 25: Agenda
Virtual Memory
Page Tables
Administrivia
Translation Lookaside Buffer (TLB)
VM Performance
VM Wrap-up

## Slide 26: Administrivia (1/2)
Project 3 (individual) due Sunday 8/5
Final Review – Friday 8/3, 3-6pm in 306 Soda
Final – Thurs 8/9, 9am-12pm, 245 Li Ka Shing
  Focus on 2nd half material, though midterm material still fair game
  MIPS Green Sheet provided again
  Two-sided handwritten cheat sheet
    Can use the back side of your midterm cheat sheet!

## Slide 27: Administrivia (2/2)
http://www.geekosystem.com/engineering-professor-meme/2/

## Slide 28: Agenda
Virtual Memory
Page Tables
Administrivia
Translation Lookaside Buffer (TLB)
VM Performance
VM Wrap-up

## Slide 29: Retrieving Data from Memory
VA1
User 1 Virtual Address Space
User 2 Virtual Address Space
PT User 1
PT User 2
VA2
1) Access page table for address translation
Physical Memory
2) Access correct physical address
Requires two accesses of physical memory!

## Slide 30: Virtual Memory Problem
2 physical memory accesses per data access = SLOW!
Since locality in pages of data, there must be locality in the translations of those pages
Build a separate cache for the Page Table
  For historical reasons, cache is called a Translation Lookaside Buffer (TLB)
  Notice that what is stored in the TLB is NOT data, but the VPN  PPN mapping translations

## Slide 31: TLBs vs. Caches
TLBs usually small, typically 16 – 512 entries
TLB access time comparable to cache (« main memory)
TLBs can have associativity
  Usually fully/highly associative
D$ / I$
Memory Address
Data at memory address
Access next cache level / main memory
On miss:
TLB
VPN
PPN
Access Page Table in main memory
On miss:

## Slide 32: Where Are TLBs Located?
Which should we check first: Cache or TLB?
  Can cache hold requested data if corresponding page is not in physical memory?
  With TLB first, does cache receive VA or PA?
No
PA
Cache
VA
PA
miss
hit
data
hit
miss
CPU
Main Memory
TLB
Page Table
Notice that it is now the TLB that does translation, not the Page Table!

## Slide 33: Address Translation Using TLB
TLB Tag
TLB Index
Page Offset
TLB Tag | PPN
(used just like in a cache) | 
. . . | 
TLB
VPN
PPN
Page Offset
Tag
Index
Offset
Virtual Address
Physical Address
 | Tag | Block Data
. . . |  | 
Data Cache
PA split two different ways!
Note: TIO for VA & PA unrelated

## Slide 34: Typical TLB Entry Format
Valid and Access Rights: Same usage as previously discussed for page tables
Dirty: Basically always use write-back, so indicates whether or not to write page to disk when replaced
Ref: Used to implement LRU
  Set when page is accessed, cleared periodically by OS
  If Ref = 1, then page was referenced recently
TLB Tag: VPN mod (# TLB entries)
Valid | Dirty | Ref | Access Rights | TLB Tag | PPN
X | X | X | XX |  | 

## Slide 35
Question: How many bits wide are the following?
16 KiB pages
40-bit virtual addresses
64 GiB physical memory
2-way set associative TLB with 512 entries
12 14 38
☐
18 8 45
☐
14 12 40
☐
17 9 43
☐
TLB Tag TLB Index TLB Entry
Valid | Dirty | Ref | Access Rights | TLB Tag | PPN
X | X | X | XX |  | 

## Slide 36: Fetching Data on a Memory Read
Check TLB (input: VPN, output: PPN)
  TLB Hit: Fetch translation, return PPN
  TLB Miss: Check page table (in memory)
    Page Table Hit: Load page table entry into TLB
    Page Table Miss (Page Fault): Fetch page from disk to memory, update corresponding page table entry, then load entry into TLB
Check cache (input: PPN, output: data)
  Cache Hit: Return data value to processor
  Cache Miss: Fetch data value from memory, store it in cache, return it to processor

## Slide 37: Page Faults
Load the page off the disk into a free page of memory
  Switch to some other process while we wait
Interrupt thrown when page loaded and the process' page table is updated
  When we switch back to the task, the desired data will be in memory
If memory full, replace page (LRU), writing back if necessary, and update both page tables
  Continuous swapping between disk and memory called “thrashing”

## Slide 38: Performance Metrics
VM performance also uses Hit/Miss Rates and Miss Penalties
  TLB Miss Rate: Fraction of TLB accesses that result in a TLB Miss
  Page Table Miss Rate: Fraction of PT accesses that result in a page fault
Caching performance definitions remain the same
  Somewhat independent, as TLB will always pass PA to cache regardless of TLB hit or miss

## Slide 39: Data Fetch Scenarios
Are the following scenarios for a single data access possible?
  TLB Miss, Page Fault
  TLB Hit, Page Table Hit
  TLB Miss, Cache Hit
  Page Table Hit, Cache Miss
  Page Fault, Cache Hit
Yes
No
Yes
Yes
No

## Slide 40
Question: A program tries to load a word at X that causes a TLB miss but not a page fault. Are the following statements TRUE or FALSE?
The page table does not contain a valid mapping for the virtual page corresponding to the address X
The word that the program is trying to load is present in physical memory
F F
☐
F T
☐
T F
☐
T T
☐
1 2

## Slide 41: Updating Scenarios
Using V = valid, D = dirty, R = ref to mean that field is set to the shown value for any entry in either PT or TLB
Which of the following scenarios for a single data access are possible?
  Read, D = 1
  Write, R = 1
  Read, V = 0
  Write, D = 0
No
Yes
Yes
No

## Slide 42
Question: Assume the page table entry in question is present in the TLB and we are using a uniprocessor system. Are the following statements TRUE or FALSE?
The valid bit for that page must be the same in the PT and TLB
The dirty bit for that page must be the same in the PT and TLB
F F
☐
F T
☐
T F
☐
T T
☐
1 2

## Slide 43: Get To Know Your Staff
Category: Wishlist

## Slide 44: Agenda
Virtual Memory
Page Tables
Administrivia
Translation Lookaside Buffer (TLB)
VM Performance
VM Wrap-up

## Slide 45: VM Performance
Virtual Memory is the level of the memory hierarchy that sits below main memory
  TLB comes before cache, but affects transfer of data from disk to main memory
  Previously we assumed main memory was lowest level, now we just have to account for disk accesses
Same CPI, AMAT equations apply, but now treat main memory like a mid-level cache

## Slide 46: Typical Performance Stats
CPU
cache
primary
memory
secondary
memory
Caching Demand paging
  cache entry page frame
  cache block (≈32 bytes) page (≈4Ki bytes)
  cache miss rate (1% to 20%) page miss rate (<0.001%)
  cache hit (≈1 cycle) page hit (≈100 cycles)
  cache miss (≈100 cycles) page miss (≈5M cycles)
primary
memory
CPU

## Slide 47: Impact of Paging on AMAT (1/2)
Memory Parameters:
  L1 cache hit = 1 clock cycles, hit 95% of accesses
  L2 cache hit = 10 clock cycles, hit 60% of L1 misses
  DRAM = 200 clock cycles (≈100 nanoseconds)
  Disk = 20,000,000 clock cycles (≈10 milliseconds)
Average Memory Access Time (no paging):
  1 + 5%×10 + 5%×40%×200 = 5.5 clock cycles
Average Memory Access Time (with paging):
  5.5 (AMAT with no paging) + ?

## Slide 48: Impact of Paging on AMAT (2/2)
Average Memory Access Time (with paging) =
  5.5 + 5%×40%× (1-HRMem)×20,000,000
AMAT if HRMem = 99%?
  5.5 + 0.02×0.01×20,000,000 = 4005.5 (≈728x slower)
  1 in 20,000 memory accesses goes to disk: 10 sec program takes 2 hours!
AMAT if HRMem = 99.9%?
  5.5 + 0.02×0.001×20,000,000 = 405.5
AMAT if HRMem = 99.9999%
  5.5 + 0.02×0.000001×20,000,000 = 5.9

## Slide 49: Impact of TLBs on Performance
Each TLB miss to Page Table ~ L1 Cache miss
TLB Reach: Amount of virtual address space that can be simultaneously mapped by TLB:
  TLB typically has 128 entries of page size 4-8 KiB
  128 × 4 KiB = 512 KiB = just 0.5 MiB
What can you do to have better performance?
  Multi-level TLBs
  Variable page size (segments)
  Special situationally-used “superpages”
Conceptually same as multi-level caches
Not covered here

## Slide 50: Agenda
Virtual Memory
Page Tables
Administrivia
Translation Lookaside Buffer (TLB)
VM Performance
VM Wrap-up

## Slide 51: Virtual Memory Motivation
Memory as cache for disk (reduce disk accesses)
  Disk is so slow it significantly affects performance
  Paging maximizes memory usage with large, evenly-sized pages that can go anywhere
Allows processor to run multiple processes simultaneously
  Gives each process illusion of its own (large) VM
  Each process uses standard set of VAs
  Access rights provide protection

## Slide 52: Paging Summary
Paging requires address translation
  Can run programs larger than main memory
  Hides variable machine configurations (RAM/HD)
  Solves fragmentation problem
Address mappings stored in page tables in memory
  Additional memory access mitigated with TLB
  Check TLB, then Page Table (if necessary), then Cache

## Slide 53: Hardware/Software Support for Memory Protection
Different tasks can share parts of their virtual address spaces
  But need to protect against errant access
  Requires OS assistance
Hardware support for OS protection
  Privileged supervisor mode (a.k.a. kernel mode)
  Privileged instructions
  Page tables and other state information only accessible in supervisor mode
  System call exception (e.g. syscall in MIPS)

## Slide 54: Context Switching
How does a single processor run many programs at once?
Context switch: Changing of internal state of processor (switching between processes)
  Save register values (and PC) and change value in Page Table Base register
What happens to the TLB?
  Current entries are for different process
  Set all entries to invalid on context switch

## Slide 55: Virtual Memory Summary
User program view:
  Contiguous memory
  Start from some set VA
  “Infinitely” large
  Is the only running program
Reality:
  Non-contiguous memory
  Start wherever available memory is
  Finite size
  Many programs running simultaneously
Virtual memory provides:
  Illusion of contiguous memory
  All programs starting at same set address
  Illusion of ~ infinite memory (232 or 264 bytes)
  Protection , Sharing
Implementation:
  Divide memory into chunks (pages)
  OS controls page table that maps virtual into physical addresses
  memory as a cache for disk
  TLB is a cache for the page table