## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Course Summary & Review

## Slide 2: Agenda
Course Summary
Administrivia
What’s Next?
Acknowledgements

## Slide 3: Six Great Ideas in Computer Architecture
Layers of Representation/Interpretation
Moore’s Law
Principle of Locality/Memory Hierarchy
Parallelism
Performance Measurement & Improvement
Dependability via Redundancy

## Slide 4: Great Idea #1: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
Higher-Level Language Program (e.g. C)
Assembly Language Program (e.g. MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g. block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation

## Slide 5: Number Representation
Anything can be represented as a number!
  With n digits in base B, can represent Bn things
IEC (vs. SI) prefixes (210 ≈ 103)
Signed and unsigned integers
  Addition, subtraction, overflow, sign extension
  Two’s complement (better than 1’s and sign&mag)
Floating point (sign, biased exp, significand)
  Inf, NaN, 0, denorms
  Precision and truncation

## Slide 6: Higher-Level Language (HLL)
We studied C because exposes more of hardware (particularly memory)
  Compiled language is machine-dependent
Arrays and strings
  Don’t run off the end or forget null terminator
Pointers hold addresses, used to pass by ref
  Pointer arithmetic
  Array vs. pointer syntax
Structs are padded collections of variables

## Slide 7: Assembly Language
Close to the level that a machine understands
  ISA in human-readable format
  TAL vs. MAL (pseudo-instructions)
RISC vs. CISC and effects
MIPS Instruction Formats: R, I, J
  Meaning and limitations of the fields
  Relative (branch) vs. absolute (jump) addressing
  Register conventions (saved/volatile; caller/callee)
Assembler: instr translation, sym/rel tables

## Slide 8: Machine Language
Everything is just 0’s and 1’s!
  Usually done by assembler & linker, but can also do manually
  At this level, just raw bits! No differentiation between instructions and different types of data
  Alignment matters
Executable produced by linker, run by loader
  OS creates new process (PT, swap space)
  Instructions loaded and run by processor

## Slide 9: Hardware Architecture Description
Processor split into Datapath and Control
  Datapath components: I$/D$, RegFile, ALU, Extender, MUXes
    Datapath Stages: IF, ID, EX, MEM, WB
  Controller: Use “AND” and “OR” Logic blocks to determine control signal values for each instruction
Can build/design components hierarchically
Behavior of many circuits/programs can be represented using Finite State Machines
  States, transition function, initial state

## Slide 10: Logic Circuit Description
Build Synchronous Digital Systems out of combinational and sequential logic
Equivalence between Circuit Diagrams, Truth Tables, and Boolean Expressions
  Can convert between all representations
Boolean algebra allows for circuit simplification (Karnaugh maps, too)
FSMs built with registers and CL
In reality, everything wires and transistors
  Voltage-controlled switches (1: high, 0: low)

## Slide 11: Great Idea #2: Moore’s Law
Predicts: Transistor count
per chip doubles
every 2 years
Gordon Moore
Intel Cofounder B.S. Cal 1950
# of transistors on an integrated circuit (IC)
Year:

## Slide 12: Technology Trends
Dynamic power = C × V2 × f
  Capacitance, voltage, switching frequency
In WSC: Power Usage Effectiveness (PUE) = Total building power / IT equipment power
Technology growth is slowing, processors have hit a power wall
  Everywhere: transistor density, CPU speed, disk and memory capacity
  Performance improvements now coming from parallelism and multicore processors

## Slide 13: Transition to Multicore
Sequential App Performance

## Slide 14: Great Idea #3: Principle of Locality/ Memory Hierarchy
Trade-off in speed and cost vs. capacity!
Increasing distance from application/user

## Slide 15: Memory
Programmer treats as one long array
  You know that this is just an illusion (VM)!
Memory is byte-addressed
  Most data (including instructions) in words and word-aligned, so all word addresses are multiples of 4 (end in 0b00)
Multicore systems use shared memory
  Synchronization/cache coherence necessary

## Slide 16: Memory Management
Program’s address space contains four regions:
  Stack: local variables, grows downward
  Heap: space requested for pointers via malloc(); resizes dynamically, grows upward
  Static Data: global and static variables, does not grow or shrink
  Code: loaded when program starts, does not change size
code
static data
heap
stack
~ FFFF FFFFhex
~ 0hex

## Slide 17: Typical Memory Hierarchy
Take advantage of the principle of locality to present the user with as much memory as is available in the cheapest technology at the speed offered by the fastest technology
On-Chip Components
Second
Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk
or Flash)
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Cost/bit: highest lowest
Speed: ½’s 1’s 10’s 100’s 1,000,000’s
(cycles)
Size: 100’s 10K’s M’s G’s T’s
(bytes)
I TLB
D TLB

## Slide 18: Accessing Data
Check TLB/PT if page is in main memory
  Page fault to load from disk (swap space) if not
Check cache for data
  Fetch from main memory on cache miss
  Return data to processor
Cache
VA
PA
miss
hit
data
hit
miss
CPU
Main Memory
TLB
Page Table

## Slide 19: Caching Details (1/2)
Move data in contiguous blocks
  Store data in cache, closer to processor
Cache organization
  Map data addresses to the limited number of block locations in cache
  Set associativity: # of slots per set
TIO breakdown
  Tag as block identifier, Index to find set in cache, Offset to find data within block
Also store management bits for each block
  Valid bit, (Dirty bit), Tag bits

## Slide 20: Caching Details (2/2)
Cache parameters affect performance
  Block size, cache size, set associativity
  Write-back/write-through policies
  Write allocate/no-write allocate policies
  Block replacement policy (Least Recently Used)
Source of cache misses: The 3 C’s
  Compulsory, capacity, conflict
Multilevel caches reduce miss penalty

## Slide 21: Virtual Memory Details (1/3)
Give main memory effective size of disk without major penalty to performance
  Move data in contiguous pages from disk to main memory
  Assumption is that memory is small compared to both disk and virtual address space (or many processes)
Also provide protection for multiple processes
  Requires a lot of work by operating system

## Slide 22: Virtual Memory Details (2/3)
Paging requires address translation
  Can run programs larger than main memory
  Hides variable machine configurations (RAM/HDD)
  Solves fragmentation problem
Address mappings stored in page tables in memory
  Additional memory access mitigated with TLB, which is a cache for page table
  Management bits: Valid, Dirty, Ref, Access Rights

## Slide 23: Virtual Memory Details (3/3)
Running multiple processes:
  Each process has its own page table and swap space in disk
  OS can switch between by saving and loading process states (PC, reg vals, page table address)
  On context switch, flush TLB and pipeline

## Slide 24: Input/Output
Disk Latency = Seek Time + Rotation Time + Transfer Time + Controller Overhead
Processor must synchronize with I/O devices before use due to difference in data rates:
  Polling works, but expensive due to repeated queries
  Exceptions are “unexpected” events in processor
  Interrupts are asynchronous events that are often used for interacting with I/O devices
In SW, need special handling code

## Slide 25: Great Idea #4: Parallelism
Smart Phone
Warehouse Scale Computer
Leverage Parallelism &
Achieve High Performance
Core
…
Memory
Input/Output
Computer
Core
Parallel Requests
  Assigned to computer
  e.g. search “Katz”
Parallel Threads
  Assigned to core
  e.g. lookup, ads
Parallel Instructions
  > 1 instruction @ one time
  e.g. 5 pipelined instructions
Parallel Data
  > 1 data item @ one time
  e.g. add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Software Hardware
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A0+B0
A1+B1
A2+B2
A3+B3
Logic Gates

## Slide 26: Types of Parallelism (1/4)
Request-Level Parallelism (RLP)
  Handling many requests per second (e.g. web search)
Data-Level Parallelism (DLP)
  Operate on many pieces of data at once
  SIMD: at the level of single instructions
  MapReduce: at the level of programs (split into map and reduce)

## Slide 27: Types of Parallelism (2/4)
Thread-Level Parallelism (TLP)
  Have many processors, run either different programs or different parts of same program at same time
  If same program, need to deal with shared memory (cache coherence and synchronization primitives to prevent data races)
  Splitting up work properly is difficult!
    Shared vs. private variables in OpenMP
    Often requires re-designing your algorithm

## Slide 28: Types of Parallelism (3/4)
Thread-Level Parallelism (TLP)
  Synchronization requires hardware support
    Test-and-set mechanism
    ll and sc in MIPS
  OpenMP directives
    parallel, for, sections, single, etc.
    critical, atomic, master

## Slide 29: Types of Parallelism (4/4)
Instruction Level Parallelism (ILP)
  Pipelining: increase throughput by adding registers
    Reduce critical path, increase max frequency
    Working on multiple instructions at once introduces hazards (structural, data, control)
    Forwarding, delay slots, code reordering
  Multiple instruction issue (superscalar)
    Register renaming, speculation, out-of-order execution
    Loop unrolling

## Slide 30: Great Idea #5: Performance Measurement and Improvement
Allows direct comparisons of architectures and quantification of improvements
  It is all about time to finish (latency)
  Includes both setup and execution.
Match application and hardware to exploit:
  Locality
  Parallelism
  Special hardware features, like specialized instructions (e.g. matrix manipulation)

## Slide 31: Performance Measurements
Execution time (latency) and work per time (throughput)
  CPU Time = Instructions × CPI × Clock Cycle Time
Memory Access:
  AMAT, CPIstall use hit time, miss rate, miss penalty
  Definitions recursive back to last level in hierarchy
Amdahl’s Law
  Speedup = 1 / [ (1-F) + F/S ]
  Why we almost never get max possible speedup

## Slide 32: Performance Programming
Key challenge: Craft parallel programs that that scale well (weak/strong scaling)
  Scheduling, load balancing, time for synchronization, overhead for communication
Some techniques:
  Register/Cache Blocking
  Data Parallelism & Loop Unrolling
  Multithreading

## Slide 33: Dependability Measures
Failure rates and time
  MTTF, MTTR, MTBF
Availability = MTTF / (MTTF + MTTR)
  Use measures in # of 9s

## Slide 34: Great Idea #6: Dependability via Redundancy
Redundancy so that a failing piece doesn’t make the whole system fail
Applies to everything from datacenters to storage to memory
  Redundant datacenters so that can lose 1 datacenter but Internet service stays online
  Redundant disks so that can lose 1 disk but not lose data (Redundant Arrays of Independent Disks/RAID)
  Redundant memory bits of so that can lose 1 bit but no data (Error Correcting Code/ECC Memory)

## Slide 35: Redundant Arrays of Inexpensive Disks
Possible to simulate behavior of single larger disk with an array of smaller disks
  Cheaper, higher bandwidth, more resistant to failure
RAID 0 – No redundancy
RAID 1 – Mirroring for redundancy
RAID 2 – Bit-level striping
RAID 3 – Parity disks
RAID 4 – Block-level striping with parity disk
RAID 5 – Striped parity

## Slide 36: Error Detection & Correction
Even parity using XOR
Hamming Distance
  Distance 2 can detect 1-bit error
  Distance 3 can correct 1-bit error
  Distance 4 can correct 1-bit error and detect 2-bit error
Hamming ECC
  Introduce extra parity bits (one per group)
  Sum of group errors indicates corrupted bit

## Slide 37: Agenda
Course Summary
Administrivia
What’s Next?
Acknowledgements

## Slide 38: Administrivia
Last discussion today
Lectures: Old finals problems & “Biological Computing”
Final Exam (Thu) @ 9am-12pm, 245 Li Ka Shing
  Two-sided handwritten cheat sheet
  Green sheet provided
Extra OH: Justin MW 12-1pm, 411 Soda

## Slide 39: Project 2: sgemm-small.c

## Slide 40: Project 2: sgemm-small.c

## Slide 41: Project 2: sgemm-openmp.c

## Slide 42: Project 2 Fastest Submissions
sgemm-small (small):
  12.4 Gflop/s Harkiran Bolaria, Andrew Cai
  11.0 Gflop/s Yun Jae Cho, Duc Nguyen
  10.4 Gflop/s Shawn Park, Tananun Songdechakraiwut
sgemm-small (36×36):
  16.4 Gflop/s Luis De Pombo, Steven Roger
  16.4 Gflop/s Bryan Cote, Myron Chen
  16.1 Gflop/s Chris Buonocore, Ali Jishi

## Slide 43: Project 2 Fastest Submissions
sgemm-openmp:
  77.2 Gflop/s Chris Buonocore, Ali Jishi
  73.0 Gflop/s Shawn Park, Tananun Songdechakraiwut
  72.8 Gflop/s Moshe Leon, Ashkon Soroudi

## Slide 44: Agenda
Course Summary
Administrivia
What’s Next?
Acknowledgements

## Slide 45: What’s Next?
Take classes from great teachers! (teacher > class)
  Distinguished Teaching Award (very hard to get)
  HKN Course evaluations (≥ 6 is very good)
  Upcoming instructors for classes: (CS / EE)
Classes related to CS 61C
  CS169 Software Engineering (for SaaS, Fox/Patterson Fall 12)
  CS194-15 Engineering Parallel Software
  CS164 Programming Languages and Compilers
  CS162 Operating Systems and Systems Programming
  CS152 Computer Architecture and Engineering (Sp13)
  CS150 Components and Design Techniques for Digital Systems

## Slide 46: Opportunities in Teaching
Interest in joining the CS staff?
  Applies for CS 10, 61A, 61B, 61C
  Usual path: Lab Assistant  Reader  TA
  Also: Self-Paced Center Tutor
Requirements:
  Interest in teaching
  Stricter grade requirements based on where you want to jump in
Applying:
  Application form (for TA, Reader, or Lab Assistant)
  Doesn’t hurt to e-mail professor as well

## Slide 47: Opportunities at Cal
Why are we a top university in the WORLD?
  Research, research, research!
  Classes are just the tip of the iceberg
  Whether you want to go to grad school or industry, you need someone to vouch for you
  Won’t know if you like it or not until you try
Find out what you like, do lots of web research (read published papers), hit OH of professor, show enthusiasm & initiative

## Slide 48: Agenda
Course Summary
Administrivia
What’s Next?
Acknowledgements

## Slide 49: Special Thanks
Professor David Patterson
Professor Randy Katz
Lecturer SOE Dan Garcia
Su11 Instructor
Michael Greenbaum

## Slide 50: Special Thanks to the Staff:
TAs: Brandon Lee Paul Ruan Raphael Townshend Sung Roa Yoon
Readers: Allen Xiao Jamie Li Linda Cai Roger Gong
Lab Assistants: Crystal Dou Hoang Nguyen Inderjit Jutla Oscar Bachtiar