## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
OpenMP, Transistors

## Slide 2: Review of Last Lecture
Amdahl’s Law limits benefits of parallelization
Multiprocessor systems uses shared memory (single address space)
Cache coherence implements shared memory even with multiple copies in multiple caches
  Track state of blocks relative to other caches (e.g. MOESI protocol)
  False sharing a concern
Synchronization via hardware primitives:
  MIPS does it with Load Linked + Store Conditional

## Slide 3
Question: Consider the following code when executed concurrently by two threads.
What possible values can result in *($s0)?
# *($s0) = 100
lw $t0,0($s0)
addi $t0,$t0,1
sw $t0,0($s0)
101 or 102
(A)
100, 101, or 102
(B)
100 or 101
(C)
102
(D)
Notes: - 102 if one thread starts executing after the other completely finishes.
- 101 if both threads execute the lw before either thread executes the sw. One thread will see “stale data”.

## Slide 4: Great Idea #4: Parallelism
Smart Phone
Warehouse Scale Computer
Leverage Parallelism &
Achieve High Performance
Core
…
Memory
Input/Output
Computer
Core
Parallel Requests
  Assigned to computer
  e.g. search “Garcia”
Parallel Threads
  Assigned to core
  e.g. lookup, ads
Parallel Instructions
  > 1 instruction @ one time
  e.g. 5 pipelined instructions
Parallel Data
  > 1 data item @ one time
  e.g. add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Software Hardware
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A0+B0
A1+B1
A2+B2
A3+B3
Logic Gates

## Slide 5: Agenda
OpenMP Introduction
Administrivia
OpenMP Directives
  Workshare
  Synchronization
OpenMP Common Pitfalls
Hardware: Transistors
Bonus: sections Example

## Slide 6: What is OpenMP?
API used for multi-threaded, shared memory parallelism
  Compiler Directives
  Runtime Library Routines
  Environment Variables
Portable
Standardized
Resources: http://www.openmp.org/ and http://computing.llnl.gov/tutorials/openMP/
Notes: API: Application Programming Interface

## Slide 7: OpenMP Specification

## Slide 8: Shared Memory Model with Explicit Thread-based Parallelism
Multiple threads in a shared memory environment, explicit programming model with full programmer control over parallelization
Pros:
  Takes advantage of shared memory, programmer need not worry (that much) about data placement
  Compiler directives are simple and easy to use
  Legacy serial code does not need to be rewritten
Cons:
  Code can only be run in shared memory environments
  Compiler must support OpenMP (e.g. gcc 4.2)

## Slide 9: OpenMP in CS61C
OpenMP is built on top of C, so you don’t have to learn a whole new programming language
  Make sure to add #include <omp.h>
  Compile with flag: gcc -fopenmp
  Mostly just a few lines of code to learn
You will NOT become experts at OpenMP
  Use slides as reference, will learn to use in lab
Key ideas:
  Shared vs. Private variables
  OpenMP directives for parallelization, work sharing, synchronization

## Slide 10: OpenMP Programming Model
Fork - Join Model:
OpenMP programs begin as single process (master thread) and executes sequentially until the first parallel region construct is encountered
  FORK: Master thread then creates a team of parallel threads
  Statements in program that are enclosed by the parallel region construct are executed in parallel among the various threads
  JOIN: When the team threads complete the statements in the parallel region construct, they synchronize and terminate, leaving only the master thread

## Slide 11: OpenMP Extends C with Pragmas
Pragmas are a preprocessor mechanism C provides for language extensions
Commonly implemented pragmas: structure packing, symbol aliasing, floating point exception modes (not covered in 61C)
Good mechanism for OpenMP because compilers that don't recognize a pragma are supposed to ignore them
  Runs on sequential computer even with embedded pragmas

## Slide 12: parallel Pragma and Scope
Basic OpenMP construct for parallelization:
#pragma omp parallel
{
/* code goes here */
}
  Each thread runs a copy of code within the block
  Thread scheduling is non-deterministic
Variables declared outside pragma are shared
  To make private, need to declare with pragma:
#pragma omp parallel private (x)
This is annoying, but curly brace MUST go on separate line from #pragma

## Slide 13: Thread Creation
Defined by OMP_NUM_THREADS environment variable (or code procedure call)
  Set this variable to the maximum number of threads you want OpenMP to use
Usually equals the number of cores in the underlying hardware on which the program is run
  But remember thread ≠ core

## Slide 14: OMP_NUM_THREADS
OpenMP intrinsic to set number of threads:
omp_set_num_threads(x);
OpenMP intrinsic to get number of threads:
num_th = omp_get_num_threads();
OpenMP intrinsic to get Thread ID number:
th_ID = omp_get_thread_num();

## Slide 15: Parallel Hello World
#include <stdio.h>
#include <omp.h>
int main () {
int nthreads, tid;
/* Fork team of threads with private var tid */
#pragma omp parallel private(tid)
{
tid = omp_get_thread_num(); /* get thread id */
printf("Hello World from thread = %d\n", tid);
/* Only master thread does this */
if (tid == 0) {
nthreads = omp_get_num_threads();
printf("Number of threads = %d\n", nthreads);
}
} /* All threads join master and terminate */
}

## Slide 16: Agenda
OpenMP Introduction
Administrivia
OpenMP Directives
  Workshare
  Synchronization
OpenMP Common Pitfalls
Hardware: Transistors
Bonus: sections Example

## Slide 17: Midterm Scores

## Slide 18: Administrivia
Midterm re-grade requests due Thursday
Project 2: Matrix Multiply Performance Improvement
  Work in groups of two!
  Part 1: Due July 28 (this Sunday)
  Part 2: Due August 4
HW 5 also due July 31

## Slide 19: Agenda
OpenMP Introduction
Administrivia
OpenMP Directives
  Workshare
  Synchronization
OpenMP Common Pitfalls
Hardware: Transistors
Bonus: sections Example

## Slide 20: OpenMP Directives (Work-Sharing)
Shares iterations of a loop across the threads
Each section is executed by a separate thread
Serializes the execution of a thread
These are defined within a parallel section
Notes: A work-sharing construct divides the execution of the enclosed code region among the members of the team that encounter it.

## Slide 21: Parallel Statement Shorthand
#pragma omp parallel
{
#pragma omp for
for(i=0;i<len;i++) { … }
}
can be shortened to:
#pragma omp parallel for
for(i=0;i<len;i++) { … }
This is the only directive in the parallel section

## Slide 22: Building Block: for loop
for (i=0; i<max; i++) zero[i] = 0;
Break for loop into chunks, and allocate each to a separate thread
  e.g. if max = 100 with 2 threads: assign 0-49 to thread 0, and 50-99 to thread 1
Must have relatively simple “shape” for an OpenMP-aware compiler to be able to parallelize it
  Necessary for the run-time system to be able to determine how many of the loop iterations to assign to each thread
No premature exits from the loop allowed
  i.e. No break, return, exit, goto statements
In general, don’t jump outside of any pragma block
Notes: “Shape” restrictions: The FOR loop cannot be a DO WHILE loop, or a loop without loop control. Also, the loop iteration variable must be an integer and the loop control parameters must be the same for all threads.

## Slide 23: Parallel for pragma
#pragma omp parallel for
for (i=0; i<max; i++) zero[i] = 0;
Master thread creates additional threads, each with a separate execution context
  Implicit synchronization at end of for loop
Loop index variable (i.e. i) made private
Divide index regions sequentially per thread
  Thread 0 gets 0, 1, …, (max/n)-1;
  Thread 1 gets max/n, max/n+1, …, 2*(max/n)-1

## Slide 24: OpenMP Timing
Elapsed wall clock time:
double omp_get_wtime(void);
  Returns elapsed wall clock time in seconds
  Time is measured per thread, no guarantee can be made that two distinct threads measure the same time
  Time is measured from “some time in the past,” so subtract results of two calls to omp_get_wtime to get elapsed time

## Slide 25: Matrix Multiply in OpenMP
start_time = omp_get_wtime();
#pragma omp parallel for private(tmp, i, j, k)
for (i=0; i<Mdim; i++){
for (j=0; j<Ndim; j++){
tmp = 0.0;
for( k=0; k<Pdim; k++){
/* C(i,j) = sum(over k) A(i,k) * B(k,j)*/
tmp += *(A+(i*Pdim+k)) * *(B+(k*Ndim+j));
}
*(C+(i*Ndim+j)) = tmp;
}
}
run_time = omp_get_wtime() - start_time;
Outer loop spread across N threads; inner loops inside a single thread

## Slide 26: Notes on Matrix Multiply Example
More performance optimizations available:
  Higher compiler optimization (-O2, -O3) to reduce number of instructions executed
  Cache blocking to improve memory performance
  Using SIMD SSE instructions to raise floating point computation rate (DLP)
  Improve algorithm by reducing computations and memory accesses in code (what happens in each loop?)

## Slide 27: OpenMP Directives (Synchronization)
These are defined within a parallel section
master
  Code block executed only by the master thread (all other threads skip)
critical
  Code block executed by only one thread at a time
atomic
  Specific memory location must be updated atomically (like a mini-critical section for writing to memory)
  Applies to single statement, not code block

## Slide 28: OpenMP Reduction
Reduction specifies that one or more private variables are the subject of a reduction operation at end of parallel region
  Clause reduction(operation:var)
  Operation: Operator to perform on the variables at the end of the parallel region
  Var: One or more variables on which to perform scalar reduction
#pragma omp for reduction(+:nSum)
for (i = START ; i <= END ; i++)
nSum += i;

## Slide 29: Agenda
OpenMP Introduction
Administrivia
OpenMP Directives
  Workshare
  Synchronization
OpenMP Common Pitfalls
Hardware: Transistors
Bonus: sections Example

## Slide 30: OpenMP Pitfall #1: Data Dependencies
Consider the following code:
  a[0] = 1;
  for(i=1; i<5000; i++)
  a[i] = i + a[i-1];
There are dependencies between loop iterations!
  Splitting this loop between threads does not guarantee in-order execution
  Out of order loop execution will result in undefined behavior (i.e. likely wrong result)

## Slide 31: Open MP Pitfall #2: Sharing Issues
Consider the following loop:
#pragma omp parallel for
for(i=0; i<n; i++){
temp = 2.0*a[i];
a[i] = temp;
b[i] = c[i]/temp;
}
temp is a shared variable!
#pragma omp parallel for private(temp)
for(i=0; i<n; i++){
temp = 2.0*a[i];
a[i] = temp;
b[i] = c[i]/temp;
}

## Slide 32: OpenMP Pitfall #3: Updating Shared Variables Simultaneously
Now consider a global sum:
#pragma omp parallel for
for(i=0; i<n; i++)
sum = sum + a[i];
This can be done by surrounding the summation by a critical/atomic section or reduction clause:
#pragma omp parallel for reduction(+:sum)
for(i=0; i<n; i++)
sum = sum + a[i];
  Compiler can generate highly efficient code for reduction

## Slide 33: OpenMP Pitfall #4: Parallel Overhead
Spawning and releasing threads results in significant overhead
Better to have fewer but larger parallel regions
  Parallelize over the largest loop that you can (even though it will involve more work to declare all of the private variables and eliminate dependencies)

## Slide 34: OpenMP Pitfall #4: Parallel Overhead
start_time = omp_get_wtime();
for (i=0; i<Mdim; i++){
for (j=0; j<Ndim; j++){
tmp = 0.0;
#pragma omp parallel for reduction(+:tmp)
for( k=0; k<Pdim; k++){
/* C(i,j) = sum(over k) A(i,k) * B(k,j)*/
tmp += *(A+(i*Pdim+k)) * *(B+(k*Ndim+j));
}
*(C+(i*Ndim+j)) = tmp;
}
}
run_time = omp_get_wtime() - start_time;
Too much overhead in thread generation to have this statement run this frequently.
Poor choice of loop to parallelize.
Notes: Row major

## Slide 35: Get To Know Your Staff
Category: Television

## Slide 36: Agenda
OpenMP Introduction
Administrivia
OpenMP Directives
  Workshare
  Synchronization
OpenMP Common Pitfalls
Hardware: Transistors
Bonus: sections Example

## Slide 37: Great Idea #1: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
Higher-Level Language Program (e.g. C)
Assembly Language Program (e.g. MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g. block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
We are here

## Slide 38: Hardware Design
Upcoming: We’ll study how a modern processor is built, starting with basic elements as building blocks
Why study hardware design?
  Understand capabilities and limitations of hardware in general and processors in particular
  What processors can do fast and what they can’t do fast (avoid slow things if you want your code to run fast!)
  Background for more in-depth courses (CS150, CS152)
  You may need to design own custom hardware for extra performance (some commercial processors today have customizable hardware)

## Slide 39: Design Hierarchy
system
datapath
control
state registers
combinational logic
multiplexer
comparator
code registers
register
logic
switching networks
Later this
week
Next
week
Today

## Slide 40: Switches (1/2)
The basic element of physical implementations
Convention: if input is a “1,” the switch is asserted
In this example, Z  A.
Z
A
A
Z
Close switch if A is “1” (asserted) and turn ON light bulb (Z)
Open switch if A is “0” (unasserted)
and turn OFF light bulb (Z)

## Slide 41: Switches (2/2)
Can compose switches into more complex ones (Boolean functions)
  Arrows show action upon assertion (1 = close)
AND:
A
B
Z  A and B
“1”
OR:
A
B
Z  A or B
“1”

## Slide 42: Transistor Networks
Modern digital systems designed in CMOS
  MOS: Metal-Oxide on Semiconductor
  C for complementary: use pairs of normally-open and normally-closed switches
CMOS transistors act as voltage-controlled switches
  Similar, though easier to work with, than relay switches from earlier era
  Three terminals: Source, Gate, and Drain
G
D
S

## Slide 43: CMOS Transistors
Switch action based on terminal voltages (VG, VD, VS) and relative voltages (e.g. VGS, VDS)
  Threshold voltage (VT) determines whether or not Source and Drain terminals are connected
  When not connected, Drain left “floating”
N-channel Transistor
VG–VS < VT: Switch OPEN
VGS–VDS > VT: Switch CLOSED
P-channel Transistor
VS–VG < -VT: Switch CLOSED
VSG–VSD > -VT: Switch OPEN
Gate
Source
Drain
Gate
Source
Drain
Circle symbol means “NOT” or “complement”
Notes: From wikipedia:
The field-effect transistor (FET) relies on an electric field to control the shape and hence the conductivity of a channel of one type of charge carrier in a semiconductor material.
The most commonly used FET is the MOSFET. The CMOS (complementary-symmetry metal oxide semiconductor) process technology is the basis for modern digital integrated circuits. This process technology uses an arrangement where the (usually "enhancement-mode") p-channel MOSFET and n-channel MOSFET are connected in series such that when one is on, the other is off.

## Slide 44: MOS Networks
What is the relationship between X and Y?
Called an inverter or NOT gate
3v
X
Y
0v
-3 V
+3 V
+3 V
+0 V
X
Y
Voltage Source (“1”)
Ground (“0”)

## Slide 45: Two Input Networks
X
Y
Z
-3 V
+3 V
-3 V
+3 V
-3 V
-3 V
+3 V
+3 V
0v
3v
X
Y
Z
3v
X
Y
0v
Z
X
Y
Z
-3 V
+3 V
-3 V
+3 V
-3 V
-3 V
+3 V
+3 V
+3 V
+3 V
+3 V
+0 V
+3 V
+0 V
+0 V
+0 V
NAND gate (NOT AND)
NOR gate (NOT OR)
Notes: Bottom
X = 0v Y = 0V both closed on top in series, so Z = 3v
X = 0v Y = 0V both open bottom
X = 0v Y = 3V 1st open on top,
X = 0v Y = 3V 2nd in series closed, so Z = 0v
X = 3v Y = 0V 2nd open on top
X = 3v Y = 0V 2nd in series closed, so Z = 0v
X = 3v Y = 3V both open on top
X = 3v Y = 3V both closed, so Z = 0v

## Slide 46: Transistors and CS61C
The internals of transistors are important, but won’t be covered in this class
  Better understand Moore’s Law
  Physical limitations relating to speed and power consumption
  Actual physical design & implementation process
  Can take EE40, EE105, and EE140
We will proceed with the abstraction of Digital Logic (0/1)

## Slide 47: Block Diagrams
In reality, chips composed of just transistors and wires
  Small groups of transistors form useful building blocks, which we show as blocks
Can combine to build higher-level blocks
  You can build AND, OR, and NOT out of NAND!
0v
3v
X
Y
Z
≡
NAND
X
Y
Z

## Slide 48
Question: Which set(s) of inputs will result in the output Z being 3 volts?
Using digital logic – “0” is -3 V, “1” is +3 V
0 0
(A)
0 1
(B)
1 0
(C)
1 1
(D)
X Y
0v
3v
X
Y
Z

## Slide 49: Summary
OpenMP as simple parallel extension to C
  During parallel fork, be aware of which variables should be shared vs. private among threads
  Work-sharing accomplished with for/sections
  Synchronization accomplished with critical/atomic/reduction
Hardware is made up of transistors and wires
  Transistors are voltage-controlled switches
  Building blocks of all higher-level blocks

## Slide 50
You are responsible for the material contained on the following slides, though we may not have enough time to get to them in lecture.
They have been prepared in a way that should be easily readable and the material will be touched upon in the following lecture.
BONUS SLIDES

## Slide 51: Agenda
OpenMP Introduction
Administrivia
OpenMP Directives
  Workshare
  Synchronization
OpenMP Common Pitfalls
Hardware: Transistors
Bonus: sections Example

## Slide 52: Workshare sections Example (1/4)
#include <omp.h>
#include <stdio.h>
#include <stdlib.h>
#define N 50
int main (int argc, char *argv[]) {
int i, nthreads, tid;
float a[N], b[N], c[N], d[N];
/* Initialize arrays with some data */
for (i=0; i<N; i++) {
a[i] = i * 1.5;
b[i] = i + 22.35;
c[i] = d[i] = 0.0;
}
/* main() continued on next slides... */

## Slide 53: Workshare sections Example (2/4)
#pragma omp parallel private(i,tid) {
tid = omp_get_thread_num();
if (tid == 0) {
nthreads = omp_get_num_threads();
printf("Number of threads = %d\n", nthreads);
}
printf("Thread %d starting...\n",tid);
#pragma omp sections nowait {
#pragma omp section {
printf("Thread %d doing section 1\n",tid);
for (i=0; i<N; i++){
c[i] = a[i] + b[i];
printf("Thread %d: c[%d]= %f\n",tid,i,c[i]);
}
}
Declare Sections
Define individual sections

## Slide 54: Workshare sections Example (3/4)
#pragma omp section {
printf("Thread %d doing section 2\n",tid);
for (i=0; i<N; i++){
d[i] = a[i] * b[i];
printf("Thread %d: d[%d]= %f\n",tid,i,d[i]);
}
}
} /* end of sections */
printf("Thread %d done.\n",tid);
} /* end of parallel section */
} /* end of main */
2nd section

## Slide 55: Workshare sections Example (4/4)
Number of threads = 2
Thread 1 starting...
Thread 0 starting...
Thread 1 doing section 1
Thread 0 doing section 2
Thread 1: c[0]= 22.350000
Thread 0: d[0]= 0.000000
Thread 1: c[1]= 24.850000
Thread 0: d[1]= 35.025002
Thread 1: c[2]= 27.350000
Thread 0: d[2]= 73.050003
Thread 1: c[3]= 29.850000
Thread 0: d[3]= 114.075005
Thread 1: c[4]= 32.349998
Thread 0: d[4]= 158.100006
Thread 1: c[5]= 34.849998
Thread 0: d[5]= 205.125000
Thread 1: c[6]= 37.349998
Thread 0: d[6]= 255.150009
Thread 1: c[7]= 39.849998
Thread 0: d[7]= 308.175018
Thread 0: d[8]= 364.200012
Thread 0: d[9]= 423.225006
Thread 0: d[10]= 485.249969
Thread 0: d[11]= 550.274963
Thread 0: d[12]= 618.299988
Thread 0: d[13]= 689.324951
Thread 0: d[14]= 763.349976
Thread 0: d[15]= 840.374939
. . .
Thread 1: c[33]= 104.849998
Thread 0: d[41]= 3896.024902
Thread 1: c[34]= 107.349998
Thread 0: d[42]= 4054.049805
Thread 1: c[35]= 109.849998
Thread 0: d[43]= 4215.074707
Thread 1: c[36]= 112.349998
Thread 0: d[44]= 4379.100098
Thread 1: c[37]= 114.849998
Thread 1: c[38]= 117.349998
Thread 1: c[39]= 119.849998
Thread 1: c[40]= 122.349998
Thread 1: c[41]= 124.849998
Thread 1: c[42]= 127.349998
Thread 1: c[43]= 129.850006
Thread 1: c[44]= 132.350006
Thread 0: d[45]= 4546.125000
Thread 1: c[45]= 134.850006
Thread 0: d[46]= 4716.149902
Thread 1: c[46]= 137.350006
Thread 0: d[47]= 4889.174805
Thread 1: c[47]= 139.850006
Thread 0: d[48]= 5065.199707
Thread 0: d[49]= 5244.225098
Thread 0 done.
Thread 1: c[48]= 142.350006
Thread 1: c[49]= 144.850006
Thread 1 done.
nowait option in sections allows threads to exit “early”
Notice inconsistent thread scheduling!