## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Functional Units,
Finite State Machines

## Slide 2: Review of Last Lecture
Synchronous Digital Systems
  Pulse of a Clock controls flow of information
  All signals are seen as either 0 or 1
Hardware systems are constructed from Stateless Combinational Logic and Stateful “Memory” Logic (registers)
Combinational Logic: equivalent circuit diagrams, truth tables, and Boolean expressions
  Boolean Algebra allows minimization of gates
State registers implemented from Flip-flops

## Slide 3: Dealing with Waveform Diagrams
Easiest to start with CLK on top
  Solve signal by signal, from inputs to outputs
  Can only draw the waveform for a signal if all of its input waveforms are drawn
When does a signal update?
  A state element updates based on CLK triggers
  A combinational element updates ANY time ANY of its inputs changes

## Slide 4
Example: T = 10 ns. tsetup = thold = 0. tclk-to-q = 1 ns. tprop = 1 ns for all gates. Each “tick” below is 1 ns. Solve for the waveform of the output Y.

## Slide 5: Hardware Design Hierarchy
system
datapath
control
state registers
combinational logic
multiplexer
comparator
code registers
register
logic
switching networks
Today

## Slide 6: Agenda
State Elements Continued
Administrivia
Logisim Introduction
Finite State Machines
Multiplexers
ALU Design
  Adder/Subtracter

## Slide 7: Model for Synchronous Systems
Collection of Combinational Logic blocks separated by registers
  Feedback is optional depending on application
Clock (CLK): square wave that synchronizes the system
  Clock signal connects only to clock input of registers
Register: several bits of state that samples input on rising edge of CLK

## Slide 8: Accumulator Revisited ...Again
reset signal shown
In practice X might not arrive to the adder at the same time as Si-1
Si temporarily is wrong, but register always captures correct value
In good circuits, instability never happens around rising edge of clk

## Slide 9: Register Timing Terms (Review)
Setup Time: how long the input must be stable before the CLK trigger for proper input read
Hold Time: how long the input must be stable after the CLK trigger for proper input read
“CLK-to-Q” Delay: how long it takes the output to change, measured from the CLK trigger

## Slide 10: Where Does Timing Come From?
Example D flip-flop implementation:
Changing the D signal around the time E (CLK) changes can cause unexpected behavior

## Slide 11: Maximum Clock Frequency
What is the max frequency of this circuit?
  Limited by how much time needed to get correct Next State to Register
Max Delay =
Max Freq = 1/Max Delay
Setup Time
+ CLK-to-Q Delay
+ CL Delay
Notes: Hold time is included in CLK-to-Q delay.

## Slide 12: The Critical Path
+
Reg
Reg
The critical path is the longest delay between any two registers in a circuit
The clock period must be longer than this critical path, or the signal will not propagate properly to that next register
1
2
3
4
Critical Path =
CL Delay 1
+ CL Delay 2
+ CL Delay 3
+ Adder Delay

## Slide 13: Pipelining and Clock Frequency (1/2)
Clock period limited by propagation delay of adder and shifter
  Add an extra register to reduce the critical path!
Timing:

## Slide 14: Pipelining and Clock Frequency (2/2)
Extra register allows higher clock freq (more outputs per sec)
However, takes two (shorter) clock cycles to produce first output (higher latency for initial output)
+ setup time
+ CLK-to-Q delay
+ CLK-to-Q delay
+ Adder delay
+ Shifter delay
+ setup time
+ CLK-to-Q delay

## Slide 15: Pipelining Basics
By adding more registers, break path into shorter “stages”
  Aim is to reduce critical path
  Signals take an additional clock cycle to propagate through each stage
New critical path must be calculated
  Affected by placement of new pipelining registers
  Faster clock rate  higher throughput (outputs)
  More stages  higher startup latency
Pipelining tends to improve performance
  More on this (application to CPUs) next week

## Slide 16
Question: Want to run on 1 GHz processor. tadd = 100 ps. tmult = 200 ps. tsetup = thold = 50 ps. What is the maximum tclk-to-q we can use?
550 ps
(A)
750 ps
(B)
500 ps
(C)
700 ps
(D)

## Slide 17: Agenda
State Elements Continued
Administrivia
Logisim Introduction
Finite State Machines
Multiplexers
ALU Design
  Adder/Subtracter

## Slide 18: Administrivia
Midterm re-grade requests due today
  We will re-grade the entire test
Project 2 Part 2 will be posted today
HW5 posted today, due Thu Aug. 1

## Slide 19: Agenda
State Elements Continued
Administrivia
Logisim Introduction
Finite State Machines
Multiplexers
ALU Design
  Adder/Subtracter

## Slide 20: Logisim
Open-source (i.e. free!) “graphical tool for designing and simulating logic circuits”
  Runs on Java on any computer
  Download to your home computer via class login or the Logisim website (we are using version 2.7.1)
No programming involved
  Unlike Verilog, which is a hardware description language (HDL)
  Click and drag; still has its share of annoying quirks
http://ozark.hendrix.edu/~burch/logisim/

## Slide 21: Gates in Logisim
Click gate type, click to place
  Can set options before placing or select gate later to change
Options
Types of Gates
bus width n
# inputs
labeling not necessary, but can help

## Slide 22: Registers in Logisim
Flip-flops and Registers in “Memory” folder
8-bit accumulator:

## Slide 23: Wires in Logisim
Click and drag on existing port or wire
Color schemes:
  Gray: unconnected
  Dark Green: low signal (0)
  Light Green: high signal (1)
  Red: error
  Blue: undetermined signal
  Orange: incompatible widths
Tunnels: all tunnels with same label are connected
“Splitter” used to adjust bus widths

## Slide 24: Common Mistakes in Logisim
Connecting wires together
  Crossing wires vs. connected wires
Losing track of which input is which
  Mis-wiring a block (e.g. CLK to Enable)
  Grabbing wrong wires off of splitter
Errors:

## Slide 25: Agenda
State Elements Continued
Administrivia
Logisim Introduction
Finite State Machines
Multiplexers
ALU Design
  Adder/Subtracter

## Slide 26: Finite State Machines (FSMs)
You may have seen FSMs in other classes
Function can be represented with a state transition diagram
With combinational logic and registers, any FSM can be implemented in hardware!
. . .

## Slide 27: FSM Overview
An FSM (in this class) is defined by:
  A set of states S (circles)
  An initial state s0 (only arrow not between states)
  A transition function that maps from the current input and current state to the output and the next state (arrows between states)
State transitions are controlled by the clock:
  On each clock cycle the machine checks the inputs and generates a new state (could be same) and new output

## Slide 28: Example: 3 Ones FSM
FSM to detect 3 consecutive 1’s in the Input
States: S0, S1, S2
Initial State: S0
Transitions of form:
input/output

## Slide 29: Hardware Implementation of FSM
Register holds a representation of the FSM’s state
  Must assign a unique bit pattern for each state
  Output is present/current state (PS/CS)
  Input is next state (NS)
Combinational Logic implements transition function (state transitions + output)
+
=

## Slide 30: FSM: Combinational Logic
Read off transitions into Truth Table!
  Inputs: Current State (CS) and Input (In)
  Outputs: Next State (NS) and Output (Out)
Implement logic for EACH output (2 for NS, 1 for Out)
CS | In | NS | Out
00 | 0 | 00 | 0
00 | 1 | 01 | 0
01 | 0 | 00 | 0
01 | 1 | 10 | 0
10 | 0 | 00 | 0
10 | 1 | 00 | 1
Notes: In lecture: Implement logic for Out (1 NOT, 2 AND gates)

## Slide 31: Unspecified Output Values (1/2)
Our FSM has only 3 states
  2 entries in truth table are undefined/unspecified
Use symbol ‘X’ to mean it can be either a 0 or 1
  Make choice to simplify final expression
CS | In | NS | Out
00 | 0 | 00 | 0
00 | 1 | 01 | 0
01 | 0 | 00 | 0
01 | 1 | 10 | 0
10 | 0 | 00 | 0
10 | 1 | 00 | 1
11 | 0 | XX | X
11 | 1 | XX | X

## Slide 32: Unspecified Output Values (2/2)
Let’s find expression for NS1
  Recall: 2-bit output is just a 2-bit bus, which is just 2 wires
Boolean algebra:
  NS1 = CS1’CS0In + CS1CS0In’ + CS1CS0In
  NS1 = CS0In
Karnaugh Map:
  NS1 = CS0In
CS | In | NS | Out
00 | 0 | 00 | 0
00 | 1 | 01 | 0
01 | 0 | 00 | 0
01 | 1 | 10 | 0
10 | 0 | 00 | 0
10 | 1 | 00 | 1
11 | 0 | XX | X
11 | 1 | XX | X
Differs by 2
Is neighbor
 | 00 | 01 | 11 | 10
0 | 0 | 0 | X | 0
1 | 0 | 1 | X | 0
CS
In

## Slide 33: 3 Ones FSM in Hardware
  2-bit Register needed for state
  CL: NS1 = CS0In, NS0 = CS1’CS0’In, Out = CS1In

## Slide 34: Agenda
State Elements Continued
Administrivia
Logisim Introduction
Finite State Machines
Multiplexers
ALU Design
  Adder/Subtracter

## Slide 35: Data Multiplexor
Multiplexor (“MUX”) is a selector
  Place one of multiple inputs onto output (N-to-1)
Shown below is an n-bit 2-to-1 MUX
  Input S selects between two inputs of n bits each
This input is passed to output if selector bits match shown value

## Slide 36: Implementing a 1-bit 2-to-1 MUX
Schematic:
Truth Table:
Boolean Algebra:
Circuit Diagram:
s | a | b | c
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 37: 1-bit 4-to-1 MUX (1/2)
Schematic:
Truth Table: How many rows?
Boolean Expression: e = s1’s0’a + s1’s0b + s1s0’c + s1s0d
26

## Slide 38: 1-bit 4-to-1 MUX (2/2)
Can we leverage what we’ve previously built?
  Alternative hierarchical approach:

## Slide 39: Subcircuits Example
Logisim equivalent of procedure or method
  Every project is a hierarchy of subcircuits
Incomplete wiring shown here

## Slide 40: Get To Know Your Instructor

## Slide 41: Agenda
State Elements Continued
Administrivia
Logisim Introduction
Finite State Machines
Multiplexers
ALU Design
  Adder/Subtracter

## Slide 42: Arithmetic and Logic Unit (ALU)
Most processors contain a special logic block called the “Arithmetic and Logic Unit” (ALU)
  We’ll show you an easy one that does ADD, SUB, bitwise AND, and bitwise OR
Schematic:
when S=00, R = A + B
when S=01, R = A – B
when S=10, R = A AND B
when S=11, R = A OR B

## Slide 43: Simple ALU Schematic
Notice that 3 values are ALWAYS calculated in parallel, but only 1 makes it to the Result

## Slide 44: Adder/Subtractor: 1-bit LSB Adder
Carry-out bit

## Slide 45: Adder/Subtractor: 1-bit Adder
Here defining XOR of many inputs to be 1 when an odd number of inputs are 1
Possible carry-in c1

## Slide 46: Adder/Subtractor: 1-bit Adder
Circuit Diagrams:

## Slide 47: N x 1-bit Adders  N-bit Adder
+
+
+
b0
Connect CarryOuti-1 to CarryIni to chain adders:

## Slide 48: Two’s Complement Adder/Subtractor
+
+
+
Subtraction accomplished by adding negated number:
x ^ 1 = x’
(flips the bits)
This signal is only high when you perform subtraction
Add 1
Where did this come from?

## Slide 49: Detecting Overflow
Unsigned overflow
  On addition, if carry-out from MSB is 1
  On subtraction, if carry-out from MSB is 0
    This case is a lot harder to see than you might think
Signed overflow
  Overflow from adding “large” positive numbers
  Overflow from adding “large” negative numbers

## Slide 50: Signed Overflow Examples (4-bit)
Overflow from two positive numbers:
  0111 + 0111, 0111 + 0001, 0100 + 0100.
  Carry-out from the 2nd MSB (but not MSB)
    pos + pos ≠ neg
Overflow from two negative numbers:
  1000 + 1000, 1000 + 1111, 1011 + 1011.
  Carry-out from the MSB (but not 2nd MSB)
    neg + neg ≠ pos
Expression for signed overflow: Cn XOR Cn-1

## Slide 51: Summary
Critical path constrains clock rate
  Timing constants: setup, hold, and clk-to-q times
  Can adjust with extra registers (pipelining)
Finite State Machines extremely useful
  Can implement systems with Register + CL
Use MUXes to select among input
  S input bits selects one of 2S inputs
  Each input is a bus n-bits wide
Build n-bit adder out of chained 1-bit adders
  Can also do subtraction with additional SUB signal

## Slide 52
You are responsible for the material contained on the following slides, though we may not have enough time to get to them in lecture.
They have been prepared in a way that should be easily readable and the material will be touched upon in the following lecture.
BONUS SLIDES

## Slide 53: Direct-Mapped Cache Internals
Four words/block, cache size = 1 Ki words
8
Index
Data (words)
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
32
Block offset
and

## Slide 54: 4-Way Set Associative Cache
28 = 256 sets each with four slots for blocks
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select
Slot 0
Slot 1
Slot 2
Slot 3