## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Multiple Instruction Issue,
Virtual Memory Introduction

## Slide 2: Great Idea #4: Parallelism
Smart Phone
Warehouse Scale Computer
Leverage Parallelism &
Achieve High Performance
Core
…
Memory
Input/Output
Computer
Core
Parallel Requests
  Assigned to computer
  e.g. search “Garcia”
Parallel Threads
  Assigned to core
  e.g. lookup, ads
Parallel Instructions
  > 1 instruction @ one time
  e.g. 5 pipelined instructions
Parallel Data
  > 1 data item @ one time
  e.g. add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Software Hardware
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A0+B0
A1+B1
A2+B2
A3+B3
Logic Gates

## Slide 3: Extended Review: Pipelining
Why pipeline?
  Increase clock speed by reducing critical path
  Increase performance due to ILP
How do we pipeline?
  Add registers to delimit and pass information between pipeline stages
Things that hurt pipeline performance
  Filling and draining of pipeline
  Unbalanced stages
  Hazards

## Slide 4: Pipelining and the Datapath
Registers hold up information between stages
  Each stage “starts” on same clock trigger
  Each stage is working on a different instruction
  Must pass ALL signals needed in any following stage
Stages can still interact by going around registers
  e.g. forwarding, hazard detection hardware
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

## Slide 5: Pipelining Hazards (1/3)
Structural, Data, and Control hazards
  Structural hazards taken care of in MIPS
  Data hazards only when register is written to and then accessed soon after (not necessarily immediately)
Forwarding
  Can forward from two different places (ALU, Mem)
  Most further optimizations assume forwarding
Delay slots and code reordering
  Applies to both branches and jumps
Branch prediction (can be dynamic)

## Slide 6: Pipelining Hazards (2/3)
Identifying hazards:
  Check system specs (forwarding? delayed branch/jump?)
  Check code for potential hazards
    Find all loads, branches, and jumps
    Anywhere a value is written to and then read in the next two instructions
  Draw out graphical pipeline and check if actually a hazard
    When is result available? When is it needed?

## Slide 7: Pipelining Hazards (3/3)
Solving hazards: (assuming the following were not present already)
  Forwarding?
    Can remove 1 stall for loads, 2 stalls for everything else
  Delayed branch?
    Exposes delay slot for branch and jumps
  Code reordering?
    Find unrelated instruction from earlier to move into delay slot (branch, jump, or load)
  Branch prediction?
    Depends on exact code execution

## Slide 8
Question: Which of the following signals is NOT needed to determine whether or not to forward for the following two instructions?
add $s1, $t0, $t1
ori $s2, $s1, 0xF
rd.EX
(A)
opcode.EX
(B)
rt.ID
(C)
opcode.ID
(D)
IF
ID
EX
MEM
WB
ALU
I$
Reg
D$
Reg
WHAT IF:
1) add was lw $s1,0($t0)?
2) random other instruction in-between?
3) ori was sw $s1,0($s0)?

## Slide 9: Agenda
Higher Level ILP
Administrivia
Dynamic Scheduling
Virtual Memory Introduction

## Slide 10: Higher Level ILP
Deeper pipeline (5 to 10 to 15 stages)
  Less work per stage  shorter clock cycle
Multiple instruction issue
  Replicate pipeline stages  multiple pipelines
  Can start multiple instructions per clock cycle
  CPI < 1 (superscalar), so can use Instructions Per Cycle (IPC) instead
  e.g. 4 GHz 4-way multiple-issue can execute 16 billion IPS with peak CPI = 0.25 and peak IPC = 4
    But dependencies reduce this in practice

## Slide 11: Multiple Issue
Static multiple issue
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 12: Superscalar Laundry: Parallel per stage
More resources, HW to match mix of parallel tasks?
T
a
s
k
O
r
d
e
r
12
2 AM
6 PM
7
8
9
10
11
1
Time
B
C
D
A
E
F
(light clothing)
(dark clothing)
(very dirty clothing)
(light clothing)
(dark clothing)
(very dirty clothing)
30
30
30
30
30

## Slide 13: Pipeline Depth and Issue Width
Intel Processors over Time
Microprocessor | Year | Clock Rate | Pipeline Stages | Issue width | Cores | Power
i486 | 1989 | 25 MHz | 5 | 1 | 1 | 5W
Pentium | 1993 | 66 MHz | 5 | 2 | 1 | 10W
Pentium Pro | 1997 | 200 MHz | 10 | 3 | 1 | 29W
P4 Willamette | 2001 | 2000 MHz | 22 | 3 | 1 | 75W
P4 Prescott | 2004 | 3600 MHz | 31 | 3 | 1 | 103W
Core 2 Conroe | 2006 | 2930 MHz | 14 | 4 | 2 | 75W
Core 2 Yorkfield | 2008 | 2930 MHz | 16 | 4 | 4 | 95W
Core i7 Gulftown | 2010 | 3460 MHz | 16 | 4 | 6 | 130W

## Slide 14: Pipeline Depth and Issue Width
Chart: 
| 1989 | 1993 | 1997 | 2001 | 2004 | 2006 | 2008 | 2010
Clock | 25 | 66 | 200 | 2000 | 3600 | 2930 | 2930 | 3460
Power | 5 | 10 | 29 | 75 | 103 | 75 | 95 | 130
Pipeline Stages | 5 | 5 | 10 | 22 | 31 | 14 | 16 | 16
Issue width | 1 | 2 | 3 | 3 | 3 | 4 | 4 | 4
Cores | 1 | 1 | 1 | 1 | 1 | 2 | 4 | 6

## Slide 15: Static Multiple Issue
Compiler groups instructions into issue packets
  Group of instructions that can be issued on a single cycle
  Determined by pipeline resources required
Think of an issue packet as a very long instruction word (VLIW)
  Specifies multiple concurrent operations

## Slide 16: Scheduling Static Multiple Issue
Compiler must remove some/all hazards
  Reorder instructions into issue packets
  No dependencies within a packet
  Possibly some dependencies between packets
    Varies between ISAs; compiler must know!
  Pad with nops if necessary

## Slide 17: MIPS with Static Dual Issue
Dual-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU/branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load/store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load/store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load/store |  |  | IF | ID | EX | MEM | WB
This prevents what kind of hazard?

## Slide 18: Datapath with Static Dual Issue
1 Extra ALU
1 Extra Sign Ext
2 Extra Reg Read Ports
1 Extra Write Port
1 Extra 32-bit instruction

## Slide 19: Hazards in the Dual-Issue MIPS
More instructions executing in parallel
EX data hazard
  Forwarding avoided stalls with single-issue
  Now can’t use ALU result in load/store in same packet
    add $t0, $s0, $s1 load $s2, 0($t0)
    Splitting these into two packets is effectively a stall
Load-use hazard
  Still one cycle use latency, but now two instructions/cycle
More aggressive scheduling required!

## Slide 20: Scheduling Example
Schedule this for dual-issue MIPS
Loop: lw $t0, 0($s1) # $t0=array element addu $t0, $t0, $s2 # add scalar in $s2 sw $t0, 0($s1) # store result addi $s1, $s1,–4 # decrement pointer bne $s1, $zero, Loop # branch $s1!=0
 | ALU/Branch | Load/Store | Cycle
Loop: | nop | lw $t0, 0($s1) | 1
 | addi $s1, $s1,–4 | nop | 2
 | addu $t0, $t0, $s2 | nop | 3
 | bne $s1, $zero, Loop | sw $t0, 4($s1) | 4
  IPC = 5/4 = 1.25 (c.f. peak IPC = 2)
This change affects scheduling but not effect

## Slide 21: Loop Unrolling
Replicate loop body to expose more instruction level parallelism
Use different registers per replication
  Called register renaming
  Avoid loop-carried anti-dependencies
    Store followed by a load of the same register
    a.k.a. “name dependence” (reuse of a register name)

## Slide 22: Loop Unrolling Example
IPC = 14/8 = 1.75
  Closer to 2, but at cost of registers and code size
 | ALU/branch | Load/store | cycle
Loop: | addi $s1, $s1,–16 | lw $t0, 0($s1) | 1
 | nop | lw $t1, 12($s1) | 2
 | addu $t0, $t0, $s2 | lw $t2, 8($s1) | 3
 | addu $t1, $t1, $s2 | lw $t3, 4($s1) | 4
 | addu $t2, $t2, $s2 | sw $t0, 16($s1) | 5
 | addu $t3, $t4, $s2 | sw $t1, 12($s1) | 6
 | nop | sw $t2, 8($s1) | 7
 | bne $s1, $zero, Loop | sw $t3, 4($s1) | 8

## Slide 23: Agenda
Higher Level ILP
Administrivia
Dynamic Scheduling
Virtual Memory Introduction

## Slide 24: Administrivia
HW5 due tonight
Project 2 Part 2 (and EC) due Sunday
“Free” lab time today
  The TAs will still be there, Lab 10 due Tue
Project 3 will be posted by Friday night
  Two-stage pipelined CPU in Logisim

## Slide 25: Agenda
Higher Level ILP
Administrivia
Dynamic Scheduling
Virtual Memory Introduction

## Slide 26: Dynamic Multiple Issue
Used in “superscalar” processors
CPU decides whether to issue 0, 1, 2, … instructions each cycle
  Goal is to avoid structural and data hazards
Avoids need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU

## Slide 27: Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example: lw $t0, 20($s2) addu $t1, $t0, $t2 subu $s4, $s4, $t3 slti $t5, $s4, 20
  Can start subu while addu is waiting for lw
Especially useful on cache misses; can execute many instructions while waiting!

## Slide 28: Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
Not all stalls are predicable
  e.g. cache misses
Can’t always schedule around branches
  Branch outcome is dynamically determined
Different implementations of an ISA have different latencies and hazards

## Slide 29: Speculation
“Guess” what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right and roll back if necessary
Examples:
  Speculate on branch outcome (Branch Prediction)
    Roll back if path taken is different
  Speculate on load
    Roll back if location is updated
Can be done in hardware or by compiler
Common to static and dynamic multiple issue

## Slide 30: Pipeline Hazard Analogy: Matching socks in later load
A depends on D; stall since folder is tied up
T
a
s
k
O
r
d
e
r
B
C
D
A
E
F
bubble
12
2 AM
6 PM
7
8
9
10
11
1
Time
30
30
30
30
30
30
30

## Slide 31: Out-of-Order Laundry: Don’t Wait
A depends on D; let the rest continue
  Need more resources to allow out-of-order (2 folders)
T
a
s
k
O
r
d
e
r
12
2 AM
6 PM
7
8
9
10
11
1
Time
B
C
D
A
30
30
30
30
30
30
30
E
bubble

## Slide 32: Not a Simple Linear Pipeline
3 major units operating in parallel:
Instruction fetch and issue unit
  Issues instructions in program order
Many parallel functional (execution) units
  Each unit has an input buffer called a Reservation Station
  Holds operands and records the operation
  Can execute instructions out-of-order (OOO)
Commit unit
  Saves results from functional units in Reorder Buffers
  Stores results once branch resolved so OK to execute
  Commits results in program order

## Slide 33: Out-of-Order Execution (1/2)
Basically, unroll loops in hardware
Fetch instructions in program order (≤ 4/clock)
Predict branches as taken/untaken
To avoid hazards on registers, rename registers using a set of internal registers (≈ 80 registers)
Collection of renamed instructions might execute in a window (≈ 60 instructions)

## Slide 34: Out-of-Order Execution (2/2)
Basically, unroll loops in hardware
Execute instructions with ready operands in 1 of multiple functional units (ALUs, FPUs, Ld/St)
Buffer results of executed instructions until predicted branches are resolved in reorder buffer
If predicted branch correctly, commit results in program order
If predicted branch incorrectly, discard all dependent results and start with correct PC

## Slide 35: Dynamically Scheduled CPU
Results also sent to any waiting reservation stations (think: forwarding!)
Reorder buffer for register and memory writes
Can supply operands for issued instructions
Preserves dependencies
Wait here until all operands available
Branch prediction,
Register renaming
Execute…
… and Hold

## Slide 36: Out-Of-Order Intel
All use O-O-O since 2001
Microprocessor | Year | Clock Rate | Pipeline Stages | Issue width | Out-of-order/ Speculation | Cores | Power
i486 | 1989 | 25MHz | 5 | 1 | No | 1 | 5W
Pentium | 1993 | 66MHz | 5 | 2 | No | 1 | 10W
Pentium Pro | 1997 | 200MHz | 10 | 3 | Yes | 1 | 29W
P4 Willamette | 2001 | 2000MHz | 22 | 3 | Yes | 1 | 75W
P4 Prescott | 2004 | 3600MHz | 31 | 3 | Yes | 1 | 103W
Core | 2006 | 2930MHz | 14 | 4 | Yes | 2 | 75W
Core 2 Yorkfield | 2008 | 2930 MHz | 16 | 4 | Yes | 4 | 95W
Core i7 Gulftown | 2010 | 3460 MHz | 16 | 4 | Yes | 6 | 130W

## Slide 37: AMD Opteron X4 Microarchitecture
72 physical registers
renaming
16 architectural registers
x86 instructions
RISC operations
Queues:
106 RISC ops
24 integer ops
36 FP/SSE ops
44 ld/st

## Slide 38: AMD Opteron X4 Pipeline Flow
For integer operations
  12 stages (Floating Point is 17 stages)
  Up to 106 RISC-ops in progress
Intel Nehalem is 16 stages for integer operations, details not revealed, but likely similar to above
  Intel calls RISC operations “Micro operations” or “μops”

## Slide 39: Does Multiple Issue Work?
Yes, but not as much as we’d like
Programs have real dependencies that limit ILP
Some dependencies are hard to eliminate
  e.g. pointer aliasing
Some parallelism is hard to expose
  Limited window size during instruction issue
Memory delays and limited bandwidth
  Hard to keep pipelines full
Speculation can help if done well

## Slide 40: Get To Know Your Instructor

## Slide 41: Agenda
Higher Level ILP
Administrivia
Dynamic Scheduling
Virtual Memory Introduction

## Slide 42: Memory Hierarchy
Regs
L2 Cache
Memory
Disk
Tape
Instr Operands
Blocks
Pages
Files
Upper Level
Lower Level
Faster
Larger
L1 Cache
Blocks
Next Up:
Virtual Memory
Earlier: Caches

## Slide 43: Memory Hierarchy Requirements
Principle of Locality
  Allows caches to offer (close to) speed of cache memory with size of DRAM memory
  Can we use this at the next level to give speed of DRAM memory with size of Disk memory?
What other things do we need from our memory system?

## Slide 44: Memory Hierarchy Requirements
Allow multiple processes to simultaneously occupy memory and provide protection
  Don’t let programs read from or write to each other’s memories
Give each program the illusion that it has its own private address space
  Suppose code starts at address 0x00400000, then different processes each think their code resides at the same address
  Each program must have a different view of memory

## Slide 45: Virtual Memory
Next level in the memory hierarchy
  Provides illusion of very large main memory
  Working set of “pages” residing in main memory (subset of all pages residing on disk)
Main goal: Avoid reaching all the way back to disk as much as possible
Additional goals:
  Let OS share memory among many programs and protect them from each other
  Each process thinks it has all the memory to itself

## Slide 46: Virtual to Physical Address Translation
Each program operates in its own virtual address space and thinks it’s the only program running
Each is protected from the other
OS can decide where each goes in memory
Hardware gives virtual  physical mapping
Program operates in its virtual address space
Virtual
Address (VA)
(inst. fetch
load, store)
HW mapping
Physical
Address (PA)
(inst. fetch
load, store)
Physical memory (including caches)

## Slide 47: VM Analogy (1/2)
Trying to find a book in the UCB library system
Book title is like virtual address (VA)
  What you want/are requesting
Book call number is like physical address (PA)
  Where it is actually located
Card catalogue is like a page table (PT)
  Maps from book title to call number
  Does not contain the actual that data you want
  The catalogue itself takes up space in the library

## Slide 48: VM Analogy (2/2)
Indication of current location within the library system is like valid bit
  Valid if in current library (main memory) vs. invalid if in another branch (disk)
  Found on the card in the card catalogue
Availability/terms of use like access rights
  What you are allowed to do with the book (ability to check out, duration, etc.)
  Also found on the card in the card catalogue

## Slide 49: Mapping VM to PM
Divide into equal sized chunks (usually 4-8 KiB)
Any chunk of Virtual Memory can be assigned to any chunk of Physical Memory (“page”)
0
Physical Memory
¥
Virtual Memory
Code
Static
Heap
Stack
64 MB
0

## Slide 50: Paging Organization
Addr
Trans
MAP
page 0
4 Ki
4 Ki
4 Ki
0x00000
0x01000
0x1F000
Virtual Memory
Virtual
Address
page 1
page 31
4 Ki
0x02000
page 2
...
...
...
page 0
0x0000
0x1000
0x7000
Physical
Address
Physical
Memory
4 Ki
4 Ki
4 Ki
page 1
page 7
...
...
...
Here assume page size is 4 KiB
  Page is both unit of mapping and unit of transfer between disk and physical memory

## Slide 51: Virtual Memory Mapping Function
How large is main memory? Disk?
  Don’t know! Designed to be interchangeable components
  Need a system that works regardless of sizes
Use lookup table (page table) to deal with arbitrary mapping
  Index lookup table by # of pages in VM (not all entries will be used/valid)
  Size of PM will affect size of stored translation

## Slide 52: Address Mapping
Pages are aligned in memory
  Border address of each page has same lowest bits
  Page size (P bytes) is same in VM and PM, so denote lowest PO = log2(P) bits as page offset
Use remaining upper address bits in mapping
  Tells you which page you want (similar to Tag)
Page Offset
Virtual Page #
Page Offset
Physical Page #
Same Size
Not necessarily the same size

## Slide 53: Address Mapping: Page Table
Page Table functionality:
  Incoming request is Virtual Address (VA), want Physical Address (PA)
  Physical Offset = Virtual Offset (page-aligned)
  So just swap Virtual Page Number (VPN) for Physical Page Number (PPN)
Implementation?
  Use VPN as index into PT
  Store PPN and management bits (Valid, Access Rights)
  Does NOT store actual data (the data sits in PM)
Page Offset
Virtual Page #
Physical Page #
Page Offset

## Slide 54: Page Table Layout
V | AR | PPN
X | XX | 
Virtual Address:
VPN
offset
Page Table
1) Index into PT using VPN
2) Check Valid and Access Rights bits
+
3) Combine PPN and offset
Physical
Address
4) Use PA to access memory

## Slide 55: Page Table Entry Format
Contains either PPN or indication not in main memory
Valid = Valid page table entry
  1  virtual page is in physical memory
  0  OS needs to fetch page from disk
Access Rights checked on every access to see if allowed (provides protection)
  Read Only: Can read, but not write page
  Read/Write: Read or write data on page
  Executable: Can fetch instructions from page

## Slide 56: Page Tables
A page table (PT) contains the mapping of virtual addresses to physical addresses
Where should PT be located?
  Physical memory, so faster to access and can be shared by multiple processors
The OS maintains the PTs
  Each process has its own page table
    “State” of a process is PC, all registers, and PT
  OS stores address of the PT of the current process in the Page Table Base Register

## Slide 57: Paging/Virtual Memory Multiple Processes
User B: Virtual Memory
¥
Code
Static
Heap
Stack
0
Code
Static
Heap
Stack
Page
Table A
Page
Table B
User A: Virtual Memory
¥
0
0
Physical
Memory
64 MB

## Slide 58: Caches vs. Virtual Memory
Caches Virtual Memory
Block Page
Cache Miss Page Fault
Block Size: 32-64B Page Size: 4Ki-8KiB
Placement: Direct Mapped, Fully Associative N-way Set Associative (almost always)
Replacement: LRU or Random LRU
Write Thru or Back Write Back

## Slide 59: Summary
More aggressive performance options:
  Longer pipelines
  Superscalar (multiple issue)
  Out-of-order execution
  Speculation
Virtual memory bridges memory and disk
  Provides illusion of independent address spaces to processes and protects them from each other
  VA to PA using Page Table