## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Input/Output

## Slide 2: Review of Last Lecture (1/2)
Great Idea: Dependability via Redundancy
  Reliability: MTTF & Annualized Failure Rate
  Availability: % uptime = MTTF/MTBF
Error Correcting Code (ECC)
  Encode data bits in larger “code words”
    Denote valid and invalid code words
  Hamming distance 2: Parity for Single Error Detect
  Hamming distance 3: Single Error Correction Code + error position identification
  Hamming distance 4: SEC/Double Error Detection

## Slide 3: Review of Last Lecture (2/2)
RAID: Redundant Arrays of Inexpensive Disks
  RAID 0: data striping, no redundancy
  RAID 1: disk mirroring
  RAID 2: bit striping with ECC disks
  RAID 3: byte striping with dedicated parity disk
  RAID 4: block striping with dedicated parity disk
  RAID 5: block striping with interleaved parity
  RAID 6: block striping with two interleaved parity disks for DEC
  Can access disks concurrently, but may require additional reads & writes for updating parity

## Slide 4
Question: What is the correct data word given the following SEC Hamming code: 0101101
Code word: 0 1 0 1 1 0 1
p4 0 0 0 1 1 1 1
p2 0 1 1 0 0 1 1
p1 1 0 1 0 1 0 1
0 1 0 1
(A)
1 0 1 0
(B)
0 0 0 1
(C)
1 1 0 1
(D)

## Slide 5
Question:
You have a 5-disk RAID 4 system with disk block size equal to your page size.
On a page fault, what is the worst case # of disk accesses (both reads and writes)?
1 (1 read, 0 writes)
(A)
2 (2 reads, 0 writes)
(B)
4 (2 reads, 2 writes)
(C)
5 (3 reads, 2 writes)
(D)

## Slide 6: Agenda
Disks
Administrivia
I/O Basics
Exceptions and Interrupts

## Slide 7: Magnetic Disks
Nonvolatile storage
  Information stored by magnetizing ferrite material on surface of rotating disk
  Retains its value without applying power to disk (SRAM)
  Long-term, inexpensive storage for files
Two Types:
  Floppy disks – slower, less dense, removable
  Hard Disk Drives (HDD) – faster, more dense, non-removable

## Slide 8: Photo of Disk Internals
Actuator
Arm
Head
Spindle
Platters (1-12)

## Slide 9: Disk Device Terminology
Several platters, with information recorded magnetically on both surfaces (usually)
Bits recorded in tracks, which in turn are divided into sectors (usually 512 Bytes)
Actuator moves head (end of arm) over track (“seek”), wait for sector to rotate under head, then read or write
Outer
Track
Inner
Track
Sector
Actuator
Head
Arm
Platter

## Slide 10: Disk Device Performance (1/3)
Disk Latency = Seek Time + Rotation Time + Transfer Time + Controller Overhead
  Seek Time depends on number of tracks to move arm and speed of actuator
Platter
Arm
Actuator
Head
Sector
Inner
Track
Outer
Track
Controller
Spindle
Notes: Use analogy to records

## Slide 11: Disk Device Performance (1/3)
Disk Latency = Seek Time + Rotation Time + Transfer Time + Controller Overhead
  Rotation Time depends on speed of disk rotation and how far sector is from head
Platter
Arm
Actuator
Head
Sector
Inner
Track
Outer
Track
Controller
Spindle
Notes: Use analogy to records

## Slide 12: Disk Device Performance (1/3)
Disk Latency = Seek Time + Rotation Time + Transfer Time + Controller Overhead
  Transfer Time depends on size of request and data rate (bandwidth) of disk, which is a function of bit density and RPM
Platter
Arm
Actuator
Head
Sector
Inner
Track
Outer
Track
Controller
Spindle
Notes: Use analogy to records

## Slide 13: Disk Device Performance (2/3)
Average distance of sector from head?
  Average Rotation Time = time for 1/2 a rotation
    7200 revolutions per minute  1 rev/8.33 ms
    1/2 rotation (revolution)  4.17 ms
Average no. tracks to move arm?
  Disk industry standard benchmark:
    Sum all time for all possible seek distances from all possible tracks / # possible
    Assumes average seek distance is random
  Seek Time usually given or to be solved for

## Slide 14: Disk Device Performance (3/3)
How long for data read/write to happen?
  Transfer Time = size of data request / transfer rate
    Note that transfer rates listed in SI prefixes (10x)
Disks have internal controllers to handle requests and data transfers
  Controller Overhead usually given or to be solved for
  Size of disk cache can strongly affect performance
    Cache built into disk system, OS knows nothing

## Slide 15: Disk Drive Performance Example
7200 RPM drive, 4 ms seek time, 20.48 MB/s transfer rate. Negligible controller overhead. Latency to read 100 KiB file?
  Rotation time = 4.17 ms (from last slide)
  Transfer time = 0.1 MiB / 20 (MiB/sec) = 5 ms
  Latency = 4 + 4.17 + 5 = 13.17 ms
  Throughput = 100 KiB/13.17 ms = 7.59 MiB/sec
How do numbers change when reading bigger/smaller file? File fragmented across multiple locations?

## Slide 16: Flash Memory
Microdrives and Flash memory (e.g. CompactFlash) are going head-to-head
  Both non-volatile (no power, data ok)
  Flash benefits: durable & lower power (no moving parts vs. need to spin µdrives up/down)
  Flash limitations: finite number of write cycles (wear on the insulating oxide layer around the charge storage mechanism). Most ≥ 100K, some ≥ 1M W/erase cycles.
How does Flash memory work?
  NMOS transistor with an additional conductor between gate and source/drain which “traps” electrons. The presence/absence is a 1 or 0.
en.wikipedia.org/wiki/Flash_memory

## Slide 17: What does Apple put in its iPods?
Samsung flash 4, 8GB
Shuffle Nano Classic Touch
Toshiba 1.8-inch HDD 80, 160GB
Toshiba flash 1, 2GB
Toshiba flash 8, 16, 32GB

## Slide 18: Solid-State Drives
Data storage devices with same electronic interfaces as HDD, but implemented (usually) with flash
 | HDD | Flash-based SSD
Access Time | ~ 12 ms ≈ 30M clock cycles | ~ 0.1 ms ≈ 250K clock cycles
Relative Power | 1 | 1/3
Cost | ~ $0.05-$0.10 / GB | ~ $0.65 / GB
SSDs are also quieter, lighter, unsusceptible to magnetic fields and fragmentation, and start up faster

## Slide 19: Agenda
Disks
Administrivia
I/O Basics
Exceptions and Interrupts

## Slide 20: Administrivia
Final Review – Tue 8/13, 7-10pm in 10 Evans
Final – Fri 8/16, 9am-12pm, 155 Dwinelle
  2nd half material + self-modifying MIPS
  MIPS Green Sheet provided again
  Two two-sided handwritten cheat sheets
    Can re-use your midterm cheat sheet!
“Dead Week” – WTh 8/14-15
HKN Course Survey at end of lecture tomorrow (8/13)

## Slide 21: Agenda
Disks
Administrivia
I/O Basics
Exceptions and Interrupts

## Slide 22: Five Components of a Computer
Components a computer needs to work
  Control
  Datapath
  Memory
  Input
  Output
Processor
Computer
Control
Datapath
Memory
Devices
Input
Output

## Slide 23: Motivation for Input/Output
I/O is how humans interact with computers
I/O gives computers long-term memory.
I/O lets computers do amazing things:
Computer without I/O like a car without wheels; great technology, but gets you nowhere
MIT Media Lab
“Sixth Sense”

## Slide 24: I/O Device Examples and Speeds
Device | Behavior | Partner | Data Rate (KB/s)
Keyboard | Input | Human | 0.01
Mouse | Input | Human | 0.02
Voice output | Output | Human | 5.00
Floppy disk | Storage | Machine | 50.00
Laser printer | Output | Human | 100.00
Magnetic disk | Storage | Machine | 10,000.00
Wireless network | Input or Output | Machine | 10,000.00
Graphics display | Output | Human | 30,000.00
Wired LAN network | Input or Output | Machine | 125,000.00
I/O speeds: 7 orders of magnitude between mouse and LAN
When discussing transfer rates, use SI prefixes (10x)

## Slide 25: What do we need for I/O to work?
A way to connect many types of devices
A way to control these devices, respond to them, and transfer data
A way to present them to user programs so they are useful
ctrl reg.
data reg.
Operating System
APIs
Files
Proc
Mem
PCI Bus
SCSI Bus

## Slide 26: Instruction Set Architecture for I/O
What must the processor do for I/O?
  Input: reads a sequence of bytes
  Output: writes a sequence of bytes
Some processors have special input and output instructions
Alternative model (used by MIPS):
  Use loads for input, stores for output (in small pieces)
  Called Memory Mapped Input/Output
  A portion of the address space dedicated to communication paths to Input or Output devices (no memory there)

## Slide 27: Memory Mapped I/O
Certain addresses are not regular memory
Instead, they correspond to registers in I/O devices
control reg.
data reg.
0
0xFFFFFFFF
0xFFFF0000
address

## Slide 28: Processor-I/O Speed Mismatch
1 GHz microprocessor can execute 1 billion load or store instr/sec (4,000,000 KB/s data rate)
  Recall: I/O devices data rates range from 0.01 KB/s to 125,000 KB/s
Input: Device may not be ready to send data as fast as the processor loads it
  Also, might be waiting for human to act
Output: Device may not be ready to accept data as fast as processor stores it

## Slide 29: Processor Checks Status Before Acting
Path to a device generally has 2 registers:
  Control Register says it’s OK to read/write (I/O ready)
  Data Register contains data
Processor reads from control register in a loop, waiting for device to set Ready bit (0  1)
Processor then loads from (input) or writes to (output) data register
  Resets Ready bit of control register (1  0)
This process is called “Polling”

## Slide 30: I/O Example (Polling in MIPS)
Input: Read from keyboard into $v0
lui $t0, 0xffff # ffff0000 Waitloop: lw $t1, 0($t0) # control reg andi $t1,$t1,0x1 beq $t1,$zero, Waitloop lw $v0, 4($t0) # data reg
Output: Write to display from $a0
lui $t0, 0xffff # ffff0000 Waitloop: lw $t1, 8($t0) # control reg andi $t1,$t1,0x1 beq $t1,$zero, Waitloop sw $a0,12($t0) # data reg
“Ready” bit is from processor’s point of view!

## Slide 31: Cost of Polling?
Processor specs: 1 GHz clock, 400 clock cycles for a polling operation (call polling routine, accessing the device, and returning)
Determine % of processor time for polling:
  Mouse: Polled 30 times/sec so as not to miss user movement
  Floppy disk: Transferred data in 2-Byte units with data rate of 50 KB/sec. No data transfer can be missed.
  Hard disk: Transfers data in 16-Byte chunks and can transfer at 16 MB/second. Again, no transfer can be missed.

## Slide 32: % Processor time to poll
Mouse polling:
  Time taken: 30 [polls/s] × 400 [clocks/poll] = 12K [clocks/s]
  % Time: 1.2×104 [clocks/s] / 109 [clocks/s] = 0.0012%
  Polling mouse has little impact on processor
Disk polling:
  Freq: 16 [MB/s] / 16 [B/poll] = 1M [polls/s]
  Time taken: 1M [polls/s] × 400 [clocks/poll] = 400M [clocks/s]
  % Time: 4×108 [clocks/s] / 109 [clocks/s] = 40%
  Unacceptable!
Problems: polling, accessing small chunks
Notes: was p 677 in book (not current edition)

## Slide 33: Alternatives to Polling?
Wasteful to have processor spend most of its time “spin-waiting” for I/O to be ready
Would like an unplanned procedure call that would be invoked only when I/O device is ready
Solution: Use exception mechanism to help trigger I/O, then interrupt program when I/O is done with data transfer
  This method is discussed next

## Slide 34: Get To Know Your Instructor

## Slide 35: Agenda
Disks
Administrivia
I/O Basics
Exceptions and Interrupts

## Slide 36: Exceptions and Interrupts
“Unexpected” events requiring change in flow of control
  Different ISAs use the terms differently
Exception
  Arises within the CPU (e.g. undefined opcode, overflow, syscall, TLB Miss)
Interrupt
  From an external I/O controller
Dealing with these without sacrificing performance is difficult!

## Slide 37: Handling Exceptions (HW)
In MIPS, exceptions managed by a System Control Coprocessor (CP0)
Save PC of offending (or interrupted) instruction
  In MIPS: save in special register called Exception Program Counter (EPC)
Save indication of the problem
  In MIPS: saved in special register called Cause register
  In simple implementation, might only need 1-bit (0 for undefined opcode, 1 for overflow)
Jump to exception handler code at address 0x80000180

## Slide 38: Exception Properties
Re-startable exceptions
  Pipeline can flush the instruction
  Handler executes, then returns to the instruction
    Re-fetched and executed from scratch
PC+4 saved in EPC register
  Identifies causing instruction
  PC+4 because it is the available signal in a pipelined implementation
    Handler must adjust this value to get right address
Notes: Non-re-startable exception example: arithmetic overflow. If instruction completes, can’t show offending values
Re-startable exception example: I/O device interrupt.

## Slide 39: Handler Actions (SW)
Read Cause register, and transfer to relevant handler
OS determines action required:
  If restartable exception, take corrective action and then use EPC to return to program
  Otherwise, terminate program and report error using EPC, Cause register, etc. (e.g. our best friend the segfault)

## Slide 40: Exceptions in a Pipeline
Another kind of control hazard
Consider overflow on add in EX stage
  add $1, $2, $1
  Prevent $1 from being clobbered
  Complete previous instructions
  Flush add and subsequent instructions
  Set Cause and EPC register values
  Transfer control to handler
Similar to mispredicted branch
  Use much of the same hardware

## Slide 41: Exception Example
I$
and
or
add
slt
lw
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
ALU
I$
Reg
D$
Reg
lui

## Slide 42: Exception Example
I$
and
or
(bubble)
(bubble)
(bubble)
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
ALU
I$
Reg
D$
Reg
sw
Save PC+4 into EPC
1st instruction of handler
Flush add, slt, lw

## Slide 43: Multiple Exceptions
Pipelining overlaps multiple instructions
  Could have multiple exceptions at once!
  e.g. page fault in lw the same clock cycle as overflow of following instruction add
Simple approach: Deal with exception from earliest instruction and flush subsequent instructions
  Called precise exceptions
  In previous example, service lw exception first
What about multiple issue or out-of-order execution?
  Maintaining precise exceptions can be difficult!

## Slide 44: Imprecise Exceptions
Just stop pipeline and save state
  Including exception cause(s)
Let the software handler work out:
  Which instruction(s) had exceptions
  Which to complete or flush
    May require “manual” completion
Simplifies hardware, but more complex handler software
  Not feasible for complex multiple-issue out-of-order pipelines to always get exact instruction
All computers today offer precise exceptions—affects performance though

## Slide 45: I/O Interrupt
An I/O interrupt is like an exception except:
  An I/O interrupt is “asynchronous”
  More information needs to be conveyed
“Asynchronous” with respect to instruction execution:
  I/O interrupt is not associated with any instruction, but it can happen in the middle of any given instruction
  I/O interrupt does not prevent any instruction from running to completion
Notes: How does an I/O interrupt different from the exception you already learned?
Well, an I/O interrupt is asynchronous with respect to the instruction execution while exception such as overflow or page fault are always associated with a certain instruction.
Also for exception, the only information needs to be conveyed is the fact that an exceptional condition has occurred but for interrupt, there is more information to be conveyed.
Let me elaborate on each of these two points.
Unlike exception, which is always associated with an instruction, interrupt is not associated with any instruction. The user program is just doing its things when an I/O interrupt occurs.
So I/O interrupt does not prevent any instruction from completing so you can pick your own convenient point to take the interrupt.
As far as conveying more information is concerned, the interrupt detection hardware must somehow let the OS know who is causing the interrupt.
Furthermore, interrupt requests needs to be prioritized. The hardware that can do all these looks like this.
+2 = 64 min. (Y:44)

## Slide 46: Interrupt-Driven Data Transfer
(1) I/O
interrupt
(2) save PC
Memory
add
sub
and
or
user
program
read
store
...
jr
interrupt
service
routine
(3) jump to interrupt
service routine
(4) perform transfer
(5)
Notes: That is, whenever an I/O device needs attention from the processor, it interrupts the processor from what it is currently doing.
This is how an I/O interrupt looks in the overall scheme of things. The processor is minding its business when one of the I/O device wants its attention and causes an I/O interrupt.
The processor then save the current PC, branch to the address where the interrupt service routine resides, and start executing the interrupt service routine.
When it finishes executing the interrupt service routine, it branches back to the point of the original program where we stop and continue.
The advantage of this approach is efficiency. The user program’s progress is halted only during actual transfer.
The disadvantage is that it require special hardware in the I/O device to generate the interrupt. And on the processor side, we need special hardware to detect the interrupt and then to save the proper states so we can resume after the interrupt.
+2 = 62 min. (Y:42)

## Slide 47: Interrupt-Driven I/O Example (1/2)
Assume the following system properties:
  500 clock cycle overhead for each transfer, including interrupt
  Disk throughput of 16 MB/s
  Disk interrupts after transferring 16 B
  Processor running at 1 GHz
If disk is active 5% of program, what % of processor is consumed by the disk?
  5% × 16 [MB/s] / 16 [B/inter] = 50,000 [inter/s]
  50,000 [inter/s] × 500 [clocks/inter] = 2.5×107 [clocks/s]
  2.5×107 [clocks/s] / 109 [clock/s] = 2.5% busy

## Slide 48: Interrupt-Driven I/O Example (2/2)
2.5% busy (interrupts) much better than 40% (polling)
Real Solution: Direct Memory Access (DMA) mechanism
  Device controller transfers data directly to/from memory without involving the processor
  Only interrupts once per page (large!) once transfer is done

## Slide 49: Summary
Disks work by positioning head over spinning platters
  Very slow relative to CPU, flash memory is alternative
I/O gives computers their 5 senses + long term memory
  I/O speed range is 7 orders of magnitude (or more!)
Processor speed means must synchronize with I/O devices before use:
  Polling works, but expensive due to repeated queries
Exceptions are “unexpected” events in processor
Interrupts are asynchronous events that are often used for interacting with I/O devices