CS 61C: Great Ideas in
Computer Architecture
Direct-Mapped Caches,
Set Associative Caches,
Cache Performance
Instructor: Alan Christopher

---
Great Idea #3: Principle of Locality/
Memory Hierarchy
Great Idea #3: Principle of Locality/
Memory Hierarchy

---
Extended Review of Last Lecture
Extended Review of Last Lecture
Why have caches?
  - Intermediate level between CPU and memory
  - In-between in size, cost, and speed
Memory (hierarchy, organization, structures) set up to exploit temporal and spatial locality
  - Temporal: If accessed, will access again soon
  - Spatial: If accessed, will access others around it
Caches hold a subset of memory (in blocks)
  - We are studying how they are designed for fast and efficient operation (lookup, access, storage)

---
Extended Review of Last Lecture
Extended Review of Last Lecture
Fully Associative Caches:
  - Every block can go in any slot
    - Use random or LRU replacement policy when cache full
  - Memory address breakdown (on request)
    - Tag field is identifier (which block is currently in slot)
    - Offset field indexes into block
  - Each cache slot holds block data, tag, valid bit, and dirty bit (dirty bit is only for write-back)
    - The whole cache maintains LRU bits

---
Extended Review of Last Lecture
Extended Review of Last Lecture
Cache read and write policies:
  - Affect consistency of data between cache and memory
  - Write-back vs. write-through
  - Write allocate vs. no-write allocate
On memory access (read or write):
  1. Look at ALL cache slots in parallel
  2. If Valid bit is 0, then ignore
  3. If Valid bit is 1 and Tag matches, then use that data
write, set Dirty bit if write-back

---
Extended Review of Last Lecture
Extended Review of Last Lecture
Fully associative cache layout
  - 8-bit address space, 32-byte cache with 8-byte blocks
  - LRU replacement (5 bits), write-back and write allocate
  - Offset – 3 bits, Tag – 5 bits
Each slot has 71 bits; cache has 4*71+5 = 289 bits
Offset
0
1
2
3
V	D	Tag	000	001	010	011	100	101	110	111
X	X	XXXXX	0x??	0x??	0x??	0x??	0x??	0x??	0x??	0x??
X	X	XXXXX	0x??	0x??	0x??	0x??	0x??	0x??	0x??	0x??
X	X	XXXXX	0x??	0x??	0x??	0x??	0x??	0x??	0x??	0x??
X	X	XXXXX	0x??	0x??	0x??	0x??	0x??	0x??	0x??	0x??
LRU
XXXXX
Slot
cache size (C)
block size (K)
256 B address space
Need dirty bit

---
Agenda
Agenda
- Direct-Mapped Caches
- Administrivia
- Set Associative Caches
- Cache Performance

---
Direct-Mapped Caches (1/3)
Direct-Mapped Caches (1/3)
Each memory block is mapped to exactly one slot in the cache (direct-mapped)
  - Every block has only one “home”
  - Use hash function to determine which slot
Comparison with fully associative
  - Check just one slot for a block (faster!)
  - No replacement policy necessary
  - Access pattern may leave empty slots in cache
[Speaker Notes: Check just one location to see if block is in cache.]

---
Direct-Mapped Caches (2/3)
Direct-Mapped Caches (2/3)
- Offset field remains the same as before
- Recall: blocks consist of adjacent bytes
  - Do we want adjacent blocks to map to same slot?
  - Index field: Apply hash function to block address to determine which slot the block goes in
    - (block address) modulo (# of blocks in the cache)
Tag field maintains same function (identifier), but is now shorter

---
TIO Address Breakdown
TIO Address Breakdown
Memory address fields:
Meaning of the field sizes:
  - O bits ↔ 2O bytes/block = 2O-2 words/block
  - I bits ↔ 2I slots in cache = cache size / block size
  - T bits = A – I – O, where A = # of address bits
    (A = 32 here)
Tag
Index
Offset
31
0
T bits
I bits
O bits

---
Direct-Mapped Caches (3/3)
Direct-Mapped Caches (3/3)
What’s actually in the cache?
  - Block of data (8 × K = 8 × 2O bits)
  - Tag field of address as identifier (T bits)
  - Valid bit (1 bit)
  - Dirty bit (1 bit if write-back)
  - No replacement management bits!
Total bits in cache = # slots × (8×K + T + 1 + 1)
        = 2I × (8×2O + T + 1 + 1) bits

---
DM Cache Example (1/5)
DM Cache Example (1/5)
Cache parameters:
  - Direct-mapped, address space of 64B, block size of 1 word, cache size of 4 words, write-through
TIO Breakdown:
  - 1 word = 4 bytes, so O = log2(4) = 2
  - Cache size / block size = 4, so I = log2(4) = 2
  - A = log2(64) = 6 bits, so T = 6 – 2 – 2 = 2
Bits in cache = 22 × (8×22 + 2 + 1) = 140 bits
XX
XX
XX
Memory Addresses:
Block address
[Speaker Notes: Compare with fully associative example from last lecture. This takes 140 bits to implement instead of 150 bits because of shorter Tag and no LRU bits.]

---
DM Cache Example (2/5)
DM Cache Example (2/5)
Cache parameters:
  - Direct-mapped, address space of 64B, block size of 1 word, cache size of 4 words, write-through
  - Offset – 2 bits, Index – 2 bits, Tag – 2 bits
35 bits per index/slot, 140 bits to implement
Offset
00
01
10
11
V	Tag	00	01	10	11
X	XX	0x??	0x??	0x??	0x??
X	XX	0x??	0x??	0x??	0x??
X	XX	0x??	0x??	0x??	0x??
X	XX	0x??	0x??	0x??	0x??
Index

---
DM Cache Example (3/5)
DM Cache Example (3/5)
Main Memory:
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Which blocks map to each row of the cache?
(see colors)
On a memory request:
(let’s say 0010112)
1) Take Index field (10)
2) Check if Valid bit is true in that row of cache
3) If valid, then check if Tag matches
Which blocks map to each row of the cache?
(see colors)
00
01
10
11
Cache:
Tag
Data
Valid
Index
Cache slots exactly match the Index field
Main Memory shown in blocks, so offset bits not shown (x’s)

---
DM Cache Example (4/5)
DM Cache Example (4/5)
Consider the sequence of memory address accesses
        0 2 4 8 20 16 0 2
Starting with a cold cache:
0
2
miss
hit
00
01
10
11
0	00	0x??	0x??	0x??	0x??
0	00	0x??	0x??	0x??	0x??
0	00	0x??	0x??	0x??	0x??
0	00	0x??	0x??	0x??	0x??
1	00	M[0]	M[1]	M[2]	M[3]
0	00	0x??	0x??	0x??	0x??
0	00	0x??	0x??	0x??	0x??
0	00	0x??	0x??	0x??	0x??
00
01
10
11
1	00	M[0]	M[1]	M[2]	M[3]
0	00	0x??	0x??	0x??	0x??
0	00	0x??	0x??	0x??	0x??
0	00	0x??	0x??	0x??	0x??
8
4
miss
miss
00
01
10
11
1	00	M[0]	M[1]	M[2]	M[3]
0	00	0x??	0x??	0x??	0x??
0	00	0x??	0x??	0x??	0x??
0	00	0x??	0x??	0x??	0x??
1	00	M[0]	M[1]	M[2]	M[3]
1	00	M[4]	M[5]	M[6]	M[7]
0	00	0x??	0x??	0x??	0x??
0	00	0x??	0x??	0x??	0x??
00
01
10
11
1	00	M[0]	M[1]	M[2]	M[3]
1	00	M[4]	M[5]	M[6]	M[7]
0	00	0x??	0x??	0x??	0x??
0	00	0x??	0x??	0x??	0x??
1	00	M[0]	M[1]	M[2]	M[3]
1	00	M[4]	M[5]	M[6]	M[7]
1	00	M[8]	M[9]	M[10]	M[11]
0	00	0x??	0x??	0x??	0x??

---
DM Cache Example (5/5)
DM Cache Example (5/5)
Consider the sequence of memory address accesses
        0 2 4 8 20 16 0 2
Starting with a cold cache:
M H M M
20
16
miss
miss
00
01
10
11
1	00	M[0]	M[1]	M[2]	M[3]
1	00	M[4]	M[5]	M[6]	M[7]
1	00	M[8]	M[9]	M[10]	M[11]
0	00	0x??	0x??	0x??	0x??
00
01
10
11
1	00	M[0]	M[1]	M[2]	M[3]
1	01	M[20]	M[21]	M[22]	M[23]
1	00	M[8]	M[9]	M[10]	M[11]
0	00	0x??	0x??	0x??	0x??
miss
hit
2
0
00
01
10
11
1	01	M[16]	M[17]	M[18]	M[19]
1	01	M[20]	M[21]	M[22]	M[23]
1	00	M[8]	M[9]	M[10]	M[11]
0	00	0x??	0x??	0x??	0x??
00
01
10
11
1	00	M[0]	M[1]	M[2]	M[3]
1	01	M[20]	M[21]	M[22]	M[23]
1	00	M[8]	M[9]	M[10]	M[11]
0	00	0x??	0x??	0x??	0x??
8 requests, 6 misses – last slot was never used!

---
Worst-Case for Direct-Mapped
Worst-Case for Direct-Mapped
- Cold DM $ that holds 4 1-word blocks
- Consider the memory accesses: 0, 16, 0, 16,...
HR of 0%
  - Ping pong effect: alternating requests that map into the same cache slot
Does fully associative have this problem?
0
   Miss
16
   Miss
0
   Miss
00 M[0-3]
00 M[0-3]
01 M[16-19]
. . .

---
Comparison So Far
Comparison So Far
Fully associative
  - Block can go into any slot
  - Must check ALL cache slots on request (“slow”)
  - TO breakdown (i.e. I = 0 bits)
  - “Worst case” still fills cache (more efficient)
Direct-mapped
  - Block goes into one specific slot (set by Index field)
  - Only check ONE cache slot on request (“fast”)
  - TIO breakdown
  - “Worst case” may only use 1 slot (less efficient)

---
Agenda
Agenda
- Direct-Mapped Caches
- Administrivia
- Set Associative Caches
- Cache Performance

---
Administrivia
Administrivia
Proj1 still due Sunday
  - My OH tomorrow “go until they finish (sorta)”
    - As long as there's a student with pertinent questions I'll hang around.
    - I won't stay later than 7pm (go to Andrew's office hours at that point)
HW4 will be released Friday, due next Sunday

---
Agenda
Agenda
- Direct-Mapped Caches
- Administrivia
- Set Associative Caches
- Cache Performance

---
Set Associative Caches
Set Associative Caches
Compromise!
  - More flexible than DM, more structured than FA
N-way set-associative: Divide $ into sets, each of which consists of N slots
  - Memory block maps to a set determined by Index field and is placed in any of the N slots of that set
  - Call N the associativity
  - New hash function:
    (block address) modulo (# sets in the cache)
  - Replacement policy applies to every set
[Speaker Notes: All of the tags of all of the elements of the set must be searched for a match.]

---
Effect of Associativity on TIO (1/2)
Effect of Associativity on TIO (1/2)
- Here we assume a cache of fixed size (C), fixed block size (K)
- Offset: Points to a byte in a block (same as before)
- Index: Instead of pointing to a slot, now points to a set, so I = log2(C/K/N)
  - Fully associative (1 set): 0 Index bits!
  - Direct-mapped (N = 1): max Index bits
  - Set associative: somewhere in-between
Tag: Remaining identifier bits (T = A – I – O)
[Speaker Notes: C = cache size, B = block size]

---
Effect of Associativity on TIO (2/2)
Effect of Associativity on TIO (2/2)
For a fixed-size cache, each increase by a factor of two in associativity doubles the number of blocks per set (i.e. the number of slots) and halves the number of sets – decreasing the size of the Index by 1 bit and increasing the size of the Tag by 1 bit
Tag
Index
Offset
Decreasing associativity
Fully associative
(only one set)
Direct mapped
(only one way)
Increasing associativity
Selects the set
Used for tag comparison
Selects the byte in the block
[Speaker Notes: For lecture In 2008, the greater size and power consumption of CAMs generally leads to 2-way and 4-way set associativity being built from standard SRAMs with comparators with 8-way and above being built using CAMs]

---
Example: Eight-Block Cache Configs
Example: Eight-Block Cache Configs
Total size of $ =
# sets × associativity
For fixed $ size, associativity ↑ means # sets ↓ and slots per set ↑
With 8 blocks, an 8-way set associative $ is same as a fully associative $

---
Block Placement Schemes
Block Placement Schemes
Place memory block 12 in a cache that holds 8 blocks
- Fully associative: Can go in any of the slots (all 1 set)
- Direct-mapped: Can only go in slot (12 mod 8) = 4
- 2-way set associative: Can go in either slot of set
  (12 mod 4) = 0

---
SA Cache Example (1/5)
SA Cache Example (1/5)
Cache parameters:
  - 2-way set associative, 6-bit addresses, 1-word blocks, 4-word cache, write-through
How many sets?
  - C/K/N = 4/1/2 = 2 sets
TIO Breakdown:
  - O = log2(4) = 2, I = log2(2) = 1,
  - T = 6 – 1 – 2 = 3
XXX
X
XX
Memory Addresses:
Block address

---
SA Cache Example (2/5)
SA Cache Example (2/5)
Cache parameters:
  - 2-way set associative, 6-bit addresses, 1-word blocks, 4-word cache, write-through
  - Offset – 2 bits, Index – 1 bit, Tag – 3 bits
36 bits per slot, 36*2+1 = 73 bits per set,
2*73 = 146 bits to implement
Offset
0
1
0
1
V	Tag	00	01	10	11
X	XXX	0x??	0x??	0x??	0x??
X	XXX	0x??	0x??	0x??	0x??
X	XXX	0x??	0x??	0x??	0x??
X	XXX	0x??	0x??	0x??	0x??
0
1
LRU
X
Index
LRU
X

---
SA Cache Example (3/5)
SA Cache Example (3/5)
Main Memory:
Each block maps into one set (either slot)
(see colors)
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
On a memory request:
(let’s say 001011two)
1) Take Index field (0)
2) For EACH slot in set, check valid bit,
then compare Tag
0
Cache:
Tag
Data
V
Slot
1
0
1
Set
0
1
Set numbers exactly match the Index field
Main Memory shown in blocks, so offset bits not shown (x’s)

---
SA Cache Example (4/5)
SA Cache Example (4/5)
Consider the sequence of memory address accesses
        0 2 4 8 20 16 0 2
Starting with a cold cache:
0
2
miss
hit
0
1
0
1
0
1
0	000	0x??	0x??	0x??	0x??
0	000	0x??	0x??	0x??	0x??
0	000	0x??	0x??	0x??	0x??
0	000	0x??	0x??	0x??	0x??
1	000	M[0]	M[1]	M[2]	M[3]
0	000	0x??	0x??	0x??	0x??
0	000	0x??	0x??	0x??	0x??
0	000	0x??	0x??	0x??	0x??
0
1
0
1
0
1
1	000	M[0]	M[1]	M[2]	M[3]
0	000	0x??	0x??	0x??	0x??
0	000	0x??	0x??	0x??	0x??
0	000	0x??	0x??	0x??	0x??
8
4
miss
miss
0
1
0
1
0
1
1	000	M[0]	M[1]	M[2]	M[3]
0	000	0x??	0x??	0x??	0x??
0	000	0x??	0x??	0x??	0x??
0	000	0x??	0x??	0x??	0x??
1	000	M[0]	M[1]	M[2]	M[3]
0	000	0x??	0x??	0x??	0x??
1	000	M[4]	M[5]	M[6]	M[7]
0	000	0x??	0x??	0x??	0x??
0
1
0
1
0
1
1	000	M[0]	M[1]	M[2]	M[3]
0	000	0x??	0x??	0x??	0x??
1	000	M[4]	M[5]	M[6]	M[7]
0	000	0x??	0x??	0x??	0x??
1	000	M[0]	M[1]	M[2]	M[3]
1	001	M[8]	M[9]	M[10]	M[11]
1	000	M[4]	M[5]	M[6]	M[7]
0	000	0x??	0x??	0x??	0x??

---
SA Cache Example (5/5)
SA Cache Example (5/5)
Consider the sequence of memory address accesses
        0 2 4 8 20 16 0 2
Starting with a cold cache:
M H M M
20
16
miss
miss
0
1
0
1
0
1
1	000	M[0]	M[1]	M[2]	M[3]
1	001	M[8]	M[9]	M[10]	M[11]
1	000	M[4]	M[5]	M[6]	M[7]
1	010	M[20]	M[21]	M[22]	M[23]
0
1
0
1
0
1
1	000	M[0]	M[1]	M[2]	M[3]
1	001	M[8]	M[9]	M[10]	M[11]
1	000	M[4]	M[5]	M[6]	M[7]
1	010	M[20]	M[21]	M[22]	M[23]
1	000	M[0]	M[1]	M[2]	M[3]
1	001	M[8]	M[9]	M[10]	M[11]
1	000	M[4]	M[5]	M[6]	M[7]
0	000	0x??	0x??	0x??	0x??
miss
hit
2
0
0
1
0
1
0
1
1	010	M[16]	M[17]	M[18]	M[19]
1	001	M[8]	M[9]	M[10]	M[11]
1	000	M[4]	M[5]	M[6]	M[7]
1	010	M[20]	M[21]	M[22]	M[23]
0
1
0
1
0
1
1	010	M[16]	M[17]	M[18]	M[19]
1	000	M[0]	M[1]	M[2]	M[3]
1	000	M[4]	M[5]	M[6]	M[7]
1	010	M[20]	M[21]	M[22]	M[23]
8 requests, 6 misses

---
Worst Case for Set Associative
Worst Case for Set Associative
Worst case for DM was repeating pattern of 2 into same cache slot (HR = 0/n)
  - Set associative for N > 1: HR = (n-2)/n
Worst case for N-way SA with LRU?
  - Repeating pattern of at least N+1 that maps into same set
  - Back to HR = 0:
0, 8, 16, 0, 8, …
M
M
M
M
M
001 M[8-11]
010 M[16-19]
000 M[0-3]
001 M[8-11]
000 M[0-3]
[Speaker Notes: For lecture Another sample string to try 0 1 2 3 0 8 11 0 3]

---
Question: What is the TIO breakdown for the following cache?
32-bit address space
32 KiB 4-way set associative cache
8 word blocks
21	8	3
(B)
19	8	5
(G)
19	10	3
(P)
17	10	5
(Y)
T	I	O

---
Get To Know Your Instructor
Technology Break

---
Agenda
Agenda
- Direct-Mapped Caches
- Administrivia
- Set Associative Caches
- Cache Performance

---
Cache Performance
Cache Performance
Two things hurt the performance of a cache:
  - Miss rate and miss penalty
  - Average Memory Access Time (AMAT): average time to access memory considering both hits and misses
AMAT = Hit time + Miss rate × Miss penalty
(abbreviated AMAT = HT + MR × MP)
- Goal 1: Examine how changing the different cache parameters affects our AMAT
- Goal 2: Examine how to optimize your code for better cache performance

---
AMAT Example
AMAT Example
Processor specs: 200 ps clock, MP of 50 clock cycles, MR of 0.02 misses/instruction, and HT of 1 clock cycle
AMAT = ???
Which improvement would be best?
  - 190 ps clock
  - MP of 40 clock cycles
  - MR of 0.015 misses/instruction
1 + 0.02 × 50 = 2 clock cycles = 400 ps
380 ps
360 ps
350 ps

---
Cache Parameter Example
Cache Parameter Effects
What is the potential impact of much larger cache on AMAT? (same block size)
  1. Increase HR
  2. Longer HT: smaller is faster
  - At some point, increase in hit time for a larger cache may overcome the improvement in hit rate, yielding a decrease in performance
Effect on TIO? Bits in cache? Cost?

---
Effect of Cache Performance on CPI
Effect of Cache Performance on CPI
Recall: CPU Performance
CPU Time = Instructions × CPI × Clock Cycle Time
- Include memory accesses in CPI:
CPIstall = CPIbase + Average Memory-stall Cycles
CPU Time = IC × CPIstall × CC
Simplified model for memory-stall cycles:
Memory-stall cycles
(IC)
(CC)
[Speaker Notes: Memory-stall clock cycles = Read-stall cycles + Write-stall cycles. Reasonable write buffer depth (e.g., four or more words) and a memory capable of accepting writes at a rate that significantly exceeds the average write frequency means write buffer stalls are small. Here we are assuming same MR and MP for reads and writes.]

---
CPI Example
CPI Example
Processor specs: CPIbase of 2, a 100 cycle MP, 36% load/store instructions, and 2% I$ and 4% D$ MRs
  - How many times per instruction do we access the I$? The D$?
  - MP is assumed the same for both I$ and D$
  - Memory-stall cycles will be sum of stall cycles for both I$ and D$
[Speaker Notes: I$ accessed at EVERY instruction (need to fetch from Code portion of memory!). D$ is accessed only on loads and stores. Naturally, you expect the I$ MR < D$ MR.]

---
CPI Example
CPI Example
Processor specs: CPIbase of 2, a 100 cycle MP, 36% load/store instructions, and 2% I$ and 4% D$ MRs
  - Memory-stall cycles
    = (100% × 2% + 36% × 4%) × 100 = 3.44
  - CPIstall = 2 + 3.44 = 5.44	(more than 2 x CPIbase!)
- What if the CPIbase is reduced to 1?
What if the D$ miss rate went up by 1%?
I$
D$
[Speaker Notes: If CPIbase = 1, CPIstall = 4.44, with memory-stall cycles accounting for 77.5% as opposed to 63.2%. If D$ MR = 0.05, then memory-stall cycles = 3.8 and CPIstall = 5.8. Memory-stall cycles now account for 65.5% of CPIstall.]

---
Impacts of Cache Performance
Impacts of Cache Performance
CPIstall = CPIbase + Memory-stall Cycles
Relative penalty of cache performance increases as processor performance improves (faster clock rate and/or lower CPIbase)
  - Relative contribution of CPIbase and memory-stall cycles to CPIstall
  - Memory speed unlikely to improve as fast as processor cycle time
What can we do to improve cache performance?
[Speaker Notes: For CPIbase = 1, then CPIstall = 4.44 and the amount of execution time spent on memory stalls would have risen from 3.44/5.44 = 63% to 3.44/4.44 = 77% For miss penalty of 200, memory stall cycles = 2% 200 + 36% x 4% x 200 = 6.88 so that CPIstall = 8.88 This assumes that hit time (so hit time is 1 cycle) is not a factor in determining cache performance. A larger cache would have a longer access time (if a lower miss rate), meaning either a slower clock cycle or more stages in the pipeline for memory access.]

---
Sources of Cache Misses: The 3Cs
Sources of Cache Misses: The 3Cs
Compulsory: (cold start or process migration, 1st reference)
  - First access to block impossible to avoid;
    Effect is small for long running programs
Capacity:
  - Cache cannot contain all blocks accessed by the program
Conflict: (collision)
  - Multiple memory locations mapped to the same cache location

---
The 3Cs: Design Solutions
The 3Cs: Design Solutions
Compulsory:
  - Increase block size (increases MP; too large blocks could increase MR)
Capacity:
  - Increase cache size (may increase HT)
Conflict:
  - Increase cache size
  - Increase associativity (may increase HT)

---
Summary
Summary
Set associativity determines flexibility of block placement
  - Fully associative: blocks can go anywhere
  - Direct-mapped: blocks go in one specific location
  - N-way: cache split into sets, each of which have n slots to place memory blocks
Cache Performance
  - AMAT = HT + MR × MP
  - CPU time = IC × CPIstall × CC
            = IC × (CPIbase + Memory-stall cycles) × CC