CS 61C: Great Ideas in
Computer Architecture
Functional Units,
Finite State Machines
Instructor: Alan Christopher

---
Review of Last Lecture
Review of Last Lecture
Synchronous Digital Systems
  - Pulse of a Clock controls flow of information
  - All signals are seen as either 0 or 1
- Hardware systems are constructed from Stateless Combinational Logic and Stateful “Memory” Logic (registers)
- Combinational Logic: equivalent circuit diagrams, truth tables, and Boolean expressions
  - Boolean Algebra allows minimization of gates
State registers implemented from Flip-flops

---
Dealing with Waveform Diagrams
Dealing with Waveform Diagrams
Easiest to start with CLK on top
  - Solve signal by signal, from inputs to outputs
  - Can only draw the waveform for a signal if all of its input waveforms are drawn
When does a signal update?
  - A state element updates based on CLK triggers
  - A combinational element updates ANY time ANY of its inputs changes

---
Example: T = 10 ns. tsetup = thold = 0. tclk-to-q = 1 ns.
tprop = 1 ns for all gates. Each “tick” below is 1 ns.
Solve for the waveform of the output Y.

---
Hardware Design Hierarchy
Hardware Design Hierarchy
system
control
datapath
code
registers
state
registers
combinational
logic
multiplexer
comparator
register
logic
switching
networks
Today

---
Agenda
Agenda
- State Elements Continued
- Administrivia
- Logisim Introduction
- Finite State Machines
- Multiplexers
- ALU Design
  - Adder/Subtracter

---
Model for Synchronous Systems
Model for Synchronous Systems
Collection of Combinational Logic blocks separated by registers
Feedback is optional depending on application
Clock (CLK): square wave that synchronizes the system
Clock signal connects only to clock input of registers
Register: several bits of state that samples input on rising edge of CLK

---
Accumulator Revisited
...Again
Accumulator Revisited
...Again
- reset signal shown
- In practice X might not arrive to the adder at the same time as Si-1
- Si temporarily is wrong, but register always captures correct value
- In good circuits, instability never happens around rising edge of clk

---
Register Timing Terms (Review)
Register Timing Terms (Review)
- Setup Time: how long the input must be stable before the CLK trigger for proper input read
- Hold Time: how long the input must be stable after the CLK trigger for proper input read
- “CLK-to-Q” Delay: how long it takes the output to change, measured from the CLK trigger

---
Where Does Timing Come From?
Where Does Timing Come From?
Example D flip-flop implementation:
Changing the D signal around the time E (CLK) changes can cause unexpected behavior

---
Maximum Clock Frequency
Maximum Clock Frequency
What is the max frequency of this circuit?
  - Limited by how much time needed to get correct Next State to Register
Max Delay =
Max Freq = 1/Max Delay
Setup Time
+ CLK-to-Q Delay
+ CL Delay
[Speaker Notes: Hold time is included in CLK-to-Q delay.]

---
The Critical Path
The Critical Path
- The critical path is the longest delay between any two registers in a circuit
- The clock period must be longer than this critical path, or the signal will not propagate properly to that next register
Critical Path =
CL Delay 1
+ CL Delay 2
+ CL Delay 3
+ Adder Delay
3
4
2
1
+
Reg
Reg

---
Pipelining and Clock Frequency (1/2)
Pipelining and Clock Frequency (1/2)
Clock period limited by propagation delay of adder and shifter
  - Add an extra register to reduce the critical path!
Timing:

---
Pipelining and Clock Frequency (2/2)
Pipelining and Clock Frequency (2/2)
Extra register allows higher clock freq (more outputs per sec)
However, takes two (shorter) clock cycles to produce first output (higher latency for initial output)
+ setup time
+ CLK-to-Q delay
+ CLK-to-Q delay
+ Adder delay
+ Shifter delay
+ setup time
+ CLK-to-Q delay

---
Pipelining Basics
Pipelining Basics
By adding more registers, break path into shorter “stages”
  - Aim is to reduce critical path
  - Signals take an additional clock cycle to propagate through each stage
New critical path must be calculated
  - Affected by placement of new pipelining registers
  - Faster clock rate => higher throughput (outputs)
  - More stages => higher startup latency
Pipelining tends to improve performance
  - More on this (application to CPUs) next week

---
Question: Want to run on 1 GHz processor.
tadd = 100 ps. tmult = 200 ps. tsetup = thold = 50 ps.
What is the maximum tclk-to-q we can use?
550 ps
(A)
750 ps
(B)
500 ps
(C)
700 ps
(D)

---
Agenda
Agenda
- State Elements Continued
- Administrivia
- Logisim Introduction
- Finite State Machines
- Multiplexers
- ALU Design
  - Adder/Subtracter

---
Administrivia
Administrivia
- HW5 will be posted today, due next Thursday
- Proj2-2 will be posted Friday/Saturday, due the following Sunday

---
Agenda
Agenda
- State Elements Continued
- Administrivia
- Logisim Introduction
- Finite State Machines
- Multiplexers
- ALU Design
  - Adder/Subtracter

---
Logisim
Logisim
Open-source (i.e. free!) “graphical tool for designing and simulating logic circuits”
  - Runs on Java on any computer
  - Download to your home computer via class login or the Logisim website (we are using version 2.7.1)
No programming involved
  - Unlike Verilog, which is a hardware description language (HDL)
  - Click and drag; still has its share of annoying quirks
http://ozark.hendrix.edu/~burch/logisim/

---
Gates in Logisim
Gates in Logisim
Click gate type, click to place
  - Can set options before placing or select gate later to change
Options
Types of Gates
bus width n
# inputs
labeling not necessary,
but can help

---
Registers in Logisim
Registers in Logisim
- Flip-flops and Registers in “Memory” folder
- 8-bit accumulator:

---
Wires in Logisim
Wires in Logisim
- Click and drag on existing port or wire
- Color schemes:
  - Gray: unconnected
  - Dark Green: low signal (0)
  - Light Green: high signal (1)
  - Red: error
  - Blue: undetermined signal
  - Orange: incompatible widths
- Tunnels: all tunnels with same label are connected
“Splitter” used to adjust bus widths

---
Common Mistakes in Logisim
Common Mistakes in Logisim
Connecting wires together
  - Crossing wires vs. connected wires
Losing track of which input is which
  - Mis-wiring a block (e.g. CLK to Enable)
  - Grabbing wrong wires off of splitter
Errors:

---
Agenda
Agenda
- State Elements Continued
- Administrivia
- Logisim Introduction
- Finite State Machines
- Multiplexers
- ALU Design
  - Adder/Subtracter

---
Finite State Machines (FSMs)
Finite State Machines (FSMs)
- You may have seen FSMs in other classes
- Function can be represented with a state transition diagram
- With combinational logic and registers,
  any FSM can be implemented
  in hardware!
. . .

---
FSM Overview
FSM Overview
An FSM (in this class) is defined by:
  - A set of states S	(circles)
  - An initial state s0 (only arrow not between states)
  - A transition function that maps from the current input and current state to the output and the next state	(arrows between states)
State transitions are controlled by the clock:
  - On each clock cycle the machine checks the inputs and generates a new state (could be same) and new output

---
Example: 3 Ones FSM
Example: 3 Ones FSM
FSM to detect 3 consecutive 1’s in the Input
States: S0, S1, S2
Initial State: S0
Transitions of form:
input/output

---
Hardware Implementation of FSM
Hardware Implementation of FSM
Register holds a representation of the FSM’s state
  - Must assign a unique bit pattern for each state
  - Output is present/current state (PS/CS)
  - Input is next state (NS)
Combinational Logic implements transition function (state transitions + output)
=
+

---
FSM: Combinational Logic
FSM: Combinational Logic
Read off transitions into Truth Table!
  - Inputs:	Current State (CS) and Input (In)
  - Outputs: Next State (NS) and Output (Out)
- Implement logic for EACH output (2 for NS, 1 for Out)
CS	In	NS	Out
00	0	00	0
00	1	01	0
01	0	00	0
01	1	10	0
10	0	00	0
10	1	00	1
[Speaker Notes: In lecture: Implement logic for Out (1 NOT, 2 AND gates)]

---
Unspecified Output Values (1/2)
Unspecified Output Values (1/2)
Our FSM has only 3 states
  - 2 entries in truth table are
    undefined/unspecified
Use symbol ‘X’ to mean it can
be either a 0 or 1
  - Make choice to simplify final
    expression
CS	In	NS	Out
00	0	00	0
00	1	01	0
01	0	00	0
01	1	10	0
10	0	00	0
10	1	00	1
11	0	XX	X
11	1	XX	X

---
Unspecified Output Values (2/2)
Unspecified Output Values (2/2)
Let’s find expression for NS1
  - Recall: 2-bit output is just a
    2-bit bus, which is just 2 wires
Boolean algebra:
  - NS1 = CS1’CS0In + CS1CS0In’
          + CS1CS0In
  - NS1 = CS0In
CS	In	NS	Out
00	0	00	0
00	1	01	0
01	0	00	0
01	1	10	0
10	0	00	0
10	1	00	1
11	0	XX	X
11	1	XX	X

---
3 Ones FSM in Hardware
3 Ones FSM in Hardware
  - 2-bit Register needed for state
  - CL: NS1 = CS0In, NS0 = CS1’CS0’In, Out = CS1In

---
Agenda
Agenda
- State Elements Continued
- Administrivia
- Logisim Introduction
- Finite State Machines
- Multiplexers
- ALU Design
  - Adder/Subtracter

---
Data Multiplexor
Data Multiplexor
Multiplexor (“MUX”) is a selector
  - Place one of multiple inputs onto output (N-to-1)
Shown below is an n-bit 2-to-1 MUX
  - Input S selects between two inputs of n bits each
This input is passed to output if selector bits match shown value

---
Implementing a 1-bit 2-to-1 MUX
Implementing a 1-bit 2-to-1 MUX
Boolean Expression:
Schematic:
Truth Table:
s	a	b	c
0	0	0	0
0	0	1	0
0	1	0	1
0	1	1	1
1	0	0	0
1	0	1	1
1	1	0	0
1	1	1	1
Circuit Diagram:

---
1-bit 4-to-1 MUX (1/2)
1-bit 4-to-1 MUX (1/2)
Schematic:
- Truth Table: How many rows?
- Boolean Expression:
  e = s1’s0’a + s1’s0b + s1s0’c + s1s0d
26=64

---
1-bit 4-to-1 MUX (2/2)
1-bit 4-to-1 MUX (2/2)
Can we leverage what we’ve previously built?
  - Alternative hierarchical approach:

---
Subcircuits Example
Subcircuits Example
Logisim equivalent of procedure or method
  - Every project is a hierarchy of subcircuits
Wiring Incomplete for legibility

---
Get To Know Your Instructor
Technology Break

---
Agenda
Agenda
- State Elements Continued
- Administrivia
- Logisim Introduction
- Finite State Machines
- Multiplexers
- ALU Design
  - Adder/Subtracter

---
Arithmetic and Logic Unit (ALU)
Arithmetic and Logic Unit (ALU)
Most processors contain a special logic block called the “Arithmetic and Logic Unit” (ALU)
  - We’ll show you an easy one that does ADD, SUB, bitwise AND, and bitwise OR
Schematic:
when S=00, R = A + B
when S=01, R = A – B
when S=10, R = A AND B
when S=11, R = A OR B

---
Simple ALU Schematic
Simple ALU Schematic
Notice that 3 values are ALWAYS calculated in parallel, but only 1 makes it to the Result

---
Adder/Subtractor: 1-bit LSB Adder
Adder/Subtractor: 1-bit LSB Adder
Carry-out bit

---
Adder/Subtractor: 1-bit Adder
Adder/Subtractor: 1-bit Adder
Here defining XOR of many inputs to be 1 when an odd number of inputs are 1
Possible carry-in c1

---
Adder/Subtractor: 1-bit Adder
Adder/Subtractor: 1-bit Adder
Circuit Diagrams:

---
N x 1-bit Adders  N-bit Adder
N x 1-bit Adders -> N-bit Adder
Connect CarryOuti-1 to CarryIni to chain adders:
b0
+
+
+

---
Two’s Complement Adder/Subtractor
Two’s Complement Adder/Subtractor
Subtraction accomplished by adding negated number:
+
+
+
x ^ 1 = x’
(flips the bits)
This signal is only
high when you
perform subtraction
Add 1
Where did this come from?

---
Detecting Overflow
Detecting Overflow
Unsigned overflow
On addition, if carry-out from MSB is 1
On subtraction, if carry-out from MSB is 0
This case is a lot harder to see than you might think
Signed overflow
Overflow from adding “large” positive numbers
Overflow from adding “large” negative numbers

---
Signed Overflow Examples (4-bit)
Signed Overflow Examples (4-bit)
Overflow from two positive numbers:
0111 + 0111, 0111 + 0001, 0100 + 0100.
Carry-out from the 2nd MSB (but not MSB)
pos + pos ≠ neg
Overflow from two negative numbers:
1000 + 1000, 1000 + 1111, 1011 + 1011.
Carry-out from the MSB (but not 2nd MSB)
neg + neg ≠ pos
Expression for signed overflow: Cn XOR Cn-1

---
Summary
Summary
Critical path constrains clock rate
  - Timing constants: setup, hold, and clk-to-q times
  - Can adjust with extra registers (pipelining)
Finite State Machines extremely useful
  - Can implement systems with Register + CL
Use MUXes to select among input
  - S input bits selects one of 2S inputs
  - Each input is a bus n-bits wide
Build n-bit adder out of chained 1-bit adders
  - Can also do subtraction with additional SUB signal