CS 61C: Great Ideas in
Computer Architecture
MIPS CPU Datapath,
Control Introduction
Instructor: Alan Christopher

---
Review of Last Lecture
Review of Last Lecture
Critical path constrains clock rate
  - Timing constants: setup, hold, and clk-to-q times
  - Can adjust with extra registers (pipelining)
Finite State Machines examples of sequential logic circuits
  - Can implement systems with Register + CL
Use MUXes to select among input
  - S input bits selects one of 2S inputs
Build n-bit adder out of chained 1-bit adders
  - Can also do subtraction and overflow detection!

---
Hardware Design Hierarchy
Hardware Design Hierarchy
system
control
datapath
code
registers
state
registers
combinational
logic
multiplexer
comparator
register
logic
switching
networks
Today

---
Agenda
Agenda
- Processor Design
- Administrivia
- Datapath Overview
- Assembling the Datapath
- Control Introduction

---
Five Components of a Computer
Five Components of a Computer
Components a computer needs to work
  - Control
  - Datapath
  - Memory
  - Input
  - Output
Computer
 Processor
Memory
Devices
Control
(“brain”)
Input
Datapath
(“brawn”)
Output
[Speaker Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts: 1) The input devices bring the data from the outside world into the computer. 2) These data are kept in the computer’s memory until... 3) The datapath request and process them. 4) The operation of the datapath is controlled by the computer’s controller. All the work done by the computer will NOT do us any good unless we can get the data back to the outside world, so… 5) Getting the data back to the outside world is the job of the output devices. The most COMMON way to connect these 5 components together is to use a network of busses.]

---
The Processor
The Processor
Processor (CPU): Implements the instructions of the Instruction Set Architecture (ISA)
  - Datapath: part of the processor that contains the hardware necessary to perform operations required by the processor (“the brawn”)
  - Control: part of the processor (also in hardware) which tells the datapath what needs to be done (“the brain”)

---
Processor Design Process
Processor Design Process
Five steps to design a processor:
1. Analyze instruction set ->
datapath requirements
2. Select set of datapath
components & establish
clock methodology
3. Assemble datapath meeting
the requirements
4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer
5. Assemble the control logic
    - Formulate Logic Equations
    - Design Circuits
Control
Datapath
Memory
Processor
Input
Output
Now

---
The MIPS-lite Instruction Subset
The MIPS-lite Instruction Subset
ADDU and SUBU
  - addu rd,rs,rt
  - subu rd,rs,rt
OR Immediate:
  - ori rt,rs,imm16
LOAD and
STORE Word
  - lw rt,rs,imm16
  - sw rt,rs,imm16
- BRANCH:
  - beq rs,rt,imm16
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

---
Register Transfer Language (RTL)
Register Transfer Language (RTL)
- All start by fetching the instruction:
- RTL gives the meaning of the instructions:
R-format: {op, rs, rt, rd, shamt, funct}  MEM[ PC ]
I-format: {op, rs, rt, imm16}  MEM[ PC ]
Inst Register Transfers
ADDU R[rd]R[rs]+R[rt]; PCPC+4
SUBU R[rd]R[rs]–R[rt]; PCPC+4
ORI R[rt]R[rs]|zero_ext(imm16); PCPC+4
LOAD R[rt]MEM[R[rs]+sign_ext(imm16)]; PCPC+4
STORE MEM[R[rs]+sign_ext(imm16)]R[rt]; PCPC+4
BEQ if ( R[rs] == R[rt] )
        then PCPC+4 + (sign_ext(imm16) || 00)
        else PCPC+4

---
Step 1: Requirements of the Instruction Set
Step 1: Requirements of the Instruction Set
Memory (MEM)
  - Instructions & data (separate: in reality just caches)
  - Load from and store to
Registers (32 32-bit regs)
  - Read rs and rt
  - Write rt or rd
PC
  - Add 4 (+ maybe extended immediate)
- Extender (sign/zero extend)
- Add/Sub/OR unit for operation on register(s) or extended immediate
  - Compare if registers equal?

---
Generic Datapath Layout
Generic Datapath Layout
- Break up the process of “executing an instruction”
  - Smaller phases easier to design and modify independently
1. Instruction
Fetch
2. Decode/
    Register Read
3. Execute
4. Memory
5. Register
     Write
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

---
Step 2: Components of the Datapath
Step 2: Components of the Datapath
Combinational Elements
  - Gates and wires
- State Elements + Clock
- Building Blocks:
32
A
B
32
Y
32
Select
MUX
Multiplexer
ALU
32
32
A
B
32
Result
OP
ALU
32
32
A
B
32
Sum
CarryOut
CarryIn
Adder
Adder

---
ALU Requirements
ALU Requirements
MIPS-lite: add, sub, OR, equality
ADDU	R[rd] = R[rs] + R[rt]; ...
SUBU	R[rd] = R[rs] – R[rt]; ...
ORI	R[rt] = R[rs] | zero_ext(Imm16)...
BEQ	if ( R[rs] == R[rt] )
- Equality test: Use subtraction and implement output to indicate if result is 0
- P&H also adds AND, Set Less Than
  (1 if A < B, 0 otherwise)
- Can see ALU from P&H C.5 (on CD)

---
Storage Element: Idealized Memory
Storage Element: Idealized Memory
Memory (idealized)
  - One input bus: Data In
  - One output bus: Data Out
Memory access:
  - Read: Write Enable = 0, data at Address is placed on Data Out
  - Write: Write Enable = 1, Data In written to Address
Clock input (CLK)
  - CLK input is a factor ONLY during write operation
  - During read, behaves as a combinational logic block: Address valid => Data Out valid after “access time”
CLK
Data In
Write Enable
32
32
DataOut
Address

---
Storage Element: Register
Storage Element: Register
As seen in Logisim intro
  - N-bit input and output buses
  - Write Enable input
- Write Enable:
  - De-asserted (0): Data Out will not change
  - Asserted (1): Data In value placed onto Data Out after CLK trigger
CLK
Data In
Write Enable
N
N
Data Out

---
Storage Element: Register File
Storage Element: Register File
Register File consists of 32 registers:
  - Output buses busA and busB
  - Input bus busW
Register selection
  - Place data of register RA (number) onto busA
  - Place data of register RB (number) onto busB
  - Store data on busW into register RW (number) when Write Enable is 1
Clock input (CLK)
  - CLK input is a factor ONLY during write operation
  - During read, behaves as a combinational logic block:
    RA or RB valid => busA or busB valid after “access time”
Clk
busW
Write Enable
32
32
busA
32
busB
5
5
5
RW
RA
RB
32 x 32-bit
Registers

---
Agenda
Agenda
- Processor Design
- Administrivia
- Datapath Overview
- Assembling the Datapath
- Control Introduction

---
Administrivia
Administrivia
- HW 5 due Thursday
- Project 2 due Sunday
- Project 1 and Midterm graded
  - See piazza for details
- No lab on Thursday – work on HW/project

---
Agenda
Agenda
- Processor Design
- Administrivia
- Datapath Overview
- Assembling the Datapath
- Control Introduction
- Clocking Methodology

---
Datapath Overview (1/5)
Datapath Overview (1/5)
Phase 1: Instruction Fetch (IF)
  - Fetch 32-bit instruction from memory
  - Increment PC (PC = PC + 4)
1. Instruction
Fetch
2. Decode/
    Register Read
3. Execute
4. Memory
5. Register
     Write
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

---
Datapath Overview (2/5)
Datapath Overview (2/5)
Phase 2: Instruction Decode (ID)
  - Read the opcode and appropriate fields from the instruction
  - Gather all necessary registers values from Register File
1. Instruction
Fetch
2. Decode/
    Register Read
3. Execute
4. Memory
5. Register
     Write
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

---
Datapath Overview (3/5)
Datapath Overview (3/5)
Phase 3: Execute (EX)
  - ALU performs operations: arithmetic (+,-,*,/), shifting, logical (&,|), comparisons (slt,==)
  - Also calculates addresses for loads and stores
1. Instruction
Fetch
2. Decode/
    Register Read
3. Execute
4. Memory
5. Register
     Write
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

---
Datapath Overview (4/5)
Datapath Overview (4/5)
Phase 4: Memory Access (MEM)
  - Only load and store instructions do anything during this phase; the others remain idle or skip this phase
  - Should hopefully be fast due to caches
1. Instruction
Fetch
2. Decode/
    Register Read
3. Execute
4. Memory
5. Register
     Write
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

---
Datapath Overview (5/5)
Datapath Overview (5/5)
Phase 5: Register Write (WB for “write back”)
  - Write the instruction result back into the Register File
  - Those that don’t (e.g. sw, j, beq) remain idle or skip this phase
1. Instruction
Fetch
2. Decode/
    Register Read
3. Execute
4. Memory
5. Register
     Write
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

---
Why Five Stages?
Why Five Stages?
Could we have a different number of stages?
  - Yes, and other architectures do
So why does MIPS have five if instructions tend to idle for at least one stage?
  - The five stages are the union of all the operations needed by all the instructions
  - There is one instruction that uses all five stages: load (lw/lb)

---
Agenda
Agenda
- Processor Design
- Administrivia
- Datapath Overview
- Assembling the Datapath
- Control Introduction

---
Step 3:  Assembling the Datapath
Step 3: Assembling the Datapath
Assemble datapath to meet RTL requirements
  - Exact requirements will change based on ISA
  - Here we will examine each instruction of MIPS-lite
The datapath is all of the hardware components and wiring necessary to carry out ALL of the different instructions
  - Make sure all components (e.g. RegFile, ALU) have access to all necessary signals and buses
  - Control will make sure instructions are properly executed (the decision making)

---
Datapath by Instruction
Datapath by Instruction
All instructions: Instruction Fetch (IF)
  - Fetch the Instruction: Mem[PC]
  - Update the program counter:
    - Sequential Code:
      PC  PC + 4
    - Branch and Jump:
      PC  “something else”
Next Address
Logic
32
Instruction
Address
Instruction
Memory
PC
CLK

---
Datapath by Instruction
Datapath by Instruction
All instructions: Instruction Decode (ID)
  - Pull off all relevant fields from instruction to make available to other parts of datapath
    - MIPS-lite only has R-format and I-format
    - Control will sort out the proper routing (discussed later)
Wires and
Splitters
32
Instr
5
5
5
5
6
16
6
opcode
rs
rt
rd
shamt
funct
imm

---
Step 3: Add & Subtract
Step 3: Add & Subtract
- ADDU R[rd]R[rs]+R[rt];
- Hardware needed:
  - Instruction Mem and PC (already shown)
  - Register File (RegFile) for read and write
  - ALU for add/subtract
CLK
busW
32
32
busA
32
busB
5
5
5
RW
RA
RB
32 x 32-bit
Registers
32
Result
ALU
32
A
32
B

---
Step 3: Add & Subtract
Step 3: Add & Subtract
- ADDU R[rd]R[rs]+R[rt];
- Connections:
  - RegFile and ALU Inputs
  - Connect RegFile and ALU
  - RegWr (1) and ALUctr (ADD/SUB) set by control in ID
5
5
5
busA
RW
RA
RB
busW
32
Result
32 x 32-bit
Registers
32
busB
32
CLK
32
ALUctr
RegWr
rs
rt
rd
ALU
32
A
32
B

---
Step 3: Or Immediate
Step 3: Or Immediate
- ORI R[rt]R[rs]|zero_ext(Imm16);
- Is the hardware below sufficient?
  - Zero extend imm16?
  - Pass imm16 to input of ALU?
  - Write result to rt?
5
5
5
busA
RW
RA
RB
busW
32
Result
32 x 32-bit
Registers
32
busB
32
CLK
32
ALUctr
RegWr
rs
rt
rd
ALU

---
Step 3: Or Immediate
Step 3: Or Immediate
- ORI R[rt]R[rs]|zero_ext(Imm16);
- Add new hardware:
  - Still support add/sub
  - New control signals:
    RegDst, ALUSrc
32
ALUctr
CLK
RegWr
32
32
busA
32
busB
5
5
RW
RA
RB
RegFile
rs
rt
rt
rd
ZeroExt
32
16
imm16
ALUSrc
0
1
0
1
ALU
5
RegDst
2:1 MUX
How to implement this?

---
Step 3: Load
Step 3: Load
- LOAD R[rt]MEM[R[rs]+sign_ext(Imm16)];
- Hardware sufficient?
  - Sign extend imm16?
  - Where’s MEM?
32
ALUctr
CLK
RegWr
32
32
busA
32
busB
5
5
RW
RA
RB
RegFile
rs
rt
rt
rd
ZeroExt
32
16
imm16
ALUSrc
0
1
0
1
ALU
5
RegDst

---
Step 3: Load
Step 3: Load
- LOAD R[rt]MEM[R[rs]+sign_ext(Imm16)];
- New control signals: ExtOp, MemWr, MemtoReg
32
ALUctr
CLK
busW
RegWr
32
32
busA
32
busB
5
5
RW
RA
RB
RegFile
rs
rt
rt
rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
CLK
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Addr
Data
Memory
5
???
Must now
also handle
sign extension
What goes here during a store?

---
Step 3: Store
Step 3: Store
- STORE MEM[R[rs]+sign_ext(Imm16)]R[rt];
- Connect busB to Data In (no extra control needed!)
32
ALUctr
CLK
busW
RegWr
32
32
busA
32
busB
5
5
RW
RA
RB
RegFile
rs
rt
rt
rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
CLK
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Addr
Data
Memory
5

---
Step 3: Branch If Equal
Step 3: Branch If Equal
- BEQ if(R[rs]==R[rt]) then PCPC+4 + (sign_ext(Imm16) || 00)
- Need comparison output from ALU
32
ALUctr
CLK
busW
RegWr
32
32
busA
32
busB
5
5
RW
RA
RB
RegFile
rs
rt
rt
rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
CLK
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Addr
Data
Memory
5
zero
=

---
Step 3: Branch If Equal
Step 3: Branch If Equal
- BEQ if(R[rs]==R[rt]) then PCPC+4 + (sign_ext(Imm16) || 00)
- Revisit “next address logic”:
Next Address
Logic
32
Instruction
Address
Instruction
Memory
PC
CLK
imm16
CLK
PC
4
PC Ext
Adder
Adder
MUX
0
1
32
Instruction
Addr
Instruction
Memory
Instr Fetch Unit
???
nPC_sel
zero
How to hook these up?
Sign extend
and ×4

---
Step 3: Branch If Equal
Step 3: Branch If Equal
- BEQ if(R[rs]==R[rt]) then PCPC+4 + (sign_ext(Imm16) || 00)
- Revisit “next address logic”:
  - nPC_sel should be 1 if branch, 0 otherwise
nPC_sel	zero	MUX
0	0	0
0	1	0
1	0	0
1	1	1
nPC_sel
zero
MUX
PC+4
0
nextPC (nPC)
1
PC+4 + branchAddr
How does this change
if we add bne?
MUX

---
Step 3: Branch If Equal
Step 3: Branch If Equal
- BEQ if(R[rs]==R[rt]) then PCPC+4 + (sign_ext(Imm16) || 00)
- Revisit “next address logic”:
nPC_sel
zero
4
Instruction
0
32
1
CLK
Instr Fetch Unit
imm16
PC
PC Ext
Adder
Adder
MUX
Addr
Instruction
Memory

---
Get To Know Your Staff
Technology Break

---
Agenda
Agenda
- Processor Design
- Administrivia
- Datapath Overview
- Assembling the Datapath
- Control Introduction

---
Processor Design Process
Processor Design Process
Five steps to design a processor:
1. Analyze instruction set ->
datapath requirements
2. Select set of datapath
components & establish
clock methodology
3. Assemble datapath meeting
the requirements
4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer
5. Assemble the control logic
    - Formulate Logic Equations
    - Design Circuits
Control
Datapath
Memory
Processor
Input
Output
Now

---
Control
Control
Need to make sure that correct parts of the datapath are being used for each instruction
  - Have seen control signals in datapath used to select inputs and operations
  - For now, focus on what value each control signal should be for each instruction in the ISA
    - Next lecture, we will see how to implement the proper combinational logic to implement the control

---
Desired Datapath For addu
Desired Datapath For addu
R[rd]R[rs]+R[rt];
+4
1
ADD
1
0
0
0
X
32
ALUctr=
CLK
busW
RegWr=
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst=
Extender
32
16
imm16
ALUSrc=
ExtOp=
MemtoReg=
CLK
Data In
32
MemWr=
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
Instruction <31:0>
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
nPC_sel=
Instr
Fetch
Unit
CLK

---
Desired Datapath For ori
Desired Datapath For ori
R[rt]R[rs]|ZeroExt(imm16);
+4
0
OR
1
0
0
1
Zero
32
ALUctr=
CLK
busW
RegWr=
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst=
Extender
32
16
imm16
ALUSrc=
ExtOp=
MemtoReg=
CLK
Data In
32
MemWr=
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
Instruction <31:0>
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
nPC_sel=
Instr
Fetch
Unit
CLK

---
Desired Datapath For load
Desired Datapath For load
R[rt]MEM{R[rs]+SignExt[imm16]};
+4
0
ADD
1
1
0
1
Sign
32
ALUctr=
CLK
busW
RegWr=
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst=
Extender
32
16
imm16
ALUSrc=
ExtOp=
MemtoReg=
CLK
Data In
32
MemWr=
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
Instruction <31:0>
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
nPC_sel=
Instr
Fetch
Unit
CLK

---
Desired Datapath For store
Desired Datapath For store
MEM{R[rs]+SignExt[imm16]}R[rt];
+4
X
0
ADD
X
1
1
Sign
32
ALUctr=
CLK
busW
RegWr=
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst=
Extender
32
16
imm16
ALUSrc=
ExtOp=
MemtoReg=
CLK
Data In
32
MemWr=
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
Instruction <31:0>
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
nPC_sel=
Instr
Fetch
Unit
CLK

---
Desired Datapath For beq
Desired Datapath For beq
BEQ if(R[rs]==R[rt]) then PCPC+4 + (sign_ext(Imm16) || 00)
Br
X
SUB
0
X
0
0
X
32
ALUctr=
CLK
busW
RegWr=
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst=
Extender
32
16
imm16
ALUSrc=
ExtOp=
MemtoReg=
CLK
Data In
32
MemWr=
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
Instruction <31:0>
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
nPC_sel=
Instr
Fetch
Unit
CLK

---
MIPS-lite Datapath Control Signals
MIPS-lite Datapath Control Signals
ExtOp:	0 -> “zero”; 1 -> “sign”
ALUsrc:	0 -> busB;	1 -> imm16
ALUctr:	“ADD”, “SUB”, “OR”
nPC_sel:	0 -> +4; 1 -> branch
MemWr:	1 -> write memory
MemtoReg:	0 -> ALU; 1 -> Mem
RegDst:	0 -> “rt”; 1 -> “rd”
RegWr:	1 -> write register
32
ALUctr
CLK
busW
RegWr
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
CLK
Data In
32
MemWr
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
nPC_sel
Instr
Fetch
Unit
CLK

---
Question: Which statement is TRUE about the MIPS-lite ISA?
When not in use, parts of the datapath cease to carry a value.
(B)
Adding the instruction jr will not change the datapath.
(G)
All control signals will be don’t care (‘X’) in at least one instruction.
(P)
Adding the instruction addiu will not change the datapath.
(Y)

---
Summary (1/2)
Summary (1/2)
Five steps to design a processor:
  1. Analyze instruction set ->
     datapath requirements
  2. Select set of datapath
     components & establish
     clock methodology
  3. Assemble datapath meeting
     the requirements
  4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer
  5. Assemble the control logic
    - Formulate Logic Equations
    - Design Circuits
Control
Datapath
Memory
Processor
Input
Output

---
Summary (2/2)
Summary (2/2)
Determining control signals
  - Any time a datapath element has an input that changes behavior, it requires a control signal
    (e.g. ALU operation, read/write)
  - Any time you need to pass a different input based on the instruction, add a MUX with a control signal as the selector
    (e.g. next PC, ALU input, register to write to)
Your datapath and control signals will change based on your ISA