## Slide 1: CS 61C: Great Ideas in Computer Architecture Multiple Instruction Issue/Virtual Memory Introduction
Guest Lecturer/TA: Andrew Luo

## Slide 2: Great Idea #4: Parallelism
Smart Phone
Warehouse Scale Computer
Leverage Parallelism &
Achieve High Performance
Core
…
Memory
Input/Output
Computer
Core
Parallel Requests
  Assigned to computer
  e.g. search “Garcia”
Parallel Threads
  Assigned to core
  e.g. lookup, ads
Parallel Instructions
  > 1 instruction @ one time
  e.g. 5 pipelined instructions
Parallel Data
  > 1 data item @ one time
  e.g. add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Software Hardware
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A0+B0
A1+B1
A2+B2
A3+B3
Logic Gates

## Slide 3: Review of Last Lecture (1/2)
A hazard is a situation that prevents the next instruction from executing in the next clock cycle
  Structural hazard
    A required resource is needed by multiple instructions in different stages
  Data hazard
    Data dependency between instructions
    A later instruction requires the result of an earlier instruction
  Control hazard
    The flow of execution depends on the previous instruction (ex. jumps, branches)

## Slide 4: Review of Last Lecture (2/2)
Hazards hurt the performance of pipelined processors
  Stalling can be applied to any hazard, but hurt performance… better solutions?
  Structural hazards
    Have separate structures for each stage
  Data hazards
    Forwarding
  Control hazards
    Branch prediction (mitigates), branch delay slot

## Slide 5: Agenda
Multiple Issue
Administrivia
Virtual Memory Introduction

## Slide 6: Multiple Issue
Modern processors can issue and execute multiple instructions per clock cycle
CPI < 1 (superscalar), so can use Instructions Per Cycle (IPC) instead
e.g. 4 GHz 4-way multiple-issue can execute 16 billion IPS with peak CPI = 0.25 and peak IPC = 4
  But dependencies and structural hazards reduce this in practice

## Slide 7: Multiple Issue
Static multiple issue
  Compiler reorders independent/commutative instructions to be issued together
  Compiler detects and avoids hazards
Dynamic multiple issue
  CPU examines pipeline and chooses instructions to reorder/issue
  CPU can resolve hazards at runtime

## Slide 8: Superscalar Laundry: Parallel per stage
More resources, HW to match mix of parallel tasks?
T
a
s
k
O
r
d
e
r
12
2 AM
6 PM
7
8
9
10
11
1
Time
B
C
D
A
E
F
(light clothing)
(dark clothing)
(very dirty clothing)
(light clothing)
(dark clothing)
(very dirty clothing)
30
30
30
30
30

## Slide 9: Pipeline Depth and Issue Width
Intel Processors over Time
Microprocessor | Year | Clock Rate | Pipeline Stages | Issue width | Cores | Power
i486 | 1989 | 25 MHz | 5 | 1 | 1 | 5W
Pentium | 1993 | 66 MHz | 5 | 2 | 1 | 10W
Pentium Pro | 1997 | 200 MHz | 10 | 3 | 1 | 29W
P4 Willamette | 2001 | 2000 MHz | 22 | 3 | 1 | 75W
P4 Prescott | 2004 | 3600 MHz | 31 | 3 | 1 | 103W
Core 2 Conroe | 2006 | 2930 MHz | 12-14 | 4* | 2 | 75W
Core 2 Penryn | 2008 | 2930 MHz | 12-14 | 4* | 4 | 95W
Core i7 Westmere | 2010 | 3460 MHz | 14 | 4* | 6 | 130W
Xeon Sandy Bridge | 2012 | 3100 MHz | 14-19 | 4* | 8 | 150W
Xeon Ivy Bridge | 2014 | 2800 MHz | 14-19 | 4* | 15 | 155W
Notes: *Intel’s instruction decoders are interesting in that they are assymetric

## Slide 10: Pipeline Depth and Issue Width
Chart: 
| 1989 | 1993 | 1997 | 2001 | 2004 | 2006 | 2008 | 2010
Clock | 25 | 66 | 200 | 2000 | 3600 | 2930 | 2930 | 3460
Power | 5 | 10 | 29 | 75 | 103 | 75 | 95 | 130
Pipeline Stages | 5 | 5 | 10 | 22 | 31 | 14 | 16 | 16
Issue width | 1 | 2 | 3 | 3 | 3 | 4 | 4 | 4
Cores | 1 | 1 | 1 | 1 | 1 | 2 | 4 | 6

## Slide 11: Static Multiple Issue
  Compiler reorders independent/commutative instructions to be issued together (an “issue packet”)
  Group of instructions that can be issued on a single cycle
  Determined by structural resources required
  Specifies multiple concurrent operations

## Slide 12: Scheduling Static Multiple Issue
Compiler must remove some/all hazards
  Reorder instructions into issue packets
  No dependencies within a packet
  Possibly some dependencies between packets
    Varies between ISAs; compiler must know!
  Pad with nops if necessary

## Slide 13: Dynamic Multiple Issue
Used in “superscalar” processors
CPU decides whether to issue 0, 1, 2, … instructions each cycle
  Goal is to avoid structural and data hazards
Avoids need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU

## Slide 14: Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example: lw $t0, 20($s2) addu $t1, $t0, $t2 subu $s4, $s4, $t3 slti $t5, $s4, 20
  Can start subu while addu is waiting for lw
Especially useful on cache misses; can execute many instructions while waiting!

## Slide 15: Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
Not all stalls are predicable
  e.g. cache misses
Can’t always schedule around branches
  Branch outcome is dynamically determined by I/O
Different implementations of an ISA have different latencies and hazards
  Forward compatibility and optimizations

## Slide 16: Speculation
“Guess” what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right and roll back if necessary
Examples:
  Speculate on branch outcome (Branch Prediction)
    Roll back if path taken is different
  Speculate on load
    Load into an internal register before instruction to minimize time waiting for memory
Can be done in hardware or by compiler
Common to static and dynamic multiple issue

## Slide 17: Not a Simple Linear Pipeline
3 major units operating in parallel:
Instruction fetch and issue unit
  Issues instructions in program order
Many parallel functional (execution) units
  Each unit has an input buffer called a Reservation Station
  Holds operands and records the operation
  Can execute instructions out-of-order (OOO)
Commit unit
  Saves results from functional units in Reorder Buffers
  Stores results once branch resolved so OK to execute
  Commits results in program order

## Slide 18: Out-of-Order Execution (1/2)
Can also unroll loops in hardware
Fetch instructions in program order (≤ 4/clock)
Predict branches as taken/untaken
To avoid hazards on registers, rename registers using a set of internal registers (≈ 80 registers)
Collection of renamed instructions might execute in a window (≈ 60 instructions)

## Slide 19: Out-of-Order Execution (2/2)
Execute instructions with ready operands in 1 of multiple functional units (ALUs, FPUs, Ld/St)
Buffer results of executed instructions until predicted branches are resolved in reorder buffer
If predicted branch correctly, commit results in program order
If predicted branch incorrectly, discard all dependent results and start with correct PC

## Slide 20: Dynamically Scheduled CPU
Results also sent to any waiting reservation stations (think: forwarding!)
Reorder buffer for register and memory writes
Can supply operands for issued instructions
Preserves dependencies
Wait here until all operands available
Branch prediction,
Register renaming
Execute…
… and Hold

## Slide 21: Out-Of-Order Intel
All use O-O-O since 2001
Microprocessor | Year | Clock Rate | Pipeline Stages | Issue width | Out-of-order/ Speculation | Cores | Power
i486 | 1989 | 25 MHz | 5 | 1 | No | 1 | 5W
Pentium | 1993 | 66 MHz | 5 | 2 | No | 1 | 10W
Pentium Pro | 1997 | 200 MHz | 10 | 3 | Yes | 1 | 29W
P4 Willamette | 2001 | 2000 MHz | 22 | 3 | Yes | 1 | 75W
P4 Prescott | 2004 | 3600 MHz | 31 | 3 | Yes | 1 | 103W
Core 2 Conroe | 2006 | 2930 MHz | 12-14 | 4* | Yes | 2 | 75W
Core 2 Penryn | 2008 | 2930 MHz | 12-14 | 4* | Yes | 4 | 95W
Core i7 Westmere | 2010 | 3460 MHz | 14 | 4* | Yes | 6 | 130W
Xeon Sandy Bridge | 2012 | 3100 MHz | 14-19 | 4* | Yes | 8 | 150W
Xeon Ivy Bridge | 2014 | 2800 MHz | 14-19 | 4* | Yes | 15 | 155W

## Slide 22: Intel Nehalem Microarchitecture

## Slide 23: Intel Nehalem Pipeline Flow

## Slide 24: Does Multiple Issue Work?
Yes, but not as much as we’d like
Programs have real dependencies that limit ILP
Some dependencies are hard to eliminate
  e.g. pointer aliasing (restrict keyword helps)
Some parallelism is hard to expose
  Limited window size during instruction issue
Memory delays and limited bandwidth
  Hard to keep pipelines full
Speculation can help if done well

## Slide 25: Agenda
Multiple Issue
Administrivia
Virtual Memory Introduction

## Slide 26: Administrivia
HW5 due tonight
Project 2 (Performance Optimization) due Sunday
No lab today
  TAs will be in lab to check-off make up labs
    Highly encouraged to make up labs today if you’re behind – treated as Tuesday checkoff for lateness
Project 3 (Pipelined Processor in Logisim) released Friday/Saturday

## Slide 27: Agenda
Multiple Issue
Administrivia
Virtual Memory Introduction

## Slide 28: Memory Hierarchy
Regs
L2 Cache
Memory
Disk
Tape
Instr Operands
Blocks
Pages
Files
Upper Level
Lower Level
Faster
Larger
L1 Cache
Blocks
Next Up:
Virtual Memory
Earlier: Caches

## Slide 29: Memory Hierarchy Requirements
Principle of Locality
  Allows caches to offer (close to) speed of cache memory with size of DRAM memory
  Can we use this at the next level to give speed of DRAM memory with size of Disk memory?
What other things do we need from our memory system?

## Slide 30: Memory Hierarchy Requirements
Allow multiple processes to simultaneously occupy memory and provide protection
  Don’t let programs read from or write to each other’s memories
Give each program the illusion that it has its own private address space
  Suppose a program has base address 0x00400000, then different processes each think their code resides at the same address
  Each program must have a different view of memory

## Slide 31: Virtual Memory
Next level in the memory hierarchy
  Provides illusion of very large main memory
  Working set of “pages” residing in main memory (subset of all pages residing on disk)
Main goal: Avoid reaching all the way back to disk as much as possible
Additional goals:
  Let OS share memory among many programs and protect them from each other
  Each process thinks it has all the memory to itself

## Slide 32: Virtual to Physical Address Translation
Each program operates in its own virtual address space and thinks it’s the only program running
Each is protected from the other
OS can decide where each goes in memory
Hardware gives virtual  physical mapping
Program operates in its virtual address space
Virtual
Address (VA)
(inst. fetch
load, store)
HW mapping
Physical
Address (PA)
(inst. fetch
load, store)
Physical memory (including caches)

## Slide 33: VM Analogy (1/2)
Trying to find a book in the UCB library system
Book title is like virtual address (VA)
  What you want/are requesting
Book call number is like physical address (PA)
  Where it is actually located
Card catalogue is like a page table (PT)
  Maps from book title to call number
  Does not contain the actual that data you want
  The catalogue itself takes up space in the library

## Slide 34: VM Analogy (2/2)
Indication of current location within the library system is like valid bit
  Valid if in current library (main memory) vs. invalid if in another branch (disk)
  Found on the card in the card catalogue
Availability/terms of use like access rights
  What you are allowed to do with the book (ability to check out, duration, etc.)
  Also found on the card in the card catalogue

## Slide 35: Mapping VM to PM
Divide into equal sized chunks (usually 4-8 KiB)
Any chunk of Virtual Memory can be assigned to any chunk of Physical Memory (“page”)
0
Physical Memory
¥
Virtual Memory
Code
Static
Heap
Stack
64 MB
0

## Slide 36: Paging Organization
Addr
Trans
MAP
page 0
4 Ki
4 Ki
4 Ki
0x00000
0x01000
0x1F000
Virtual Memory
Virtual
Address
page 1
page 31
4 Ki
0x02000
page 2
...
...
...
page 0
0x0000
0x1000
0x7000
Physical
Address
Physical
Memory
4 Ki
4 Ki
4 Ki
page 1
page 7
...
...
...
Here assume page size is 4 KiB
  Page is both unit of mapping and unit of transfer between disk and physical memory

## Slide 37: Virtual Memory Mapping Function
How large is main memory? Disk?
  Don’t know! Designed to be interchangeable components
  Need a system that works regardless of sizes
Use lookup table (page table) to deal with arbitrary mapping
  Index lookup table by # of pages in VM (not all entries will be used/valid)
  Size of PM will affect size of stored translation

## Slide 38: Address Mapping
Pages are aligned in memory
  Border address of each page has same lowest bits
  Page size (P bytes) is same in VM and PM, so denote lowest PO = log2(P) bits as page offset
Use remaining upper address bits in mapping
  Tells you which page you want (similar to Tag)
Page Offset
Virtual Page #
Page Offset
Physical Page #
Same Size
Not necessarily the same size

## Slide 39: Address Mapping: Page Table
Page Table functionality:
  Incoming request is Virtual Address (VA), want Physical Address (PA)
  Physical Offset = Virtual Offset (page-aligned)
  So just swap Virtual Page Number (VPN) for Physical Page Number (PPN)
Implementation?
  Use VPN as index into PT
  Store PPN and management bits (Valid, Access Rights)
  Does NOT store actual data (the data sits in PM)

## Slide 40: Page Table Layout
V | AR | PPN
X | XX | 
Virtual Address:
VPN
offset
Page Table
1) Index into PT using VPN
2) Check Valid and Access Rights bits
+
3) Combine PPN and offset
Physical
Address
4) Use PA to access memory

## Slide 41: Page Table Entry Format
Contains either PPN or indication not in main memory
Valid = Valid page table entry
  1  virtual page is in physical memory
  0  OS needs to fetch page from disk
Access Rights checked on every access to see if allowed (provides protection)
  Read Only: Can read, but not write page
  Read/Write: Read or write data on page
  Executable: Can fetch instructions from page

## Slide 42: Page Tables
A page table (PT) contains the mapping of virtual addresses to physical addresses
Where should PT be located?
  Physical memory, so faster to access and can be shared by multiple processors
The OS maintains the PTs
  Each process has its own page table
    “State” of a process is PC, all registers, and PT
  OS stores address of the PT of the current process in the Page Table Base Register

## Slide 43: Paging/Virtual Memory Multiple Processes
User B: Virtual Memory
¥
Code
Static
Heap
Stack
0
Code
Static
Heap
Stack
Page
Table A
Page
Table B
User A: Virtual Memory
¥
0
0
Physical
Memory
64 MB

## Slide 44: Caches vs. Virtual Memory
Caches Virtual Memory
Block Page
Cache Miss Page Fault
Block Size: 32-64B Page Size: 4KiB-8KiB
Placement: Direct Mapped, Fully Associative N-way Set Associative (almost always)
Replacement: LRU or Random LRU
Write Thru or Back Write Back

## Slide 45: Technology Break

## Slide 46: Notes on Page Table
OS must reserve “Swap Space” on disk for each process
To grow a process, ask Operating System
  If unused pages, OS uses them first
  If not, OS swaps some old pages to disk
  (Least Recently Used to pick pages to swap)
Each process has own Page Table
Will add details, but Page Table is essence of Virtual Memory

## Slide 47: Why would a process need to “grow”?
A program’s address space contains 4 regions:
  stack: local variables, grows downward
  heap: space requested for pointers via malloc() ; resizes dynamically, grows upward
  static data: variables declared outside main, does not grow or shrink
  code: loaded when program starts, does not change
code
static data
heap
stack
For now, OS somehow prevents accesses between stack and heap (gray hash lines).
~ FFFF FFFFhex
~ 0hex

## Slide 48: Virtual Memory and Caches
Physical memory is slow, so we cache data
  Why not do the same with the page table?
Translation Lookaside Buffer (TLB) is the equivalent of cache for the page table

## Slide 49: Virtual to Physical Address Translation
Check TLB
Check page tables (in main memory)
Page fault – OS handles
OS: Check disk
OS: Swap on disk/Segmentation fault

## Slide 50: Translation Look-Aside Buffers (TLBs)
TLBs usually small, typically 128 - 256 entries
Like any other cache, the TLB can be direct mapped, set associative, or fully associative
Processor
TLB
Lookup
Cache
Main
Memory
VA
PA
miss
hit
data
Trans-
lation
hit
miss
On TLB miss, get page table entry from main memory

## Slide 51: Context Switching and VM
Context Switching now requires that both the TLB and caches be flushed
  In reality, TLB entries have a context tag

## Slide 52: Peer Instruction
Locality is important yet different for cache and virtual memory (VM): temporal locality for caches but spatial locality for VM
VM helps both with security and cost
12
blue) FF
green) FT
purple) TF
yellow) TT
Notes: Answer: [correct=5, TFF] Individual (6, 3, 6, 3, 34, 37, 7, 4)% & Team (9, 4, 4, 4, 39, 34, 0, 7)%
A: T [18/82 & 25/75] (The game breaks up very quickly into separate, independent games -- big win to solve separated & put together)
B: F [80/20 & 86/14] (The game tree grows exponentially! A better static evaluator can make all the difference!)
C: F [53/57 & 52/48] (If you're just looking for the best move, just keep theBestMove around [ala memoizing max])

## Slide 53: Peer Instruction Answer
Locality is important yet different for cache and virtual memory (VM): temporal locality for caches but spatial locality for VM
VM helps both with security and cost
F A L S E
1. No. Both for VM and cache
2. Yes. Protection and a bit smaller memory
T R U E
12
blue) FF
green) FT
purple) TF
yellow) TT

## Slide 54: Summary
More aggressive performance options:
  Longer pipelines
  Superscalar (multiple issue)
  Out-of-order execution
  Speculation
Virtual memory bridges memory and disk
  Provides illusion of independent address spaces to processes and protects them from each other
  VA to PA using Page Table
  TLB