## Slide 1: CS 61C: Great Ideas in Computer Architecture Lecture 5: Intro to Assembly Language, MIPS Intro
Instructor: Sagar Karandikar
sagark@eecs.berkeley.edu
http://inst.eecs.berkeley.edu/~cs61c

## Slide 2: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
Logic Circuit Description (Circuit Schematic Diagrams)

## Slide 3: Assembly Language
Basic job of a CPU: execute lots of instructions.
Instructions are the primitive operations that the CPU may execute.
Different CPUs implement different sets of instructions. The set of instructions a particular CPU implements is an Instruction Set Architecture (ISA).
  Examples: ARM, Intel x86, MIPS, RISC-V, IBM/Motorola PowerPC (old Mac), Intel IA64, ...

## Slide 4: Instruction Set Architectures
Early trend was to add more and more instructions to new CPUs to do elaborate operations
  VAX architecture had an instruction to multiply polynomials!
RISC philosophy (Cocke IBM, Patterson, Hennessy, 1980s) – Reduced Instruction Set Computing
  Keep the instruction set small and simple, makes it easier to build fast hardware.
  Let software do complicated operations by composing simpler ones.

## Slide 5: MIPS Architecture
MIPS – semiconductor company that built one of the first commercial RISC architectures
We will study the MIPS architecture in some detail in this class (upper-div arch classes like 150, 152 use a similar ISA, RISC-V)
Why MIPS instead of Intel x86?
  MIPS is simple, elegant. Don’t want to get bogged down in gritty details.
  MIPS widely used in embedded apps, x86 little used in embedded, and more embedded computers than PCs

## Slide 6: Assembly Variables: Registers
Unlike HLL like C or Java, assembly cannot use variables
  Why not? Keep Hardware Simple
Assembly Operands are registers
  Limited number of special locations built directly into the hardware
  Operations can only be performed on these!
Benefit: Since registers are directly in hardware, they are very fast (faster than 1 ns - light travels 30cm in 1 ns!!! )

## Slide 7: Number of MIPS Registers
Drawback: Since registers are in hardware, there are a predetermined number of them
  Solution: MIPS code must be very carefully put together to efficiently use registers
32 registers in MIPS
  Why 32? Smaller is faster, but too small is bad. Goldilocks problem.
Each MIPS register is 32 bits wide
  Groups of 32 bits called a word in MIPS

## Slide 8: Names of MIPS Registers
Registers are numbered from 0 to 31
Each register can be referred to by number or name
Number references:
  $0, $1, $2, … $30, $31
For now:
  $16 - $23 $s0 - $s7 (correspond to C variables)
  $8 - $15  $t0 - $t7 (correspond to temporary variables)
  Later will explain other 16 register names
In general, use names to make your code more readable

## Slide 9: C, Java variables vs. registers
In C (and most High Level Languages) variables declared first and given a type
  Example: int fahr, celsius; char a, b, c, d, e;
Each variable can ONLY represent a value of the type it was declared as (cannot mix and match int and char variables).
In Assembly Language, registers have no type; operation determines how register contents are treated

## Slide 10: Addition and Subtraction of Integers
Addition in Assembly
  Example: add $s0,$s1,$s2 (in MIPS)
  Equivalent to: a = b + c (in C)
  where C variables ⇔ MIPS registers are:
  a ⇔ $s0, b ⇔ $s1, c ⇔ $s2
Subtraction in Assembly
  Example: sub $s3,$s4,$s5 (in MIPS)
  Equivalent to: d = e - f (in C)
  where C variables ⇔ MIPS registers are: d ⇔ $s3, e ⇔ $s4, f ⇔ $s5

## Slide 11: Addition and Subtraction of Integers Example 1
How to do the following C statement?
a = b + c + d - e;
Break into multiple instructions
  add $t0, $s1, $s2 # temp = b + c
  add $t0, $t0, $s3 # temp = temp + d
  sub $s0, $t0, $s4 # a = temp - e
A single line of C may break up into several lines of MIPS.
Notice the use of temporary registers – don’t want to modify the variable registers $s
Everything after the hash mark on each line is ignored (comments)

## Slide 12: Immediates
Immediates are numerical constants.
They appear often in code, so there are special instructions for them.
Add Immediate:
  addi $s0,$s1,-10 (in MIPS)
  f = g - 10 (in C)
  where MIPS registers $s0,$s1 are associated with C variables f, g
Syntax similar to add instruction, except that last argument is a number instead of a register.
  add $s0,$s1,$zero (in MIPS)
  f = g (in C)

## Slide 13: Overflow in Arithmetic
Reminder: Overflow occurs when there is a “mistake” in arithmetic due to the limited precision in computers.
Example (4-bit unsigned numbers):
  15 1111
  + 3 + 0011
  18 10010
But we don’t have room for 5-bit solution, so the solution would be 0010, which is +2, and “wrong”.

## Slide 14: Overflow handling in MIPS
Some languages detect overflow (Ada), some don’t (most C implementations)
MIPS solution is 2 kinds of arithmetic instructions:
  These cause overflow to be detected
    add (add)
    add immediate (addi)
    subtract (sub)
  These do not cause overflow detection
    add unsigned (addu)
    add immediate unsigned (addiu)
    subtract unsigned (subu)
Compiler selects appropriate arithmetic
  MIPS C compilers produce addu, addiu, subu

## Slide 15: Data Transfer: Load from and Store to memory
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data = Store to memory
Read Data = Load from
memory
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data

## Slide 16: Memory Addresses are in Bytes
0
1
2
3
…
Lots of data is smaller than 32 bits, but rarely smaller than 8 bits – works fine if everything is a multiple of 8 bits
8 bit chunk is called a byte
(1 word = 4 bytes)
Memory addresses are really in bytes, not words
Word addresses are 4 bytes apart
  Word address is same as address of leftmost byte (i.e. Big-endian)
0
4
8
12
…
1
5
9
13
…
2
6
10
14
…
3
7
11
15
…
Addr of lowest byte in word is addr of word

## Slide 17: Transfer from Memory to Register
C code
int A[100];
g = h + A[3];
Using Load Word (lw) in MIPS:
lw $t0,12($s3) # Temp reg $t0 gets A[3]
add $s1,$s2,$t0 # g = h + A[3]
Note: $s3 – base register (pointer)
12 – offset in bytes
Offset must be a constant known at assembly time
Notes: 80 – 5 (Clicker) – 3 (News/Administrativia) = 72 (36 slides max)
Clicker at 20 (half+)

## Slide 18: Transfer from Register to Memory
C code
int A[100];
A[10] = h + A[3];
Using Store Word (sw) in MIPS:
lw $t0,12($s3) # Temp reg $t0 gets A[3]
add $t0,$s2,$t0 # Temp reg $t0 gets h + A[3]
sw $t0, 40($s3) # A[10] = h + A[3]
Note: $s3 – base register (pointer)
12,40 – offsets in bytes
$s3+12 and $s3+40 must be multiples of 4
Notes: 80 – 5 (Clicker) – 3 (News/Administrativia) = 72 (36 slides max)
Clicker at 20 (half+)

## Slide 19: Loading and Storing bytes
In addition to word data transfers (lw, sw), MIPS has byte data transfers:
  load byte: lb
  store byte: sb
Same format as lw, sw
E.g., lb $s0, 3($s1)
  contents of memory location with address = sum of “3” + contents of register $s1 is copied to the low byte position of register $s0.
byte loaded
zzz zzzz
x
…is copied to “sign-extend”
This bit
xxxx xxxx xxxx xxxx xxxx xxxx
$s0:

## Slide 20: Speed of Registers vs. Memory
Given that
  Registers: 32 words (128 Bytes)
  Memory: Billions of bytes (2 GB to 8 GB on laptop)
and the RISC principle is…
  Smaller is faster
How much faster are registers than memory??
About 100-500 times faster!
  in terms of latency of one access

## Slide 21: How many hours h on Homework 0?
A: 0 ≤ h < 5
B: 5 ≤ h < 10
C: 10 ≤ h < 15
D: 15 ≤ h < 20
E: 20 ≤ h

## Slide 22: Clickers/Peer Instruction
  We want to translate *x = *y +1 into MIPS
  (x, y pointers to ints, stored in: $s0 $s1)
  A: addi $s0,$s1,1
  B: lw $s0,1($s1)
  sw $s1,0($s0)
  C: lw $t0,0($s1)
  addi $t0,$t0,1
  sw $t0,0($s0)
  D: sw $t0,0($s1)
  addi $t0,$t0, 1
  lw $t0,0($s0)
  E: lw $s0,1($t0)
  sw $s1,0($t0)
Notes: Answer: [correct=c]
We must first load the contents of y’s pointee into a temp variable [$t0], which is 5. Then we have to store $t0 back into x’s pointee

## Slide 23: Break

## Slide 24: MIPS Logical Instructions
Logical operations | C operators | Java operators | MIPS instructions
Bit-by-bit AND | & | & | and
Bit-by-bit OR | ¦ | ¦ | or
Bit-by-bit NOT | ~ | ~ | not
Shift left | << | << | sll
Shift right | >> | >>> | srl
Useful to operate on fields of bits within a word
  e.g., characters within a word (8 bits)
Operations to pack /unpack bits into words
Called logical operations

## Slide 25: Logic Shifting
Shift Left: sll $s1,$s2,2 #s1=s2<<2
  Store in $s1 the value from $s2 shifted 2 bits to the left (they fall off end), inserting 0’s on right; << in C.
    Before: 0000 0002hex 0000 0000 0000 0000 0000 0000 0000 0010two
  After: 0000 0008hex 0000 0000 0000 0000 0000 0000 0000 1000two
  What arithmetic effect does shift left have?
Shift Right: srl is opposite shift; >>

## Slide 26: Arithmetic Shifting
Shift right arithmetic moves n bits to the right (insert high order sign bit into empty bits)
For example, if register $s0 contained
  1111 1111 1111 1111 1111 1111 1110 0111two= -25ten
If executed sra $s0, $s0, 4, result is:
1111 1111 1111 1111 1111 1111 1111 1110two= -2ten
  Unfortunately, this is NOT same as dividing by 2n
    Fails for odd negative numbers
    C arithmetic semantics is that division should round towards 0
Notes: \

## Slide 27: Computer Decision Making
Based on computation, do something different
In programming languages: if-statement
MIPS: if-statement instruction is
beq register1,register2,L1
means: go to statement labeled L1 if (value in register1) == (value in register2)
….otherwise, go to next statement
beq stands for branch if equal
Other instruction: bne for branch if not equal

## Slide 28: Types of Branches
Branch – change of control flow
Conditional Branch – change control flow depending on outcome of comparison
  branch if equal (beq) or branch if not equal (bne)
Unconditional Branch – always branch
  a MIPS instruction for this: jump (j)

## Slide 29: Example if Statement
Assuming translations below, compile if block
f → $s0 g → $s1 h → $s2
i → $s3 j → $s4
if (i == j) bne $s3,$s4,Exit
f = g + h; add $s0,$s1,$s2
Exit:
May need to negate branch condition

## Slide 30: Example if-else Statement
Assuming translations below, compile
f → $s0 g → $s1 h → $s2
i → $s3 j → $s4
if (i == j) bne $s3,$s4,Else
f = g + h; add $s0,$s1,$s2
else j Exit
f = g – h; Else: sub $s0,$s1,$s2
Exit:
Notes: trace all the paths in the c code through assembly

## Slide 31: Administrivia
Hopefully everyone completed HW0
HW1 out
Proj 1 out
  Make sure you test your code on hive machines, that’s where we’ll grade them
First Guerrilla Session this Thursday (07/02) from 5-7pm in the Woz
  Optional (not part of EPA)
  Covers Number Rep and MIPS

## Slide 32: Administrivia
Midterm one week from Thursday
  In this room, at this time
  One 8.5”x11” handwritten cheatsheet
  We’ll provide a MIPS green sheet
  No electronics
  Covers up to and including this Thursday’s lecture (07/02)
  TA-led review session on Monday 07/06 from 5-8pm in HP Auditorium
Feedback form at the end of lab 2 – tell us how lecture, disc, and lab are going

## Slide 33: CS61C In the News MIPS steers spacecraft to Pluto
4 MIPS R3000 32bit CPUs
  Command and Data handling
  Guidance and Control
Launched 2006, first pics in July 2015
http://www.electronicsweekly.com/news/military-aerospace-electronics/mips-steers-spacecraft-pluto-2015-01/

## Slide 34: CS61C in the News RISC-V Workshop
Notes: ARM license fees

## Slide 35: CS61C in the News RISC-V Workshop
Workshop happening right now at International House
A modest goal: To become the industry standard ISA (replacing x86, ARM, MIPS, etc.)
CS150, CS152, CS250, CS252 use RISC-V

## Slide 36: CS61C in the News pt. 2

## Slide 37: Inequalities in MIPS
Until now, we’ve only tested equalities (== and != in C). General programs need to test < and > as well.
Introduce MIPS Inequality Instruction:
  “Set on Less Than”
  Syntax: slt reg1,reg2,reg3
  Meaning: if (reg2 < reg3) reg1 = 1; else reg1 = 0;
  “set” means “change to 1”, “reset” means “change to 0”.

## Slide 38: Inequalities in MIPS Cont.
How do we use this? Compile by hand: if (g < h) goto Less; #g:$s0, h:$s1
Answer: compiled MIPS code…
slt $t0,$s0,$s1 # $t0 = 1 if g<h bne $t0,$zero,Less # if $t0!=0 goto Less
Register $zero always contains the value 0, so bne and beq often use it for comparison after an slt instruction
sltu treats registers as unsigned

## Slide 39: Immediates in Inequalities
slti an immediate version of slt to test against constants
  Loop: . . . slti $t0,$s0,1 # $t0 = 1 if # $s0<1 beq $t0,$zero,Loop # goto Loop # if $t0==0 # (if ($s0>=1))

## Slide 40: Loops in C/Assembly
Simple loop in C; A[] is an array of ints
  do { g = g + A[i]; i = i + j; } while (i != h);
Use this mapping: g, h, i, j, &A[0] $s1, $s2, $s3, $s4, $s5
Loop: sll $t1,$s3,2 # $t1= 4*i addu $t1,$t1,$s5 # $t1=addr A+4i lw $t1,0($t1) # $t1=A[i] add $s1,$s1,$t1 # g=g+A[i] addu $s3,$s3,$s4 # i=i+j bne $s3,$s2,Loop # goto Loop # if i!=h

## Slide 41: Which of the following are true for the addiu instruction?
1: The instruction performs a different operation at the hardware level than add (excluding overflow reporting)
2: The instruction tells the hardware not to report an overflow
3: The instruction sign extends the immediate
A: F, F, F
B: T, T, T
C: F, T, F
D: F, T, T
E: T, F, F

## Slide 42: And In Conclusion …
Computer words and vocabulary are called instructions and instruction set respectively
MIPS is example RISC instruction set in this class
Rigid format: 1 operation, 2 source operands, 1 destination
  add,sub,mul,div,and,or,sll,srl,sra
  lw,sw,lb,sb to move data to/from registers from/to memory
  beq, bne, j, slt, slti for decision/flow control
Simple mappings from arithmetic expressions, array access, if-then-else in C to MIPS instructions