## Slide 1: CS 61C: Great Ideas in Computer Architecture Lecture 7: MIPS Instruction Formats
Instructor: Sagar Karandikar
sagark@eecs.berkeley.edu
http://inst.eecs.berkeley.edu/~cs61c

## Slide 2: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
Logic Circuit Description (Circuit Schematic Diagrams)

## Slide 3: Review: Allocating Space on Stack
C has two storage classes: automatic and static
  Automatic variables are local to function and discarded when function exits
  Static variables exist across exits from and entries to procedures
Use stack for automatic (local) variables that don’t fit in registers
Procedure frame or activation record: segment of stack with saved registers and local variables
Some MIPS compilers use a frame pointer ($fp) to point to first word of frame

## Slide 4: Stack Before, During, After Call

## Slide 5: Using the Stack (1/2)
So we have a register $sp which always points to the last used space in the stack.
To use stack, we decrement this pointer by the amount of space we need and then fill it with info.
So, how do we compile this?
  int sumSquare(int x, int y) { return mult(x,x)+ y; }

## Slide 6: Using the Stack (2/2)
Hand-compile sumSquare: addi $sp,$sp,-8 # space on stack sw $ra, 4($sp) # save ret addr sw $a1, 0($sp) # save y add $a1,$a0,$zero # mult(x,x) jal mult # call mult lw $a1, 0($sp) # restore y add $v0,$v0,$a1 # mult()+y lw $ra, 4($sp) # get ret addr addi $sp,$sp,8 # restore stack jr $ra mult: ...
  int sumSquare(int x, int y) { return mult(x,x)+ y; }
“push”
“pop”

## Slide 7: Basic Structure of a Function
entry_label: addi $sp,$sp, -framesize sw $ra, framesize-4($sp) # save $ra save other regs if need be
...
restore other regs if need be lw $ra, framesize-4($sp) # restore $ra addi $sp,$sp, framesize jr $ra
Epilogue
Prologue
Body (call other functions…)
ra
memory

## Slide 8: Where is the Stack in Memory?
MIPS convention
Stack starts in high memory and grows down
  Hexadecimal (base 16) : 7fff fffchex
MIPS programs (text segment) in low end
  0040 0000hex
static data segment (constants and other static variables) above text for static variables
  MIPS convention global pointer ($gp) points to static
Heap above static for data structures that grow and shrink ; grows up to high addresses

## Slide 9: MIPS Memory Allocation

## Slide 10: Register Allocation and Numbering

## Slide 11: Note about setting $ra
Your green sheet says that jal instructions set $ra to PC + 8, a result of an optimization we’ll discuss later
Unless otherwise stated, we will assume that $ra is set to PC + 4 by jal

## Slide 12: Administrivia
Hopefully everyone completed HW0
HW1 out
Proj 1 out
  Make sure you test your code on hive machines, that’s where we’ll grade them
First Guerrilla Session this Thursday (07/02) from 5-7pm in the Woz
  Optional (not part of EPA)
  Covers Number Rep and MIPS

## Slide 13: Administrivia
Midterm one week from Thursday
  In this room, at this time
  One 8.5”x11” handwritten cheatsheet
  We’ll provide a MIPS green sheet
  No electronics
  Covers up to and including this Thursday’s lecture (07/02)
  TA-led review session on Monday 07/06 from 5-8pm in HP Auditorium
Proj 2 Team Registration on Piazza

## Slide 14: My Personal Study Advice
Review slides, book, worksheets, etc. and add to your cheatsheet as you do so
  This step is not the end
Take a mock exam in the allotted time, using only your cheatsheet
Go over solutions, look at why the answers are what they are (especially for questions you answered incorrectly)
Update cheatsheet as necessary
if (time != midterm1_time) goto 2;
Notes: see hkn for old exams

## Slide 15: In the News: 1,000 year life Blu-Ray Discs
Verbatim and Milleniata launch MDISC 100GB Blu-ray optical media with >1,000 year lifetime
“average lifetime of significantly more than 2,000 years with no more than one failure per 100,000 discs expected, after more than 1,000 years at 250C (770F) and 50 per cent relative humidity.”

## Slide 16: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
Logic Circuit Description (Circuit Schematic Diagrams)

## Slide 17: Agenda
The green sheet
Review the Stored-Program Concept
Instruction Formats
  R Type
  I Type
    Dealing with large immediates
  J Type
Conclusion

## Slide 18: Let’s look at the green sheet

## Slide 19: Big Idea: Stored-Program Computer
  Instructions are represented as bit patterns - can think of these as numbers.
  Therefore, entire programs can be stored in memory to be read or written just like data.
  Can reprogram quickly (seconds), don’t have to rewire computer (days)
  Known as the “von Neumann” computers after widely distributed tech report on EDVAC project
First Draft of a Report on the EDVAC
by
John von Neumann
Contract No. W–670–ORD–4926
Between the
United States Army Ordnance Department and the
University of Pennsylvania
Moore School of Electrical Engineering
University of Pennsylvania
June 30, 1945

## Slide 20: Consequence #1: Everything Addressed
Since all instructions and data are stored in memory, everything has a memory address: instructions, data words
  both branches and jumps use these
C pointers are just memory addresses: they can point to anything in memory
  Unconstrained use of addresses can lead to nasty bugs; up to you in C; limited in Java by language design
One register keeps address of instruction being executed: “Program Counter” (PC)
  Basically a pointer to memory: Intel calls it Instruction Pointer (a better name)

## Slide 21: Consequence #2: Binary Compatibility
Programs are distributed in binary form
  Programs bound to specific instruction set
  Different version for Macintoshes and PCs
New machines want to run old programs (“binaries”) as well as programs compiled to new instructions
Leads to “backward-compatible” instruction set evolving over time
Selection of Intel 8086 in 1981 for 1st IBM PC is major reason latest PCs still use 80x86 instruction set (Pentium 4); could still run program from 1981 PC today

## Slide 22: Instructions as Numbers (1/2)
Currently all data we work with is in words (32-bit chunks):
  Each register is a word.
  lw and sw both access memory one word at a time.
So how do we represent instructions?
  Remember: Computer only understands 1s and 0s, so “add $t0,$0,$0” is meaningless.
  MIPS/RISC seeks simplicity: since data is in words, make instructions be fixed-size 32-bit words also

## Slide 23: Instructions as Numbers (2/2)
One word is 32 bits, so divide instruction word into “fields”.
Each field tells processor something about instruction.
We could define different fields for each instruction, but MIPS seeks simplicity, so define 3 basic types of instruction formats:
  R-format
  I-format
  J-format

## Slide 24: Instruction Formats
I-format: used for instructions with immediates, lw and sw (since offset counts as an immediate), and branches (beq and bne),
  (but not the shift instructions; later)
J-format: used for j and jal
R-format: used for all other instructions
It will soon become clear why the instructions have been partitioned in this way.

## Slide 25: R-Format Instructions (1/5)
Define “fields” of the following number of bits each: 6 + 5 + 5 + 5 + 5 + 6 = 32
For simplicity, each field has a name:
Important: On these slides and in book, each field is viewed as a 5- or 6-bit unsigned integer, not as part of a 32-bit integer.
  Consequence: 5-bit fields can represent any number 0-31, while 6-bit fields can represent any number 0-63.
6
5
5
5
6
5
opcode
rs
rt
rd
funct
shamt

## Slide 26: R-Format Instructions (2/5)
What do these field integer values tell us?
  opcode: partially specifies what instruction it is
    Note: This number is equal to 0 for all R-Format instructions.
  funct: combined with opcode, this number exactly specifies the instruction
Question: Why aren’t opcode and funct a single 12-bit field?
  We’ll answer this later.

## Slide 27: R-Format Instructions (3/5)
More fields:
  rs (Source Register): usually used to specify register containing first operand
  rt (Target Register): usually used to specify register containing second operand (note that name is misleading)
  rd (Destination Register): usually used to specify register which will receive result of computation

## Slide 28: R-Format Instructions (4/5)
Notes about register fields:
  Each register field is exactly 5 bits, which means that it can specify any unsigned integer in the range 0-31. Each of these fields specifies one of the 32 registers by number.
  The word “usually” was used because there are exceptions that we’ll see later. E.g.,
    mult and div have nothing important in the rd field since the dest registers are hi and lo
    mfhi and mflo have nothing important in the rs and rt fields since the source is determined by the instruction (see COD)

## Slide 29: R-Format Instructions (5/5)
Final field:
  shamt: This field contains the amount a shift instruction will shift by. Shifting a 32-bit word by more than 31 is useless, so this field is only 5 bits (so it can represent the numbers 0-31).
  This field is set to 0 in all but the shift instructions.
For a detailed description of field usage for each instruction, see green insert in COD (You can bring with you to all exams)

## Slide 30: R-Format Example (1/2)
MIPS Instruction:
  add $8,$9,$10
  opcode = 0 (look up in table in book)
  funct = 32 (look up in table in book)
  rd = 8 (destination)
  rs = 9 (first operand)
  rt = 10 (second operand)
  shamt = 0 (not a shift)

## Slide 31: R-Format Example (2/2)
MIPS Instruction:
  add $8,$9,$10
  Decimal number per field representation:
  Binary number per field representation:
  hex representation: 012A 4020hex
  decimal representation: 19,546,144ten
  Called a Machine Language Instruction
0
9
10
8
32
0
000000
01001
01010
01000
100000
00000
hex

## Slide 32: I-Format Instructions (1/4)
What about instructions with immediates?
  5-bit field only represents numbers up to the value 31: immediates may be much larger than this
  Ideally, MIPS would have only one instruction format (for simplicity): unfortunately, we need to compromise
Define new instruction format that is partially consistent with R-format:
  First notice that, if instruction has immediate, then it uses at most 2 registers.

## Slide 33: I-Format Instructions (2/4)
Define “fields” of the following number of bits each: 6 + 5 + 5 + 16 = 32 bits
  Again, each field has a name:
  Key Concept: Only one field is inconsistent with R-format. Most importantly, opcode is still in same location.
6
5
5
16
opcode
rs
rt
immediate

## Slide 34: I-Format Instructions (3/4)
What do these fields mean?
  opcode: same as before except that, since there’s no funct field, opcode uniquely specifies an instruction in I-format
  This also answers question of why R-format has two 6-bit fields to identify instruction instead of a single 12-bit field: in order to be consistent as possible with other formats while leaving as much space as possible for immediate field.
  rs: specifies a register operand (if there is one)
  rt: specifies register which will receive result of computation (this is why it’s called the target register “rt”) or other operand for some instructions.

## Slide 35: I-Format Instructions (4/4)
The Immediate Field:
  addi, slti, sltiu, the immediate is sign-extended to 32 bits. Thus, it’s treated as a signed integer.
  16 bits  can be used to represent immediate up to 216 different values
  This is large enough to handle the offset in a typical lw or sw, plus a vast majority of values that will be used in the slti instruction.
  Later, we’ll see what to do when a value is too big for 16 bits

## Slide 36: I-Format Example (1/2)
MIPS Instruction:
  addi $21,$22,-50
  opcode = 8 (look up in table in book)
  rs = 22 (register containing operand)
  rt = 21 (target register)
  immediate = -50 (by default, this is decimal in assembly code)

## Slide 37: I-Format Example (2/2)
MIPS Instruction:
  addi $21,$22,-50
8
22
21
-50
001000
10110
10101
1111111111001110
  Decimal/field representation:
  Binary/field representation:
  hexadecimal representation: 22D5 FFCEhex
  decimal representation: 584,449,998ten

## Slide 38: Clicker/Peer Instruction
Which instruction has same representation as integer 35ten?
  a) add $0, $0, $0
  b) subu $s0,$s0,$s0
  c) lw $0, 0($0)
  d) addi $0, $0, 35
  e) subu $0, $0, $0
  Registers numbers and names:
  0: $0, .. 8: $t0, 9:$t1, ..15: $t7, 16: $s0, 17: $s1, .. 23: $s7
  Opcodes and function fields (if necessary)
  add: opcode = 0, funct = 32
  subu: opcode = 0, funct = 35
  addi: opcode = 8
  lw: opcode = 35
opcode
rs
rt
offset
rd
funct
shamt
opcode
rs
rt
opcode
rs
rt
immediate
rd
funct
shamt
opcode
rs
rt
rd
funct
shamt
opcode
rs
rt

## Slide 39: Dealing With Large Immediates
How do we deal with 32-bit immediates?
  Sometimes want to use immediates > ± 215 with addi, lw, sw and slti
  Bitwise logic operations with 32-bit immediates
Solution: Don’t mess with instruction formats, just add a new instruction
Load Upper Immediate (lui)
  lui reg,imm
  Moves 16-bit imm into upper half (bits 16-31) of reg and zeros the lower half (bits 0-15)

## Slide 40: lui Example
Want: addiu $t0,$t0,0xABABCDCD
  This is a pseudo-instruction!
Translates into:
lui $at,0xABAB # upper 16 ori $at,$at,0xCDCD # lower 16 addu $t0,$t0,$at # move
Now we can handle everything with a 16-bit immediate!
Only the assembler gets to use $at

## Slide 41: Break

## Slide 42: Branching Instructions
beq and bne
  Need to specify a target address if branch taken
  Also specify two registers to compare
Use I-Format:
  opcode specifies beq (4) vs. bne (5)
  rs and rt specify registers
  How to best use immediate to specify addresses?
opcode
rs
rt
immediate
31
0

## Slide 43: Branching Instruction Usage
Branches typically used for loops (if-else, while, for)
  Loops are generally small (< 50 instructions)
  Function calls and unconditional jumps handled with jump instructions (J-Format)
Recall: Instructions stored in a localized area of memory (Code/Text)
  Largest branch distance limited by size of code
  Address of current instruction stored in the program counter (PC)

## Slide 44: PC-Relative Addressing
PC-Relative Addressing: Use the immediate field as a two’s complement offset to PC
  Branches generally change the PC by a small amount
  Can specify ± 215 addresses from the PC
So just how much of memory can we reach?

## Slide 45: Branching Reach
Recall: MIPS uses 32-bit addresses
  Memory is byte-addressed
Instructions are word-aligned
  Address is always multiple of 4 (in bytes), meaning it ends with 0b00 in binary
  Number of bytes to add to the PC will always be a multiple of 4
Immediate specifies words instead of bytes
  Can now branch ± 215 words
  We can reach 216 instructions = 218 bytes around PC

## Slide 46: Branch Calculation
If we don’t take the branch:
  PC = PC + 4 = next instruction
If we do take the branch:
  PC = (PC+4) + (immediate*4)
Observations:
  immediate is number of instructions to jump (remember, specifies words) either forward (+) or backwards (–)
  Branch from PC+4 for hardware reasons; will be clear why later in the course

## Slide 47: Branch Example (1/2)
MIPS Code:
  Loop: beq $9,$0,End addu $8,$8,$10 addiu $9,$9,-1 j Loop End:
I-Format fields:
  opcode = 4 (look up on Green Sheet)
  rs = 9 (first operand)
  rt = 0 (second operand)
  immediate = ???
Start counting from instruction AFTER the branch
1
2
3
3

## Slide 48: Branch Example (2/2)
MIPS Code:
  Loop: beq $9,$0,End addu $8,$8,$10 addiu $9,$9,-1 j Loop End:
  Field representation (decimal):
  Field representation (binary):
4
9
0
3
31
0
000100
01001
00000
0000000000000011
31
0

## Slide 49: Questions on PC-addressing
Does the value in branch immediate field change if we move the code?
  If moving individual lines of code, then yes
  If moving all of code, then no
What do we do if destination is > 215 instructions away from branch?
  Other instructions save us
  beq $s0,$0,far bne $s0,$0,next # next instr  j far next: # next instr
Notes: As we will see, jumping instructions can reach farther than branching

## Slide 50: J-Format Instructions (1/4)
For branches, we assumed that we won’t want to branch too far, so we can specify a change in the PC
For general jumps (j and jal), we may jump to anywhere in memory
  Ideally, we would specify a 32-bit memory address to jump to
  Unfortunately, we can’t fit both a 6-bit opcode and a 32-bit address into a single 32-bit word

## Slide 51: J-Format Instructions (2/4)
Define two “fields” of these bit widths:
As usual, each field has a name:
Key Concepts:
  Keep opcode field identical to R-Format and I-Format for consistency
  Collapse all other fields to make room for large target address
6
26
31
0
opcode
target address
31
0

## Slide 52: J-Format Instructions (3/4)
We can specify 226 addresses
  Still going to word-aligned instructions, so add 0b00 as last two bits (multiply by 4)
  This brings us to 28 bits of a 32-bit address
Take the 4 highest order bits from the PC + 4
  Cannot reach everywhere, but adequate almost all of the time, since programs aren’t that long
  Only problematic if code straddles a 256MB boundary
If necessary, use 2 jumps or jr (R-Format) instead

## Slide 53: J-Format Instructions (4/4)
Jump instruction:
  New PC = { (PC+4)[31..28], target address, 00 }
Notes:
  { , , } means concatenation { 4 bits , 26 bits , 2 bits } = 32 bit address
    Book uses || instead
  Array indexing: [31..28] means highest 4 bits
  For hardware reasons, use PC+4 instead of PC

## Slide 54: Assembler Pseudo-Instructions
Certain C statements are implemented unintuitively in MIPS
  e.g. assignment (a=b) via add zero
MIPS has a set of “pseudo-instructions” to make programming easier
  More intuitive to read, but get translated into actual instructions later
Example:
move dst,src translated into addi dst,src,0

## Slide 55: Assembler Pseudo-Instructions
List of pseudo-instructions: http://en.wikipedia.org/wiki/MIPS_architecture#Pseudo_instructions
  List also includes instruction translation
Load Address (la)
  la dst,label
  Loads address of specified label into dst
Load Immediate (li)
  li dst,imm
  Loads 32-bit immediate into dst
MARS has additional pseudo-instructions
  See Help (F1) for full list

## Slide 56: Assembler Register
Problem:
  When breaking up a pseudo-instruction, the assembler may need to use an extra register
  If it uses a regular register, it’ll overwrite whatever the program has put into it
Solution:
  Reserve a register ($1 or $at for “assembler temporary”) that assembler will use to break up pseudo-instructions
  Since the assembler may use this at any time, it’s not safe to code with it

## Slide 57: MAL vs. TAL
True Assembly Language (TAL)
  The instructions a computer understands and executes
MIPS Assembly Language (MAL)
  Instructions the assembly programmer can use (includes pseudo-instructions)
  Each MAL instruction becomes 1 or more TAL instruction
TAL ⊂ MAL

## Slide 58: Clicker Question
Which of the following place the address of LOOP in $v0?
la $t1, LOOP
lw $v0, 0($t1)
2) jal LOOP
LOOP: addu $v0, $ra, $zero
3) la $v0, LOOP
T, T, T
T, T, F
F, T, T
F, T, F
F, F, T

## Slide 59: Summary
I-Format: instructions with immediates, lw/sw (offset is immediate), and beq/bne
  But not the shift instructions
  Branches use PC-relative addressing
J-Format: j and jal (but not jr)
  Jumps use absolute addressing
R-Format: all other instructions
opcode
rs
rt
immediate
I:
opcode
target address
J:
opcode
funct
rs
rt
rd
shamt
R: