## Slide 1: CS 61C: Great Ideas in Computer Architecture Lecture 12: Single-Cycle CPU, Datapath & Control Part 2
Instructor: Sagar Karandikar
sagark@eecs.berkeley.edu
http://inst.eecs.berkeley.edu/~cs61c

## Slide 2: Midterm 1 Results
You may submit regrade requests by Wednesday @ 23:59:59
Solutions posted on Piazza

## Slide 3: If you didn’t do as well as you’d hoped
You can still get an A with the clobber
  3 days preceding the final: there are no assignments, labs and discussions are OH
Lots of resources to help:
  12 hours of OH/week
    Go earlier in the week for conceptual questions (or come to mine)
  Guerrilla section every Thursday (goes over exam-style problems)
  You may go to multiple discussions (good to hear things from multiple perspectives)

## Slide 4: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions

## Slide 5: No More Magic!
CS61A
CS61B
CS61C ✔
CS61C ✔
CS61C ✔
CS61C 
CS61C ✔
EE40
Phys 7B
I/O system
Processor
Compiler
Operating
System
(Mac OSX)
Application (ex: browser)
Digital Design
Circuit Design
Instruction Set Architecture
Datapath & Control
transistors
Memory
Hardware
Software
Assembler

## Slide 6: Last time: Processor Design: 3 of 5 steps
  Step 1: Analyze instruction set to determine datapath requirements
  Meaning of each instruction is given by register transfers
  Datapath must include storage element for ISA registers
  Datapath must support each register transfer
  Step 2: Select set of datapath components & establish clock methodology
  Step 3: Assemble datapath components that meet the requirements
  Step 4: Analyze implementation of each instruction to determine setting of control points that realizes the register transfer
  Step 5: Assemble the control logic

## Slide 7: Step 1: The MIPS Instruction Formats
All MIPS instructions are 32 bits long. 3 formats:
  R-type
  I-type
  J-type
The different fields are:
  op: operation (“opcode”) of the instruction
  rs, rt, rd: the source and destination register specifiers
  shamt: shift amount
  funct: selects the variant of the operation in the “op” field
  address / immediate: address offset or immediate value
  target address: target address of jump instruction
op
target address
0
26
31
6 bits
26 bits
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
address/immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: One of the most important thing you need to know before you start designing a processor is how the instructions look like.
Or in more technical term, you need to know the instruction format. One good thing about the MIPS instruction set is that it is very simple.
First of all, all MIPS instructions are 32 bits long and there are only three instruction formats: (a) R-type, (b) I-type, and (c) J-type.
The different fields of the R-type instructions are:
(a) OP specifies the operation of the instruction.
(b) Rs, Rt, and Rd are the source and destination register specifiers.
(c) Shamt specifies the amount you need to shift for the shift instructions.
(d) Funct selects the variant of the operation specified in the “op” field.
For the I-type instruction, bits 0 to 15 are used as an immediate field. I will show you how this immediate field is used differently by different instructions.
Finally for the J-type instruction, bits 0 to 25 become the target address of the jump.
+3 = 10 min. (X:50)

## Slide 8: Step 1: Register Transfer Level (RTL)
Colloquially called “Register Transfer Language”
RTL gives the meaning of the instructions
All start by fetching the instruction itself
{op , rs , rt , rd , shamt , funct}  MEM[ PC ]
{op , rs , rt , Imm16}  MEM[ PC ]
Inst Register Transfers
ADDU R[rd]  R[rs] + R[rt]; PC  PC + 4
SUBU R[rd]  R[rs] – R[rt]; PC  PC + 4
ORI R[rt]  R[rs] | zero_ext(Imm16); PC  PC + 4
LOAD R[rt]  MEM[ R[rs] + sign_ext(Imm16)]; PC  PC + 4
STORE MEM[ R[rs] + sign_ext(Imm16) ]  R[rt]; PC  PC + 4
BEQ if ( R[rs] == R[rt] ) PC  PC + 4 + {sign_ext(Imm16), 2’b00}
else PC  PC + 4
Notes: Show green sheet.
RTL – like most programming langs:
precise and unambiguous
must be debugged
code can be checked automatically for certain properties – type checking, check against abstract state machine, etc.
TOOLS – simulator, processor, tape out
Verilog is a popular RTL (used in 150 for FPGA development)
10 mins

## Slide 9: Step 1: Requirements of the Instruction Set
Memory (MEM)
  Instructions & data (will use one for each)
Registers (R: 32, 32-bit wide registers)
  Read RS
  Read RT
  Write RT or RD
Program Counter (PC)
Extender (sign/zero extend)
Add/Sub/OR/etc unit for operation on register(s) or extended immediate (ALU)
Add 4 (+ maybe extended immediate) to PC
Compare registers?
Notes: 15 mins

## Slide 10: Step 2: Components of the Datapath
Combinational Elements
Storage Elements + Clocking Methodology
Building Blocks
32
32
A
B
32
Sum
CarryOut
CarryIn
Adder
32
A
B
32
Y
32
Select
MUX
Multiplexer
32
32
A
B
32
Result
OP
ALU
ALU
Adder
Notes: Adder – why no overflow detect?
Multiplexer – talk about specs – width of data multiplexed, # of select bits

## Slide 11: Step 2: ALU Needs for MIPS-lite + Rest of MIPS
Addition, subtraction, logical OR, ==:
  ADDU R[rd] = R[rs] + R[rt]; ...
  SUBU R[rd] = R[rs] – R[rt]; ...
  ORI R[rt] = R[rs] | zero_ext(Imm16)...
  BEQ if ( R[rs] == R[rt] )...
Test to see if output == 0 for any ALU operation gives == test. How?
P&H also adds AND, Set Less Than (1 if A < B, 0 otherwise)
ALU follows Chapter 5
Notes: 20 mins

## Slide 12: Step 2: Storage Element: Idealized Memory
“Magic” Memory
  One input bus: Data In
  One output bus: Data Out
Memory word is found by:
  For Read: Address selects the word to put on Data Out
  For Write: Set Write Enable = 1: address selects the memory word to be written via the Data In bus
Clock input (CLK)
  CLK input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block: Address valid  Data Out valid after “access time”
Clk
Data In
Write Enable
32
32
DataOut
Address
Notes: The last storage element you will need for the datapath is the idealized memory to store your data and instructions.
This idealized memory block has just one input bus (DataIn) and one output bus (DataOut).
When Write Enable is 0, the address selects the memory word to put on the Data Out bus.
When Write Enable is 1, the address selects the memory word to be written via the DataIn bus at the next clock tick.
Once again, the clock input is a factor ONLY during the write operation.
During read operation, it behaves as a combinational logic block.
That is if you put a valid value on the address lines, the output bus DataOut will become valid after the access time of the memory.
+2 = 35 min. (Y:15)

## Slide 13: Step 2: Storage Element: Register (Building Block)
Similar to D Flip Flop except
  N-bit input and output
  Write Enable input
Write Enable:
  Negated (or deasserted) (0): Data Out will not change
  Asserted (1): Data Out will become Data In on positive edge of clock
clk
Data In
Write Enable
N
N
Data Out
Notes: As far as storage elements are concerned, we will need a N-bit register that is similar to the D flip-flop I showed you in class.
The significant difference here is that the register will have a Write Enable input.
That is the content of the register will NOT be updated if Write Enable is not asserted (0).
The content is updated at the clock tick ONLY if the Write Enable signal is asserted (1).
Show how to build Register from FF
25 mins

## Slide 14: Step 2: Storage Element: Register File
Register File consists of 32 registers:
  Two 32-bit output busses:
  busA and busB
  One 32-bit input bus: busW
Register is selected by:
  RA (number) selects the register to put on busA (data)
  RB (number) selects the register to put on busB (data)
  RW (number) selects the register to be written via busW (data) when Write Enable is 1
Clock input (clk)
  Clk input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block:
    RA or RB valid  busA or busB valid after “access time.”
Clk
busW
Write Enable
32
32
busA
32
busB
5
5
5
RW
RA
RB
32 x 32-bit
Registers
Notes: We will also need a register file that consists of 32 32-bit registers with two output busses (busA and busB) and one input bus.
The register specifiers Ra and Rb select the registers to put on busA and busB respectively.
When Write Enable is 1, the register specifier Rw selects the register to be written via busW.
In our simplified version of the register file, the write operation will occurs at the clock tick.
Keep in mind that the clock input is a factor ONLY during the write operation.
During read operation, the register file behaves as a combinational logic block.
That is if you put a valid value on Ra, then bus A will become valid after the register file’s access time.
Similarly if you put a valid value on Rb, bus B will become valid after the register file’s access time. In both cases (Ra and Rb), the clock input is not a factor.
+2 = 33 min. (Y:13)

## Slide 15: Example: RegFile with 8 Registers
https://jindongpu.files.wordpress.com/2012/03/register_file.gif

## Slide 16: Step 2: Clocking Methodology
Storage elements clocked by same edge
Flip-flops (FFs) and combinational logic have some delays
  Gates: delay from input change to output change
  Signals at FF D input must be stable before active clock edge to allow signal to travel within the FF (set-up time), and we have the usual clock-to-Q delay
“Critical path” (longest path through logic) determines length of clock period
Clk
.
.
.
.
.
.
.
.
.
.
.
.
Notes: Remember, we will be using a clocking methodology where all storage elements are clocked by the same clock edge.
Consequently, our cycle time will be the sum of:
(a) The Clock-to-Q time of the input registers.
(b) The longest delay path through the combinational logic block.
(c) The set up time of the output register.
(d) And finally the clock skew.
In order to avoid hold time violation, you have to make sure this inequality is fulfilled.
+2 = 18 min. (X:58)

## Slide 17: Step 3a: Instruction Fetch Unit
Register Transfer Requirements  Datapath Assembly
Instruction Fetch
Read Operands and Execute Operation
Common RTL operations
  Fetch the Instruction: mem[PC]
  Update the program counter:
    Sequential Code: PC  PC + 4
    Branch and Jump: PC  “something else”
32
Instruction Word
Address
Instruction
Memory
PC
clk
Next Address
Logic

## Slide 18: Step 3b: Add & Subtract
R[rd] = R[rs] op R[rt] (addu rd,rs,rt)
  Ra, Rb, and Rw come from instruction’s Rs, Rt, and Rd fields
  ALUctr and RegWr: control logic after decoding the instruction
… Already defined the register file & ALU
32
Result
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 x 32-bit
Registers
Rs
Rt
Rd
ALU
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Notes: And here is the datapath that can do the trick.
First of all, we connect the register file’s Ra, Rb, and Rw input to the Rd, Rs, and Rt fields of the instruction bus (points to the format diagram).
Then we need to connect busA and busB of the register file to the ALU.
Finally, we need to connect the output of the ALU to the input bus of the register file.
Conceptually, this is how it works.
The instruction bus coming out of the Instruction memory will set the Ra and Rb to the register specifiers Rs and Rt.
This causes the register file to put the value of register Rs onto busA and the value of register Rt onto busB, respectively.
By setting the ALUctr appropriately, the ALU will perform either the Add and Subtract for us.
The result is then fed back to the register file where the register specifier Rw should already be set to the instruction bus’s Rd field.
Since the control, which we will design in our next lecture, should have already set the RegWr signal to 1, the result will be written back to the register file at the next clock tick (points to the Clk input).
30 mins

## Slide 19: Register-Register Timing: One Complete Cycle (Add/Sub)
Clk
PC
Rs, Rt, Rd,
Op, Func
ALUctr
Instruction Memory Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA, B
Register File Access Time
Old Value
New Value
busW
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
Register Write
Occurs Here
32
ALUctr
clk
busW
RegWr
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
ALU
5
Rd
Notes: Let’s take a more quantitative picture of what is happening.
At each clock tick, the Program Counter will present its latest value to the Instruction memory after Clk-to-Q time.
After a delay of the Instruction Memory Access time, the Opcode, Rd, Rs, Rt, and Function fields will become valid on the instruction bus.
Once we have the new instruction, that is the Add or Subtract instruction, on the instruction bus, two things happen in parallel.
First of all, the control unit will decode the Opcode and Func field and set the control signals ALUctr and RegWr accordingly. We will cover this in the next lecture.
While this is happening (points to Control Delay), we will also be reading the register file (Register File Access Time).
Once the data is valid on busA and busB, the ALU will perform the Add or Subtract operation based on the ALUctr signal.
Hopefully, the ALU is fast enough that it will finish the operation (ALU Delay) before the next clock tick.
At the next clock tick, the output of the ALU will be written into the register file because the RegWr signal will be equal to 1.
+3 = 45 min. (Y:25)

## Slide 20: Peer Instruction
We should use the main ALU to compute PC=PC+4 in order to save some gates
The ALU is inactive for memory reads (loads) or writes (stores).
 | 1 | 2
A | F | F
B | F | T
C | T | F
D | T | T

## Slide 21: Administrivia
HW3 Out
  Covers SDS topics from last week
Proj 2-2 out
  Make sure you test your code on hive machines, that’s where we’ll grade them

## Slide 22: Break

## Slide 23: End of the review
Now let’s finish steps 3, 4, and 5
By the end of today, you’ll know how an entire computer works!

## Slide 24: 3c: Logical Op (or) with Immediate
R[rt] = R[rs] op ZeroExt[imm16]
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
immediate
0
16
15
31
16 bits
16 bits
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
What about Rt Read?
32
ALUctr
clk
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
ZeroExt
32
16
imm16
ALUSrc
0
1
0
1
ALU
5
RegDst
Writing to Rt register (not Rd)!!
Notes: Here is the datapath for the Or immediate instructions.
We cannot use the Rd field here (Rw) because in this instruction format, we don’t have a Rd field. The Rd field in the R-type is used here as part of the immediate field.
For this instruction type, Rw input of the register file, that is the address of the register to be written, comes from the Rt field of the instruction.
Recalled from earlier slide that for R-type instruction, the Rw comes from the Rd field.
That’s why we need a MUX here to put Rd onto Rw for R-type instructions and to put Rt onto Rw for the I-type instruction.
Since the second operation of this instruction will be the immediate field zero extended to 32 bits, we also need a MUX here to block off bus B from the register file.
Since bus B is blocked off by the MUX, the value on bus B is don’t care. Therefore we do not have to worry about what ends up on the register file’s Rb register specifier.
To keep things simple, we may just as well keep it the same as the R-type instruction and put the Rt field here.
So to summarize, this is how this datapath works. With Rs on Register File’s Ra input, bus A will get the value of Rs as the first ALU operand.
The second operand will come from the immediate field of the instruction.
Once the ALU complete the OR operation, the result will be written into the register specified by the instruction’s Rt field.
+3 = 50 min. (Y:30)

## Slide 25: 3d: Load Operations
R[rt] = Mem[R[rs] + SignExt[imm16]] Example: lw rt,rs,imm16
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
32
ALUctr
clk
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
ZeroExt
32
16
imm16
ALUSrc
0
1
0
1
ALU
5
RegDst
Notes: Once again we cannot use the instruction’s Rd field for the Register File’s Rw input because load is a I-type instruction and there is no such thing as the Rd field in the I format.
So instead of Rd, the Rt field is used to specify the destination register through this two to one multiplexor.
The first operand of the ALU comes from busA of the register file which contains the value of Register Rs (points to the Ra input of the register file).
The second operand, on the other hand, comes from the immediate field of the instruction.
Instead of using the Zero Extender I used in datapath for the or immediate datapath, I have to use a more general purpose Extender that can do both Sign Extend and Zero Extend.
The ALU then adds these two operands together to form the memory address.
Consequently, the output of the ALU has to go to two places:
(a) First the address input of the data memory.
(b) And secondly, also to the input of this two-to-one multiplexer.
The other input of this multiplexer comes from the output of the data memory so we can place the output of the data memory onto the register file’s input bus for the load instruction.
For Add, Subtract, and the Or immediate instructions, the output of the ALU will be selected to be placed on the input bus of the register file.
In either case, the control signal RegWr should be asserted so the register file will be written at the end of the cycle.
+3 = 60 min. (Y:40)

## Slide 26: 3d: Load Operations
R[rt] = Mem[R[rs] + SignExt[imm16]] Example: lw rt,rs,imm16
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
0
1
0
1
ALU
0
1
Adr
Data
Memory
5
Notes: Once again we cannot use the instruction’s Rd field for the Register File’s Rw input because load is a I-type instruction and there is no such thing as the Rd field in the I format.
So instead of Rd, the Rt field is used to specify the destination register through this two to one multiplexor.
The first operand of the ALU comes from busA of the register file which contains the value of Register Rs (points to the Ra input of the register file).
The second operand, on the other hand, comes from the immediate field of the instruction.
Instead of using the Zero Extender I used in datapath for the or immediate datapath, I have to use a more general purpose Extender that can do both Sign Extend and Zero Extend.
The ALU then adds these two operands together to form the memory address.
Consequently, the output of the ALU has to go to two places:
(a) First the address input of the data memory.
(b) And secondly, also to the input of this two-to-one multiplexer.
The other input of this multiplexer comes from the output of the data memory so we can place the output of the data memory onto the register file’s input bus for the load instruction.
For Add, Subtract, and the Or immediate instructions, the output of the ALU will be selected to be placed on the input bus of the register file.
In either case, the control signal RegWr should be asserted so the register file will be written at the end of the cycle.
+3 = 60 min. (Y:40)

## Slide 27: 3e: Store Operations
Mem[ R[rs] + SignExt[imm16] ] = R[rt] Ex.: sw rt, rs, imm16
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Adr
Data
Memory
5
Notes: And here is the datapath for the store instruction.
The Register File, the ALU, and the Extender are the same as the datapath for the load instruction because the memory address has to be calculated the same exact way:
(a) Put the register selected by Rs onto bus A and sign extend the 16 bit immediate field.
(b) Then make the ALU (ALUctr) adds these two (busA and output of Extender) together.
The new thing we added here is busB extension (DataIn).
More specifically, in order to send the register selected by the Rt field (Rb of the register file) to data memory, we need to connect bus B to the data memory’s Data In bus.
Finally, the store instruction is the first instruction we encountered that does not do any register write at the end.
Therefore the control unit must make sure RegWr is zero for this instruction.
+2 = 64 min. (Y:44)

## Slide 28: 3e: Store Operations
Mem[ R[rs] + SignExt[imm16] ] = R[rt] Ex.: sw rt, rs, imm16
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Adr
Data
Memory
5
Notes: And here is the datapath for the store instruction.
The Register File, the ALU, and the Extender are the same as the datapath for the load instruction because the memory address has to be calculated the same exact way:
(a) Put the register selected by Rs onto bus A and sign extend the 16 bit immediate field.
(b) Then make the ALU (ALUctr) adds these two (busA and output of Extender) together.
The new thing we added here is busB extension (DataIn).
More specifically, in order to send the register selected by the Rt field (Rb of the register file) to data memory, we need to connect bus B to the data memory’s Data In bus.
Finally, the store instruction is the first instruction we encountered that does not do any register write at the end.
Therefore the control unit must make sure RegWr is zero for this instruction.
+2 = 64 min. (Y:44)

## Slide 29: 3f: The Branch Instruction
beq rs, rt, imm16
  mem[PC] Fetch the instruction from memory
  Equal = (R[rs] == R[rt]) Calculate branch condition
  if (Equal) Calculate the next instruction’s address
    PC = PC + 4 + ( SignExt(imm16) x 4 )
  else
    PC = PC + 4
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: How does the branch on equal instruction work?
Well it calculates the branch condition by subtracting the register selected by the Rt field from the register selected by the Rs field.
If the result of the subtraction is zero, then these two registers are equal and we take a branch. Otherwise, we keep going down the sequential path (PC = PC +4).
+1 = 65 min. (Y:45)

## Slide 30: Datapath for Branch Operations
beq rs, rt, imm16
Datapath generates condition (Equal)
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Already have mux, adder, need special sign extender for PC, need equal compare (sub?)
imm16
clk
PC
00
4
nPC_sel
PC Ext
Adder
Adder
Mux
Inst Address
32
ALUctr
clk
busW
RegWr
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
ALU
5
=
Equal
Notes: The datapath for calculating the branch condition is rather simple.
All we have to do is feed the Rs and Rt fields of the instruction into the Ra and Rb inputs of the register file.
Bus A will then contain the value from the register selected by Rs.
And bus B will contain the value from the register selected by Rt.
The next thing to do is to ask the ALU to perform a subtract operation and feed the output Zero to the next address logic.
How does the next address logic block look like?
Well, before I show you that, let’s take a look at the binary arithmetics behind the program counter (PC).
+2 = 67 min. (Y:47)

## Slide 31: Instruction Fetch Unit including Branch
if (Zero == 1) then PC = PC + 4 + SignExt[imm16]*4 ; else PC = PC + 4
op
rs
rt
immediate
0
16
21
26
31
How to encode nPC_sel?
  Direct MUX select?
  Branch inst. / not branch inst.
Let’s pick 2nd option
Adr
Inst
Memory
nPC_sel
Instruction<31:0>
Equal
nPC_sel
Q: What logic gate?
imm16
clk
PC
00
4
PC Ext
Adder
Adder
Mux
0
1
MUX ctrl
Notes: Let’s look at the interesting case where the branch condition Zero is true (Zero = 1).
Well, if Zero is not asserted, we will have our boring case where PC + 1 is selected.
Anyway, with Branch = 1 and Zero = 1, the output of the second adder will be selected.
That is, we will add the seqential address, that is output of the first adder, to the sign extended version of the immediate field, to form the branch target address (output of 2nd adder).
With the control signal Jump set to zero, this branch target address will be written into the Program Counter register (PC) at the end of the clock cycle.
+2 = 35 min. (Y:15)

## Slide 32: Putting it All Together:A Single Cycle Datapath
imm16
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
Equal
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
clk
PC
00
4
nPC_sel
PC Ext
Adr
Inst
Memory
Adder
Adder
Mux
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
Notes: So here is the single cycle datapath we just built.
If you push into the Instruction Fetch Unit, you will see the last slide showing the PC, the next address logic, and the Instruction Memory.
Here I have shown how we can get the Rt, Rs, Rd, and Imm16 fields out of the 32-bit instruction word.
The Rt, Rs, and Rd fields will go to the register file as register specifiers while the Imm16 field will go to the Extender where it is either Zero and Sign extended to 32 bits.
The signals ExtOp, ALUSrc, ALUctr, MemWr, MemtoReg, RegDst, RegWr, Branch, and Jump are control signals.
And I will show you how to generate them on Friday.
+2 = 80 min. (Z:00)

## Slide 33: Processor Design: 5 steps
  Step 1: Analyze instruction set to determine datapath requirements
  Meaning of each instruction is given by register transfers
  Datapath must include storage element for ISA registers
  Datapath must support each register transfer
  Step 2: Select set of datapath components & establish clock methodology
  Step 3: Assemble datapath components that meet the requirements
  Step 4: Analyze implementation of each instruction to determine setting of control points that realizes the register transfer
  Step 5: Assemble the control logic

## Slide 34: Datapath Control Signals
ExtOp: “zero”, “sign”
ALUsrc: 0  regB; 1  immed
ALUctr: “ADD”, “SUB”, “OR”
MemWr: 1  write memory
MemtoReg: 0  ALU; 1  Mem
RegDst: 0  “rt”; 1  “rd”
RegWr: 1  write register
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Adr
Data
Memory
5
imm16
clk
PC
00
4
nPC_sel & Equal
PC Ext
Adder
Adder
Mux
Inst Address
0
1

## Slide 35: Given Datapath: RTL  Control
ALUctr
RegDst
ALUSrc
ExtOp
MemtoReg
MemWr
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rs
Rt
nPC_sel
Adr
Inst
Memory
DATA PATH
Control
Op
<0:5>
Fun
RegWr
<26:31>

## Slide 36: RTL: The Add Instruction
add rd, rs, rt
  MEM[PC] Fetch the instruction from memory
  R[rd] = R[rs] + R[rt] The actual operation
  PC = PC + 4 Calculate the next instruction’s address
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Notes: OK, let’s get on with today’s lecture by looking at the simple add instruction.
In terms of Register Transfer Language, this is what the Add instruction need to do.
First, you need to fetch the instruction from Memory.
Then you perform the actual add operation. More specifically:
(a) You add the contents of the register specified by the Rs and Rt fields of the instruction.
(b) Then you write the results to the register specified by the Rd field.
And finally, you need to update the program counter to point to the next instruction.
Now, let’s take a detail look at the datapath during various phase of this instruction.
+2 = 10 min. (X:50)

## Slide 37: Instruction Fetch Unit at the Beginning of Add
Fetch the instruction from Instruction memory: Instruction = MEM[PC]
  same for all instructions
imm16
clk
PC
00
4
nPC_sel
PC Ext
Adder
Adder
Mux
Inst Address
Inst
Memory
Instruction<31:0>

## Slide 38: Single Cycle Datapath during Add
R[rd] = R[rs] + R[rt]
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
32
ALUctr=ADD
clk
busW
RegWr=1
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst=1
Extender
32
16
imm16
ALUSrc=0
ExtOp=x
MemtoReg=0
clk
Data In
32
MemWr=0
zero
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
nPC_sel=+4
instr
fetch
unit
clk
Notes: This picture shows the activities at the main datapath during the execution of the Add or Subtract instructions.
The active parts of the datapath are shown in different color as well as thicker lines.
First of all, the Rs and Rt of the instructions are fed to the Ra and Rb address ports of the register file and cause the contents of registers specified by the Rs and Rt fields to be placed on busA and busB, respectively.
With the ALUctr signals set to either Add or Subtract, the ALU will perform the proper operation and with MemtoReg set to 0, the ALU output will be placed onto busW.
The control we are going to design will also set RegWr to 1 so that the result will be written to the register file at the end of the cycle.
Notice that ExtOp is don’t care because the Extender in this case can either do a SignExt or ZeroExt. We DON’T care because ALUSrc will be equal to 0--we are using busB.
The other control signals we need to worry about are:
(a) MemWr has to be set to zero because we do not want to write the memory.
(b) And Branch and Jump, we have to set to zero. Let me show you why.
+3 = 15 min. (X:55)

## Slide 39: Instruction Fetch Unit at End of Add
PC = PC + 4
  Same for all instructions except: Branch and Jump
imm16
clk
PC
00
4
nPC_sel=+4
PC Ext
Adder
Adder
Mux
Inst Address
Inst
Memory
Notes: This picture shows the control signals setting for the Instruction Fetch Unit at the end of the Add or Subtract instruction.
Both the Branch and Jump signals are set to 0.
Consequently, the output of the first adder, which implements PC plus 1, is selected through the two 2-to-1 mux and got placed into the input of the Program Counter register.
The Program Counter is updated to this new value at the next clock tick.
Notice that the Program Counter is updated at every cycle. Therefore it does not have a Write Enable signal to control the write.
Also, this picture is the same for or all instructions other than Branch andJjump.
Therefore I will only show this picture again for the Branch and Jump instructions and will not repeat this for all other instructions.
+2 = 17 min. (X:57)

## Slide 40: Single Cycle Datapath during Jump
32
ALUctr =
Clk
busW
RegWr =
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 x 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst =
Extender
Mux
Mux
32
16
imm16
ALUSrc =
ExtOp =
Mux
MemtoReg =
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr =
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rs
Rt
New PC = { PC[31..28], target address, 00 }
nPC_sel=
op
target address
0
26
31
J-type
jump
25
Jump=
<0:25>
TA26
Notes: So how does the branch instruction work?
As far as the main datapath is concerned, it needs to calculate the branch condition. That is, it subtracts the register specified in the Rt field from the register specified in the Rs field and set the condition Zero accordingly.
In order to place the register values on busA and busB, we need to feed the Rs and Rt fields of the instruction to the Ra and Rb ports of the register file and set ALUSrc to 0.
Then we have to instruction the ALU to perform the subtract (ALUctr = sub) operation and set the Zero bit accordingly.
The Zero bit is sent to the Instruction Fetch Unit. I will show you the internal of the Instruction Fetch Unit in a second.
But before we leave this slide, I want you to notice that ExtOp, MemtoReg, and RegDst are don’t cares but RegWr and MemWr have to be ZERO to prevent any write to occur.
And finally, the controller needs to set the Branch signal to 1 so the Instruction Fetch Unit knows what to do. So now let’s take a look at the Instruction Fetch Unit.
+2 = 33 min. (Y:13)

## Slide 41: Single Cycle Datapath during Jump
32
ALUctr =x
Clk
busW
RegWr = 0
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 x 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst = x
Extender
Mux
Mux
32
16
imm16
ALUSrc = x
ExtOp = x
Mux
MemtoReg = x
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Rd
Rs
Rt
New PC = { PC[31..28], target address, 00 }
nPC_sel=?
Jump=1
Imm16
<0:25>
TA26
op
target address
0
26
31
J-type
jump
25
Notes: So how does the branch instruction work?
As far as the main datapath is concerned, it needs to calculate the branch condition. That is, it subtracts the register specified in the Rt field from the register specified in the Rs field and set the condition Zero accordingly.
In order to place the register values on busA and busB, we need to feed the Rs and Rt fields of the instruction to the Ra and Rb ports of the register file and set ALUSrc to 0.
Then we have to instruction the ALU to perform the subtract (ALUctr = sub) operation and set the Zero bit accordingly.
The Zero bit is sent to the Instruction Fetch Unit. I will show you the internal of the Instruction Fetch Unit in a second.
But before we leave this slide, I want you to notice that ExtOp, MemtoReg, and RegDst are don’t cares but RegWr and MemWr have to be ZERO to prevent any write to occur.
And finally, the controller needs to set the Branch signal to 1 so the Instruction Fetch Unit knows what to do. So now let’s take a look at the Instruction Fetch Unit.
+2 = 33 min. (Y:13)

## Slide 42: Instruction Fetch Unit at the End of Jump
Adr
Inst
Memory
Adder
Adder
PC
Clk
00
Mux
4
nPC_sel
imm16
Instruction<31:0>
0
1
Zero
nPC_MUX_sel
New PC = { PC[31..28], target address, 00 }
op
target address
0
26
31
J-type
jump
25
How do we modify this to account for jumps?
Jump
Notes: Let’s look at the interesting case where the branch condition Zero is true (Zero = 1).
Well, if Zero is not asserted, we will have our boring case where PC + 1 is selected.
Anyway, with Branch = 1 and Zero = 1, the output of the second adder will be selected.
That is, we will add the seqential address, that is output of the first adder, to the sign extended version of the immediate field, to form the branch target address (output of 2nd adder).
With the control signal Jump set to zero, this branch target address will be written into the Program Counter register (PC) at the end of the clock cycle.
+2 = 35 min. (Y:15)

## Slide 43: Instruction Fetch Unit at the End of Jump
Adr
Inst
Memory
Adder
Adder
PC
Clk
00
Mux
4
nPC_sel
imm16
Instruction<31:0>
0
1
Zero
nPC_MUX_sel
New PC = { PC[31..28], target address, 00 }
op
target address
0
26
31
J-type
jump
25
Mux
1
0
Jump
TA
4 (MSBs)
00
Query
Can Zero still get asserted?
Does nPC_sel need to be 0?
  If not, what?
26
Notes: Let’s look at the interesting case where the branch condition Zero is true (Zero = 1).
Well, if Zero is not asserted, we will have our boring case where PC + 1 is selected.
Anyway, with Branch = 1 and Zero = 1, the output of the second adder will be selected.
That is, we will add the seqential address, that is output of the first adder, to the sign extended version of the immediate field, to form the branch target address (output of 2nd adder).
With the control signal Jump set to zero, this branch target address will be written into the Program Counter register (PC) at the end of the clock cycle.
+2 = 35 min. (Y:15)

## Slide 44: Clickers/Peer Instruction
imm16
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
Equal
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
clk
PC
00
4
nPC_sel
PC Ext
Adr
Inst
Memory
Adder
Adder
Mux
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
What new instruction would need no new datapath hardware?
A: branch if reg==immediate
B: add two registers and branch if result zero
C: store with auto-increment of base address:
  sw rt, rs, offset // rs incremented by offset after store
D: shift left logical by one bit
Notes: So here is the single cycle datapath we just built.
If you push into the Instruction Fetch Unit, you will see the last slide showing the PC, the next address logic, and the Instruction Memory.
Here I have shown how we can get the Rt, Rs, Rd, and Imm16 fields out of the 32-bit instruction word.
The Rt, Rs, and Rd fields will go to the register file as register specifiers while the Imm16 field will go to the Extender where it is either Zero and Sign extended to 32 bits.
The signals ExtOp, ALUSrc, ALUctr, MemWr, MemtoReg, RegDst, RegWr, Branch, and Jump are control signals.
And I will show you how to generate them on Friday.
+2 = 80 min. (Z:00)

## Slide 45: In The News: Tile-Mx100 100 64-bit ARM cores on one chip
EZChip (bought Tilera)
100 64-bit ARM Cortex A53
Dual-issue, in-order

## Slide 46: Break

## Slide 47: P&H Figure 4.17

## Slide 48: Summary of the Control Signals (1/2)
inst Register Transfer
add R[rd]  R[rs] + R[rt]; PC  PC + 4
ALUsrc=RegB, ALUctr=“ADD”, RegDst=rd, RegWr, nPC_sel=“+4”
sub R[rd]  R[rs] – R[rt]; PC  PC + 4
ALUsrc=RegB, ALUctr=“SUB”, RegDst=rd, RegWr, nPC_sel=“+4”
ori R[rt]  R[rs] + zero_ext(Imm16); PC  PC + 4
ALUsrc=Im, Extop=“Z”, ALUctr=“OR”, RegDst=rt,RegWr, nPC_sel=“+4”
lw R[rt]  MEM[ R[rs] + sign_ext(Imm16)]; PC  PC + 4
ALUsrc=Im, Extop=“sn”, ALUctr=“ADD”, MemtoReg, RegDst=rt, RegWr, nPC_sel = “+4”
sw MEM[ R[rs] + sign_ext(Imm16)]  R[rs]; PC  PC + 4
ALUsrc=Im, Extop=“sn”, ALUctr = “ADD”, MemWr, nPC_sel = “+4”
beq if (R[rs] == R[rt]) then PC  PC + sign_ext(Imm16)] || 00 else PC  PC + 4
nPC_sel = “br”, ALUctr = “SUB”

## Slide 49: Summary of the Control Signals (2/2)
add
sub
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
nPCsel
Jump
ExtOp
ALUctr<2:0>
1
0
0
1
0
0
0
x
Add
1
0
0
1
0
0
0
x
Subtract
0
1
0
1
0
0
0
0
Or
0
1
1
1
0
0
0
1
Add
x
1
x
0
1
0
0
1
Add
x
0
x
0
0
1
0
x
Subtract
x
x
x
0
0
?
1
x
x
op
target address
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
op
rs
rt
immediate
R-type
I-type
J-type
add, sub
ori, lw, sw, beq
jump
func
op
00 0000
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
Appendix A
10 0000
See
10 0010
We Don’t Care :-)
Notes: Here is a table summarizing the control signals setting for the seven (add, sub, ...) instructions we have looked at.
Instead of showing you the exact bit values for the ALU control (ALUctr), I have used the symbolic values here.
The first two columns are unique in the sense that they are R-type instrucions and in order to uniquely identify them, we need to look at BOTH the op field as well as the func fiels.
Ori, lw, sw, and branch on equal are I-type instructions and Jump is J-type. They all can be uniquely idetified by looking at the opcode field alone.
Now let’s take a more careful look at the first two columns. Notice that they are identical except the last row.
So we can combine these two rows here if we can “delay” the generation of ALUctr signals.
This lead us to something call “local decoding.”
+3 = 42 min. (Y:22)

## Slide 50: Boolean Expressions for Controller
RegDst = add + sub ALUSrc = ori + lw + sw MemtoReg = lw RegWrite = add + sub + ori + lw MemWrite = sw nPCsel = beq Jump = jump ExtOp = lw + sw ALUctr[0] = sub + beq (assume ALUctr is 00 ADD, 01 SUB, 10 OR) ALUctr[1] = or
Where:
rtype = ~op5  ~op4  ~op3  ~op2  ~op1  ~op0, ori = ~op5  ~op4  op3  op2  ~op1  op0 lw = op5  ~op4  ~op3  ~op2  op1  op0 sw = op5  ~op4  op3  ~op2  op1  op0 beq = ~op5  ~op4  ~op3  op2  ~op1  ~op0 jump = ~op5  ~op4  ~op3  ~op2  op1  ~op0
add = rtype  func5  ~func4  ~func3  ~func2  ~func1  ~func0 sub = rtype  func5  ~func4  ~func3  ~func2  func1  ~func0
How do we implement this in gates?
Notes: ADD 0000 00ss ssst tttt dddd d000 0010 0000
SUB 0000 00ss ssst tttt dddd d000 0010 0010
ORI 0011 01ss ssst tttt iiii iiii iiii iiii
LW 1000 11ss ssst tttt iiii iiii iiii iiii
SW 1010 11ss ssst tttt iiii iiii iiii iiii
BEQ 0001 00ss ssst tttt iiii iiii iiii iiii
JUMP 0000 10ii iiii iiii iiii iiii iiii iiii

## Slide 51: Controller Implementation
add
sub
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
nPCsel
Jump
ExtOp
ALUctr[0]
ALUctr[1]
“AND” logic
“OR” logic
opcode
func

## Slide 52: Clicker Question
Which of the following is TRUE?
The CPU’s control needs only opcode/funct to determine the next PC value to select
The clock can have a shorter period for instructions that don’t use memory
The CPU requires a separate instruction memory and data memory
The ALU is used to set PC to PC+4 when necessary

## Slide 53: Summary: Single-cycle Processor
Five steps to design a processor:
  1. Analyze instruction set  datapath requirements
  2. Select set of datapath components & establish clock methodology
  3. Assemble datapath meeting the requirements
  4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer.
  5. Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output