## Slide 1: CS 61C: Great Ideas in Computer Architecture Lecture 16: Caches, Part 3
Instructor: Sagar Karandikar
sagark@eecs.berkeley.edu
http://inst.eecs.berkeley.edu/~cs61c

## Slide 2: You Are Here!
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s
Lecture

## Slide 3: Caches Review
Processor issues addresses, cache breaks them into Tag/Index/Offset
Direct-Mapped vs. Set-Associative vs. Fully Associative
AMAT = Hit Time + Miss Rate * Miss Penalty
3 Cs of cache misses: Compulsory, Capacity, Conflict
Effect of cache parameters on performance

## Slide 4: Review: Processor Address Fields used by Cache Controller
Block Offset: Byte address within block
  #bits = log_2(block size in bytes)
Index: Selects which index (set) we want
  # bits = log_2(number of sets)
Tag: Remaining portion of processor address
  processor address size - offset bits - index bits
Block offset
Set Index
Tag
Processor Address (32-bits total)
Notes: For class handout

## Slide 5: Review: Direct Mapped Cache
One word blocks, cache size = 1Ki words (or 4KiB)
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Block offset
20
Data
32
Hit
Valid bit ensures something useful in cache for this index
Compare Tag with upper part of Address to see if a Hit
Read data from cache instead of memory if a Hit
Comparator
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
Temporal!

## Slide 6: Review: Multiword-Block Direct-Mapped Cache
Four words/block, cache size = 1Ki words
8
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
32
Block offset
Notes: to take advantage for spatial locality want a cache block that is larger than word word in size.

## Slide 7: Review: Four-Way Set-Associative Cache
28 = 256 sets each with four ways (each with one block)
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select
Way 0
Way 1
Way 2
Way 3
Notes: This is called a 4-way set associative cache because there are four cache entries for each cache index. Essentially, you have four direct mapped cache working in parallel.
This is how it works: the cache index selects a set from the cache. The four tags in the set are compared in parallel with the upper bits of the memory address.
If no tags match the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data from the way where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 8: Review: Cache Measurement Terms
Hit rate: fraction of accesses that hit in the cache
Miss rate: 1 – Hit rate
Miss penalty: time to replace a block from lower level in memory hierarchy to cache
Hit time: time to access cache memory (including tag comparison)
These are controlled by the myriad cache parameters we can set…

## Slide 9: Primary Cache Parameters
Block size (aka line size)
  how many bytes of data in each cache entry?
Associativity
  how many ways in each set?
  Direct-mapped => Associativity = 1
  Set-associative => 1 < Associativity < #Entries
  Fully associative => Associativity = #Entries
Capacity (bytes) = Total #Entries * Block size
#Entries = #Sets * Associativity

## Slide 10: Other Cache Parameters
Write Policy
Replacement policy

## Slide 11: Write Policy Choices
Cache hit:
  write through: writes both cache & memory on every access
    Generally higher memory traffic but simpler pipeline & cache design
  write back: writes cache only, memory `written only when dirty entry evicted
    A dirty bit per line reduces write-back traffic
    Must handle 0, 1, or 2 accesses to memory for each load/store
Cache miss:
  no write allocate: only write to main memory
  write allocate (aka fetch on write): fetch into cache
Common combinations:
  write through and no write allocate
  write back with write allocate

## Slide 12: Replacement Policy
In an associative cache, which line from a set should be evicted when the set becomes full?
Random
Least-Recently Used (LRU)
  LRU cache state must be updated on every access
  True implementation only feasible for small sets (2-way)
  Pseudo-LRU binary tree often used for 4-8 way
First-In, First-Out (FIFO) a.k.a. Round-Robin
  Used in highly associative caches
Not-Most-Recently Used (NMRU)
  FIFO with exception for most-recently used line or lines
This is a second-order effect. Why?
Replacement only happens on misses
Notes: NLRU used in Alpha TLBs (jse)

## Slide 13: Sources of Cache Misses (3 C’s)
Compulsory (cold start, first reference):
  1st access to a block in memory, “cold”, fact of life, not a lot you can do about it.
    If running billions of instructions, compulsory misses are insignificant
Capacity:
  Cache cannot contain all blocks accessed by the program
    Misses that would not occur with infinite cache
Conflict (collision):
  Multiple memory locations mapped to same cache set
    Misses that would not occur with ideal fully associative cache
Notes: (Capacity miss) That is the cache misses are due to the fact that the cache is simply not large enough to contain all the blocks that are accessed by the program.
The solution to reduce the Capacity miss rate is simple: increase the cache size.
Here is a summary of other types of cache miss we talked about.
First is the Compulsory misses. These are the misses that we cannot avoid. They are caused when we first start the program.
Then we talked about the conflict misses. They are the misses that caused by multiple memory locations being mapped to the same cache location.
There are two solutions to reduce conflict misses. The first one is, once again, increase the cache size. The second one is to increase the associativity.
For example, say using a 2-way set associative cache instead of directed mapped cache.
But keep in mind that cache miss rate is only one part of the equation. You also have to worry about cache access time and miss penalty. Do NOT optimize miss rate alone.
Finally, there is another source of cache miss we will not cover today. Those are referred to as invalidation misses caused by another process, such as IO , update the main memory so you have to flush the cache to avoid inconsistency between memory and cache.
+2 = 43 min. (Y:23)

## Slide 14: Rules for Determining Miss Type for a Given Access Pattern in 61C
1) Compulsory: A miss is compulsory if and only if it results from accessing the data for the first time. If you have ever brought the data you are accessing into the cache before, it's not a compulsory miss, otherwise it is.
2) Conflict: A conflict miss is a miss that's not compulsory and that would have been avoided if the cache was fully associative. Imagine you had a cache with the same parameters but fully-associative (with LRU). If that would've avoided the miss, it's a conflict miss.
3) Capacity: This is a miss that would not have happened with an infinitely large cache. If your miss is not a compulsory or conflict miss, it's a capacity miss.
Notes: In order to determine what kind of miss you are dealing with, you can first check 1, then 2 and then 3. The type of your miss is the first of these definitions that applies. Note that making the capacity infinitely large also eliminates conflict misses, which is why you should check whether it is a conflict miss first.

## Slide 15: Impact of Cache Parameters on Performance
AMAT = Hit Time + Miss Rate * Miss Penalty
  Note, we assume always first search cache, so must incorporate hit time for both hits and misses!
For misses, characterize by 3Cs

## Slide 16: Administrivia
Project 3-1 Out
  Last week, we built a CPU together, this week, you start building your own!
HW4 Out - Caches
Guerrilla Section on Pipelining, Caches on Thursday, 5-7pm, Woz

## Slide 17: Administrivia
Midterm 2 is one week from tomorrow
  In this room, at this time
  Two double-sided 8.5”x11” handwritten cheatsheets
  We’ll provide a MIPS green sheet
  No electronics
  Covers up to and including tomorrow’s lecture (07/21)*
  Review session is Friday, 7/24 from 1-4pm in HP Aud.
  * This is one less lecture than initially indicated

## Slide 18: Break

## Slide 19: CPU-Cache Interaction (5-stage pipeline)
PC
addr
inst
Primary
Instruction
Cache
0x4
Add
IR
D
bubble
hit?
  PCen
Decode,
Register
Fetch
wdata
R
addr
wdata
rdata
Primary
Data
Cache
we
A
B
Y
Y
ALU
MD1
MD2
Cache Refill Data from Lower Levels of Memory Hierarchy
hit?
Stall entire CPU on data cache miss
To Memory Control
M
E
Stall at fetch stage on inst cache miss (but not the whole CPU)
Notes: How are writes to istream handled?

## Slide 20: Increasing Block Size?
Hit time as block size increases?
  Hit time unchanged, but might be slight hit-time reduction as number of tags is reduced, so faster to access memory holding tags
Miss rate as block size increases?
  Goes down at first due to spatial locality, then increases due to increased conflict misses due to fewer blocks in cache
Miss penalty as block size increases?
  Rises with longer block size, but with fixed constant initial latency that is amortized over whole block

## Slide 21: Increasing Associativity?
Hit time as associativity increases?
  Increases, with large step from direct-mapped to >=2 ways, as now need to mux correct way to processor
  Smaller increases in hit time for further increases in associativity
Miss rate as associativity increases?
  Goes down due to reduced conflict misses, but most gain is from 1->2->4-way with limited benefit from higher associativities
Miss penalty as associativity increases?
  Unchanged, replacement policy runs in parallel with fetching missing line from memory

## Slide 22: Increasing #Entries? (Capacity)
Hit time as #entries increases?
  Increases, since reading tags and data from larger memory structures
Miss rate as #entries increases?
  Goes down due to reduced capacity and conflict misses
  Architects rule of thumb: miss rate drops ~2x for every ~4x increase in capacity (only a gross approximation)
Miss penalty as #entries increases?
  Unchanged

## Slide 23: How to Reduce Miss Penalty?
Could there be locality on misses from a cache?
Use multiple cache levels!
With Moore’s Law, more room on die for bigger L1 caches and for second-level (L2) cache
And in some cases even an L3 cache!
IBM mainframes have ~1GB L4 cache off-chip.

## Slide 24: Review: Memory Hierarchy
Processor
Size of memory at each level
Increasing distance from processor, decreasing speed
Level 1
Level 2
Level n
Level 3
. . .
Inner
Outer
Levels in memory hierarchy
As we move to outer levels the latency goes up and price per bit goes down.

## Slide 25: Local vs. Global Miss Rates
Local miss rate – the fraction of references to one level of a cache that miss
  Local Miss rate L2$ = # $L2 Misses / # L1$ Misses
Global miss rate – the fraction of references that miss in all levels of a multilevel cache
L2$ local miss rate >> than the global miss rate
    L2$ Global Miss rate = L2$ Misses / Total Accesses

## Slide 26
L1 Cache: 32KB I$, 32KB D$
L2 Cache: 256 KB
L3 Cache: 4 MB
Notes: Global miss rates.
as you keep going, l3 < l2 < l1, as we get lower in the hierarchy, more hit in the caches, fewer miss
numerator = misses at this level
denominator = accesses issued
so a hit at L3 means miss at L1 and miss at L2, so L1, L2 misses must be >= L3 misses

## Slide 27: Local vs. Global Miss Rates
Local miss rate – the fraction of references to one level of a cache that miss
    Local Miss rate L2$ = $L2 Misses / L1$ Misses
Global miss rate – the fraction of references that miss in all levels of a multilevel cache
    L2$ Global Miss rate = L2$ Misses / Total Accesses
  = L2$ Misses / L1$ Misses x L1$ Misses / Total Accesses
  = Local Miss rate L2$ x Local Miss rate L1$
  AMAT = Time for a hit + Miss rate x Miss penalty
  AMAT = Time for a L1$ hit + (local) Miss rate L1$ x (Time for a L2$ hit + (local) Miss rate L2$ x L2$ Miss penalty)

## Slide 29: On a 2012 Retina MBP
~ » sudo sysctl -a | grep cache
hw.cachelinesize = 64
hw.l1icachesize = 32768
hw.l1dcachesize = 32768
hw.l2cachesize = 262144
hw.l3cachesize = 6291456
kern.flush_cache_on_write: 0
kern.namecache_disabled: 0
vm.vm_page_filecache_min: 209715
vfs.generic.nfs.client.access_cache_timeout: 60
vfs.generic.nfs.server.reqcache_size: 64
net.inet.ip.rtmaxcache: 128
net.inet6.ip6.rtmaxcache: 128
hw.cacheconfig: 8 2 2 8 0 0 0 0 0 0
hw.cachesize: 17179869184 32768 262144 6291456 0 0 0 0 0
hw.cachelinesize: 64
hw.l1icachesize: 32768
hw.l1dcachesize: 32768
hw.l2cachesize: 262144
hw.l3cachesize: 6291456
machdep.cpu.cache.linesize: 64
machdep.cpu.cache.L2_associativity: 8
machdep.cpu.cache.size: 256
------------------------------------------------------------
On a hive machine, run:
cat /sys/devices/system/cpu/cpu0/cache/index0/*
A cool thing about Unix: you can poke around by reading files

## Slide 30: CPI/Miss Rates/DRAM Access SpecInt2006
Instructions and Data
Data Only
Data Only
Notes: compare L1 to L2
compare inst to data (there’s also an L3, which is why sometimes Inst + Data < Data only L2)

## Slide 31: Clickers/Peer Instruction
Overall, what are L2 and L3 local miss rates?
A: L2 > 50%, L3 > 50%
B: L2 < 50%, L3 < 50%
C: L2 ~ 50%, L3 ~ 50%
D: L2 > 50%, L3 < 50%
E: L2 > 50%, L3 ~50%

## Slide 32: CS61C In the News
2 “Privacy-respecting” Laptops on the frontpage of Hacker News yesterday:
  The Gluglug Libreboot X200
  Purism Librem 13/15
Why does it matter?
  You can run all the free software you want, but:
    1) Who knows what the hardware is really doing?
    2) 99.999% of your machines still have proprietary “blobs” of driver/firmware code
      (some are even encrypted)
https://news.ycombinator.com/item?id=9912034
https://news.ycombinator.com/item?id=9912863

## Slide 33: Break

## Slide 34: Analyzing Code Performance on a Cache
Let’s say we’re interested in analyzing program performance with respect to the cache:
#define SZ 2048 // 2^11
int foo() {
int a[SZ];
int sum = 0;
for (int i = 0; i < SZ; i++) {
sum += a[i];
}
return sum;
}

## Slide 35: Analyzing Code Performance on a Cache
#define SZ 2048 // 2^11
int foo() {
int a[SZ];
int sum = 0;
for (int i = 0; i < SZ; i++) {
sum += a[i];
}
return sum;
}
1) Assume we only care about D$
So what do we care about?
The sequence of accesses to array a
2) Assume array is “block aligned”
i.e. First byte of a[0] is the first
byte in a block
3) Assume local vars live in registers
Notes: I$ is fairly predictable. Not too much the programmer could do wrong here.
Probably what will happen anyway. In any-case, won’t have a big effect on the analysis

## Slide 36: Analyzing Code Performance on a Cache
#define SZ 2048 // 2^11
int foo() {
int a[SZ];
int sum = 0;
for (int i = 0; i < SZ; i++) {
sum += a[i];
}
return sum;
}
Cache specs:
4 KiB Direct-Mapped
16 B Blocks
What’s the miss rate?
Important first questions:
What does our access pattern look like within a block?
How many cache blocks does our array take up? Does it fit entirely in the cache at once?

## Slide 37: Analyzing Code Performance on a Cache
#define SZ 2048 // 2^11
int foo() {
int a[SZ];
int sum = 0;
for (int i = 0; i < SZ; i++) {
sum += a[i];
}
return sum;
}
Cache specs:
4 KiB Direct-Mapped
16 B Blocks
What’s the miss rate?
What does our access pattern look like within a block?
We’re iterating over 2048 ints, each of which are 4 bytes. A block in this cache holds 4 ints: (16 B/block)/(4 B/int) = 4 ints/block

## Slide 38: Analyzing Code Performance on a Cache
What does our access pattern look like within a block?
We’re iterating over 2048 ints, each of which are 4 bytes. A block in this cache holds 4 ints: (16 B/block)/(4 B/int) = 4 ints/block
Block as bytes:
Block as ints:
a[0] | a[1] | a[2] | a[3]…
Iteration 0:
Compulsory Miss
Iteration 1:
Hit
Iteration 2:
Hit
Iteration 3:
Hit
This repeats over and over!
25% miss rate

## Slide 39: Analyzing Code Performance on a Cache #2
#define SZ 2048 // 2^11
int foo() {
int a[SZ];
int sum = 0;
for (int i = 0; i < SZ; i+=2) sum += a[i];
for (int i = 0; i < SZ; i+=2) sum += a[i];
return sum;
}
Cache specs:
4 KiB Direct-Mapped
16 B Blocks
What’s the miss rate?
What does our access pattern look like within a block?
We’re iterating over an array of 2048 ints (but only accessing 1024 of them), each of which are 4 bytes. A block in this cache holds 4 ints: (16 B/block)/(4 B/int) = 4 ints/block

## Slide 40: Analyzing Code Performance on a Cache
What does our access pattern look like within a block? (let’s stick with the first loop)
We’re iterating over 2048 ints 1024 ints, each of which are 4 bytes. A block in this cache holds 4 ints: (16 B/block)/(4 B/int) = 4 ints/block
Block as bytes:
Block as ints:
a[0] | a[1] | a[2] | a[3]…
Iteration 0:
Compulsory Miss
Iteration 1:
Hit
This repeats over and over for the first loop!
50% miss rate

## Slide 41: Analyzing Code Performance on a Cache
But now, we have to worry about question 2:
2) How many cache blocks does our array take up?
The array contains 2048 ints. That’s 2048*4 = 8192 B. Cache blocks are 16 B each, so 8192/16 = 512 blocks.
Does it fit entirely in the cache at once?
No. Cache is only 4096 B, contains
only 256 blocks.
Cache specs:
4 KiB Direct-Mapped
16 B Blocks

## Slide 42: Analyzing Code Performance on a Cache #2
#define SZ 2048 // 2^11
int foo() {
int a[SZ];
int sum = 0;
for (int i = 0; i < SZ; i+=2) sum += a[i];
for (int i = 0; i < SZ; i+=2) sum += a[i];
return sum;
}
Cache specs:
4 KiB Direct-Mapped
16 B Blocks
What’s the miss rate?
So, to figure out what loop 2’s performance is going to be like, we need to know what’s in the cache at the end of loop 1…

## Slide 43: Analyzing Code Performance on a Cache #2
#define SZ 2048 // 2^11
int foo() {
int a[SZ];
int sum = 0;
for (int i = 0; i < SZ; i+=2) sum += a[i];
// what’s the state of the cache here?
}
Cache specs:
4 KiB Direct-Mapped
16 B Blocks
What’s the miss rate?
Say for the sake of argument that our array starts at address 0. Then, halfway through the first loop (between i = 1022 and i = 1024), the first half of the array is in the cache.
a[0] …………………………………………………………………………………………………………………………………………………...............................a[1023]

## Slide 44: Analyzing Code Performance on a Cache #2
#define SZ 2048 // 2^11
int foo() {
int a[SZ];
int sum = 0;
for (int i = 0; i < SZ; i+=2) sum += a[i];
// what’s the state of the cache here?
}
Cache specs:
4 KiB Direct-Mapped
16 B Blocks
What’s the miss rate?
Now, when we execute the second half of the accesses in loop one, we replace everything already in the cache:
a[0] …………………………………………………………………………………………………………………………………………………...............................a[1023]
a[1024] …………………………………………………………………………………………………………………………………………………...............................a[2047]

## Slide 45: Analyzing Code Performance on a Cache #2
a[1024] …………………………………………………………………………………………………………………………………………………...............................a[2047]
#define SZ 2048 // 2^11
int foo() {
int a[SZ];
int sum = 0;
for (int i = 0; i < SZ; i+=2) sum += a[i];
// what’s the state of the cache here?
}
Cache specs:
4 KiB Direct-Mapped
16 B Blocks
What’s the miss rate?
So, at the end of the first loop, the second half of the array is in the cache.

## Slide 46: Analyzing Code Performance on a Cache #2
#define SZ 2048 // 2^11
int foo() {
int a[SZ];
int sum = 0;
for (int i = 0; i < SZ; i+=2) sum += a[i];
for (int i = 0; i < SZ; i+=2) sum += a[i];
return sum;
}
Cache specs:
4 KiB Direct-Mapped
16 B Blocks
What’s the miss rate?
Now, let’s take a look at loop 2. Notice that it’s going to start by accessing the first half of the array, none of which is in the cache.

## Slide 47: Analyzing Code Performance on a Cache
What does our access pattern look like within a block? (now, for the second loop)
We’re iterating over 2048 ints 1024 ints, each of which are 4 bytes. A block in this cache holds 4 ints: (16 B/block)/(4 B/int) = 4 ints/block
Block as bytes:
Block as ints:
a[0] | a[1] | a[2] | a[3]…
Iteration 0:
Capacity Miss
a[1024] was in this spot in the cache…
Iteration 1:
Hit
This repeats over and over for the second loop!
50% miss rate

## Slide 48: Analyzing Code Performance on a Cache #2
#define SZ 2048 // 2^11
int foo() {
int a[SZ];
int sum = 0;
for (int i = 0; i < SZ; i+=2) sum += a[i];
for (int i = 0; i < SZ; i+=2) sum += a[i];
return sum;
}
Cache specs:
4 KiB Direct-Mapped
16 B Blocks
What’s the miss rate?
So, we got a 50% miss rate for loop #1 and a 50% miss rate for loop #2. Now, we compute a weighted average:
Total miss rate = weighted average of miss rates.
Half the accesses were in loop 1, the other half in loop 2:
Total miss rate = 0.5 * loop1 miss rate + 0.5 * loop2 miss rate
Total miss rate = 0.5 * 50% + 0.5 * 50% = 50%

## Slide 49: Clicker Question p1
#define SZ 2048 // 2^11
int foo() {
int a[SZ];
int sum = 0;
for (int i = 0; i < SZ; i+=256) sum += a[i];
for (int i = 0; i < SZ; i+=256) sum += a[i];
return sum;
}
Cache specs:
1 KiB Direct-Mapped
16 B Blocks
What’s the miss rate for the first loop?
A. 0 % B. 25 % C. 50 % D. 75 % E. 100%
Notes: E

## Slide 50: Clicker Question p2
#define SZ 2048 // 2^11
int foo() {
int a[SZ];
int sum = 0;
for (int i = 0; i < SZ; i+=256) sum += a[i];
for (int i = 0; i < SZ; i+=256) sum += a[i];
return sum;
}
Cache specs:
1 KiB Direct-Mapped
16 B Blocks
What’s the miss rate for the second loop?
A. 0 % B. 25 % C. 50 % D. 75 % E. 100%
Notes: E

## Slide 51: Clicker Question p3
#define SZ 2048 // 2^11
int foo() {
int a[SZ];
int sum = 0;
for (int i = 0; i < SZ; i+=256) sum += a[i];
for (int i = 0; i < SZ; i+=256) sum += a[i];
return sum;
}
Cache specs:
1 KiB Direct-Mapped
16 B Blocks
What types of misses do we get in the first/second loops?
A. Capacity/Capacity B. Compulsory/Capacity
C. Compulsory/Conflict D. Conflict/Capacity
E. Compulsory/Compulsory
Notes: C

## Slide 52: In Conclusion, Huge Cache Design Space
Several interacting dimensions
  Cache size
  Block size
  Associativity
  Replacement policy
  Write-through vs. write-back
  Write-allocation
Optimal choice is a compromise
  Depends on access characteristics
    Workload
    Use (I-cache, D-cache)
  So we learned how to analyze code performance on a cache
Simplicity often wins
Associativity
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B