## Slide 1
EE130/230A Discussion 10
Peng Zheng

## Slide 2: Interface Trap Charge, QIT
Traps cause “sloppy” C-V and also greatly degrade mobility in channel
“Donor-like” traps are
charge-neutral when
filled, positively charged
when empty
Positive oxide charge
causes C-V curve to
shift toward left.
As VG decreases, there is more positive interface charge and hence the “ideal C-V curve” is shifted more to the left.
(a)
(a)
(b)
(b)
(c)
(c)
EE130/230A Fall 2013
Lecture 18, Slide 2
R. F. Pierret, Semiconductor Device Fundamentals, Fig. 18.10
R. F. Pierret, Semiconductor Device Fundamentals, Fig. 18.12
(a)(c) : inversiondepletionaccumulation

## Slide 3: Poly-Si Gate Technology
A heavily doped film of polycrystalline silicon (poly-Si) is often employed as the gate-electrode material in MOS devices.
  There are practical limits to the electrically active dopant concentration (usually less than 1x1020 cm-3)
  The gate must be considered as a semiconductor, rather than a metal
p-type Si
n+ poly-Si
n-type Si
p+ poly-Si
NMOS
PMOS
EE130/230A Fall 2013
Lecture 18, Slide 3

## Slide 4: MOS Band Diagram w/o Gate Depletion
Ec
EFS
Ev
Ec= EFM
Ev
qVG
qVox
qfs
M
O
S
WT
qfF
Lecture 16, Slide 4
qfF
EE130/230A Fall 2013

## Slide 5: MOS Band Diagram w/ Gate Depletion
How can gate depletion
be minimized?
VG is effectively reduced:
Ec
EFS
Ev
Ev
qVG
qfS
WT
p-type Si
n+ poly-Si gate
Ec
qVpoly
Wpoly
Si biased to inversion:
EE130/230A Fall 2013
Lecture 18, Slide 5

## Slide 6: Gate Depletion Effect
n+ poly-Si
Gauss’s Law dictates that Wpoly = eoxEox / qNpoly
xo is effectively increased:
p-type Si
-
-
-
-
-
-
+
+
+
+
+
+
N+
+
+
-
-
-
Cpoly
Cox
EE130/230A Fall 2013
Lecture 18, Slide 6

## Slide 7: Inversion-Layer Thickness, Tinv
The average inversion-layer location below the Si/SiO2 interface is called the inversion-layer thickness, Tinv .
EE130/230A Fall 2013
Lecture 18, Slide 7
C. C. Hu, Modern Semiconductor Devices for Integrated Circuits, Figure 5-24

## Slide 8: Effective Oxide Thickness, Toxe
(VG + VT)/Toxe can be shown to be the average electric field in the inversion layer. Tinv of holes is larger than that of electrons due to difference in effective masses.
EE130/230A Fall 2013
Lecture 18, Slide 8
C. C. Hu, Modern Semiconductor Devices for Integrated Circuits, Figure 5-25

## Slide 9: MOS Capacitor vs. MOS Transistor C-V (p-type Si)
VG
accumulation
depletion
inversion
VFB
VT
C
MOS transistor at any f,
MOS capacitor at low f, or
quasi-static C-V
MOS capacitor at high f
Cmin
Cmax=Cox
CFB
Lecture 17, Slide 9
EE130/230A Fall 2013

## Slide 10: Effective Oxide Capacitance, Coxe
EE130/230A Fall 2013
Lecture 18, Slide 10
C. C. Hu, Modern Semiconductor Devices for Integrated Circuits, Figure 5-26

## Slide 11: MOSFET Linear Region of Operation
For small values of VDS (i.e. for VDS << VGVT),
where meff is the effective carrier mobility
Hence the NMOSFET can be modeled as a resistor:
EE130/230A Fall 2013
Lecture 19, Slide 11

## Slide 12: Field-Effect Mobility, meff
Scattering mechanisms:
Coulombic scattering
phonon scattering
surface roughness
scattering
EE130/230A Fall 2013
Lecture 19, Slide 12
C. C. Hu, Modern Semiconductor Devices for Integrated Circuits, Figure 6-9

## Slide 13: MOSFET Saturation Region of Operation
When VD is increased to be equal to VG-VT, the inversion-layer charge density at the drain end of the channel equals 0, i.e. the channel becomes “pinched off”
As VD is increased above VG-VT, the length DL of the “pinch-off” region increases. The voltage applied across the inversion layer is always VDsat=VGS-VT, and so the current saturates.
VDS = VGS-VT
VDS > VGS-VT
VDS
ID
Lecture 19, Slide 13
R. F. Pierret, Semiconductor Device Fundamentals, Figs. 17.2, 17-3

## Slide 14: Ideal NMOSFET I-V Characteristics
EE130/230A Fall 2013
Lecture 19, Slide 14
R. F. Pierret, Semiconductor Device Fundamentals, Fig. 17.4