## Slide 1
EE130/230A Discussion 11
Peng Zheng

## Slide 2: Sample MOSFET I-V problem-Quiz 5 SP2013

## Slide 3: Sample MOSFET I-V problem-Quiz 5 SP2013

## Slide 4: Problem with “Square Law Theory”
Ignores variation in depletion width with distance y:
where
Lecture 20, Slide 4
EE130/230A Fall 2013

## Slide 5: MOSFET Small Signal Model (Saturation Region)
Conductance parameters:
A small change in VG or VDS will result in a small change in ID
Lecture 21, Slide 5
low-frequency:
high-frequency:
EE130/230A Fall 2013
R. F. Pierret, Semiconductor Device Fundamentals, Fig. 17.12

## Slide 6: Transconductance and Output Conductance
We hope to maximize transconductance gm
and minimize output conductance gd.
How?
In order to maximize the transconductance gm of an n-channel MOSFET:
  The equivalent gate oxide thickness (Toxe) should be decreased to increase the capacitive coupling between the gate and the inversion-layer channel.
Although µeff decreases with decreasing Toxe, Coxe and (VGS –VT) each increase (since VT
decreases) while m decreases with decreasing Toxe.
  The channel/body dopant concentration (NA) should be decreased to increase µeff and to decrease the capacitive coupling between the inversion-layer channel and the body, i.e. to decrease the body effect, so that (VGS –VT) increases and m decreases.
  The channel length (L) should be decreased to increase the saturation bias current and hence the change in saturation current for a given change in gate voltage.
In order to minimize the output conductance gd an n-channel MOSFET:
  Channel Length Modulation

## Slide 7: Channel Length Modulation
As VDS is increased above VDsat, the width DL of the depletion region between the pinch-off point and the drain increases, i.e. the inversion layer length decreases.
IDS
VDS
If DL is significant compared to L, then IDS will increase slightly with increasing VDS>VDsat, due to “channel-length modulation”
EE130/230A Fall 2013
Lecture 19, Slide 7
R. F. Pierret, Semiconductor Device Fundamentals, Figs. 17.2, 17-3

## Slide 8: Sub-Threshold Current
For |VG| < |VT|, MOSFET current flow is limited by carrier diffusion into the channel region.
The electric potential in the channel region varies linearly with VG, according to the capacitive voltage divider formula:
As the potential barrier to diffusion increases linearly with decreasing VG, the diffusion current decreases exponentially:
Lecture 21, Slide 8
EE130/230A Fall 2013

## Slide 9: Sub-Threshold Swing, S
Lecture 21, Slide 9
Inverse slope is subthreshold swing, S
[mV/dec]
log ID
VT
VGS
0
NMOSFET Energy Band Profile
increasing E
distance
n(E)  exp(-E/kT)
Source
Drain
increasing
VGS
EE130/230A Fall 2013

## Slide 10: Drain Induced Barrier Lowering (DIBL)
As the source and drain get closer, they become electrostatically coupled, so that the drain bias can affect the potential barrier to carrier diffusion at the source junction.
 VT decreases (i.e. OFF state leakage current increases)
Lecture 22, Slide 10
EE130/230A Fall 2013
C. C. Hu, Modern Semiconductor Devices for Integrated Circuits, Figure 7-5
Notes: The extreme case of SCE
Short-channel MOSFET Id-Vg: DIBL & S degradation -> Ioff increasing

## Slide 11: Questions regarding project? Good luck to Quiz#5!