## Slide 1
EE130/230A Discussion 13
Peng Zheng

## Slide 2: Why New Transistor Structures?
Off-state leakage (IOFF) must be suppressed as Lg is scaled down
  allows for reductions in VT and hence VDD
Leakage occurs in the region away from the channel surface
   Let’s get rid of it!
Drain
Source
Gate
Lg
Thin-Body
MOSFET:
Buried Oxide
Source
Drain
Gate
Substrate
“Silicon-on-Insulator” (SOI)
Wafer
2

## Slide 3: Thin-Body MOSFETs
IOFF is suppressed by using an adequately thin body region.
  Body doping can be eliminated
   higher drive current due to higher carrier mobility
Ultra-Thin Body (UTB)
Buried Oxide
Substrate
Source
Drain
Gate
TSi
Lg
TSi < (1/4)  Lg
Double-Gate (DG)
Gate
Source
Drain
Gate
TSi
TSi < (2/3)  Lg
3

## Slide 4: Effect of TSi on OFF-state Leakage
IOFF = 19 A/m
IOFF = 2.1 nA/m
Leakage Current
Density [A/cm2]
@ VDS = 0.7 V
106
10-1
3x102
0.0
4.0
8.0
12.0
16.0
20.0
G
G
S
D
G
G
S
D
Si Thickness [nm]
Lg = 25 nm; tox,eq = 12Å
TSi = 10 nm
TSi = 20 nm
4

## Slide 5: BJT Types and Definitions
Electrostatics:
  Under normal operating conditions, the BJT may be viewed electrostatically as two independent pn junctions
The BJT is a 3-terminal device, with two types: PNP and NPN
VEB = VE – VB
VCB = VC – VB
VEC = VE – VC
= VEB - VCB
VBE = VB – VE
VBC = VB – VC
VCE = VC – VE
= VCB - VEB
EE130/230A Fall 2013
Lecture 25, Slide 5
R. F. Pierret, Semiconductor Device Fundamentals, p. 372

## Slide 6: BJT Circuit Configurations
Output Characteristics for Common-Emitter Configuration
EE130/230A Fall 2013
Lecture 25, Slide 6
R. F. Pierret, Semiconductor Device Fundamentals, Fig. 10.4
R. F. Pierret, Semiconductor Device Fundamentals, Fig. 10.3

## Slide 7: BJT Modes of Operation
Common-emitter output characteristics
(IC vs. VCE)
Mode | Emitter Junction | Collector Junction
CUTOFF | reverse bias | reverse bias
Forward ACTIVE | forward bias | reverse bias*
Reverse ACTIVE | reverse bias* | forward bias
SATURATION | forward bias | forward bias
*more precisely: not strongly forward biased
EE130/230A Fall 2013
Lecture 25, Slide 7
R. F. Pierret, Semiconductor Device Fundamentals, Fig. 10.5

## Slide 8: Sample Problem

## Slide 9: Sample Problem

## Slide 10: Questions regarding the MOSFET design project?
Happy Holidays!