UNIVERSITY OF CALIFORNIA

College of Engineering

Department of Electrical Engineering and Computer Sciences

EE 130	Prof. Liu

Spring 2007

Term Project Update (4/14/07)

Part I: Manual Design of Ideal BJT Structure [75 points]

In addition to the performance parameters given in the sample design, we have also included the following values as checkpoints throughout your design.

# Sample design:

To allow you to verify your equations/program, a sample BJT design and its resulting performance parameters are provided below:

|  | Emitter | Base | Collector |
| --- | --- | --- | --- |
| Width | 5e-5 cm | 1e-5 | 2e-4 |
| Doping | 1.5e19 | 2e17 | 1e15 |

T=273K, VBE=0.8598 V

| μE (cm2/V/s) | 67.05 |
| --- | --- |
| μB (cm2/V/s) | 652.88 |
| μC (cm2/V/s) | 554.77 |
| Vbi,EB | 0.968 V |
| Vbi,BC | 0.782 V |
| Cdep,EB | 39.0 fF |
| Cdep,BC | 1.03 fF |
| tF | 8.67 ps |

T=273K, IC = 1 mA

| (dc | 110.84 |
| --- | --- |
| VA | 21.16 V |
| Vpunchthrough | 103.15 V |
| fT, edge of saturation | 11.8 GHz |

T=300K, VBE=0.8164 V

| μE (cm2/V/s) | 64.42 |
| --- | --- |
| μB (cm2/V/s) | 601.92 |
| μC (cm2/V/s) | 457.89 |
| Vbi,EB | 0.951 V |
| Vbi,BC | 0.732 V |
| Cdep,EB | 34.9 fF |
| Cdep,BC | 1.07 fF |
| tF | 5.43 ps |

T=300K, IC = 1 mA

| (dc | 184.98 |
| --- | --- |
| VA | 19.59 V |
| Vpunchthrough | 107.92 V |
| fT, edge of saturation | 13.9 GHz |

T=343K, VBE=0.7457 V

| μE (cm2/V/s) | 60.83 |
| --- | --- |
| μB (cm2/V/s) | 525.62 |
| μC (cm2/V/s) | 350.10 |
| Vbi,EB | 0.923 V |
| Vbi,BC | 0.651 V |
| Cdep,EB | 30.4 fF |
| Cdep,BC | 1.13 fF |
| tF | 3.28 ps |

T=343K, IC = 1 mA

| (dc | 335.82 |
| --- | --- |
| VA | 17.33 V |
| Vpunchthrough | 116.54 V |
| fT, edge of saturation | 13.5 GHz |

Part II: Computer Simulation of a More Realistic BJT Structure [25 points]

- Add a statement to generate an IC vs. VCE plot for multiple values of IB: 10 A, 20 A, 30 A, 40 A and 50 A. To plot the output characteristics, assume that IB only depends on VBE.

We are providing the MEDICI code that allows you to generate a family of curves for the IC vs. VCE plot. At the end of your input file (Line 107) add the following lines of code:

COMMENT  	Generate Ic vs Vce characteristics

COMMENT  	Solve Ic for Ib=10uA

SOLVE         	V(Base)=[Value of VBE that corresponds to IB=10uA] V(Collector)=0.1

LOG             	OUT.FILE=Ib10uA

SOLVE    	V(Collector)=0  ELEC=Collector  VSTEP=0.5  NSTEP=10

LOG       	CLOSE

COMMENT   Solve Ic for Ib=20uA

SOLVE     	V(Base)=[Value of VBE that corresponds to IB=20uA]  V(Collector)=0.1

LOG       	OUT.FILE=Ib20uA

SOLVE     	V(Collector)=0  ELEC=Collector  VSTEP=0.5  NSTEP=10

LOG       	CLOSE

COMMENT   Solve Ic for Ib=30uA

SOLVE     	V(Base)=[Value of VBE that corresponds to IB=30uA] V(Collector)=0.1

LOG       	OUT.FILE=Ib30uA

SOLVE     	V(Collector)=0  ELEC=Collector  VSTEP=0.5  NSTEP=10

LOG       	CLOSE

Following the pattern, repeat the above section of code for IB: 40 A and 50 A

To plot the characteristics, add these lines:

COMMENT   	Plot Ic vs. Vce output characteristics

PLOT.1D   	Y.AXIS=I(Collector)  X.AXIS=V(Collector)

+         	TITLE="Ic vs. Vce" IN.FILE=Ib50uA PRINT LINE=2 POINTS COLOR=5

PLOT.1D   	Y.AXIS=I(Collector) X.AXIS=V(Collector) IN.FILE=Ib40uA

+         		PRINT LINE=2 POINTS COLOR=4 UNCHANGE

PLOT.1D   	Y.AXIS=I(Collector) X.AXIS=V(Collector) IN.FILE=Ib30uA

+         		PRINT LINE=2 POINTS COLOR=3 UNCHANGE

PLOT.1D   	Y.AXIS=I(Collector) X.AXIS=V(Collector) IN.FILE=Ib20uA

+         PRINT LINE=2 POINTS COLOR=2 UNCHANGE

PLOT.1D   	Y.AXIS=I(Collector) X.AXIS=V(Collector) IN.FILE=Ib10uA

+         		PRINT LINE=2 POINTS COLOR=1 UNCHANGE