UNIVERSITY OF CALIFORNIA

College of Engineering

Department of Electrical Engineering and Computer Sciences

EE 130	Discussion Section 101

Spring 2007	Frank Liao

Worksheet 6A

(Adapted from EE130 2003 and 2004)

1) Suppose an NMOSFET has a VT of 0.5V. Sketch a band diagram for this MOSFET along slice Q-Q’ (shown below) for VDS = 1.0V and VGS = 1.0V. Also sketch a band diagram for the same device along the W-W’ slice. Assume that Q-Q’ is the drain side.

2) Suppose we increase the channel doping of this MOSFET. Assume I change the gate workfunction so that the threshold voltage stays unchanged.

a) What would be the impact on the output resistance? Give reasons.

Output resistance should generally increase, since I would reduce the penetration of drain-side depletion region into the channel.

b) When I changed the gate workfunction – should I have increased it or decreased it to

keep the VT constant?

The gate workfunction should be decreases, resulting in a reduction in VFB and therefore in VT, to compensate for the increase in VT due to increased doping.

3) Suppose I increase the L of the MOSFET, how will the small-signal output resistance change? Why?

The MOSFET should have a higher small-signal output resistance, since it will suffer less from channel length modulation effects.

4) Assume the MOSFET has a series resistance that is approximately 25% of the large signal channel resistance (IDsat/VDS). Draw a band diagram for the MOSFET along slice X-Y for the MOSFET, assuming VT = 0.5V, VG = 1V, and VD = 1V. Make sure you include the source/drain regions in your band diagram.

5) For this MOSFET, indicate how Vdsat and Idsat change (increase (↑) or decrease (↓) or unchanged (n/c)) when various device parameters are changed as indicated:

# Text boxes

Q-Q’

W-W’