## Slide 1: Discussion today
Over the next two class periods we will be designing a ring resonator based 2-channel wavelength division multiplexing (WDM) optical link.
Today we will look at the following:
  Discuss modulation of light
  Review ring resonator and how we can use a ring resonator to modulate light
  Introduce Lumerical DEVICE, an optoelectronic charge transport solver
  Simulate carrier density in ring resonator modulator as a function of applied bias
  Simulate effective index of ring resonator modulator waveguide as a function of applied bias.

## Slide 2: (Amplitude) modulation of light
CW Laser
Modulator
Data in
Light out
intensity
intensity
voltage

## Slide 3: Ring resonator
Light traveling down waveguide can couple to resonant mode within the ring resonator.
Resonance wavelength occurs when light accumulates a phase shift of when traveling around the ring:
Waveguide
Ring Resonator

## Slide 4: Power transmission

## Slide 5: Modulation of light with ring resonator
Recall
If we have a means to change the effective index on-demand we can shift the resonance frequency of the ring resonator.
6

## Slide 6: Modulation of light with ring resonator
6

## Slide 7: Refractive index of silicon depends on free carrier density
Silicon has weak non-linear effect
Instead, through electrical bias we can change the free carrier density to modulate the index of refraction.
Very small change though! to
*R. A. Soref and B. R. Bennett, SPIE Integr. Opt. Circuit Eng. 704, 32 (1987)

## Slide 8: Depletion width modulation in pn junction
p-type
n-type
p-type
n-type
V=0
V<0
junction
junction
Depletion region
Depletion region
+
-
+
-

## Slide 9: pn junction ring resonator
p-contact
n-contact
ring
Input
Output
V
p
n
Reverse bias V < 0  carriers are swept out of junction
No applied bias (V=0)
hole concentration
electron concentration
hole concentration
electron concentration
Cross section of ring waveguide

## Slide 10: On-off keying modulation
Laser frequency
Output = 1
Laser frequency
Output = 0
Input
Input
x
p-contact
n-contact
ring
p-contact
n-contact
ring
Apply voltage
Frequency
Frequency

## Slide 11: 4-Channel WDM
fiber
fiber
Data in
CW lasers
Transmitter
Receiver

## Slide 12: Simulation strategy
Use DEVICE to calculate carrier density in the ring waveguide as a function of applied voltage bias
Import carrier density into MODE and calculate effective index as a function of applied bias
Import effective index as function of voltage into INTERCONNECT and design ring resonator dimensions using analytical model
Simulate entire optical link using INTERCONNECT

## Slide 13: Simple pn-junction simulation
Open the file pn_junction.ldev
You will see the geometry of a 10 um thick silicon slab contacted on either side by aluminum.
Geometry can be created in DEVICE just as you would in FDTD or MODE
In the next steps we will add p and n-type doping to create a pn-junction within the silicon slab.

## Slide 14: Edit simulation region
Right-click simulation region on left panel
Click Edit object

## Slide 15: Create CHARGE solver
Click CHARGE in Solvers bar
Right click, Edit object

## Slide 16: Create p-type doping
Under CHARGE tab (top), Doping  Constant
Right click, Edit object
Click OK

## Slide 17: Create n-type doping
Under CHARGE tab (top), Doping  Constant
Right click, Edit object
Click OK

## Slide 18: pn junction
p-type
n-type
Contact (Al)
Contact (Al)

## Slide 19: Add mesh refinement at junction
Click Solver Constraint
Click Edit Object

## Slide 20: Add n contact
Click Boundary conditions Electrical
Right-click, Edit object

## Slide 21: Add n contact

## Slide 22: Add p contact
Click Boundary conditions Electrical
Right-click, Edit object

## Slide 23: Add p contact

## Slide 24: Simulation
Click Run
Right-click CHARGE  Visualize  pos to plot I-V curve
Under Attributes, select Vs and Vc and click Remove, to show only currents
e- current
p+ current
Displacement current
(none since DC simulation)

## Slide 25: Simulation
We can plot other data such as quasi-fermi levels, carrier concentration, etc. but will not explore that further here.

## Slide 26: pn junction ring resonator
Open the file ring_resonator_pn_junction.ldev
Simulates the carrier density as a function of applied bias for a pn junction ring resonator
Silicon rib waveguide
p-contact
n-contact
pn junction
p
n-type
n
p-type

## Slide 27: pn junction ring resonator
Run simulation (at home)
Right-click CHARGE  Visualize  charge
Scroll wheel to zoom in

## Slide 28: pn junction ring resonator
Right-click CHARGE  Visualize  charge
Scroll wheel to zoom in
Vcathode = 0 V
Vcathode = 3 V

## Slide 29: Import carrier density into MODE
Carrier density information has been saved to the file mod_carriers.mat
Open the file pn_junction_waveguide.lms
You will see the same pn junction waveguide geometry in MODE.
We now need to import the charge density that we simulated in DEVICE.

## Slide 30: Create np density attribute
Click Attributes  np Density
Right-click Edit object.
Click Import Data…
Select mod_carriers.mat

## Slide 31: Run simulation
Next we will run a simulation sweep that will sweep through each of the carrier densities that we measured at each applied voltage
Run the sweep reverse (at home)
Run the script plot_MODE_data.lsf (click and drag into simulation window; click run)
This will plot two graphs showing the change in effective index and waveguide loss for each applied voltage.

## Slide 32: Effective index and loss
Small change in effective index!
Why does loss go down with increasing reverse bias voltage?