## Slide 1
Vanishing points

## Slide 2: ML estimate of a vanishing point from imaged parallel scene lines
Estimate the VP and fitted lines simultaneously by solving a nonlinear
Levenson Marquardt optimization algorithm;
One option:
find pariwise intersection, then compute centrod of that intersection

## Slide 3
Vanishing lines

## Slide 4: If K is known, then plane vanishing line may be used to find information about the plane
Can show that plane with vanishing Line l has orientation KT l in camera’s Euclidean coordinate frame
Plane can be metrically rectified given only its vanishing line:
compute normal from vanishing line, then synthetically rotate
camera by homography so that the plane is fronto parallel, ie.
parallel to the image plane
If l1 and l2 are vanishing lines for two Planes, then the angle between the planes Is given by :
θ
ω
ω
ω

## Slide 5
Vanishing point of a line parallel to a plane lies on the vanishing line of the plane
a
B c

## Slide 7
Orthogonality relation: can help find ω and K
ω
θ

## Slide 8: Affine properties can be measured only from vanishing line of a plane and vanishing point of a direction not parallel to the plane
Convenient to think of scene plane π as the horizontal ground plane; vanishing line is l is the horizon.
Convenient to think of the direction orthogonal to the scene plane as vertical; v is the vertical vanishing point
Given l and v, we can measure the relative length of two line segments in the vertical direction;
No need to know K
In general direction v need not be orthogonal to plane π

## Slide 11
π
Use the tiles on the floor (horizontal plane) to find the vanishing line of the plane. Use the vertical lines in the scene
To determine the vertical vanishing point.

## Slide 12
Five constraints gives us five equations and can determine w

## Slide 13: Computing K from scene and internal constraints

## Slide 14
Calibration from vanishing points and lines
Assumes zero skew, square pixels and 3 orthogonal vanishing points
Principal point is the orthocenter of the trinagle made of 3 orthogonol vanishing lines

## Slide 16
Assume zero skew, square pixels,  calibrating conic is a circle;
How to find it, so that we can get K?

## Slide 17
Assume zero skew , square pixels, and principal point is at the image center
Then ω is diagonal{1/f^2, 1/f^2,1) i.e. one degree of freedom need one more
Constraint to determine f, the focal length  two vanishing points corresponding
To orthogonal directions.
From two vanishing point, can also find vanishing line of the building façade;
Given K and vanishing line l, synthetically rotate the camera so that façade is
Fronto parallel: map the image with a homography

## Slide 18
Scene consists of three dominant and mutually orthogonal planes: building façade on the right; on the left, and ground plane
Parallels line sets in three orthogonal directions define three vanishing points and together with the constraint of square pixels of
camera , calibration can be performed.
From vanishing points find three vanishing lines for the 3 planes.
Vanishing lines and ω can be used to find homography for each plane
Use homography to texture map the appropriate image regions onto the orthogonal planes of the model

## Slide 19
The calibrating conic: image of a cone with apex angle 45 degrees ; axis coinciding with the principal axis of the camera
If camera matrix is P = K [ I 0 ] then map of the cone is a calibrating conic given by: