## Slide 1: EE40 Lecture 11 Josh Hug
7/19/2010

## Slide 2: Logistical Things
Lab 4 tomorrow
Lab 5 (active filter lab) on Wednesday
  Prototype for future lab for EE40
  Prelab is very short, sorry.
  Please give us our feedback
  Google docs for labs and general class comments now available (link shared via email)
  Bring a music player if you have one (if not, you can use the signal generator in the lab)
HW5 due tomorrow at 2PM
HW6 due Friday at 5PM (also short)
Midterm next Wednesday 7/28
  Focus is heavily on HW4, 5, 6, and Labs P1, 4, 5
  Will reuse concepts from HW 1,2,3

## Slide 3: Logistics
No lunch today
Slightly shorter lecture today
Midterm regrade requests due today
Office hours Cory 240 2:30-4PM or so

## Slide 4: iClicker Question #1
Consider a capacitor with a capacitance of . Total resistance of circuit is small .
If we compile an I-V table in lab with a voltage source and multimeter by:
  Applying a set of test voltages
  Measuring current through the capacitor for each source
What I-V characteristic will we get?
  A. Horizontal line at I=0
  B. Vertical line at I=0
  C. Line of slope 1/RC
  D. Horizontal line at I=V/1Ω
  E. Something else

## Slide 5: iClicker Question #2
Consider an inductor with an inductance of H. Total resistance of circuit is small .
If we compile an I-V table in lab with a voltage source and multimeter by:
  Applying a set of test voltages
  Measuring current through the inductor for each source
What I-V characteristic will we get?
  A. Horizontal line at I=0
  B. Vertical line at I=0
  C. Line of slope R/L
  D. Line at I=V/1Ω
  E. Something else

## Slide 6: Easy Method for AC Circuits
We want to find the voltage across the capacitor for the following circuit
Homogenous solution is easy, since source is irrelevant
Finding particular solution the usual way (plugging in a guess, finding coefficients that cancel) is painful

## Slide 7: Easy Method for AC Circuits
Guess
Guess
Plug into ODE
Divide by . Now is gone
Solve for (easy)
Plug into ODE
Solve for A and (hard)

## Slide 8: Memory Circuits with Exponential Source
Homogeneous solution is just
Pick particular solution , plug in:
Divide by , and solve for k1
Real part of gives solution for cosine source

## Slide 9: Inverse Superposition
Superposition tells us that our output will just be the sum of the effect of these two sources
Luckily for us, all complex numbers are the sum of their real and imaginary parts
Just find real part and we’re done!

## Slide 10: Real Part of Expression
Finding the real part of the expression is easy, it just involves some old school math that you’ve probably forgotten (HW5 has complex number exercises)
Key thing to remember is that complex numbers have two representations
  Rectangular form:
  Polar form:

## Slide 11: Real Part of Expression
What we have is basically the product of two complex numbers
Let’s convert the left one to polar form
  Rectangular form:
  Polar form:

## Slide 12: Real Part of Expression

## Slide 13: Real Part of Expression
Superposition tells us that our output will just be the sum of the effect of these two sources
Thus, particular solution (forced response) of original cosine source is just the real part

## Slide 14: Easy Method for AC Circuits
Guess
Plug into ODE
Divide by . Now is gone
Solve for (easy)
Write ODE
Just as actually writing the ODE isn’t necessary for DC sources, we can avoid the ODE again in AC circuits:
Impedance Analysis

## Slide 15: Impedance
For a complex exponential source:
Rewrite as:
Let
Looks a lot like…
voltage divider
Real part gives solution for

## Slide 16: Method of Impedance Analysis (without Phasors)
Replace passive components with equivalent impedance, , ,
Replace all sources with complex exponentials
    e.g.
Solve using Ohm’s Law of Impedances for complex exponential sources
  Just like normal node voltage, but with complex numbers
  Real part of node voltage gives true output
Lugging these complex exponential functions is algebraically annoying

## Slide 17: Phasors (not in the book!)
Definition: A phasor is a complex number which represents a sinusoid
Three parameters
  A: Magnitude
  : Frequency
  Phase
The phasor representation of the sinusoid above is
In shorthand we write phasor as

## Slide 18: Phasors
If we have a voltage
The phasor version of the voltage is =
If we have a phasor =, the time function this phasor represents is

## Slide 19: Why are phasors useful?
Sources that look like result in lots of terms in our algebra
When you apply a sinusoidal source to a circuit, the amplitude and phase will vary across components, but it will always still be
  Important: doesn’t change!
    Otherwise we’d need REALLY complex numbers
Thus, we’ll just replace our sources with a complex number and just keep in mind that this number represents a function throughout

## Slide 20: Why are phasors useful?
We know that for complex exponential sources, we have that:
Phasors are complex numbers and which represent cosine functions and
Cosine functions are just the real parts of complex exponentials
Thus, in the world of phasors, we can just rewrite Ohm’s Law of Impedances as:

## Slide 21: Method of Impedance Analysis (with Phasors)
Replace passive components with equivalent impedance, , ,
Replace all sources with phasor representation: e.g.
Solve using Ohm’s Law of Impedances:
  Just like normal node voltage, but with complex numbers, attaining voltage phasors ,
  Output is just
Original sources are implicitly represented by phasors
  Time is gone completely from our problem

## Slide 22: Example
,
Find in
steady state

## Slide 23: Example
Polar divided by non polar, so convert bottom to polar
Find in
steady state

## Slide 24: Example
So
Find in
steady state

## Slide 25: Example
[in steady state]
Find in
steady state

## Slide 26: Example
Current has same shape as voltage
Current is times smaller than source voltage
Current leads source voltage by radians or
  seconds
Not to scale

## Slide 27: Harder Example
On board

## Slide 28: Filters
Often, we’ll want to build circuits which react differently based on different signal frequencies, e.g.
  Splitting audio signals into low and high portions (for delivery to tweeter and subwoofer)
  Removing noise of a particular frequency (e.g. 60 Hz noise or vuvuzela sound)
  Removing signals except those at a certain frequency

## Slide 29: Example Filter
Find vc in
steady state
- Transfer Function

## Slide 30: Transfer Functions
Maps system input signal to system output signal
  Plug an input voltage into
  Get an output voltage
    Output is scaled and shifted in time
      Scaling and shifting depend on frequency
    Frequency is unchanged (linear system)
Tells you how system will respond to any frequency, a.k.a. frequency response

## Slide 31: Using a Transfer Function
Suppose is
Output phasor is just
  )

## Slide 32: Using a Transfer Function (general)
Suppose is
Output phasor is just
  )

## Slide 33: Bode Magnitude Plot
Magnitude plot is just a plot of as a function of
Linear Scale
Log Scale

## Slide 34: Bode Magnitude Plot in Context of Circuit
All frequencies below get
through pretty well. Above, that
increasingly attenuated

## Slide 35: Bode Phase Plot
Phase plot is just a plot of as a function of
Linear Scale
Semilog Scale

## Slide 36: Bode Phase Plot in Context of Circuit
All frequencies below
move in time with the source, above
that, gets out of phase

## Slide 37: Frequency vs. Time Domain
Almost always, our signals consist of multiple frequencies
Examples:
  Sound made when you press a buttons on a phone is two pure sine waves added together (DTMF)
  Antennas on radio theoretically pick up ALL frequencies of ALL transmissions
Using a technique known as the Fourier Transform, we can convert any signal into a sum of sinusoids
  See EE20 for more details

## Slide 38: Fourier Transform Example
If someone whistles a signal that is approximately , and we apply the Fourier Transform, then:

## Slide 39: Fourier Transform Example
The 1 button on a phone is just

## Slide 40: Fourier Transform Example
If we apply a filter with the frequency response on the left to the signal on the right
Then we’ll get:

## Slide 41: Types of Filters
Passive Filters
  Filters with no sources (i.e. just R, L, and C)
  Don’t require power source
  Scale to larger signals (no op-amp saturation)
  Cheap
Active Filters
  Filters with active elements, e.g. op-amps
  More complex transfer function
    No need for inductors (can be large and expensive, hard to make in integrated circuits)
    More easily tunable
  Response more independent of load (buffering)

## Slide 42: Filter Examples
On board

## Slide 43: Manually Plotting
In this day and age, it is rarely necessary to make our Bode plots manually
However, learning how to do this will build your intuition for what a transfer function means
Manual plotting of bode plots is essentially a set of tricks for manually plotting curves on a loglog axis
We will only teach a subset of the full method (see EE20 for a more thorough treatment)

## Slide 44: Example Filter
Intuitive plot on board
More thorough algorithm next time
Find vc in
steady state

## Slide 45: Extra Slides

## Slide 46: Why do equivalent Impedances work?
Components with memory just integrate or take the derivative of , giving scaled versions of the same function
  This is unlike forcing functions like or
  This allows us to divide by the source, eliminating from the problem completely
  Left with an algebra problem
  [For those of you who have done integral transforms, this whole process can be thought of as just using Laplace/Fourier transforms]