## Slide 1: EE40 Lecture 15 Josh Hug
7/30/2010

## Slide 2: Logistics
HW7 due Tuesday
HW8 will be due next Friday
Homeworks will be less mathematically intense starting with the second half of HW7
Details on Project 2 demo and Mini-Midterm 3 details on Monday

## Slide 3: Midterm 2
I can show you your midterm 2 grade, but problem 5 needs regrading [most people will get 3 to 6 more points]
At the moment, mean is 102 and standard deviation is 24
First midterm was mean 103, standard deviation 20
Some oochness will happen here

## Slide 4: Logic Gates and Static Discipline
(On the board before we started)

## Slide 5: iClicker Warmup
We’re going to have a ton of iClicker questions today
A quick warmup. Have you played Starcraft 2?
  Yes
  No
  Starwhat?

## Slide 6: Field Effect Transistor
+
–
C
P is (effectively) a high resistance block of material, so current can barely flow from + to –
The n region is a reservoir of extra electrons (we will discuss the role of the n region later)
When C is “on”, i.e. is relatively positive, then electrons from inside the P region collect at bottom of insulator, forming a “channel”
- - - - - - - - - - - - -
(Drain)
(Source)
(Gate)
+
-

## Slide 7: Field Effect Transistor
+
–
C
When the channel is present, then effective resistance of P region dramatically decreases
Thus:
  When C is “off”, switch is open
  When C is “on”, switch is closed
- - - - - - - - - - - - -
(Drain)
(Source)
(Gate)
+
-

## Slide 8: Field Effect Transistor
+
–
C
If we apply a positive voltage to the plus side
  Current begins to flow from + to –
  Channel on the + side is weakened
If we applied a different positive voltage to both sides?
- - - - - -
(Drain)
(Source)
(Gate)
+
-
+
-

## Slide 9: Field Effect Transistor Summary
“Switchiness” is due to a controlling voltage which induces a channel of free electrons
Extremely easy to make in unbelievable numbers
Ubiquitous in all computational technology everywhere

## Slide 10: Discussion Today
In discussion today, we’ll go over the physics of MOSFETs for those of you who are curious
Time permitting, we’ll discuss at a future date in class as well (so yeah, it will be slightly redundant)

## Slide 11: MOSFET Model
Schematically, we represent the MOSFET as a three terminal device
Can represent all the voltages and currents between terminals as shown to the right

## Slide 12: MOSFET Model
What do you expect to be?
+
–
C
(Drain)
(Source)
(Gate)

## Slide 13: S Model of the MOSFET
The simplest model basically says that the MOSFET is:
  Open for
  Closed for

## Slide 14: Building a NAND gate using MOSFETs
Consider the circuit to the right where
On your worksheet, we’ll show that
Demonstration also on page 294 of the book
A
B
C

## Slide 15: MOSFET modeling
MOSFET models vary greatly in complexity
For example, an “ON” MOSFET has some effective resistance (not an ideal switch)
We will progressively refine our model of the MOSFET
  Will add capacitance later today
  If we have time in the next 2 weeks, we will also talk about using MOSFETs as analog amplifiers which will necessitate an even better model

## Slide 16: SR Model of the MOSFET
[Has nothing to do with SR flip-flop]

## Slide 17: NAND with the SR Model
What is when either of the inputs is low?
Draw the equivalent circuit when both inputs are high. What is
Q2

## Slide 18: NAND with the SR Model
Assume static discipline requires V and
Assume is
Choose a such that the static discipline for is met:
A.
B.
C.
D.
OHigh:
OLow:
Q3

## Slide 19: NAND with the SR Model
Assume static discipline requires V and
Assume and
Choose an and such that meets the static discipline
OHigh:
OLow:
Note: is usually called a “Pull-up resistor”
Q4

## Slide 20: Another SR Model Example
Replace the left MOSFET with the equivalent circuit when A is high
What is on the right NMOS if A is high?
  A.
  B.
  C.
  D.
Q5

## Slide 21: Another SR Model Example
When A is on,
What is when A is high?
  A.
  B.
  C.
  D.
Q6

## Slide 22: The power of digital circuits
At each stage, circuit restores the signal
Can think of each MOSFET as diverting the 5V or 0V power supply into the next gate
Tolerant to noise and manufacturing error
0.48V
5V
0.45V

## Slide 23: The power of digital circuits
How much noise could we tolerate on the input of the 2nd gate?
On the input of the 3rd gate?
0.48V
5V
0.45V
OUT
A
G1
G2

## Slide 24: The power of digital circuits (literally)
Like all circuits, digital circuits consume power
Amount of power will be dependent on state of our MOSFET switches

## Slide 25: Power Example
What is the power dissipation when A=1, B=1, C=0?
First, draw circuit with ON MOSFETS replaced with resistors
Then, calculate
Q7

## Slide 26: Power Example
In general, power consumption will depend on which inputs are high and which are low
“Worst case analysis” is when we pick the set of inputs which consumes the most power

## Slide 27: Static Power
Using only NMOS to implement our gates will result in a gate which constantly eats up power
  If you wire such a gate up on a breadboard, it will hum along using power all day
Later today, we will see a technique called CMOS to avoid this static power dissipation
But first, let’s discuss delay

## Slide 28: The SRC Model of an NMOS Transistor
So far, our NMOS implementation of logic gates allow for instantaneous switching
In real life, of course, an NMOS implementation will take some non-zero time to switch
Simulation by Wade Barnes
Green: Inverter Input
Red: Inverter Output

## Slide 29: The SRC Model
The SRC Model is almost identical to the SR model, except that each gate node has a capacitance
Like SR model: open when OFF and resistive when ON
Note that now is non-zero!

## Slide 30: The SRC Model
Useful for modeling:
  Gate delay: Takes time to charge up
  Dynamic power:

## Slide 31: SRC Model
Consider our familiar pair of inverters
We’re going to focus on the behavior of our left inverter
Let’s assume that both MOSFETs have a gate capacitance of or

## Slide 32: SRC Model of our 2 Inverters
We decide to ignore the function of the gate on the right, keeping it in mind only because we know we’ll have to charge it

## Slide 33: Analysis of SRC Model
When the gate voltage has been less than (i.e. the gate capacitor is not charged) for a long time, what is ?
Q8

## Slide 34: Analysis of SRC Model
Now assume has been low for a long time and thus
If the logic gate upstream of rises above 1V, the SRC model of the left MOSFET says it should instantly switch to “ON”
Draw the equivalent circuit on the MOSFET worksheet
Q9

## Slide 35: Analysis of SRC Model
If , and the resistor suddenly appears at t=0
What is ?
Q10

## Slide 36: Timing Analysis of the SRC model
What is the time constant for the discharge of ?
Q11

## Slide 37: Timing Analysis of the SRC model
Since , , and , then:
How long will it take for the next inverter in the chain to turn on?

## Slide 38: Timing Analysis of the SRC model
So
We call this the “Fall Time”: gives time for to fall from 5V to 1V

## Slide 39: Fall Time
Gives:

## Slide 40: Timing Analysis of the SRC model
How do we find the Rise Time?
Have to replace by new equivalent circuit where:
  Capacitor is initially discharged (0.476 V)
  Switch is open

## Slide 41: Timing Analysis of the SRC model
How do we find the Rise Time?
Have to replace by new equivalent circuit where:
  Capacitor is initially discharged (0.476 V)
  Switch is open

## Slide 42: Timing Analysis of the SRC model

## Slide 43: Timing Analysis of the SRC model

## Slide 44: Propagation Delay
Rise and Fall Time are also called “Propagation Delays”
Gives “delay time” between when the logical input changes and the logical output changes
Book calls them and

## Slide 45: Reminder of Where We Started
OUT
A
G1
Wanted to study gate delay of:
So used SRC model:
Which implements:
Giving delay of LEFT gate!

## Slide 46: Using Propagation Delays
OUT
A
G1
Suppose A has been zero a long time and switches to 1
  How long does it take for to go to 0?
  How long does it take for to go to ?
0
1
0
1
0
1

## Slide 47: Propagation Delays
OUT
A
G1
In general is not equal to
Thus, we usually just take the maximum and call that the propagation delay of the gate
Means that no matter what input you give the gate, output will be correct within

## Slide 48: Bonus Question for CS61C Veterans
OUT
A
G1
Assume now that the rise and fall times of both gates are
Assume that we have a register driving “A” and a register receiving “OUT”
Assume the registers operate instantaneously
What is the minimum clock time if this very boring buffer is our longest pipeline stage?

## Slide 49
This is where we stopped

## Slide 50: Power in the SRC Model
Static power in the SRC Model is exactly as SR Model, compare:
We’re also interested in the dynamic power while capacitance is charging
Algebra is a bit involved. We’ll outline the concept. Book has a very thorough treatment in sections 11.1 through 11.3

## Slide 51: Dynamic Power in NMOS Circuits
When our inverter is going from low to high, we have the circuit on the left:
In general, looks like circuit on the right:

## Slide 52: Dynamic Power in NMOS Circuits
When our inverter is going from high to low, we have the circuit on the left:
In general, looks like circuit on the right:

## Slide 53: Dynamic Power
Worst case is that inverter is driven by a sequence of 1s and 0s
  Circuit constantly switching behavior
  Gate capacitor constantly charging and discharging
Discharges down towards
Charges up towards

## Slide 54: Problem Setup
is
  0 for some time
    Dissipates some energy
  1 for some time
    Dissipates some energy
See 11.1 through 11.3 for derivation
Discharges down towards
Charges up towards

## Slide 55: Solution

## Slide 56: Avoiding Static Power Loss
Next we will talk about CMOS, which stands for Complementary MOS
So far, all of our transistors have been NMOS transistors, where they are on if
Next, we will discuss a new type of FET transistor called a PMOS
Only difference is that they will be on when

## Slide 57: PMOS Transistor
Drawn with a bubble at the input:
Usually drawn with source on top and drain on bottom (for reasons that will become clear)
Just as before, have ON and OFF states, now on when

## Slide 58: Anything logical we can do with NMOS…
…we can do with PMOS
Example, we can build an inverter, try it for 60 seconds or so on the worksheet using a PMOS, 5V source, ground, and resistor
Assume input signal is 0V or 5V and
A
OUT
RL
5V
G
S
D
Here: acts as a pulldown resistor
Q13

## Slide 59: Analysis of PMOS Logic
We could go through and repeat everything we did for NMOS, but it would be almost exactly the same thing
Instead, we’re now going to use NMOS and PMOS in a clever way

## Slide 60: CMOS Inverter
Two complementary implementations of the same logic function
When is high:
  Path to ground is closed
  Path to is open

## Slide 61: CMOS Inverter
When is high:
  Path to ground is closed
  Path to is open
Huge resistance on open PMOS acts as a pull-up resistor

## Slide 62: CMOS Inverter
When is low:
  Path to ground is open
  Path to is closed
Huge resistance on open NMOS acts as a pull-down resistor

## Slide 63: Static Power in CMOS
What is the static power consumed by this CMOS inverter when IN=0?
When IN=1?
In reality, as gate insulator gets thinner, there is a significant leakage component
IN=0
IN=1

## Slide 64: Dynamic Power in CMOS
Load power: Since our CMOS gates will be driving capacitive loads, they will still draw power when switching (since power is provided to the load)

## Slide 65: Dynamic Power in CMOS
Leakage Power: Unless you’re careful about timing, both MOSFETs could be closed at the same time
  Power flows directly from to ground
Even if timing is perfect, both transistors will at some point be “weakly on” – subthreshold leakage

## Slide 66: Dynamic Power
These days, subthreshold leakage is a big issue
  Thresholds have been reduced to decrease switching times
  Reduced thresholds mean leakier MOSFETs
In this class, we won’t analyze this case, but be aware that in the world of digital integrated circuits, it plays a big role

## Slide 67: CMOS
CMOS Summary:
  No need for a pull-up or pull-down resistor
    Though you can avoid this even with purely NMOS logic (see HW7)
  Greatly reduced static power dissipation vs. our simple NMOS only logic
    In reality, thin gate oxides lead to some static non-zero , so static power is not zero
  Dynamic power is still hugely significant
  Uses twice the number of transistors as our simple purely NMOS logic

## Slide 68: Implementation of Complex Gates Using NMOS and CMOS
In class today, we’ve discussed analysis of NMOS and CMOS circuits
Haven’t discussed how to design them
Luckily, it is easy

## Slide 69: That’s it for today

## Slide 70: Extra Slides

## Slide 71: SR Model of the PMOS MOSFET
No, has nothing to do with SR flip-flop