## Slide 1: EE40 Lecture 16 Josh Hug
8/02\/2010

## Slide 2: Logistics
HW7 due tomorrow
HW8 will be due Friday
Mini-midterm 3 next Wednesday
  80/160 points will be a take-home set of design problems which will utilize techniques we’ve covered in class
    Handed out Friday
    Due next Wednesday
  Other 80/160 will be an in class midterm covering HW7 and HW8
Final will include Friday and Monday lecture
  Design problems will provide practice

## Slide 3: Project 2
Active filter lab and Booster lab due this week
  For Booster lab, ignore circuit simulation, though it may be instructive to try the Falstad simulator
Project 2 due next Wednesday

## Slide 4: Design Problems
ALL WORK MUST BE DONE COMPLETELY SOLO!
Maximum allowed time will be 5 hours
  Will be written so that it can be completed in approximately 2 hours
Allowed resources:
  May use any textbook (incl. Google Books)
  Anything posted on the EE40 website
  Only allowed websites are Google Books, wikipedia, and EE40 websites
  Not allowed to use other websites like facebook answers, yahoo answers, etc. even if you are reading other people’s responses
  When in doubt, email me or text me
  We will be very serious about cheating on this!

## Slide 5: Example Design Problem
Design a circuit which will sum three sinusoidal input voltages and attenuate any frequencies above 10,000 Hz by at least 20 dB

## Slide 6: Project 2
For those of you who want to demo Project 2, we’ll be doing demos in lab on Wednesday
  Either at 1 PM after mini-midterm
  Or at 2 PM during usual lab period
  Opinions?

## Slide 7: Interactive Lecture Question
Did you like the interactive worksheet intensive MOSFET lecture?
  Yes, it was extremely useful and I highly prefer this type of lecture
  Yes, it was useful, but the usual 1-way lecture is fine
  No real opinion
  Didn’t like it
  Hated it

## Slide 8: MOSFET Model
Schematically, we represent the MOSFET as a three terminal device
Can represent all the voltages and currents between terminals as shown to the right

## Slide 9: MOSFET modeling
MOSFET models vary greatly in complexity
S Model: Good for explaining MOSFETs to someone with no EE knowledge
SR Model: Includes effective resistance of a MOSFET. Good for understanding how to choose pull-up resistance
SR Model: Include gate capacitance. Good for understanding dynamic power and gate delay

## Slide 10: S Model of the MOSFET
The simplest model basically says that the MOSFET is:
  Open for
  Closed for

## Slide 11: SR Model of the MOSFET
[Has nothing to do with SR flip-flop]

## Slide 12: The SRC Model
The SRC Model is almost identical to the SR model, except that each gate node has a capacitance
Like SR model: open when OFF and resistive when ON
Note that now is non-zero!

## Slide 13: The SRC Model
Useful for modeling:
  Gate delay: Takes time to charge up
  Dynamic power:

## Slide 14: SRC Model
Consider our familiar pair of inverters
We’re going to focus on the behavior of our left inverter
Let’s assume that both MOSFETs have a gate capacitance of or

## Slide 15: SRC Model of our 2 Inverters
We decide to ignore the function of the gate on the right, keeping it in mind only because we know we’ll have to charge it

## Slide 16: Timing Analysis of the SRC model
Since , , and , then:
How long will it take for the next inverter in the chain to turn on?

## Slide 17: Timing Analysis of the SRC model
So
We call this the “Fall Time”: gives time for to fall from 5V to 1V

## Slide 18: Fall Time
Gives:

## Slide 19: Timing Analysis of the SRC model
How do we find the Rise Time?
Have to replace by new equivalent circuit where:
  Capacitor is initially discharged (0.476 V)
  Switch is open

## Slide 20: Timing Analysis of the SRC model
How do we find the Rise Time?
Have to replace by new equivalent circuit where:
  Capacitor is initially discharged (0.476 V)
  Switch is open

## Slide 21: Timing Analysis of the SRC model

## Slide 22: Timing Analysis of the SRC model

## Slide 23: Propagation Delay
Rise and Fall Time are also called “Propagation Delays”
Gives “delay time” between when the logical input changes and the logical output changes
Book calls them and

## Slide 24: Reminder of Where We Started
OUT
A
G1
Wanted to study gate delay of:
So used SRC model:
Which implements:
Giving delay of LEFT gate!

## Slide 25: Propagation Delays
OUT
A
G1
In general is not equal to
Thus, we usually just take the maximum and call that the propagation delay of the gate
Means that no matter what input you give the gate, output will be correct within

## Slide 26: Propagation Delay
Is our analysis still correct if we add more output gates?
No, gate capacitance increases! Takes 3 times as long.
OUT2
A
G1
OUT1
OUT3

## Slide 27: Power in the SRC Model
Static power in the SRC Model is exactly as SR Model, compare:
We’re also interested in the dynamic power while capacitance is charging
Algebra is a bit involved. We’ll outline the concept. Book has a very thorough treatment in sections 11.1 through 11.3

## Slide 28: Dynamic Power in NMOS Circuits
When our inverter is going from low to high, we have the circuit on the left:
In general, looks like circuit on the right:

## Slide 29: Dynamic Power in NMOS Circuits
When our inverter is going from high to low, we have the circuit on the left:
In general, looks like circuit on the right:

## Slide 30: Dynamic Power
Worst case is that inverter is driven by a sequence of 1s and 0s
  Circuit constantly switching behavior
  Gate capacitor constantly charging and discharging
Discharges down towards
Charges up towards

## Slide 31: Problem Setup
is
  0 for some time
    Dissipates some energy
  1 for some time
    Dissipates some energy
See 11.1 through 11.3 for derivation
Discharges down towards
Charges up towards

## Slide 32: Solution

## Slide 33: Avoiding Static Power Loss
Next we will talk about CMOS, which stands for Complementary MOS
So far, all of our transistors have been NMOS transistors, where they are on if
Next, we will discuss a new type of FET transistor called a PMOS
Only difference is that they will be on when

## Slide 34: PMOS Transistor
Drawn with a bubble at the input:
Usually drawn with source on top and drain on bottom (for reasons that will become clear)
Just as before, have ON and OFF states, now on when

## Slide 35: Anything logical we can do with NMOS…
…we can do with PMOS
Example, we can build an inverter, try it for a minute or so on the worksheet using a PMOS, 5V source, ground, and resistor
Assume input signal is 0V or 5V and
A
OUT
RL
5V
G
S
D
Here: acts as a pulldown resistor
Q13

## Slide 36: Analysis of PMOS Logic
We could go through and repeat everything we did for NMOS, but it would be almost exactly the same thing
Instead, we’re now going to use NMOS and PMOS together in a new clever way

## Slide 37: CMOS Inverter
Two complementary implementations of the same logic function
When is high:
  Path to ground is closed
  Path to is open

## Slide 38: CMOS Inverter
When is high:
  Path to ground is closed
  Path to is open
Huge resistance on open PMOS acts as a pull-up resistor

## Slide 39: CMOS Inverter
When is low:
  Path to ground is open
  Path to is closed
Huge resistance on open NMOS acts as a pull-down resistor

## Slide 40: Static Power in CMOS
What is the static power consumed by this CMOS inverter when IN=0?
When IN=1?
In reality, there is a substantial static power component
IN=0
IN=1

## Slide 41: Static Power in CMOS
Gate Power: As gate oxides get smaller, gate current grows
Subthreshold Leakage Power: As thresholds are reduced (to increase speed),
transistors are never fully OFF, so current
always flows from to

## Slide 42: Dynamic Power in CMOS
Load power: Since our CMOS gates will be driving capacitive loads, they will still draw power when switching (since power is provided to the load)
STL: Both transistors are again weakly on
at intermediate values

## Slide 43: Power in CMOS
Though subthreshold leakage is a significant component to MOSFET power (>50%), it involves a more complex MOSFET model we haven’t studied
We’ll instead focus on dynamic load power
  Still accounts for vast portion of chip power consumption

## Slide 44: Load Power Analysis
Assume our inverter is driven by a square wave
Capacitor will be constantly charging and discharging

## Slide 45: Load Power Analysis
When input is low, capacitor charges to , energy stored is
When input is high, capacitor charges to , energy stored is

## Slide 46: Rising Case
From homework, how much energy is dissipated in the resistor as charges to ?

## Slide 47: Falling Case
If capacitor starts with Joules of energy, and it all gets dissipated through resistor, then energy dissipated is

## Slide 48: Dynamic Load Power
Thus, if clock cycle is long enough, each switching event consumes joules of energy
In seconds, we consume
Power is

## Slide 49: CMOS
CMOS Summary:
  No need for a pull-up or pull-down resistor
    Though you can avoid this even with purely NMOS logic (see HW7)
  Greatly reduced static power dissipation vs. our simple NMOS only logic
    In reality, MOSFETs are never truly off, and static leakage power consumes >50% of chip power
  Dynamic power is still hugely significant
  Uses twice the number of transistors as our simple purely NMOS logic

## Slide 50: Preview of Tradeoffs in Digital Circuits
Processor can do more work per second if is high
  Increasing and lowering give faster rise and fall times, letting us increase
  Dynamic power (and heat) in CMOS scales as
  Subthreshold leakage power (and heat) gets larger as gets smaller and as heat increases
Smarter hardware takes more transistors
  More area means fewer chips per wafer
  More transistors means more power consumption

## Slide 51: Implementation of Complex Gates Using NMOS and CMOS
In class, we’ve discussed analysis of NMOS and CMOS circuits
Haven’t discussed how to design them
Luckily, it is isn’t very hard

## Slide 52: Design of NMOS Circuits
Gates can be designed which use only NMOS transistors and a pull-up resistor
  Easy to pick parameters to satisfy static discipline
The basic idea is to construct an NMOS network which:
  Provides a path from to ONLY when logical function is false
  When path from to is not available, then through pull-up resistor
Examples on board

## Slide 53: Example on Board

## Slide 54: CMOS Design
In the CMOS case, things are almost exactly the same
NMOS network which connects to only when function is false
  Same network as in NMOS only logic
PMOS network which connects to only when function is true
Examples on board

## Slide 55
This is where we stopped

## Slide 56: Model Corner Cases
What happens if:
Real MOSFET model is more complicated
  Switch can be semi-on
  saturates for large [not really a resistor]

## Slide 57: Real MOSFET Model
If we have time this week, we’ll discuss a more realistic model of the MOSFET
Useful for understanding invalid input voltages in logic circuits
More importantly, tells us how we can utilize MOSFETs in analog circuits
  Op-amps are built from transistors

## Slide 58: Nonlinear Elements
This more realistic MOSFET model is nonlinear
MOSFETs are three terminal devices, and it will be tough to begin our nonlinear adventure
  Functionality is similar to what we’ve seen before (op-amps)
  Analysis is tough
We’ll instead turn to diodes
  Interesting new function
  Analysis is easier
If we have time, we will talk on Friday or Monday about analog MOSFET circuits

## Slide 59
Diode Physical Behavior and Equation
N
P
Schematic Device
+
-
I
I
Symbol
+
-
Qualitative I-V characteristics:
I
VD
V positive, high conduction
V negative, low conduction
Quantitative I-V characteristics:
to
to
Allows significant current flow in only one direction

## Slide 60
The pn Junction I vs. V Equation
In EECS 105, 130, and other courses you will learn why the I vs. V relationship for PN junctions is of the form
where I0 is a constant related to device area and materials used to make the diode,
k is Boltzman constant, and T is absolute temperature.
a typical value for I0 is
We note that in forward bias, I increases exponentially and is in the A-mA range for voltages typically in the range of 0.6-0.8V. In reverse bias, the current is essentially zero.
I-V characteristic of PN junctions

## Slide 61: Solving diode circuits
VTh
+

+
V
–
RTh
I
Quantitative I-V characteristics:
No algebraic solution!
How do we solve this circuit?
KCL at the top right node:
n=1

## Slide 62: Load Line Analysis Method
Graph the I-V relationships for the non-linear element and for the rest of the circuit
The operating point of the circuit is found from the intersection of these two curves.
VTh
+

+
V
–
RTh
I
I
V
The I-V characteristic of all of the circuit except the non-linear element is called the load line
VTh
VTh/RTh
operating point

## Slide 63: Load Line Example: Power Conversion Circuits
Converting AC to DC
Potential applications: Charging a battery
Can we use phasors?
Example on board
VI=Vm cos (wt)
R
Vo

## Slide 64: Piecewise Linear Model
reverse bias
forward bias
ID (A)
VD (V)
ID
+
VD
–
+
VD
–
ID
Circuit symbol
I-V characteristic
Switch model
VDon
+

VDon
RULE 1: When ID > 0, VD = VDon
RULE 2: When VD < VDon, ID = 0
Diode behaves like a voltage source in series with a switch:
closed in forward bias mode
open in reverse bias mode
For a Si pn diode, VDon  0.7 V

## Slide 65: How to Analyze Diode Circuits with Piecewise Linear Model
A diode has only two states:
  forward biased: ID > 0, VD = 0.7 V
  reverse biased: ID = 0, VD < 0.7 V
Procedure:
Guess the state(s) of the diode(s)
Check to see if KCL and KVL are obeyed.
If KCL and KVL are not obeyed, refine your guess
Repeat steps 1-3 until KCL and KVL are obeyed.
Example:
vs(t)
If vs(t) > 0.7 V, diode is forward biased (else KVL is disobeyed – try it)
If vs(t) < 0.7 V, diode is reverse biased (else KVL is disobeyed – try it)
+

+
vR(t)
–

## Slide 66: Diode Logic: AND Gate
Diodes can be used to perform logic functions:
AND gate
output voltage is high only if
both A and B are high
A
B
RAND
Vcc
C
Inputs A and B vary between 0 Volts (“low”) and Vcc (“high”)
Between what voltage levels does C vary?
VOUT
VIN
0
5
0
5
Slope =1
Shift 0.7V Up
EOC

## Slide 67: Diode Logic: OR Gate
Diodes can be used to perform logic functions:
OR gate
output voltage is high if
either (or both) A and B are high
A
B
ROR
C
Inputs A and B vary between 0 Volts (“low”) and Vcc (“high”)
Between what voltage levels does C vary?
VOUT
VIN
0
5
0
5
0.7V
Slope =1
Shift 0.7V Down
EOC

## Slide 68: Diode Logic: Incompatibility and Decay
Diode Only Gates are Basically Incompatible:
AND gate
output voltage is high only if
both A and B are high
A
B
RAND
Vcc
CAND
OR gate
output voltage is high if
either (or both) A and B are high
A
B
ROR
COR
Signal Decays with each stage (Not regenerative)

## Slide 69: That’s all for today
Next time, more Diodes and a little more on the more realistic model of MOSFETs