## Slide 1: EE40 Lecture 17 Josh Hug
8/04/2010

## Slide 2: Logistics
HW8 will be due Friday
Mini-midterm 3 next Wednesday
  80/160 points will be a take-home set of design problems which will utilize techniques we’ve covered in class
    Handed out Friday
    Due next Wednesday
  Other 80/160 will be an in class midterm covering HW7 and HW8
Final will include Friday and Monday lecture, Midterm won’t
  Design problems will provide practice

## Slide 3: Project 2
Booster lab actually due next week
  For Booster lab, ignore circuit simulation, though it may be instructive to try the Falstad simulator
Project 2 due next Wednesday
  Presentation details to come [won’t be mandatory, but we will ask everyone about their circuits at some point]

## Slide 4: Project 2
For those of you who want to demo Project 2, we’ll be doing demos in lab on Wednesday at some point
  Will schedule via online survey

## Slide 5: CMOS/NMOS Design Correction
(Sent by email)
My on-the-fly explanation was correct, but not the most efficient way
  If your FET circuit is implementing a logic function with a bar over it, i.e.
  Then don’t put an inverter at the output, it just makes things harder and less efficient
Sorry, on-the-fly-explanations can be dicey

## Slide 6: CMOS
CMOS Summary:
  No need for a pull-up or pull-down resistor
    Though you can avoid this even with purely NMOS logic (see HW7)
  Greatly reduced static power dissipation vs. our simple NMOS only logic
    In reality, MOSFETs are never truly off, and static leakage power consumes >50% of chip power
  Dynamic power is still hugely significant
  Uses twice the number of transistors as our simple purely NMOS logic

## Slide 7: Tradeoffs in Digital Circuits
Processor can do more work per second if is high
  Increasing and lowering give faster rise and fall times, letting us increase
  Dynamic power (and heat) in CMOS scales as
  Subthreshold leakage power (and heat) gets larger as gets smaller and as heat increases
Smarter hardware takes more transistors
  More area means fewer chips per wafer
  More transistors means more power consumption

## Slide 8: Model Corner Cases
What happens if:
Real MOSFET model is more complicated
  Switch can be semi-on
  saturates for large [not really a resistor]

## Slide 9: Real MOSFET Model
If we have time this week, we’ll discuss a more realistic model of the MOSFET
Useful for understanding invalid input voltages in logic circuits
More importantly, tells us how we can utilize MOSFETs in analog circuits
  Op-amps are built from transistors

## Slide 10: Nonlinear Elements
This more realistic MOSFET model is nonlinear
MOSFETs are three terminal nonlinear devices. We will get back to these briefly on Friday
  Functionality is similar to what we’ve seen before (op-amps)
  Analysis isn’t too bad, but will take too long to go through. If you’re curious see chapters 7 and 8.
We’ll instead turn to diodes
  Interesting new function
  Analysis is easier

## Slide 11
Diode Physical Behavior and Shockley Equation
N
P
Physical Device
+
-
I
I
Symbol
+
-
Qualitative I-V characteristics:
I
VD
V positive, high conduction
V negative, low conduction
Quantitative I-V characteristics:
to
to
Allows significant current flow in only one direction

## Slide 12
The pn Junction I vs. V Equation
In EECS 105, 130, and other courses you will learn why the I vs. V relationship for PN junctions is of the form
where I0 is a constant related to device area and materials used to make the diode,
k is Boltzman constant, and T is absolute temperature.
a typical value for I0 is
We note that in forward bias, I increases exponentially and is in the A-mA range for voltages typically in the range of 0.6-0.8V. In reverse bias, the current is essentially zero.
I-V characteristic of PN junctions

## Slide 13
I
Symbol
+
-
(volts) | I (amps)
-1 | 
-0.1 | 
0 | 0
0.1 | 
0.3 | 
0.6 | 0.01
0.7 | 0.49
0.8 | 23
0.9 | 1080
 | I (amps)
-1 | 
-0.1 | 
0 | 0
0.1 | 
0.3 | 
0.6 | 0.01
0.7 | 0.49
0.8 | 23
0.9 | 1080
For typical values:
Real Diodes will eventually become linear for large , and for really large they’ll die
Shockley Equation for the Diode

## Slide 14
I
VD
Linear
Diode dies
Diode dies
Qualitative I-V characteristics: (small V)
I
VD
V positive, high conduction
V negative, low conduction
Qualitative I-V characteristics: (large V)
Large Voltage Limits of the Diode
Green LEDs in lab:
Linear for 2.3V
Die at 6V

## Slide 15: Solving diode circuits
VTh
+

+
V
–
RTh
I
Quantitative I-V characteristics:
No algebraic solution!
How do we solve this circuit assuming zoomed-in region?
KCL at the top right node:
n=1

## Slide 16: Load Line Analysis Method
Graph the I-V relationships for the non-linear element and for the rest of the circuit
The operating point of the circuit is found from the intersection of these two curves.
VTh
+

+
V
–
RTh
I
I
V
The I-V characteristic of all of the circuit except the non-linear element is called the load line
VTh
VTh/RTh
operating point

## Slide 17: Load Line Example: Power Conversion Circuits
Converting AC to DC
Potential applications: Charging a battery
Can we use phasors?
Example on board
VI=Vm cos (wt)
R
Vo

## Slide 18: Simple Model of a Diode
Just as we did with MOSFETs, we will utilize a simpler model
  Goal: Accurate enough that we can design circuits
For Diodes, we started with the “real” model and are now simplifying
For MOSFETs, we started with the simplest model, and added complexity
  Omitted real model for MOSFETs because it’s not very intuitive [unlike real diodes]

## Slide 19: Simpler Diode Model
I
VD
V positive, high conduction
V negative, low conduction
I
Symbol
+
-
reverse bias
forward bias
I (A)
VD (V)
VDon
Goal: To give us approximately the right answer for most inputs

## Slide 20: Voltage Source Model
reverse bias
forward bias
I (A)
VD (V)
I
+
VD
–
+
VD
–
I
Circuit symbol
I-V characteristic
VS model
VDon
+

VDon
ON: When ID > 0, VD = VDon
OFF: When VD < VDon, ID = 0
Diode behaves like a voltage source in series with a switch:
closed in forward bias mode
open in reverse bias mode
For a Si pn diode, VDon  0.7 V

## Slide 21: How to Analyze Diode Circuits with Method of Assumed States
A diode has only two states:
  forward biased: ID > 0, VD = 0.7 V (or some other )
  reverse biased: ID = 0, VD < 0.7 V
Procedure:
Guess the state(s) of the diode(s), drawing equivalent circuit given diode states
Check to see if your resulting voltages and currents match assumptions.
If results don’t match assumptions, guess again
Repeat until you get a consistent guess
Example:
vs(t)
If vs(t) > 0.7 V, diode is forward biased
If vs(t) < 0.7 V, diode is reverse biased
+

+
vR(t)
–

## Slide 22: Bigger Examples on Board
DC Source with 2 Diodes
Half-wave rectifier
Full-wave rectifier
See written notes

## Slide 23: That’s all for today
Next time, maybe a little more diodes and then semiconductor physics and how solar cells, diodes, and MOSFETs work
Time permitting we may talk about real model of a MOSFET

## Slide 24: Extra Slides

## Slide 25: Diode Logic: AND Gate
Diodes can be used to perform logic functions:
AND gate
output voltage is high only if
both A and B are high
A
B
RAND
Vcc
C
Inputs A and B vary between 0 Volts (“low”) and Vcc (“high”)
Between what voltage levels does C vary?
VOUT
VIN
0
5
0
5
Slope =1
Shift 0.7V Up
EOC

## Slide 26: Diode Logic: OR Gate
Diodes can be used to perform logic functions:
OR gate
output voltage is high if
either (or both) A and B are high
A
B
ROR
C
Inputs A and B vary between 0 Volts (“low”) and Vcc (“high”)
Between what voltage levels does C vary?
VOUT
VIN
0
5
0
5
0.7V
Slope =1
Shift 0.7V Down
EOC

## Slide 27: Diode Logic: Incompatibility and Decay
Diode Only Gates are Basically Incompatible:
AND gate
output voltage is high only if
both A and B are high
A
B
RAND
Vcc
CAND
OR gate
output voltage is high if
either (or both) A and B are high
A
B
ROR
COR
Signal Decays with each stage (Not regenerative)

## Slide 28: Switch Model
reverse bias
forward bias
I (A)
VD (V)
I
+
VD
–
+
VD
–
I
Circuit symbol
I-V characteristic
Switch model
ON: When ID > 0, VD = 0
OFF: When VD < VDon, ID = 0
Diode behaves like a voltage source in series with a switch:
closed in forward bias mode
open in reverse bias mode
For a Si pn diode, VDon  0.7 V

## Slide 29: VSR Model
reverse bias
forward bias
I (A)
VD (V)
I
+
VD
–
+
VD
–
I
Circuit symbol
I-V characteristic
VSR model
VDon
+

VDon
ON: When , then
OFF: When VD < VDon, ID = 0
Typical

## Slide 30: Design Problems
ALL WORK MUST BE DONE COMPLETELY SOLO!
Maximum allowed time will be 5 hours
  Will be written so that it can be completed in approximately 2 hours
Allowed resources:
  May use any textbook (incl. Google Books)
  Anything posted on the EE40 website
  Only allowed websites are Google Books, wikipedia, and EE40 websites
  Not allowed to use other websites like facebook answers, yahoo answers, etc. even if you are reading other people’s responses
  When in doubt, email me or text me
  We will be very serious about cheating on this!

## Slide 31: Example Design Problem
Design a circuit which will sum three sinusoidal input voltages and attenuate any frequencies above 10,000 Hz by at least 20 dB

## Slide 32: Example: Diodes in Lab
What happens if we connect our DC source in the lab to a diode?
  Will it blow up?
VTh
+

+
V
–
RTh
I
I
V
The I-V characteristic of all of the circuit except the non-linear element is called the load line
VTh
VTh/RTh
operating point

## Slide 33: Peak Detection
Let’s go back to our sinusoidal source connected to a diode
This time, let’s add a capacitor in parallel with our output resistor and see what happens
Without Capacitor: