## Slide 1: EE40 Lecture 2 Josh Hug
6/23/2010

## Slide 2: Logistical Changes and Notes
Friday Lunch is now Monday lunch (starting next Monday)
  Email me by Saturday evening if you’d like to come: JHUG aat eecs.berkeley.edu
My office hours will be Wednesday and Friday, 11:00-12:00, room TBA
Google calendar with important dates now online
Did anybody not get my email sent out Monday (that said no discussion yesterday)?
Will curate the reading a little more carefully next time

## Slide 3: Lab/HW Deadlines and Dates
Discussions start Friday
Labs start next Tuesday
HW0 Due Today
Homework 1 will be posted by 3PM, due Friday at 5 PM
Tuesday homeworks now due at 2PM, not 5PM in Cory 240 HW box

## Slide 4: Summary From Last Time
Current = rate of charge flow
Voltage = energy per unit charge created by charge separation
Power = energy per unit time
Ideal Basic Circuit Element
  2-terminal component that cannot be sub-divided
  Described mathematically in terms of its terminal voltage and current
Circuit Schematics
  Networks of ideal basic circuit elements
  Equivalent to a set of algebraic equations
  Solution provides voltage and current through all elements of the circuit

## Slide 5: Heating Elements
Last time we posed a question:
  Given a fixed voltage, should we pick a thick or thin wire to maximize heat output
  Note that resistance decreases with wire radius
Most of you said that we’d want a thin wire to maximize heat output, why is that?
  Believed that low resistance wire would give the most heat?
  Didn’t believe me that thick wire has low resistance?
  General intuition?

## Slide 6: Intuitive Answer
I blasted through some equations and said “thicker is better, Q.E.D.”, but I’m not sure you guys were convinced, so here’s another view
You can think of a big thick wire as a bunch of small wires connected to a source
  The thicker the wire, the more little wires
  Since they are all connected directly to the source, they all have same voltage and current and hence power
  Adding more wires gives us more total current flow (same voltage), and hence more power

## Slide 7: Then Why Don’t Toasters and Ovens Have Thicker Elements?
Thicker elements mean hotter elements
  Will ultimately reach higher max temperature
  Will get to maximum faster [see message board after 6 or 7 PM tonight for why]
Last time, you guys asked “Well if thickness gives you more heat, why aren’t toaster elements thicker?”
The answer is most likely:
  More burned toast. Nobody likes burned toast.

## Slide 8: Toaster Element Design Goals
Make heating element that can:
  Can reach a high temperature, but not too high
  Can reach that temperature quickly
  Isn’t quickly oxidized into oblivion by high temperature
  Doesn’t cost very much money
  Will not melt at desired temperature
Nichrome is a typical metal alloy in elements:
  Low oxidation
  High resistance (so normal gauge wire will not draw too much power and get too hot)
Size was tweaked to attain desired temperature

## Slide 9: Continue the Discussion on BSpace
Let’s get working on some more complicated circuits than this:

## Slide 10: Topic 2
Setting Up and Solving Resistive Circuit Models

## Slide 11: Circuit Schematics
Many circuit elements can be approximated as simple ideal two terminal devices or ideal basic circuit elements
These elements can be combined into circuit schematics
Circuit schematics can be converted into algebraic equations
These algebraic equations can be solved, giving voltage and current through any element of the circuit

## Slide 12: Today
We’ll enumerate the types of ideal basic circuit elements
We’ll more carefully define a circuit schematic
We’ll discuss some basic techniques for analyzing circuit schematics
  Kirchoff’s voltage and current laws
  Current and voltage divider
  Node voltage method

## Slide 13: Circuit Elements
There are 5 ideal basic circuit elements (in our course):
  voltage source
  current source
  resistor
  inductor
  capacitor
Many practical systems can be modeled with just sources and resistors
The basic analytical techniques for solving circuits with inductors and capacitors are the same as those for resistive circuits
active elements, capable of
generating electric energy
passive elements, incapable of
generating electric energy

## Slide 14: Electrical Sources
An electrical source is a device that is capable of converting non-electric energy to electric energy and vice versa.
  Examples:
  battery: chemical electric
  dynamo (generator/motor): mechanical electric
Electrical sources can either deliver or absorb power

## Slide 15: The Big Three
+
_
vs
is
R
i
v
i
v
Constant current, unknown voltage
i
v

## Slide 16: Circuit Schematics
A circuit schematic is a diagram showing a set of interconnected circuit elements, e.g.
  Voltage sources
  Current sources
  Resistors
Each element in the circuit being modeled is represented by a symbol
Lines connect the symbols, which you can think of as representing zero resistance wires

## Slide 17: Terminology: Nodes and Branches
Node: A point where two or more circuit elements are connected – entire wire
Can also think of as the “vertices” of our schematic

## Slide 18: Terminology: Nodes and Branches
Branch: A path that connects exactly two nodes
Branch
Not a branch

## Slide 19: Terminology: Loops
A loop is formed by tracing a closed path in a circuit through selected basic circuit elements without passing through any intermediate node more than once
Example: (# nodes, # branches, # loops)
6 nodes
7 branches
3 loops
Notes: Robot good job

## Slide 20: Kirchhoff’s Laws
Kirchhoff’s Current Law (KCL):
  The algebraic sum of all the currents at any node in a circuit equals zero.
  “What goes in, must come out”
  Basically, law of charge conservation
50 mA
20 mA
40 mA
10 mA

## Slide 21: Using Kirchhoff’s Current Law (KCL)
Use reference directions to determine whether reference currents are said to be “entering” or “leaving” the node – with no concern about actual current directions
i1
i4
i3
i2
Often we’re considering unknown currents and only have reference directions:
i1+i2=i3+i4
i1+i2-i3-i4=0
-i1-i2+i3+i4=0
or
or

## Slide 22: KCL Example
5 mA
15 mA
i
-10 mA
5+(-10)=15+i
i=-20mA

## Slide 23: A Major Implication of KCL
KCL tells us that all of the elements along a single uninterrupted* path carry the same current
We say these elements are connected in series.
Current entering node = Current leaving node
i1 = i2
*: To be precise, by uninterrupted path I mean all branches along the path connected EXACTLY two nodes

## Slide 24: Generalization of KCL
The sum of currents entering/leaving a closed surface is zero. Circuit branches can be inside this surface, i.e. the surface can enclose more than one node!
This could be a big chunk of a circuit, e.g. a “black box”
i1
i2
i3
i4

## Slide 25: Generalized KCL Examples
5mA
2mA
i
50 mA
i
50 mA
7mA

## Slide 26: Kirchhoff’s Laws
Kirchhoff’s Voltage Law (KVL):
  The algebraic sum of all the voltages around any loop in a circuit equals zero.
  “What goes up, must come down”
20V
+
–
50V
+
–
80V
+
–
10V
+
–
80=20+50+10

## Slide 27: A Major Implication of KVL
KVL tells us that any set of elements which are connected at both ends carry the same voltage.
We say these elements are connected in parallel.
Applying KVL, we have that:
vb – va = 0  vb = va
+
va
_
+
vb
_

## Slide 28: KVL Example
Path 1:
Path 2:
Path 3:
vc
va
+

+

3
2
1
+ 
vb
v3
v2
+ 
+
-
Three closed paths:
a
b
c
Va=V2+Vb
Vb+V3=Vc
Va+V3=V2+Vc
If you want a mechanical rule:
If you hit a – first, LHS
If you hit a + first, RHS
LHS is left hand side

## Slide 29: An Underlying Assumption of KVL
No time-varying magnetic flux through the loop
  Otherwise, there would be an induced voltage (Faraday’s Law)
  Voltage around a loop would sum to a nonzero value
How do we deal with antennas (EECS 117A)?
Include a voltage source as the circuit representation of the induced voltage or “noise”.
(Use a lumped model rather than a distributed (wave) model.)
Note: Antennas are designed to “pick up” electromagnetic waves; “regular circuits” often do so undesirably.
+ 

## Slide 30: Mini-Summary
KCL tells us that all elements on an uninterrupted path have the same current.
  We say they are “in series”
KVL tells us that a set of elements whose terminals are connected at the same two nodes have the same voltage
  We say they are “in parallel”

## Slide 31: Nonsense Schematics
Just like equations, it is possible to write nonsense schematics:
  1=7
A schematic is nonsense if it violates KVL or KCL
1V
7V

## Slide 32: Verifying KCL and KVL
5V
20A
Is this schematic valid?
How much power is consumed/provided by each source?
Yes
Voltage source: PV=5V*20A =100W (consumed)
Current source: PI=-20A*5V=100W (provided)

## Slide 33: Verifying KCL and KVL
Is this valid?
100V
10A
5A
5A
KCL:
Top left node: I100=10A
Top right node: 10A=5A+5A Bottom node: 5A+5A=I100
No contradiction
KVL:
Left loop: 100V=V10+V5
Right loop: V5=V5
Big loop: 100V=V10+V5
No contradiction
Yes

## Slide 34: Verifying KCL and KVL
Is this valid?
100V
10A
5A
5A
KCL:
Top left node: I100=10A
KVL:
Left loop: 100V=V10+V5
So what are V10 and V5?
  Whatever we want that sums to 100V
  Multiple circuit solutions
2 equations
3 unknowns
Yes

## Slide 35: iClicker #1
Are these interconnections permissible?
A. Both are bad
B. Left is ok, right is bad
C. Left is bad, right is ok
D. Both are ok

## Slide 36: On to Solving Circuits
Next we’ll talk about a general method for solving circuits
  The book calls this the “basic method”
  It’s a naïve way of solving circuits, and is way more work than you need
    Basic idea is to write every equation you can think of to write, then solve
  However, it will build up our intuition for solving circuits, so let’s start here

## Slide 37: Solving Circuits (naïve way)
Label every branch with a reference voltage and current
  If two branches are in parallel, share voltage label
  If in series, share same current label
For each branch:
  Write Ohm’s law if resistor
  Get branch voltage “for free” if known voltage source
  Get branch current “for free” if known current source

## Slide 38: Solving Circuits (naïve way)
Label every branch with a reference voltage and current
  If two branches are in parallel, share voltage label
  If in series, share same current label
For each branch:
  Write Ohm’s law if resistor
  Get branch voltage “for free” if known voltage source
  Get branch current “for free” if known current source
For each node touching at least 2 reference currents:
  Write KCL – gives reference current relationships
  Can omit nodes which contain no new currents
For each loop:
  Write KVL – gives reference voltage relationships
  Can omit loops which contain no new voltages
Could also call this the “kitchen sink” approach

## Slide 39: Example: KCL and KVL applied to circuits
Find the current through the resistor
Use KVL, we see we can write:
Now solving, we have:
5V
3V
20Ω
V1
VR
V2
IR
+

+

+ 
V1=VR+V2
5V=VR+3V
2V=VR
IR=2V/20Ω=0.1 Amps
V1=5V
V2=3V
IR=VR/20Ω
4 equations
4 “unknowns”
Note: We had no node touching 2 ref currents, so no reference current relationships

## Slide 40: Bigger example
V1
+

V30
+ 
V80
+

V1=ia*80Ω
V30=1.6A*30Ω
Vg=1.6A*90 Ω
Branches:
Two nodes which touch two different reference currents:
ig=ia+1.6
ia+1.6=ig
Three loops, but only one needed to touch all voltages:
V1=V30+Vg
[no new currents]
5 equations
5 unknowns
V30=48V
Vg=144V
V1=192V
ia=2.4A
ig=4A
ig
vg
ia
+


## Slide 41: iClicker Proof
How many KCL and KVL equations will we need to cover every branch voltage and branch current?
2 KVL, 1 KCL
I1
I2
I3
Top node:
I1=I2+I3
Bottom node:
I3+I2=I1

## Slide 42: There are better ways to solve circuits
The kitchen sink method works, but we can do better
  Current divider
  Voltage divider
  Lumping series and parallel elements together (circuit simplification)
  Node voltage

## Slide 43: Voltage Divider
Voltage divider
  Special way to handle N resistors in series
  Tells you how much voltage each resistor consumes
  Given a set of N resistors R1,…,Rk,…, RN in series with total voltage drop V, the voltage through Rk is given by
Or more compactly:
Can prove with kitchen sink method (see page 78)

## Slide 44: Voltage Divider Example
85Ω
10Ω
5Ω
100V
And likewise for other resistors

## Slide 45: Current Divider
Current divider
  Special way to handle N resistors in parallel
  Tells you how much current each resistor consumes
  Given a set of N resistors R1,…,Rk,…, RN in parallel with total current I the current through Rk is given by
Can prove with kitchen sink method (see http://www.elsevierdirect.com/companions/9781558607354/casestudies/02~Chapter_2/Example_2_20.pdf)
Where:
We call Gp the conductance of a resistor, in units of Mhos (℧)
-Sadly, not units of Shidnevacs ( )

## Slide 46: Current Divider Example
20A
5Ω
10Ω
5Ω
2Ω
Conductances are:
1/5Ω=0.2℧
1/10Ω=0.1℧
1/5Ω=0.2℧
1/2Ω=0.5℧
Current through 5Ω resistor is:
Sum of conductances is 1℧ (convenient!)

## Slide 47: Circuit Simplification
Next we’ll talk about some tricks for combining multiple circuit elements into a single element
Many elements in series  One single element
Many elements in parallel  One single element

## Slide 48: Circuit Simplification Example Combining Voltage Sources
KVL trivially shows voltage across resistor is 15 V
Can form equivalent circuit as long as we don’t care about individual source behavior
  For example, if we want power provided by each source, we have to look at the original circuit
5V
9V
1V
15Ω
15V
15Ω

## Slide 49: Example – Combining Resistances
Can use kitchen sink method or voltage divider method to show that current provided by the source is equivalent in the two circuits below
5Ω
11Ω
4Ω
20Ω

## Slide 50: Source Combinations
Voltage sources in series combine additively
Voltage sources in parallel
  This is like crossing the streams – “Don’t cross the streams”
  Mathematically nonsensical if the voltage sources are not exactly equal
Current sources in parallel combine additively
Current sources in series is bad if not the same current

## Slide 51: Resistor Combinations
Resistors in series combine additively
Resistors in parallel combine weirdly
  More natural with conductance:
N resistors in parallel with the same resistance R have equivalent resistance Req=R/N

## Slide 52: Algorithm For Solving By Combining Circuit Elements
Check circuit diagram
  If two or more elements of same type in series
    Combine using series rules
  If two or more elements of same type in parallel
    Combine using parallel rules
If we combined anything, go back to
If not, then solve using appropriate method (kitchen sink if complicated, divider rule if possible)

## Slide 53: Using Equivalent Resistances

+
30 V
I
15
15
10
40
6
50
Example: Find I
Are there any circuit elements in parallel?
No!
Are there any circuit elements in series?
Yes!

## Slide 54: Using Equivalent Resistances

+
30 V
I
30
10
40
6
50
Example: Find I
Are there any circuit elements in parallel?
Yes!
Are there any circuit elements in series?
Yes!

## Slide 55: Using Equivalent Resistances

+
30 V
I
30
50
6
50
Example: Find I
Are there any circuit elements in parallel?
Yes!
Are there any circuit elements in series?
No!

## Slide 56: Using Equivalent Resistances

+
30 V
I
5
50
50
Example: Find I
Are there any circuit elements in parallel?
Yes!
Are there any circuit elements in series?
No!

## Slide 57: Using Equivalent Resistances

+
30 V
I
5
25
Example: Find I
Are there any circuit elements in parallel?
No!
Are there any circuit elements in series?
Yes!

## Slide 58: Using Equivalent Resistances

+
30 V
I
30
Example: Find I
Are there any circuit elements in parallel?
No!
Are there any circuit elements in series?
No!
I=30V/30Ω=1A

## Slide 59: Working Backwards
Assume we’ve combined several elements to understand large scale behavior
Now suppose we want to know something about one of those circuit elements that we’ve combined
  For example, current through a resistor that has been combined into equivalent resistance
We undo our combinations step by step
  At each step, use voltage and current divider tricks
  Only undo enough so that we get the data we want

## Slide 60: Working Backwards Example
Suppose we want to know the voltage across the 40Ω Resistor

+
30 V
I
15
15
10
40
6
50

## Slide 61: Using Equivalent Resistances

+
30 V
I
30
I=1 Amp
Starting from here…

## Slide 62: Using Equivalent Resistances
I=1 Amp
V25=I*25Ω=25V

+
30 V
I
5
25
We back up one step…
Then another…
V25
+


## Slide 63: Using Equivalent Resistances
I=1 Amp
V25=I*25Ω=25V

+
30 V
I
5
50
50
Then another…
We back up one step…
V25
+

Then one more…

## Slide 64: Using Equivalent Resistances
I=1 Amp
V25=I*25Ω=25V

+
30 V
I
5
50
Then another…
We back up one step…
Now we can use the voltage divider rule, and get
V25
+

Then one more…
10
40

## Slide 65: Using Equivalent Resistances
I=1 Amp
V25=I*25Ω=25V
Then another…
We back up one step…
Now we can use the voltage divider rule, and get
Then one more…

+
I
15
15
10
40
6
50

## Slide 66: Equivalent Resistance Between Two Terminals
We often want to find the equivalent resistance of a network of resistors with no source attached
Tells us the resistance that a hypothetical source would “see” if it were connected
  e.g. In this example, the resistance that provides the correct source current
Req
10Ω
10Ω
10Ω
10Ω

## Slide 67: Equivalent Resistance Between Two Terminals
Pretend there is a source of some kind between the circuits
Perform the parallel/series combination algorithm as before
10Ω
10Ω
10Ω
10Ω
10Ω
10Ω
5Ω
25Ω

## Slide 68: Can Pick Other Pairs of Terminals
These resistors do nothing (except maybe confuse us)
Combine these parallel resistors
10Ω
10Ω
10Ω
5Ω

## Slide 69: There are better ways to solve circuits
The kitchen sink method works, but we can do better
  Current divider
  Voltage divider
  Lumping series and parallel elements together (circuit simplification)
  Node voltage

## Slide 70: The Node Voltage Technique
We’ll next talk about a general technique that will let you convert a circuit schematic with N nodes into a set of N-1 equations
These equations will allow you to solve for every single voltage and current
Works on any circuit, linear or nonlinear!
Much more efficient than the kitchen sink

## Slide 71: Definition: Node Voltage and Ground Node
Remember that voltages are always defined in terms of TWO points in a circuit
It is convenient to label one node in our circuit the “Ground Node”
  Any node can be “ground”, it doesn’t matter which one you pick
Once we have chosen a ground node, we say that each node has a “node voltage”, which is the voltage between that node and the arbitrary ground node
Gives each node a universal single valued voltage level

## Slide 72: Node Voltage Example
Pick a ground, say the bottom left node.
Label nodes a, b, c, d. Node voltages are:
  Vd=voltage between node d and d=0V
  Vc=voltage between node c and d=V10=20V
  Vb=voltage between node b and d=V85+V10=190V
  Va=voltage between node a and d=200V
85Ω
10Ω
5Ω
200V
a
b
c
d
V5=10V
V85=170V
V10=20V
+

 +
+ 

## Slide 73: iClicker #4: Node Voltages
85Ω
10Ω
5Ω
200V
a
b
c
d
V5=10V
V85=170V
V10=20V
+

 +
+ 
  What is Va?
200V
20V
160V
180V
Va=V5+V85=180V

## Slide 74: Relationship: Node and Branch Voltages
Node voltages are useful because:
  The branch voltage across a circuit element is simply the difference between the node voltages at its terminals
  It is easier to find node voltages than branch voltages
  Example:
V85=Vb-Vc=190V-20V=170V
85Ω
5Ω
200V
a
b
c
d
+

 +
+ 
  Vd=V
  Vc=20V
  Vb=190V
  Va=200V

## Slide 75: Why are Node Voltages Easier to Find?
4A
KCL is easy to write in terms of node voltages
For example, at node a:
  4A=Va/80Ω+(Va-Vb)/30Ω
And at node b:
  (Vb-Va)/30Ω=Vb/90Ω
Well look, two equations, two unknowns. We’re done.
Better than 5 equations, 5 unknowns with kitchen sink method
a
b

## Slide 76: (Almost) The Node Voltage Method
Assign a ground node
For every node except the ground node, write the equation given by KCL in terms of the node voltages
  Be very careful about reference directions
This gives you a set of N-1 linearly independent algebraic equations in N-1 unknowns
  Solvable using whatever technique you choose

## Slide 77: What about Voltage Sources?
Suppose we have the circuit below
When we try to write KCL at node a, what happens?
How do we get around this?
  Write fixed node voltage relationship: Va=Vd+200
85Ω
10Ω
5Ω
200V
a
b
c
d

## Slide 78: Full Node Voltage Method
Assign a ground node
For every node (except the ground node):
  If there is no voltage source connected to that node, then write the equation given by KCL in terms of the node voltages
  If there is a voltage source connecting two nodes, write down the simple equation giving the difference between the node voltages
  Be very careful about reference directions (comes with practice)
This gives you a set of N-1 linearly independent algebraic equations in N-1 unknowns
Solvable using whatever technique you choose
More Examples Next Time!

## Slide 79: Next Class
Node voltage practice and examples
Why we are bothering to understand so deeply the intricacies of purely resistive networks
  Things we can build other than the most complicated possible toaster
How we actually go about measuring voltages and currents
More circuit tricks
  Superposition
  Source transformations

## Slide 80: Quick iClicker Question
How was my pacing today?
  Way too slow
  A little too slow
  Pretty good
  Too fast
  Way too fast

## Slide 81: Extra Slides

## Slide 82: Summary (part one)
There are five basic circuit elements
  Voltage Sources
  Current Sources
  Resistors
  Capacitors
  Inductors
Circuit schematics are a set of interconnect ideal basic circuit elements
A connection point between elements is a node, and a path that connects two nodes is a branch
A loop is a path around a circuit which starts and ends at the same node without going through any circuit element twice

## Slide 83: Summary (part two)
Kirchoff’s current law states that the sum of the currents entering a node is zero
Kirchoff’s voltage law states that the sum of the voltages around a loop is zero
From these laws, we can derive rules for combining multiple sources or resistors into a single equivalent source or resistor
The current and voltage divider rules are simple tricks to solve simple circuits
The node voltage technique provides a general framework for solving any circuit using the elements we’ve used so far

## Slide 84: Short Circuit and Open Circuit
Wire (“short circuit”):
R = 0  no voltage difference exists
  (all points on the wire are at the same potential)
Current can flow, as determined by the circuit
Air (“open circuit”):
R =   no current flows
Voltage difference can exist,
as determined by the circuit

## Slide 85: Ideal Voltage Source
Circuit element that maintains a prescribed voltage across its terminals, regardless of the current flowing in those terminals.
  Voltage is known, but current is determined by the circuit to which the source is connected.
The voltage can be either independent or dependent on a voltage or current elsewhere in the circuit, and can be constant or time-varying.
Circuit symbols:
+
_
vs
+
_
vs=m vx
+
_
vs=r ix
independent
voltage-controlled
current-controlled

## Slide 86: Ideal Current Source
Circuit element that maintains a prescribed current through its terminals, regardless of the voltage across those terminals.
  Current is known, but voltage is determined by the circuit to which the source is connected.
The current can be either independent or dependent on a voltage or current elsewhere in the circuit, and can be constant or time-varying.
Circuit symbols:
is
is=a vx
is=b ix
independent
voltage-controlled
current-controlled