## Slide 1: EE40 Lecture 3 Josh Hug
6/25/2010
“Users [are] reporting a drop in signal strength when the phone is held.” -BBC
“If you ever experience this on your iPhone 4, avoid gripping it in the lower left corner in a way that covers both sides of the black strip in the metal band, or simply use one of many available cases.”-Apple

## Slide 2: Logistical Notes
Office Hours – Room reservation has been put in, but no word from the people yet. I’ve got someone looking into it
HW1 due today at 5 PM in the box in 240 Cory
No i>Clicker today [couldn’t get hardware today]

## Slide 3: Nodal Analysis: Example
V
2
V
1
R
2
R
1
R
4
R
5
R
3
I
1
5 unknowns
2 KCL equations
3 KVL equations
Using the basic method

## Slide 4: Nodal Analysis: Example
V
2
V
1
R
2
R
1
R
4
R
5
R
3
I
1
a
b
c
With Node Voltage:
One equation, one unknown

## Slide 5: Nodal Analysis: Example
V
2
V
1
R
2
R
1
R
4
R
5
R
3
I
1
a
b
c
It’s fine to leave your
answer in terms of conductances on HW and exams

## Slide 6: Dependent Sources
In practice, we’ll want to use controllable sources
  Called “dependent sources” since their output is dependent on something external to the source itself
+
_
vs
independent
+
_
vs(x)
dependent
In theory, a dependent source could be a function of anything in the universe
  Intensity of light incident on the source
  Number of fish within 3 miles

## Slide 7: Dependent Sources
Since we’re building electrical circuits, dependent sources have been developed which are functions of other electrical quantities
5V
10Ω
40Ω
100Ω

## Slide 8: Dependent Sources
Dependent sources allow us to decouple the controller from the controlled
  Acceleration of the engine affect by gas pedal
  Gas pedal not affected by engine acceleration
This is in contrast to our circuits so far where everything is connected

## Slide 9: Dependent Sources With Feedback
Dependent sources can be coupled to their controller
This is useful for when the controller needs feedback from the thing being controlled
Can be a little tricky to analyze

## Slide 10: Node Voltage With Dependent Source
100Ω
20Ω
100V
There are two ways to proceed:
    Direct substitution (almost always better)
  Indirect substitution (tough part of the reading)

## Slide 11: Direct Substitution Method for Dependent Sources

## Slide 12: Node Voltage With Dependent Source
100Ω
20Ω
100V
There are two ways to proceed:
    Direct substitution (almost always better)
  Indirect substitution (tough part of the reading)
?
?
?

## Slide 13: Indirect Substitution Method for Dependent Sources
100Ω
20Ω
100V
I
Real source vs. dummy source
Node voltage vs. dummy source
Node voltage vs. controlling current

## Slide 14: Summary So Far
Dependent sources model controllable electrical sources
Node voltage can be used with dependent sources
  Controlling input can be seemingly difficult to deal with, e.g.
  Direct Substitution: Replace controlling input with expression in terms of
    The node voltages you’re trying to solve for
    Known currents if controlling input driven by current source
  Indirect Substitution: Treat dependent source as a new variable and solve (better in rare cases)

## Slide 15: Useful Resistive Circuits
Wheatstone Bridge
  Used for measuring unknown resistances
Strain Gauge
  Used for measuring weight

## Slide 16: Wheatstone Bridge
Named for Charles Wheatstone
Used for measuring resistance of an unknown resistor
+
V
–
R1
R2
R3
Rx
Parts:
  Known resistors R1 and R2
  Adjustable resistor R3
  Unknown resistance Rx
Basic concept:
  If , then no current will flow in the middle branch
Invented 1833 by Samuel Christie
Hit the charts when remixed by Wheatstone in 1843

## Slide 17: Finding the value of Rx
Adjust R3 until there is no current in the detector
Then,
+
V
–
R1
R2
R3
Rx
Rx = R3
R2
R1
Derivation:
  i1 = i3 and i2 = ix
  i3R3 = ixRx and i1R1 = i2R2
  i1R3 = i2Rx
KCL =>
KVL =>
R3
R1
Rx
R2
=

## Slide 18: Strain Gauge Intuition
Resistance is a function of wire length and area
Weight stretches a wire, changing its shape
Can theoretically get weight of a load by seeing how resistance varies when a load is added

## Slide 19: Resistivity
Wire resistance:
is resistivity, measured in Ω·m
Can think of as how tightly molecular lattice holds on to electrons
Material | 
Copper | 1.68x10-8
Aluminum | 2.82x10-8
Nichrome | 1.1x10-6
Glass | 1010
Material | 
Copper | 1.68x10-8
Aluminum | 2.82x10-8
Nichrome | 1.1x10-6
Glass | 1010

## Slide 20: Wire Gauge
Gauge | Diameter [mm] | Area [mm2]
10 | 2.58 | 5.26
14 | 1.62 | 2.08
16 | 1.29 | 1.31
Resistance of 30m, 16 gauge extension cord?
0.384Ω
If carrying 10 amps, how much power dissipated?

## Slide 21: Basic Principle
Pull on resistor:
  L=L0+ΔL
  A=A0-ΔA
  V=LA [constant]
Length wins the battle to control resistance
R=R0+ΔR
Define strain
Where the Gauge Factor relates to how length/area change. GF~2

## Slide 22: Using Strain to Measure Weight
We’ll attempt to design a circuit which can measure ε
  Convert into a voltage
We’ll leave it to the mechanical engineers to map ε back to load
Our Circuit
Vx(ε)
Microcontroller
ε

## Slide 23: Using Strain to Measure Weight
Our Circuit
Vx(ε)
ADC
vx
vx_to_delRr0(vx)
delRr0
calc_eps(delRr0)
eps
eps2weight(eps)
weight
Microcontroller
ε

## Slide 24: One Possible Design
Here, Rx is a variable resistor, where Rx is dependent on strain
As strain varies, so will vx

## Slide 25: One Possible Design
μController calculates ε from known quantities Vx, Vs, R0, Rref, GF, and then weight from ε
vx is what μController sees

## Slide 26: Better Circuits
This will work, but:
  for
  As source voltage varies (e.g. battery gets old), calibration changes – “zero drift”

## Slide 27: Improvement #1: Half Bridge
Works, but requires balanced sources

## Slide 28: Improvement #2: Full Bridge
Want
Use voltage divider
Works, but requires resistors with value equal to R0

## Slide 29: Strain Gauge Summary
We can map strain (weight) to resistance
Simplest design (voltage divider) works, but is subject to zero-drift
More complex circuits give different design tradeoffs
  Wheatstone-bridge provides arguably the best design
We will explore these tradeoffs in lab on Wednesday

## Slide 30: Useful Resistive Circuit Summary
The Wheatstone bridge (and other designs) provide us with a way to measure an unknown resistance
There are resistors which vary with many useful parameters, e.g.
  Incident light
  Temperature
  Strain
And then… there are always toasters

## Slide 31: Back to Circuit Analysis
Next we’ll discuss a few more circuit analysis concepts
  Superposition
  Equivalent Resistance
    Deeper explanation of equivalent resistance
    For circuits with dependent sources
  Thevenin/Norton Equivalent Circuits
  Simulation

## Slide 32: Superposition
Principle of Superposition:
In any linear circuit containing multiple independent sources, the current or voltage at any point in the network may be calculated as the algebraic sum of the individual contributions of each source acting alone.
A linear circuit is one constructed only of linear elements (linear resistors, and linear capacitors and inductors, linear dependent sources) and independent sources.
Linear means I-V characteristic of all parts are straight when plotted

## Slide 33
Superposition
Procedure:
  Determine contribution due to one independent source
    Set all other sources to 0:
      Replace independent voltage source by short circuit
      independent current source by open circuit
  Repeat for each independent source
  Sum individual contributions to obtain desired voltage
  or current

## Slide 34: Easy Example
Find Vo
12 W
4 W
4 A
4 V
+ –
+
Vo
–
12 W
4 W
4 V
+ –
+
Vo
–
Voltage Divider: -1V

## Slide 35: Easy Example
Find Vo
12 W
4 W
4 A
4 V
+ –
+
Vo
–
12 W
4 W
4 A
+
Vo
–
Current Divider: -(3A*4Ω)=-12V

## Slide 36: Easy Example
Find Vo
12 W
4 W
4 A
4 V
+ –
+
Vo
–
V0=-12V-1V=-13V
Due to current source
Due to voltage source

## Slide 37: Hard Example

## Slide 38: Example
Equivalent resistance:
3+2+(3||2) = 5+(3*2)/(3+2)=6.2V
Current is 10A
50V loss through top 5Ω, leaving 12V across v0

## Slide 39: Example
VT
Vo
This will work…
But algebra is easier if we pick a better ground

## Slide 40: Example
VT
VB

## Slide 41: Example
Vo=-12V
Vo=12V

## Slide 42: Note on Dependent Sources
You can use superposition in circuits with dependent sources
However, DON’T remove the dependent sources! Just leave them there.

## Slide 43: Equivalent Resistance Review
If you add a source to any two terminals in a purely resistive circuit
  The added source will “see” the resistive circuit as a single resistor
10Ω
10Ω
10Ω
10Ω
25Ω
25V
1A
25V
1A

## Slide 44: Alternate Viewpoint
We can think of the circuit above as a two terminal circuit element with an I-V characteristic
10Ω
10Ω
10Ω
10Ω
i
v
Slope: 1/25Ω

## Slide 45: Equivalent Resistance
Let’s consider the IV characteristic of the following circuit:
R1
R2
αV2
V
I
V2
+
-

## Slide 46: Equivalent Resistance
R1
R2
αV2)
V
I
V2
+
-

## Slide 47: Equivalent Resistance
R1
R2
αV2
V
I
V2
+
-
i
v
Slope:
= 1/Req
This circuit just acts like a resistor!

## Slide 48: Equivalent Resistance Summary So Far
Purely resistive networks have an I-V characteristic that looks just like their equivalent resistance
Purely resistive networks which also include dependent sources also act like resistors
Let’s see what happens with a circuit with an independent source
V
I
10V
5Ω

## Slide 49: Equivalent Resistance Summary So Far
V
I
10V
5Ω
i
v
Doesn’t match our basic I-V characteristics… good!

## Slide 50: Interestingly…
20V
10Ω
10Ω
V
I
i
v

## Slide 51: Equivalent Circuits
20V
10Ω
10Ω
Has the exact same I-V characteristic as:
10V
5Ω

## Slide 52: Thevenin Equivalents
We saw before that we can replace a network of resistors (and dependent sources) with a single equivalent resistance
Now, we have that we can replace any circuit we can build so far with a single voltage source and resistor
  Not proven, but it’s true, trust me
This two element network is known as a Thevenin equivalent
Generalization of the idea of equivalent resistance
Again: Discovered twice, named after the second guy!

## Slide 53: Why is this useful?
Can swap out elements and not have to resolve a big circuit again
Captures the fundamental operation of the circuit as a whole (at chosen two terminals only!)

## Slide 54: Thevenin Algorithm for Independently Sourced Circuits
What you’re ultimately doing is finding the I-V characteristic of the circuit
You can do this by attaching a made up V, and calculating I as on slides 49 and 50
  Often called a “Test Voltage”
This is equivalent to:
  Finding the “open circuit” voltage
  Finding the “short circuit” current

## Slide 55: Calculating a Thévenin Equivalent
Calculate the open-circuit voltage, voc
Calculate the short-circuit current, isc
  Note that isc is in the direction of the open-circuit voltage drop across the terminals a,b !
network
of
sources
and
resistors
a
b
+
voc
–
network
of
sources
and
resistors
a
b
isc

## Slide 56: Example – On the Board
8A
12Ω
2Ω
6Ω
12V
Find the Thevenin Equivalent circuit, by finding
1. VOC
2. ISC

## Slide 57: Finding Thevenin Resistance Directly
If there are no dependent sources in the circuit, we can find the Thevenin Resistance directly
Algorithm is easy:
  Set all independent sources to zero
    Voltage source becomes short circuit
    Current source becomes open circuit
  Leave dependent sources intact
  Find equivalent resistance between terminals of interest

## Slide 58: Norton Equivalent Circuit
Norton equivalent circuit
Any network of voltage sources, current sources, and resistors can also be replaced by an equivalent circuit consisting of an independent current source in parallel with a resistor without affecting the operation of the rest of the circuit.
network
of
sources
and
resistors
≡
RL
iL
+
vL
–
a
b
RL
iL
+
vL
–
iN
a
b
RN

## Slide 59: Example – On the Board
8A
12Ω
2Ω
6Ω
12V
Find the Thevenin Equivalent resistance directly

## Slide 60: Finding IN and RN
We can derive the Norton equivalent circuit from a Thévenin equivalent circuit simply by making a source transformation:
RL
RN
iL
iN
+
vL
–
a
b
–
+
RL
iL
+
vL
–
vTh
RTh
a
b

## Slide 61: Circuit Simulation
Automated equation solvers use our algorithm:
  Choose a ground node
  Assign node voltage labels to all nodes
  Write out a system of N-1 linear equations
  Solve (using standard linear algebra techniques)
One pretty handy tool is falstad.com’s circuit simulator
Let’s try a live demo

## Slide 62: Extra Slides

## Slide 63: Delta-Wye Conversion

## Slide 64: Equivalent Resistances
R1

+
R4
R5
R2
V
R3
Are there any circuit elements in parallel?
Are there any circuit elements in parallel?
Are there any circuit elements in series?
No
No
What do we do?
Be clever and find I-V characteristic directly
Apply weirder transformation rules than series or parallel

## Slide 65: Y-Delta Conversion
These two resistive circuits are equivalent for voltages and currents external to the Y and D circuits. Internally, the voltages and currents are different.
R1 =
RbRc
Ra + Rb + Rc
R2 =
RaRc
Ra + Rb + Rc
R3 =
RaRb
Ra + Rb + Rc

## Slide 66: D-Y and Y-D Conversion Formulas
R1 =
RbRc
Ra + Rb + Rc
R2 =
RaRc
Ra + Rb + Rc
R3 =
RaRb
Ra + Rb + Rc
Delta-to-Wye conversion
Wye-to-Delta conversion
Ra =
R1R2 + R2R3 + R3R1
R1
Rb =
R1R2 + R2R3 + R3R1
R2
Rc =
R1R2 + R2R3 + R3R1
R3

## Slide 67: Circuit Simplification Example
Find the equivalent resistance Rab:
2W
a
b
18W
6W
12W
4W
9W
≡
2W
a
b
4W
9W
Rb=18
Ra=12
Rc=6
R3 =
RaRb
Ra + Rb + Rc
=6
R2=2
3

## Slide 68: General Versions of Thevenin Slides

## Slide 69: Equivalent Resistance Summary So Far
Purely resistive networks have an I-V characteristic that look just like their equivalent resistance
Networks which include dependent sources also act like resistors
Let’s see what happens with a circuit with a source
V
I
Vs
R1

## Slide 70: Equivalent Resistance Summary So Far
V
I
Vs
R1
i
v
Doesn’t match our basic I-V characteristics… good!

## Slide 71: Interestingly…
Vs
R1
R2
V
I
i
v

## Slide 72
Vs
R1
R2
Has the exact same I-V characteristic as:
Vs
Req

## Slide 73
2 W
1 W
4 W
30 V
+
Vo
–
I