CS252	HOMEWORK 2

D. A. Patterson

Due Thu. 10/12/06

Problem 1:

In the following problem, use a simple pipelined RISC architecture with a branch delay cycle.  The architecture has pipelined functional units with the flowing execution cycles:

1. Floating point op: 3 cycles

#### 2. Integer op: 1 cycles

The following table shows the minimum number of intervening cycles between the producer and consumer instructions to avoid stalls.   Assume 0 intervening cycle for combinations not listed.

| Instruction producing result | Instruction using result | Latency in clock cycles |
| --- | --- | --- |
| FP ALU op | Another FP ALU op | 2 |
| FP ALU op | Store and move double | 2 |
| Load double | FP ALU op | 1 |
| Load double | Store double | 0 |

As an example, if the result of an ADD.D instruction is used by the next instruction, which is also ADD.D, there has to be two stalls between these two instructions.

The following code computes a 3-tap filter.  R1 contains address of the next input to the filter, and the output overwrites the input for the iteration.  R2 contains the loop counter.  The tab values are contained in F10, F11, F12.

LOOP:		L.D 		F0, 0(R1)	#load the filter input for the iteration

MULT.D	F2, F1, F12	#multiply elements

ADD.D	F0, F2, F0	#add elements

MULT.D	F2, F1, F11

MOV.D	F1, F0		#move value in F0 to F1

MULT.D	F0, F0, F10

ADD.D	F0, F0, F2

S.D		F0, 0(R1)	#store the result

ADDI		R1, R1, 8	#increment pointer, 8 bytes per DW

BNEZ		R2, LOOP	#continue till all inputs are processed

SUBI		R2, R2, 1	#decrement element count

a. How many cycles does the current code take for each iteration?

b. Rearrange the code without unrolling to achieve 2 less cycles per iteration.  Show execution cycle next to each code line.

c. If there is an extra floating point register, F8, available, show a place in the above code where register renaming can be use to allow more rearrangement to achieve further improvement with out unrolling.   Write out the modified code with execution cycle next to each code line.

d. Unroll your code in b. twice (so contains 3 iterations) and schedule it to minimize number of stalls.  Assume the second iteration has F0 renamed to F3, F1 renamed to F4, and F2 renamed to F5. Assume the third iteration has F0 renamed to F6, F1 renamed to F7, and F2 renamed to F8

e. What is the effective cycle per iteration for the unrolled loop, where the iteration is referring to an iteration for the original code?

Problem 2:

The following results are seen from a simulation study of five floating-point benchmarks and two integer benchmarks from the SPEC92 suite. The branch misprediction rate nearly doubles from 5% to 9.1% going from 1 thread to 8 threads in an SMT processor. However, the wrong-path instructions fetched (on a misprediction) drops from 24% on a single-threaded processor to 7% on an 8-thread processor.

a. What causes the increase in branch misprediction rate?

b. Why is there a decrease in the number of wrong-path instructions fetched even though there is an increase in branch misprediction rates? (Hint: This is related to the scheduling of threads.)

c. Based on these numbers, what conclusions can you draw about the conflicts caused due to contention and interference on various resources in a multithreaded processor?

Problem 3:

Here is some code for a vector machine:

LP:	LV		V1, R5		#load V1 with new value

MULTSV	V2, F0, V1	#perform the calculation

MULTSV	V3, F1, V1

ADDV		V2, V2, V3

MULTSV	V3, F2, V1

ADDV		V2, V2, V3

SV		V2, R5

SUBI		R5, R5, 8

BNEZ		R5, LP

a) Show the convoys in the above code. (Note that when analyzing convoys you may ignore the last two instructions since those are not vector computations.)

b) Show the execution time in clock cycles of this loop with n elements (Tn); assume Tloop = 15, and Tstart = 7 for all vector codes. Show the equation, and give the value of execution time for vector length n=64.