CS252	HOMEWORK 1

D. A. Patterson

Due Mon. 7/24/06

Problem 1:

Suppose that you have analyzed a benchmark that runs on your company’s processor. This processor runs at 300MHz and has the following characteristics:

Instruction Type 		Frequency (%) 	Cycles

Arithmetic and logical 	35 			1

Load and Store 		25 			2

Branches 			25 			3

Floating Point 			15 			5

Your company is considering a cheaper, lower-performance version of the processor. Their plan is to remove some of the floating-point hardware to reduce the die size.

The wafer on which the chip is produced has a diameter of 10cm, a cost of $2000, and a defect rate of 1 / (cm2). The manufacturing process has an 80% wafer yield and a value of 2 for alpha.

The current processor has a die size of 12mm 12mm. The new chip has a die size of 10mm x 10mm, and floating point instructions will take 13 cycles to execute.

a) What is the CPI and MIPS rating of this processor running this benchmark?

b) What is the CPI and MIPS rating of the new processor?

c) What is the original cost per (working) processor?

d) What is the new cost per (working) processor?

e) Assume that we are considering the other direction of improving the original processor by increasing the speed of floating point. What is the best possible speedup that we could get, and what would the CPI and MIPS rating be of the new processor?

Problem 2:

Here is some code for a vector machine:

LP:	LV		V1, R5		#load V1 with new value

MULTSV	V2, F0, V1	#perform the calculation

MULTSV	V3, F1, V1

ADDV		V2, V2, V3

MULTSV	V3, F2, V1

ADDV		V2, V2, V3

SV		V2, R5

SUBI		R5, R5, 8

BNEZ		R5, LP

a) Show the convoys in the above code:

b) Show the execution time in clock cycles of this loop with n elements (Tn); assume Tloop = 15. Show the equation, and give the value of execution time for n = 64.

Problem 3:

Consider a branch-target buffer that has penalties of 0, 2, and 2 clock cycles for correct conditional branch prediction, incorrect prediction, and a buffer miss, respectively. Consider a branch-target buffer design that distinguishes conditional and unconditional branches, storing the target address for a conditional branch and the target instruction for an unconditional branch.

a) What is the penalty in clock cycles when an unconditional branch is found in the buffer?

b) Determine the improvement from branch folding for unconditional branches. Assume a 90% hit rate, an unconditional branch frequency of 5%, and a 2-cycle penalty for a buffer miss. How much improvement is gained by this enhancement? How high must the hit rate be for this enhancement to provide a performance gain?

Problem 4:

a) What are pipelining hazards? Give a few examples and describe how they can be resolved.

b) How do you optimize cache performance to achieve the following:

- Reduce miss rate

- Reduce miss penalty

- Reduce hit time

c) What is static branch prediction? What is the downside to it?

d) Why is it important for Tomasulo to issue instructions in-order?

e) What is the limiting factor of Tomasulo’s performance?